## Slide 1
<number>
Lecture 7:
Network & System Management
By: Adal ALashban
1nd semester 1437-1438

## Slide 2
<number>
Telephone Network
- Characteristics:
Reliable - does what is expected of it.
Dependable - always there when you need it.
Good quality (connection) - hearing each other well.
- Reasons:
Good planning, design, and implementation.
Good operation and management of network.

## Slide 3
<number>
Telephone Network Model
Notes: Notice the hierarchy of switches
Primary and secondary routes programmed
Automatic routing
Where is the most likely failure?
Use of Operations Systems to ensure QoS
<number>

## Slide 4
<number>
Data Communication Network
Notes: <number>

## Slide 5
<number>
Internet Configuration
Notes: Walk through the scenario of e-mail from Joe to Sally
<number>

## Slide 6
<number>
Internet Topology

## Slide 7
<number>
Comparison
Telephone Network | TCP/IP, Internet
Terminal telephone | Terminal PDAs, PC, Workstations, …
Application (Content) Voice | Application (Content) Data: File, Message Voice, Image, Video.
Bandwidth Requirement Static (64 kbps) | Bandwidth Requirement Dynamic (kbps ~ Mbps)
Transmission Loop: UTP Trunk: Optical Fiber | Transmission Access: UTP, Coaxial Cable, … Trunk: Coaxial Cable, Optical Fiber
Network Elements (NEs) CPE, Switch, Mux, Cross connect | Network Elements (NEs) Hub, Switch, Bridge, Router

## Slide 8
<number>
Telephone Network | TCP/IP, Internet
Addressing telephone number Intelligent Networks | Addressing MAC, IP, Port, Domain Name, URL
Network Configuration fixed, or seldom changed | Network Configuration Changed frequently
Growth Stable, not changed | Growth grow in dog years, new applications
Network Management Well planned NOCs | Network Management ? Network Management Tools/Systems
Comparison (cont.)

## Slide 9
<number>
Protocols Used in NM
1. SNMP(v1, v2, v3)
Simple Network Management Protocol.
2. ICMP
Internet Control Message Protocol.
Ping , trace route.
3. ARP/RARP
Address Resolution Protocol/ (Reverse ARP).
4. TCP
Socket.
Telnet/SSH
HTTP+XML

## Slide 10
<number>
Common Network Problems
1. Loss of connectivity (Link, Node, Interface)
2. Duplicate IP address (Procedural)
3. Intermittent problems
A system interface problem in a shared medium.
4. Network configuration issues
5. Non-problems
The cause of failure is a mystery. (Turn off , Turn on).
6. Performance problems
The cause of long network delay and increasing the response time.

## Slide 11
<number>
What is Network Management?
Goal:
To ensure that the users of a network receive the IT services with the quality of service (QoS) that they expect.
- Network management includes the deployment, integration and coordination of the hardware, software, and human elements to monitor, test, configure, analyze, evaluate, and control the network and element resources to meet the
real-time, operational performance, and Quality of Service requirements at a reasonable cost.

## Slide 12
<number>
Top-Down View of NM Functions

## Slide 13
<number>
NM Functional Requirements
Fault Management
detection, isolation and correction of abnormal operations.
2. Configuration Management
identify managed resources and their connectivity, discovery.
3. Accounting Management
keep track of usage for charging.
4. Performance Management
monitor and evaluate the behavior of managed resources.
5. Security Management
allow only authorized access and control.
FCAPS

## Slide 14
<number>
1. Fault Management
Manages network problems to keep the network running reliably and efficiently..
Fault management process involves the following steps:
Detecting the problem symptoms.
Isolating the problem.
Fixing the problem automatically (if possible) or manually.
Logging the detection and resolution of the problem.

## Slide 15
<number>
2. Configuration Management
Configuration Management monitors network and system configuration information and stores it in a configuration management database.
The maintenance of this database allows network administrators to track hardware, software, and other network resources.

## Slide 16
<number>
2. Configuration Management (cont.)
Each network device has a variety of information associated with it:
Software version information for the operating system, protocol software, or management software.
Hardware version information for the interfaces or hardware controllers.
Contact information indicating who to contact if problems with the device arise.
Location information indicating the physical location of the device.

## Slide 17
<number>
2. Configuration Management (cont.)
CM Information Associated with a Managed Device.

## Slide 18
<number>
3. Accounting Management
Measures network utilization parameters in order to regulate individual and group uses of the network.
Minimizes network problems and maximizes fairness of user access to the network because network resources can be portioned based on network capacity and user needs.

## Slide 19
<number>
4. Performance Management
Maintains internetwork performance at acceptable levels by measuring and managing various network performance variables.
Performance variables include network throughput, user response times, line utilization, and others.
Performance management involves three basic steps:
Gathering data relating to key performance variables.
Analyzing data to determine the normal (baseline) performance levels.
Determining appropriate performance thresholds for each variable so that exceeding these thresholds indicates a network problem worthy of attention.

## Slide 20
<number>
4. Performance Management (cont.)
100
80
60
40
20
10
Last
3.000
Average
16.154
Minimum
63.000
Maximum
2.000
Duration
1:40
Color
Scale
Counter
Instance
Parent
Object
Computer
1.000
1.000
1.000
1.000
1.000
- - -
- - -
- - -
- - -
- - -
\\LONDON
\\LONDON
\\LONDON
\\LONDON
\\LONDON
Processor
Process
PhysicalDisk
Memory
FTP Service
% Processor Time
% Processor Time
% Disk Time
Page/sec
Bytes Received/sec
_Total
explorer
0 C: D:
- - -
Default FTP Site
Performance
Console
Window
Help
Action View Favorites
Tree
Favorites
Console Root
System Monitor
Performance Logs and Alerts

## Slide 21
<number>
4. Performance Management (cont.)
Reactive:
When performance becomes unacceptable (that is, a user-defined threshold is exceeded), the managed device reacts by sending an alert to the network management system (NMS).
Proactive:
Simulation is used to project how network growth will affect performance metrics. These simulations alert administrators to impending problems before they affect network users.

## Slide 22
<number>
4. Performance Management (cont.)
Reactive PM Components:
The management entity continually monitors performance variables in managed devices.
When a particular performance threshold is exceeded, the NMS or the managed device detects the problem.
If the managed device detects the problem, it generates an alert and sends it to the NMS.
The NMS takes an appropriate action, such as alerting the network administrator.

## Slide 23
<number>
Windows Task Manager
Windows Task Manager
File Options View Windows Help
Applications
Processes
Performance
Task
Status
Building Schematic - Paint
Memo to Supervisor - WordPad
Calculator
My Computer
Running
Running
Running
Running
End Task
Switch To
New Task...
Processes: 30
CPU Usage: 2%
Mem Usage: 103500K / 310892K
Windows Task Manager
File Options View Help
Processes: 30
CPU Usage: 6%
Mem Usage: 103452K / 310892K
Applications
Processes
Performance
Image Name
PID
CPU
CPU Time
Mem Usage
System Idle Process
System
smss.exe
csrss.exe
winlogon.exe
services.exe
lsass .exe
svchost .exe
spoolsv .exe
mspaint .exe
msdtc .exe
inojobsv .exe
dfssvc .exe
svchost .exe
ismserv .exe
llssrv .exe
ntfrs.exe
regsvc.exe
0
8
168
196
220
148
160
472
492
624
704
808
824
840
864
880
928
968
96
00
00
00
00
00
00
00
00
00
02
00
00
00
00
00
00
00
4:52:37
0:00:27
0:00:00
0:00:20
0:00:09
0:00:14
0:00:32
0:00:00
0:00:00
0:00:04
0:00:00
0:07:46
0:00:00
0:00:00
0:00:00
0:00:01
0:00:09
0:00:00
16 K
212 K
344 K
1,820 K
4,408 K
8,228 K
15,768 K
2,648 K
4,184 K
352 K
3,428 K
5,704 K
2,336 K
3,416 K
5,348 K
3,860 K
1,108 K
844 K
Show processes from all users
End Process
Windows Task Manager
File Options View Help
Applications
Processes
Performance
Processes: 30
CPU Usage: 3%
Mem Usage: 101600K / 310892K
CPU Usage
MEM Usage
CPU Usage History
Memory Usage History
Totals
Commit Charge (K)
Physical Memory (K)
Kernel Memory (K)
3%
10 1600K
Handles
Threads
Processes
Total
Limit
Peak
Total
Available
System Cache
Total
Paged
Nonpaged
5932
381
30
130612
27740
50704
101600
310892
116896
22804
15704
7100

## Slide 24
<number>
5. Security Management
Access control:
Controls access to network resources, and prevents network sabotage (intentional or unintentional) and unauthorized access to sensitive information.
Aids administrators in creating a secure network environment. This includes:
partitioning network resources into authorized and unauthorized areas,
mapping groups of users to those areas, and monitoring, policing, and logging user access to resources in those areas.
Security monitoring:
Security event collection.
Event analysis, correlation and alert generation.
Alert handling.

## Slide 25
<number>
Network Management Systems
- A network management system (NMS) is a collection of tools for network monitoring and control based on the manager-agent paradigm.
- NMS typically provides a GUI through which most or all management tasks can be performed.
- Many commercial and freely available NMSs exist:
1. Commercial:
HP OpenView, IBM NetView, Sun Net Manager, Cisco works and etc.
2. Open source:
OpenNMS , Nagios and etc.

## Slide 26
<number>
Standard Management Frameworks
1. Internet Network Management Framework (IETF)
SNMPv1
SNMPv2
SNMPv3
2. OSI Network Management Framework (ISO/ITU-T)
CMIP (X.700 Series)
3. Telecommunication Management Network (ITU-T)
TMN (M.3000 Series)

## Slide 27
<number>
Standard Management Frameworks (cont.)
4. Distributed Management Task Force (DMTF)
DMI, CIM, WBEM
5. TeleManagement Forum
MTNM, eTOM, and etc.

## Slide 28
<number>
Status and Future Trends
Status:
SNMP management.
Limited CMIP management.
Operations systems
Future trends:
Object-oriented approach.
Service and policy management.
Web-based management.
XML-base management.

## Slide 29
<number>
Thank You