## Slide 1: Lecture 7: Data Link Layer Protocols (Part2): Frame Relay
RISANURI HIDAYAT
FRAME RELAY
<number>

## Slide 2: Frame Relay
Frame Relay is a high-performance WAN protocol that operates at the physical and data link layers of the OSI reference model.
Frame Relay originally was designed for use across Integrated Services Digital Network (ISDN) interfaces
FRAME RELAY
<number>

## Slide 3: Packet Switching
Frame Relay is based on packet-switched technology.
The following two techniques are used in packet-switching technology:
  Variable-length packets
  Statistical multiplexing
FRAME RELAY
<number>

## Slide 4: Frame Relay Devices
Devices attached to a Frame Relay WAN fall into the following two general categories:
  Data terminal equipment (DTE)
  Data circuit-terminating equipment (DCE)
Examples of DTE devices are terminals, personal computers, routers, and bridges.
FRAME RELAY
<number>

## Slide 5
DCEs are carrier-owned internetworking devices.
The purpose of DCE equipment is to provide clocking and switching services in a network, which are the devices that actually transmit data through the WAN.
In most cases, these are packet switches
FRAME RELAY
<number>
Packet Switching

## Slide 6: Frame Relay Devices
FRAME RELAY
<number>

## Slide 7: Frame Relay Virtual Circuits
Frame Relay provides connection-oriented data link layer communication.
This service is implemented by using a Frame Relay virtual circuit, which is a logical connection created between two data terminal equipment (DTE) devices across a Frame Relay packet-switched network (PSN).
FRAME RELAY
<number>

## Slide 8: Frame Relay Virtual Circuits
Virtual circuits provide a bidirectional communication path from one DTE device to another and are uniquely identified by a data-link connection identifier (DLCI).
A number of virtual circuits can be multiplexed into a single physical circuit for transmission across the network.
FRAME RELAY
<number>

## Slide 9: Frame Relay Virtual Circuits
A virtual circuit can pass through any number of intermediate DCE devices (switches) located within the Frame Relay Packet Switched Network (PSN).
Frame Relay virtual circuits fall into two categories:
  Switched virtual circuits (SVCs)
  Permanent virtual circuits (PVCs).
FRAME RELAY
<number>

## Slide 10: Switched Virtual Circuits
Switched virtual circuits (SVCs) are temporary connections used in situations requiring only interrupted data transfer between DTE devices across the Frame Relay network.
  Call setup—VC between two Frame Relay DTE devices is established.
  Data transfer—Data is transmitted between the DTE devices over the VC.
  Idle—The connection between DTE devices is still active, but no data is transferred. If an SVC remains in an idle state for a defined period of time, the call can be terminated.
  Call termination—The virtual circuit between DTE devices is terminated.
FRAME RELAY
<number>

## Slide 11: Switched Virtual Circuits
Few manufacturers of Frame Relay DCE equipment support switched virtual circuit connections. Therefore, their actual deployment is minimal in today's Frame Relay networks.
Previously not widely supported by Frame Relay equipment, SVCs are now the norm.
Companies have found that SVCs save money in the end because the circuit is not open all the time
FRAME RELAY
<number>

## Slide 12: Permanent Virtual Circuits
Permanent virtual circuits (PVCs) are permanently established connections that are used for frequent and consistent data transfers between DTE devices across the Frame Relay network.
DTE devices can begin transferring data whenever they are ready because the circuit is permanently established.
FRAME RELAY
<number>

## Slide 13: Permanent Virtual Circuits
Communication across a PVC does not require the call setup and termination states that are used with SVCs.
    Data transfer—Data is transmitted between the DTE devices over the virtual circuit.
    Idle—The connection between DTE devices is active, but no data is transferred. Unlike SVCs, PVCs will not be terminated under any circumstances when in an idle state.
FRAME RELAY
<number>

## Slide 14: Data-Link Connection Identifier
Frame Relay virtual circuits are identified by data-link connection identifiers (DLCIs).
DLCI values typically are assigned by the Frame Relay service provider (for example, the telephone company).
Frame Relay DLCIs have local significance, which means that their values are unique in the LAN, but not necessarily in the Frame Relay WAN
FRAME RELAY
<number>

## Slide 15: Data-Link Connection Identifier
A Single Frame Relay Virtual Circuit Can Be Assigned Different DLCIs on Each End of a VC
FRAME RELAY
<number>

## Slide 16: Congestion-Control Mechanisms
Frame Relay reduces network overhead by implementing simple congestion-notification mechanisms rather than explicit, per-virtual-circuit flow control.
Frame Relay implements two congestion-notification mechanisms:
  Forward-explicit congestion notification (FECN)
  Backward-explicit congestion notification (BECN)
FRAME RELAY
<number>

## Slide 17: Congestion-Control Mechanisms
FECN and BECN each is controlled by a single bit contained in the Frame Relay frame header.
The Frame Relay frame header also contains a Discard Eligibility (DE) bit, which is used to identify less important traffic that can be dropped during periods of congestion.
FRAME RELAY
<number>

## Slide 18: Congestion-Control Mechanisms
The FECN bit is part of the Address field in the Frame Relay frame header.
The FECN mechanism is initiated when a DTE device sends Frame Relay frames into the network.
FRAME RELAY
<number>
If the network is congested, DCE devices (switches) set the value of the frames' FECN bit to 1. When the frames reach the destination DTE device, the Address field (with the FECN bit set) indicates that the frame experienced congestion in the path from source to destination. The DTE device can relay this information to a higher-layer protocol for processing. Depending on the implementation, flow control may be initiated, or the indication may be ignored.

## Slide 19: Congestion-Control Mechanisms
The BECN bit is part of the Address field in the Frame Relay frame header.
DCE devices set the value of the BECN bit to 1 in frames traveling in the opposite direction of frames with their FECN bit set.
FRAME RELAY
<number>

## Slide 20
This informs the receiving DTE device that a particular path through the network is congested.
The DTE device then can relay this information to a higher-layer protocol for processing.
Depending on the implementation, flow-control may be initiated, or the indication may be ignored
FRAME RELAY
<number>
Congestion-Control Mechanisms

## Slide 21: Frame Relay Discard Eligibility
The DE bit is part of the Address field in the Frame Relay frame header.
The Discard Eligibility (DE) bit is used to indicate that a frame has lower importance than other frames.
FRAME RELAY
<number>

## Slide 22: Frame Relay Discard Eligibility
DTE devices can set the value of the DE bit of a frame to 1 to indicate that the frame has lower importance than other frames.
When the network becomes congested, DCE devices will discard frames with the DE bit set.
FRAME RELAY
<number>

## Slide 23: Frame Relay Error Checking
Frame Relay uses a common error-checking mechanism known as the cyclic redundancy check (CRC).
The CRC compares two calculated values to determine whether errors occurred during the transmission from source to destination.
Frame Relay reduces network overhead by implementing error checking rather than error correction.
FRAME RELAY
<number>

## Slide 24: Frame Relay Local Management Interface
The Local Management Interface (LMI) is a set of enhancements to the basic Frame Relay specification
The LMI global addressing extension gives Frame Relay (DLCI) values global rather than local significance.
DLCI values become DTE addresses that are unique in the Frame Relay WAN.
FRAME RELAY
<number>

## Slide 25: Frame Relay Local Management Interface
LMI virtual circuit status messages provide communication and synchronization between Frame Relay DTE and DCE devices.
These messages are used to periodically report on the status of PVCs.
FRAME RELAY
<number>

## Slide 26: Frame Relay Network Implementation
A common private Frame Relay network implementation is to equip a T1 multiplexer with both Frame Relay and non-Frame Relay interfaces.
Frame Relay traffic is forwarded out the Frame Relay interface and onto the data network.
FRAME RELAY
<number>

## Slide 27: Frame Relay Network Implementation
Non-Frame Relay traffic is forwarded to the appropriate application or service, such as a private branch exchange (PBX) for telephone service or to a video-teleconferencing application.
FRAME RELAY
<number>

## Slide 28: Frame Relay Network Implementation
FRAME RELAY
<number>

## Slide 29: Public Carrier-Provided Networks
In public carrier-provided Frame Relay networks, the Frame Relay switching equipment is located in the central offices of a telecommunications carrier.
Subscribers are charged based on their network use but are relieved from administering and maintaining the Frame Relay network equipment and service.
FRAME RELAY
<number>

## Slide 30: Public Carrier-Provided Networks
DCE equipment either will be customer-owned or perhaps will be owned by the telecommunications provider as a service to the customer. Generally, the DCE equipment also is owned by the telecommunications provider.
The majority of today's Frame Relay networks are public carrier-provided networks.
FRAME RELAY
<number>

## Slide 31: Private Enterprise Networks
More frequently, organizations worldwide are deploying private Frame Relay networks.
In private Frame Relay networks, the administration and maintenance of the network are the responsibilities of the enterprise (a private company).
All the equipment, including the switching equipment, is owned by the customer
FRAME RELAY
<number>

## Slide 32: Frame Relay Frame Formats
Flags indicate the beginning and end of the frame.
Three primary components make up the Frame Relay frame: the header and address area, the user-data portion, and the frame check sequence (FCS).
The address area, which is 2 bytes in length, is comprised of 10 bits representing the actual circuit identifier and 6 bits of fields related to congestion management. This identifier commonly is referred to as the data-link connection identifier (DLCI).
<number>
Fields length in bytes

## Slide 33: Frame Relay Frame Formats
Flags—Delimits the beginning and end of the frame. The value of this field is always the same and is represented either as the hexadecimal number 7E or as the binary number 01111110.
Address—Contains the following information:
  DLCI
  Extended Address (EA)
  C/R
  Congestion Control
    (FECN)
    (BECN)
    Discard eligibility (DE)
FRAME RELAY
<number>

## Slide 34: Frame Relay Frame Formats
DLCI—The 10-bit DLCI is the essence of the Frame Relay header.
  This value represents the virtual connection between the DTE device and the switch.
  Each virtual connection that is multiplexed onto the physical channel will be represented by a unique DLCI.
  The DLCI values have local significance only, which means that they are unique only to the physical channel on which they reside.
FRAME RELAY
<number>

## Slide 35: Frame Relay Frame Formats
Extended Address (EA)—The EA is used to indicate whether the byte in which the EA value is 1 is the last addressing field.
  If the value is 1, then the current byte is determined to be the last DLCI octet.
  .The eighth bit of each byte of the Address field is used to indicate the EA.
FRAME RELAY
<number>

## Slide 36: Frame Relay Frame Formats
C/R—The C/R is the bit that follows the most significant DLCI byte in the Address field. The C/R bit is not currently defined.
Congestion Control—This consists of the 3 bits that control the Frame Relay congestion-notification mechanisms.
  These are the FECN, BECN, and DE bits, which are the last 3 bits in the Address field.
FRAME RELAY
<number>

## Slide 37: Frame Relay Frame Formats
Forward-explicit congestion notification (FECN)
  A single-bit field that can be set to a value of 1 by a switch to indicate to an end DTE device, such as a router, that congestion happened in the direction of the frame transmission from source to destination.
  The primary benefit of the use of the FECN and BECN fields is the capability of higher-layer protocols to react intelligently to these congestion indicators.
FRAME RELAY
<number>

## Slide 38: Frame Relay Frame Formats
  Backward-explicit congestion notification (BECN)
    Single-bit field that, when set to a value of 1 by a switch, indicates that congestion happened in the network in the direction opposite of the frame transmission from source to destination.
  Discard eligibility (DE)
    Set by the DTE device, such as a router, to indicate that the marked frame is of lesser importance relative to other frames being transmitted.
    Frames that are marked as "discard eligible" should be discarded before other frames in a congested network.
FRAME RELAY
<number>

## Slide 39: Frame Relay Frame Formats
Data—
  Contains encapsulated upper-layer data.
  Each frame in this variable-length field includes a user data or payload field that will vary in length up to 16,000 octets.
  This field serves to transport the higher-layer protocol packet (PDU) through a Frame Relay network.
Frame Check Sequence—
  Ensures the integrity of transmitted data.
  This value is computed by the source device.
  Verified by the receiver to ensure integrity of transmission.
FRAME RELAY
<number>