## Slide 1: Lecture 8: ATM
Networks: ATM
Asynchronous Transfer Mode
Dr. Najla Al-Nabhan
CT 1403,

## Slide 2: ATM overview
Promising technology in early 90s (why?)
Connection-oriented (virtual circuits)
Support for QoS (reserve bandwidth and buffer space for each VC at switches)

## Slide 3: ATM
Networks: ATM
ATM is a high-speed networking standard designed to support both voice and data communications.
ATM is normally utilized by Internet service providers on their private long-distance networks.
ATM operates at the data link layer (Layer 2 in the OSI model) over either fiber or twisted-pair cable.

## Slide 4: Areas of Application
Infrastructure: LANs and Backbones
Asynchronous transfer mode (ATM) is a high-performance, cell-oriented switching and multiplexing technology that utilizes fixed-length packets to carry different types of traffic.
ATM is a technology that will enable carriers to capitalize on a number of revenue opportunities through multiple ATM classes of services;
  high-speed local-area network (LAN) interconnection;
  voice, video, and future multimedia applications in business markets in the short term; and in community and residential markets in the longer term.

## Slide 5: Circuit Switching and Packet Switching
ATM is circuit switched because it establishes virtual circuits for communication
At the same time, the virtual circuits are established over packet switched networks
As such, it combines the benefits of circuit switched and packet switched technologies

## Slide 6: ATM Usage and Bandwidth
In theory, ATM can be deployed from small LANs to very large WANs
  At present, it is used mostly on backbones, but this may change in the future with declining prices for ATM equipment
ATM deployments can operate at speeds starting in the Mbps range scaling up to Gpbs range
  Speed wise, it is very scalable

## Slide 7: ATM’s Efficiency
It is an asynchronous technology and it uses the links based on the need for information to be transmitted
ATM carries information based on fixed length cells
  Compare this to the other packet switching technologies such as Frame Relay etc. where each packet may be of a different length
The length of each cell is 53 Bytes
  First 5 bytes are used as the cell header
  Next 48 bytes are used as the payload carrying the data

## Slide 8: ATM Cell Format
Header
Payload (Data)
5 Bytes
48 Bytes

## Slide 9: Fixed Length Cell Advantage
Delay or latency is significantly reduced
  ATM is therefore suited for voice and video transmission
Fixed length cells make it easier to switch data across multiple networks
  ATM networks are built based on switches and not routers
Fixed length cell is similar to container based road transportation
  Some parallels can be drawn with respect to the advantage of fixed length transportation based on the benefits of container transportation

## Slide 10
Networks: ATM
MUX
`
Wasted bandwidth
ATM
TDM
4 3 2 1 4 3 2 1 4 3 2 1
4 3 1 3 2 2 1
Voice
Data packets
Images
Figure 7.37
Asynchronous Transfer Mode (ATM)
Leon-Garcia & Widjaja: Communication Networks
Copyright ©2000 The McGraw Hill Companies

## Slide 11
ATM Network
H
H
H
H
H
H
H
H
Voice Video Data
Voice Video Data
BISDN
Services
BISDN
Services
Reassembly
User Applications
User Applications
Workstation
Workstation
Multiplexing
Demultiplexing
H
H
H
H
H
H
Segmentation

## Slide 12: ATM Devices
ATM networks are built around two categories of devices
  ATM Switch
  ATM end-point
An ATM switch can be connected to either another ATM switch or and ATM end-point

## Slide 13: ATM End-Points
Will contain and ATM end-point adapter
Examples of ATM end-points
  Workstations
  LAN switches
  Routers
  DSU/CSU Units
  Video Coder-Decoders (CODECs)

## Slide 14: ATM Switches and Interfaces
ATM switch supports two types of interfaces
  User-Network Interface (UNI)
    Connects an ATM end-point to a switch
  Network-Network Interface (NNI)
    Connects two ATM switches
  Broadband Inter-Carrier Interface (BICI)
    Connects two public switches from different service providers

## Slide 15: Public and Private Interfaces
UNI and NNI can further be divided to two types
One is known as the private type and the other is known as the public type
Public | Private | 
1- Connects an ATM end-point to a public ATM switch. 2- Connect private ATM switch to public ATM switch. | Connects an ATM end-point to a private ATM switch. | UNI
Connects two ATM switches within the same public organization. | Connects two ATM switches within the same private organization. | NNI

## Slide 16: Public and Private Interfaces
Source: CISCO
Public

## Slide 17: Virtual Connection Composition
There can be a number of virtual paths (VP) along a physical connection (Transmission Path)
Also there can be a number of virtual circuits (VC) within a virtual path

## Slide 18: VPIs and VCIs
ATM connection identifiers: 8b VPI + 16b VCI
Two-level hierarchy:
  Virtual paths are used between major network nodes
  Virtual circuits are multiplexed in same virtual paths
Objective: backbone switches need smaller VC table

## Slide 19: ATM Cell Structure
Flow Control | VPI (First 4 bits) | 
VPI (Last 4 bits) | VCI (First 4 bits) | 
VCI (Middle 8 bits) |  | 
VCI (Last 4 bits) | Payload type | PRIO
Cyclic Redundancy Check |  | 
Bits: 0 7
48 Data Octets start here

## Slide 20: ATM Protocol Architecture
Networks: ATM
ATM Adaptation Layer (AAL) – the protocol for packaging data into cells is collectively referred to as AAL.
Must efficiently package higher level data such as voice samples, video frames and datagram packets into a series of cells.

## Slide 21
Networks: ATM
AAL
ATM
User information
User information
AAL
ATM
PHY
PHY
ATM
PHY
ATM
PHY
…
End system
End system
Network
Figure 9.4
Leon-Garcia & Widjaja: Communication Networks
Copyright ©2000 The McGraw Hill Companies

## Slide 22: ATM Architecture
Networks: ATM
An AAL is further divided into:
  The Convergence Sublayer (CS)
  manages the flow of data to and from SAR sublayer.
  The Segmentation and Reassembly Sublayer (SAR)
  breaks data into cells at the sender and reassembles
  cells into larger data units at the receiver.

## Slide 23: Segmentation And Reassembly (SAR)
Also referred to as “fragmentation and reassembly” (in the IP context)
SAR is performed by ATM Adaptation Layer (AAL)
  AAL attaches an additional header to the packet needed for reassembly at the receiver
  Five different AAL protocols were defined; AAL5 was the most popular in data networks
AAL
A
TM
AAL
A
TM
…
…