## Slide 1: CT 1502 Planning and Design of Communication Networks Local Area Networks (LANs) & Networks Inter-Connection Chapter 5
Nada Al Dosary Aldosary.na@gmail.com
http://ct1502.edublogs.org

## Slide 2
Outlines
Understanding Local Area Networks (LANs)
LAN Connectivity
LAN Protocols
Network Inter-connectivity

## Slide 3
Understanding Local Area Networks (LANs)

## Slide 4
Understanding Local Area
Networks (LANs)
Networks are categorized by:
  Distance (المسافة)
  Capacity(السعة)

## Slide 5
Understanding Local Area
Networks (LANs)
Capacity (speed)
(bps)
Distance (meter)
Local
Area Network
(LAN)
Metropolitan Area Network
(MAN)
Wide Area Network
(WAN)
Processor
Connection
High-Speed LAN
High-Speed WAN

## Slide 7: Understanding Local Area Networks (LANs)
Local Area Network(LAN): is a computer network within a small geographical area such as a home, school, computer laboratory, office building or group of buildings.
Local is “close” (قريب)
  10m – 1000m
Using high speed, high capacity transmitter mediums with low cost
Capacity and traffic can be balanced(يُوازن) easily

## Slide 8: General LAN Structure
user
user
user
user
user
user
user
user
Connection networks
of network center
User connections and service centers
services and access

## Slide 9: Sending Data Through LAN Types
Baseband: send one signal through wire medium connection
Broadband: send more then one signal through medium connection using supporting hardware

## Slide 10
LAN Connectivity

## Slide 11: LAN Connectivity
LAN Channels
Network Topology
Structured Cabling

## Slide 12: LAN Channels
Wire channels:
  Twisted Pair:
    Shielded
    Unshielded
  Coaxial Cable:
    Baseband
    Broadband
  Fiber optical cables
    Different types
    High speed networks

## Slide 13: LAN Channels
Wireless channels:
  Microwave: 900 MHz- 20 GHz
  Infrared: 103 GHz - 105 GHz

## Slide 14
LAN Topology

## Slide 15: LAN Topology
Bus topology
Ring topology
Star topology

## Slide 16: LAN Topology
Bus topology

## Slide 17: LAN Topology
Ring topology

## Slide 18: LAN Topology
Star topology

## Slide 19: Structured Cabling
Network cabling has to be fixable(مرنة)
To change the structure cabling to meet the organization's need
Cabling types:
  Horizontal: between room at the same floor
  Vertical: between floors

## Slide 20
LAN Protocols

## Slide 21: LAN Protocols: Basic Elements
ISO-OSI Protocols
Set on Data Link Layer
Two parts:
  LLC: Logical Link Control
  MAC: Medium Access Control
  LLC: Logical Link Control
  (Linked to upper layer)
  MAC: Medium Access Control
  (Linked to physical layer)
  Data Link
  Layer
  Physical Layer

## Slide 22: MAC (Medium Access Control)
CSMA-CD: Carrier Sense Multiple Access with Collision Detection
Token Detection

## Slide 23: MAC: CSMA-CD

## Slide 24: MAC: CSMA-CD
Collision(تصادم): is the result of two devices on the same Ethernet network attempting to transmit data at exactly the same time.
The network detects(يكشف) the "collision" of the two transmitted packets and discards(يتجاهل) them both.
Jam signal: is a signal that carries a 32-bit binary pattern sent by a data station to inform the other stations that they must not transmit.

## Slide 25: MAC: Token Detection
Token Detection: no message can be access the network unless get “Token”(إذن)
LAN Network gives tokens to number of users at one time to avoid collision

## Slide 26: Standard Specifications
Table 5-1 illustrates the standard specifications of LAN networks
Known as “IEEE 802”,missions and achievement.

## Slide 27
Status
Used
Inactive
Active
Inactive
Used
Used
Used
Canceled
Inactive
Inactive
Active
Inactive
Rejected
Inactive
Inactive
Active
Active

## Slide 28
Network Inter-Connectivity

## Slide 29: Network Inter-Connectivity
“Adaptation”(التوافق) is necessary between protocols to connect two networks
ISO-OSI | Internet | ATM | LANs | 
Application | Service Protocols | Higher Protocols |  | 
Presentation |  |  |  | 
Session |  |  |  | 
Transportation | TCP |  |  | 
Network | IP |  |  | 
 |  | Adaptation | Interface | IEEE 802
Data Link | Connections protocols | ATM | LLC MAC | 
Physical Layer |  |  |  | 
Communication Medium |  |  |  | 

## Slide 30: Inter-connection Equipment
Repeater: Physical layer level
Bridge: Data link layer level
Router: Network layer level
Gateway: Application layer level

## Slide 31: Inter-connection Equipment
Communication channel
Communication channel
Gateway
Inter-connection Equipment
Router
Bridge
Repeater

## Slide 32: Thank you!