## Slide 1: Chapter 2: Introduction to Switched Networks
Routing And Switching
2.0
Notes: <number>
<number>
Cisco Networking Academy program
Routing & Switching
Chapter 2: Introduction to Switched Networks

## Slide 2: Chapter 2
2.0 Introduction
2.1 Basic Switch Configuration
2.2 Switch Security: Management and Implementation
2.0
Notes: <number>
<number>
Chapter 2

## Slide 3: Chapter 2: Objectives
Explain the advantages and disadvantages of static routing
Configure initial settings on a Cisco switch
Configure switch ports to meet network requirements
Configure the management switch virtual interface
Describe basic security attacks in a switched environment
Describe security best practices in a switched environment
Configure the port security feature to restrict network access
2.0.1.1
Notes: <number>
<number>
2.

## Slide 4: Basic Switch Configuration Switch Boot Sequence
POST
Run boot loader software
Boot loader does low-level CPU initialization
Boot loader initializes the flash filesystem
Boot loader locates and loads a default IOS operating system software image into memory and hands control of the switch over to the IOS.
2.0.1.1
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.1 Configure a Switch With Initial Settings
2.1.1.1 Switch Boot Sequence

## Slide 5: Basic Switch Configuration Switch Boot Sequence
In order to find a suitable IOS image, the switch goes through the following steps:
It attempts to automatically boot by using information in the BOOT environment variable
If this variable is not set, the switch performs a top-to-bottom search through the flash file system. It will load and execute the first executable file, if it can.
The IOS operating system then initializes the interfaces using the Cisco IOS commands found in the configuration file, startup configuration, which is stored in NVRAM.
Note: the command boot system can be used to set the BOOT environment variable.
2.1.1.1
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.1 Configure a Switch With Initial Settings
2.1.1.1 Switch Boot Sequence
Note: the BOOT environment variable is set using the boot system global configuration mode command. Use the show bootvar command to see to what the current IOS boot file is set.

## Slide 6: Basic Switch Configuration Recovering From a System Crash
The boot loader can also be used to manage the switch if the IOS can’t be loaded.
The boot loader can be accessed through a console connection by:
  Connect a PC by console cable to the switch console port. Unplug the switch power cord.
  Reconnect the power cord to the switch and press and hold down the Mode button.
  The System LED turns briefly amber and then solid green. Release the Mode button.
The boot loader switch:prompt appears in the terminal emulation software on the PC.
2.1.1.2
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.1 Configure a Switch With Initial Settings
2.1.1.2 Recovering From a System Crash

## Slide 7: Basic Switch Configuration Switch LED Indicators
Each port on Cisco Catalyst switches have status LED indicator lights.
By default these LED lights reflect port activity but they can also provide other information about the switch through the Mode button
The following modes are available on Cisco Catalyst 2960 switches:
System LED
Redundant Power System (RPS) LED
Port Status LED
Port Duplex LED
Port Speed LED
Power over Ethernet (PoE) Mode LED
2.1.1.3
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.1 Configure a Switch With Initial Settings
2.1.1.3 Switch LED Indicators

## Slide 8: Basic Switch Configuration Switch LED Indicators
Cisco Catalyst 2960 switch modes
2.1.1.3
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.1 Configure a Switch With Initial Settings
2.1.1.3 Switch LED Indicators

## Slide 9: Basic Switch Configuration Preparing for Basic Switch Management
In order to remotely manage a Cisco switch, it needs to be configured to access the network
An IP address and a subnet mask must be configured
If managing the switch from a remote network, a default gateway must also be configured
The IP information (address, subnet mask, gateway) is to be assigned to a switch SVI (switch virtual interface)
Although these IP settings allow remote management and remote access to the switch, they do not allow the switch to route Layer 3 packets.
2.1.1.4
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.1 Configure a Switch With Initial Settings
2.1.1.4 Preparing for Basic Switch Management

## Slide 10: Basic Switch Configuration Preparing for Basic Switch Management
2.1.1.5
Do the Buttons on 2.1.1.5
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.1 Configure a Switch With Initial Settings
2.1.1.5 Preparing for Basic Switch Management

## Slide 11: Configure Switch Ports Duplex Communication
2.1.2.1
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.2 Configure Switch Ports
2.1.2.1 Duplex Communication

## Slide 12: Configure Switch Ports Configure Switch Ports at the Physical Layer
2.1.2.2
Do the Buttons on 2.1.2.2
Students do button 2
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.2 Configure Switch Ports
2.1.2.2 Configure Switch Ports at the Physical Layer

## Slide 13: Configure Switch Ports MDIX Auto Feature
Certain cable types (straight-through or crossover) were required when connecting devices
The automatic medium-dependent interface crossover (auto-MDIX) feature eliminates this problem
When auto-MDIX is enabled, the interface automatically detects and configures the connection appropriately
When using auto-MDIX on an interface, the interface speed and duplex must be set to auto
2.1.2.3
Do the Buttons on 2.1.2.3
Students do button 3
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.2 Configure Switch Ports
2.1.2.3 MDIX Auto Feature

## Slide 14: Configure Switch Ports MDIX Auto Feature
2.1.2.3
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.2 Configure Switch Ports
2.1.2.3 MDIX Auto Feature

## Slide 15: Configure Switch Ports MDIX Auto Feature
2.1.2.3
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.2 Configure Switch Ports
2.1.2.3 MDIX Auto Feature

## Slide 16: Configure Switch Ports Verifying Switch Port Configuration
2.1.2.4
Do the Buttons on 2.1.2.4
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.2 Configure Switch Ports
2.1.2.4 Verifying Switch Port Configuration

## Slide 17: Configure Switch Ports Network Access Layer Issues
2.1.2.5
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.2 Configure Switch Ports
2.1.2.5 Network Access Layer Issues

## Slide 18: Configure Switch Ports Network Access Layer Issues
2.1.2.5
Do the Buttons on 2.1.2.5
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.2 Configure Switch Ports
2.1.2.5 Network Access Layer Issues

## Slide 19: Configure Switch Ports Network Access Layer Issues
Troubleshooting Switch Media (connection) issues
2.1.2.6
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.2 Configure Switch Ports
2.1.2.6 Troubleshooting Network Access Layer Issues

## Slide 20: Configure Switch Ports Network Access Layer Issues
Troubleshooting Interface-related issues
2.1.2.6
Notes: <number>
<number>
2.1 Basic Switch Configuration
2.1.2 Configure Switch Ports
2.1.2.6 Troubleshooting Network Access Layer Issues

## Slide 21
Tada!
Notes: <number>