## Slide 1: Lecture 3: Introduction to WAN
WAN Technology Overview
Notes: Cisco Networking Academy program
Connecting Networks
Chapter 2: Connecting to the WAN

## Slide 2: Purpose of WANs Why Choose a WAN?
Operates beyond the geographic scope of a LAN
Used to interconnect the enterprise LAN to remote LANs in branch sites and telecommuter sites
Owned by a service provider
Organization must pay a fee to use the provider’s services to connect sites
Notes: 2.1.1.1 Why a WAN?

## Slide 3: Purpose of WANs Are WANs Necessary?
Businesses require communication among geographically separated sites. Examples include:
Regional or branch offices must be able to communicate and share data.
Organizations must share information with other customer organizations.
Mobile workers must access information that resides on corporate networks.
Home computer users must send and receive data across increasingly larger distances. Examples include:
Consumers communicate over the Internet with banks, stores, and a variety of providers of goods and services.
Students do research by accessing library indexes and publications located in other parts of the country and in other parts of the world.
Notes: 2.1.1.2 Are WANs Necessary?

## Slide 4: Purpose of WANs Evolving Networks
Companies expect their networks to perform optimally and to be able to deliver an ever increasing array of services and applications to support productivity and profitability.
SPAN Engineering – example used in the curriculum
Notes: 2.1.1.3 Evolving Networks

## Slide 5: Purpose of WANs Small Office
SPAN Engineering – Environmental Consulting Firm
Been in business for four years, has grown to include 15 employees: six engineers, four computer-aided drawing (CAD) designers, a receptionist, two senior partners, and two office assistants
Uses a single LAN to share information between computers, and to share peripherals, such as a printer, a large-scale plotter, and fax equipment
Upgraded LAN to provide inexpensive VoIP service to save on the costs of separate phone lines for their employees
Connection to the Internet is through a common broadband service called DSL
Uses support services purchased from the DSL provider
Uses a hosting service rather than purchasing and operating its own FTP and email servers
Notes: 2.1.1.4 Small Office

## Slide 6: Purpose of WANs Campus Network
SPAN Engineering – Environmental Consulting Firm
Five years later has grown rapidly.
Contracted to design and implement a full-sized waste conversion facility.
Won other projects in neighboring municipalities and in other parts of the country.
Hired more staff and leased more office space with several hundred employees, organized itself into functional departments.
Network now consists of several subnetworks, each devoted to a different department.
Multiple LANs are joined to create a company-wide network or campus, which spans several floors of the building.
Notes: 2.1.1.5 Campus Network

## Slide 7: Purpose of WANs Small Office – Campus Network
Notes: 2.1.1.5 Campus Network

## Slide 8: Purpose of WANs Branch Networks
Another six years later, SPAN Engineering demand for its services has skyrocketed.
To manage those projects, the company has opened small branch offices closer to the project sites.
SPAN Engineering now has a data center, which houses the various databases and servers of the company. They must now implement a WAN.
For its branch offices that are in nearby cities, the company decides to use private dedicated lines through their local service provider.
For those offices that are located in other countries, the Internet is an attractive WAN connection option.
Although connecting offices through the Internet is economical, it introduces security and privacy issues that the IT team must address.
Notes: 2.1.1.6 Branch Networks

## Slide 9: Purpose of WANs Branch Networks (cont.)
Notes: 2.1.1.6 Branch Networks

## Slide 10: Purpose of WANs Distributed Networks
SPAN Engineering has now been in business for 20 years and has grown to thousands of employees distributed in offices worldwide.
Cost of the network and its related services is a big expense.
Looking to provide the best network services at the lowest cost.
Encouraging teleworking and virtual teams, web-based applications are being used to increase productivity and reduce costs.
Site-to-site and remote access Virtual Private Networks (VPNs) enable the company to use the Internet to connect easily and securely with employees and facilities around the world.
Notes: 2.1.1.7 Distributed Network

## Slide 11: Purpose of WANs Distributed Networks (cont.)
Network requirements can change dramatically as the company grows.
Distributing employees saves costs in many ways, but it puts increased demands on the network.
Network must be able to adapt and grow as the company changes.
Network designers and administrators meet these challenges by carefully choosing network technologies, protocols, and service providers, and by optimizing their networks.
Notes: 2.1.1.7 Distributed Network

## Slide 12: Purpose of WANs Distributed Networks (cont.)
Notes: 2.1.1.7 Distributed Network

## Slide 13: WAN Operations WANs in the OSI Model
WAN access standards typically describe both physical layer delivery methods and data link layer requirements, including physical addressing, flow control, and encapsulation.
Notes: 2.1.2.1 WANs in the OSI Model

## Slide 14: What’s Internet
millions of connected computing devices:
hosts = end systems
Home network
Institutional network
Mobile network
Global ISP
Regional ISP
router
PC
server
wireless
laptop
cellular
handheld
wired
links
access
points
communication links
  fiber, copper, radio, satellite
Packet switches: forward packets (chunks of data)
routers and switches
protocols control sending, receiving of messages
  e.g., TCP, IP, HTTP, Ethernet

## Slide 15: What’s Internet?
  Simply is a “network of networks” or Interconnected ISPs
The Internet is a global system of interconnected computer networks that use the standard Internet protocol suite (TCP/IP) to serve several billion users worldwide.
It is a network of networks that consists of millions of private, public, academic, business, and government networks, of local to global scope, that are linked by a broad array of electronic, wireless, and optical networking technologies.
The Internet carries an extensive range of information resources and services, such as the inter-linked hypertext documents of the World Wide Web (WWW), the infrastructure to support email, etc.

## Slide 16: A closer look at network structure:
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 17: Core Networks
Tier 1 ISP

## Slide 18: Internet Structure: Network of Networks
A packet passes through many networks!
Tier 1 ISP
Tier 1 ISP
Tier 1 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
Tier-2 ISP
local
ISP
local
ISP
local
ISP
local
ISP
local
ISP
Tier 3
ISP
local
ISP
local
ISP
local
ISP