## Slide 1: Binary Number System And Conversion
Digital Electronics
Notes: Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 2: Bridging the Digital Divide
721
234
534
63
935
23
137
275
16
935
145
00100
0101011
10101
010
10010
1101
011011
1101
010
00101101
00100
0101011
011011
1101
00101101
00100
001011
10101
010
10010
1101
011011
1101
010
00101101
00100
0101011
011011
1101
00101
10010
10010
00101101
721
234
534
63
935
23
137
275
16
935
145
Binary-to-Decimal
Conversion
Decimal-to-Binary
Conversion
<number>
Notes: Introductory Slide / Overview of Presentation
Explain that humans use base ten (or decimal), because we have ten fingers and that digital electronics uses base-two (binary) because it only understands two states; ON and OFF. For students to be able to analyze and design digital electronics, they need to be proficient at converting numbers between these two number systems.
Base ten has ten unique symbols (0 – 9) while binary has two unique symbols (0 – 1). Any number can represent a base and the number of symbols it utilizes will always be that number. This is discussed further later in Unit 2.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 3: Decimal ‒to‒ Binary Conversion
The Process : Successive Division
  Divide the Decimal Number by 2; the remainder is the LSB of Binary Number .
  If the quotation is zero, the conversion is complete; else repeat step (a) using the quotation as the Decimal Number. The new remainder is the next most significant bit of the Binary Number.
Example:
  Convert the decimal number 610 into its binary equivalent.
 610 = 1102
<number>
Notes: Review the DECIMAL-to-BINARY conversion process.
Remind the students to subscript all numbers (i.e. Subscript 10 for decimal & subscript 2 for binary)
A common mistake is inverting the LSB and MSB.
The three-dot triangular symbol here stands for the word “therefore” and is used commonly among mathematics scholars.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 4: Dec → Binary : Example #1
Example:
  Convert the decimal number 2610 into its binary equivalent.
<number>
Notes: Pause the power point and allow the student to work on the example. The solution is on the next slide.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 5: Dec → Binary : Example #1
Example:
  Convert the decimal number 2610 into its binary equivalent.
Solution:
 2610 = 110102
<number>
Notes: Here is the solution. If you print handouts, don’t print this page.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 6: Dec → Binary : Example #2
Example:
  Convert the decimal number 4110 into its binary equivalent.
<number>
Notes: Pause the power point and allow the student to work on the example. The solution is on the next slide.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 7: Dec → Binary : Example #2
Example:
  Convert the decimal number 4110 into its binary equivalent.
Solution:
 4110 = 1010012
<number>
Notes: Here is the solution. If you print handouts, don’t print this page.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 8: Dec → Binary : More Examples
1310 = ?
2210 = ?
4310 = ?
15810 = ?
<number>
Notes: If the students need more practice, here are four additional example of DECIMAL to BINARY conversion. The solution is on the next slide.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 9: Dec → Binary : More Examples
1310 = ?
2210 = ?
4310 = ?
15810 = ?
1 1 0 1 2
1 0 1 1 0 2
1 0 1 0 1 1 2
1 0 0 1 1 1 1 0 2
<number>
Notes: Here are the solutions. If you print handouts, don’t print this page.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 10: Binary ‒to‒ Decimal Process
The Process : Weighted Multiplication
  Multiply each bit of the Binary Number by it corresponding bit-weighting factor (i.e. Bit-0→20=1; Bit-1→21=2; Bit-2→22=4; etc).
  Sum up all the products in step (a) to get the Decimal Number.
Example:
  Convert the decimal number 01102 into its decimal equivalent.
 0110 2 = 6 10
0 |  | 1 |  | 1 |  | 0 |  | 
23 |  | 22 |  | 21 |  | 20 |  | 
8 |  | 4 |  | 2 |  | 1 |  | 
0 | + | 4 | + | 2 | + | 0 | = | 610
Bit-Weighting
Factors
<number>
Notes: Review the BINARY-to-DECIMAL conversion process.
Remind the students to subscript all numbers (i.e. Subscript 10 for decimal & subscript 2 for decimal)
Let the students know that as the become more proficient at the conversions, they may not need to write out the Bit-Weighting Factors.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 11: Binary → Dec : Example #1
Example:
  Convert the binary number 100102 into its decimal equivalent.
<number>
Notes: Pause the power point and allow the student to work on the example. The solution is on the next slide.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 12: Binary → Dec : Example #1
Example:
  Convert the binary number 100102 into its decimal equivalent.
100102 = 1810
1 |  | 0 |  | 0 |  | 1 |  | 0 |  | 
24 |  | 23 |  | 22 |  | 21 |  | 20 |  | 
16 |  | 8 |  | 4 |  | 2 |  | 1 |  | 
16 | + | 0 | + | 0 | + | 2 | + | 0 | = | 1810
Solution:
<number>
Notes: Here is the solution. If you print handouts, don’t print this page.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 13: Binary → Dec : Example #2
Example:
  Convert the binary number 01101012 into its decimal equivalent.
<number>
Notes: Pause the power point and allow the student to work on the example. The solution is on the next slide.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 14: Binary → Dec : Example #2
Example:
  Convert the binary number 01101012 into its decimal equivalent.
01101012 = 5310
0 |  | 1 |  | 1 |  | 0 |  | 1 |  | 0 |  | 1 |  | 
26 |  | 25 |  | 24 |  | 23 |  | 22 |  | 21 |  | 20 |  | 
64 |  | 32 |  | 16 |  | 8 |  | 4 |  | 2 |  | 1 |  | 
0 | + | 32 | + | 16 | + | 0 | + | 4 | + | 0 | + | 1 | = | 5310
Solution:
<number>
Notes: Here is the solution. If you print handouts, don’t print this page.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 15: Binary → Dec : More Examples
0110 2 = ?
11010 2 = ?
0110101 2 = ?
11010011 2 = ?
<number>
Notes: If the students need more practice, here are four additional example of DECIMAL to BINARY conversions. The solution is on the next slide.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 16: Binary → Dec : More Examples
0110 2 = ?
11010 2 = ?
0110101 2 = ?
11010011 2 = ?
6 10
26 10
53 10
211 10
<number>
Notes: Here are the solutions. If you print handouts, don’t print this page.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>

## Slide 17: Summary & Review
Successive
Division
  Divide the Decimal Number by 2; the remainder is the LSB of Binary Number .
  If the Quotient Zero, the conversion is complete; else repeat step (a) using the Quotient as the Decimal Number. The new remainder is the next most significant bit of the Binary Number.
  Multiply each bit of the Binary Number by it corresponding bit-weighting factor (i.e. Bit-0→20=1; Bit-1→21=2; Bit-2→22=4; etc).
  Sum up all the products in step (a) to get the Decimal Number.
Weighted
Multiplication
<number>
Notes: Prior to assigning the activity, review the process for DECIMAL-to-BINARY and BINARY-to-DECIMAL.
Binary Number System
Digital Electronics
2.1 Introduction to AOI Logic
Project Lead The Way, Inc.
Copyright 2009
<number>