## Slide 1: Lecture 4: Mobile Computing
By D. Najla Al-Nabhan

## Slide 2: Overview
What is it?
Who needs it?
History
Future

## Slide 3: A computer in 2014?
• Advances in technology
    – More computing power in smaller devices
    – Flat, lightweight displays with low power consumption
    – New user interfaces due to small dimensions
    – More bandwidth (per second? per space?)
    – Multiple wireless techniques
• Technology in the background
    – Device location awareness: computers adapt to their environment
  – User location awareness: computers recognize the location of the user and react appropriately (call forwarding)
• “Computers” evolve
    – Small, cheap, portable, replaceable
    – Integration or disintegration?

## Slide 4: What is Mobile Computing?
• Aspects of mobility
– User mobility: users communicate “anytime, anywhere, with anyone”
(example: read/write email on web browser)
– Device portability: devices can be connected anytime, anywhere to the network
• Wireless vs. mobile Examples
    􀀸 􀀸 Stationary computer
    􀀸 √ Notebook in a hotel
    √ 􀀸 Wireless LANs in historic buildings
    √ √ Personal Digital Assistant (PDA)

## Slide 5: What is Mobile Computing?
• The demand for mobile communication creates the need for
integration of wireless networks and existing fixed networks
– Local area networks: standardization of IEEE 802.11 or HIPERLAN
– Wide area networks: GSM and ISDN
– Internet: Mobile IP extension of the Internet protocol IP

## Slide 6: Application Scenarios
• Vehicles
• Nomadic user
• Smart mobile phone
• Invisible computing
• Wearable computing
• Intelligent house or office
• Meeting room/conference
• Taxi/Police/Fire squad fleet
• Service worker
• Lonely wolf
• Disaster relief and Disaster alarm
• Games
• Military / Security
What is important?

## Slide 7: Vehicles

## Slide 8: Nomadic users
• Nomadic user has laptop/palmtop
• Connect to network infrequently
• Interim period operate in disconnected mode
• Access her or customer data
• Consistent database for all agents
• Print on local printer (or other service)
    – How do we find it?
    – Is it safe?
    – Do we need wires?
• Does nomadic user need her own hardware?
    • Read/write email on web browser
    • Access data OK too

## Slide 9: Smart mobile phone
• Mobile phones get smarter
• Converge with PDA?
• Voice calls, video calls (really?)
• Email or instant messaging
• Play games
• Up-to-date localized information
    Map
    Pull: Find the next Pizzeria
    Push: “Hey, we have great Pizza!”
• Stock/weather/sports info
• Ticketing
• Trade stock
• etc.

## Slide 10: Invisible/ubiquitous/pervasive and wearable computing
• Tiny embedded “computers”
• Everywhere
• Example: Microsoft’s Doll

## Slide 11: Intelligent Office and Intelligent House
• Bluetooth replaces cables
• Plug and play, without the “plug”
• Again: Find the local printer
• House recognizes inhabitant
• House regulates temperature
according to person in a room
• Trade Shows
• Home without cables looks better
• LAN in historic buildings

## Slide 12: Meeting room or Conference
• Share data instantly
• Send a message to someone else in the room
• Secretly vote on controversial issue
• Find person with similar interests
• Broadcast last minute changes
• Ad-Hoc Network

## Slide 13: Taxi / Police / Fire squad / Service fleet
• Connect
• Control
• Communicate
Service Worker
Example: SBB service workers have PDA
  – Map help finding broken signal
  – PDA gives type of signal, so that service person can bring the right tools right away

## Slide 14: Lonely wolf= Remote users
• We really mean everywhere!
• Cargo’s and yachts
• Journalists
• Scientists
• Travelers
• Sometimes cheaper than infrastructure?

## Slide 15: Disaster relief
• After earthquake, tsunami,
volcano, etc:
• You cannot rely on
infrastructure but you need to
orchestrate disaster relief
• Early transmission of patient
data to hospital
• Satellite
• Ad-Hoc network

## Slide 16: Disaster alarm
• With sensors you might be
able to alarm early
• Example: Tsunami
• Example: Cooling room
• Or simpler: Weather station
•Satellite
• Ad-Hoc network

## Slide 17: Games
• Nintendo Gameboy [Advance]: Industry standard mobile game station
• Connectable to other Gameboys
• Can be used as game pad for Nintendo Gamecube
• Cybiko [Extreme] is a competitor that has radio capabilities built in
• Second generation already
• Also email, chat, etc.

## Slide 18: Military / Security
• From a technology standpoint this is similar to disaster relief
• Sensoria says “US army is the
best costumer”
• Not (important) in this course

## Slide 19: Application Scenarios: Discussion
• Vehicles
• Nomadic user
• Smart mobile phone
• Invisible computing
• Wearable computing
• Intelligent house or office
• Meeting room/conference
• Taxi/Police/Fire squad fleet
• Service worker
• Lonely wolf
• Disaster relief and Disaster alarm
• Games
• Military / Security
• Anything missing?
What is important?

## Slide 20: Mobile devices

## Slide 21: Effect of Device Portability
• Energy consumption
– there is no Moore’s law for batteries or solar cells
– limited computing power, low quality displays, small disks
– Limited memory (no moving parts)
– Radio transmission has a high energy consumption
– CPU: power consumption = CV2f
  • C: total capacitance, reduced by integration
  • V: supply voltage, can be reduced to a certain limit
  • f: clock frequency, can be reduced temporally

## Slide 22: Effect of Device Portability
• Limited user interfaces
– compromise between size of fingers and portability
– integration of character/voice recognition, abstract symbols
• Loss of data
– higher probability (e.g., defects, theft)

## Slide 23: Wireless networks in comparison to fixed networks
• Higher loss-rates due to interference
– emissions of, e.g., engines, lightning
• Restrictive regulations of frequencies
– frequencies have to be coordinated, useful frequencies are almost all
occupied
• Low transmission rates
– local some Mbit/s, regional currently, e.g., 9.6kbit/s with GSM

## Slide 24: Wireless networks in comparison to fixed networks
• Higher delays, more jitter
– connection setup time with GSM in the second range, several hundred
milliseconds for other wireless systems, tens of seconds with Bluetooth
• Lower security, simpler active attacking
– radio interface accessible for everyone, base station can be simulated,
thus attracting calls from mobile phones
• Always shared medium
– secure access mechanisms important

## Slide 25: History of Wireless Technologies Development (1980-200?)

## Slide 26: EXISTING CELLULAR NETWORK ARCHITECTURE
A cellular network consists of mobile units linked together to switching equipment, which interconnect the different parts of the network and allow access to the fixed Public Switched Telephone Network (PSTN).
It's incorporated in a number of transceivers called Base Stations (BS).
Every BS is located at a strategically selected place and covers a given area or cell - hence the name cellular communications.
A number of adjacent cells grouped together form an area and the corresponding BSs communicate through a so called Mobile Switching Centre (MSC).

## Slide 27: EXISTING CELLULAR NETWORK ARCHITECTURE
The MSC is the heart of a cellular radio system.
MSC is responsible for
  routing, or switching, calls from the originator to the destination.
  managing the cell,
  for set-up, routing control and termination of the call,
  for management of inter-MSC hand over and supplementary services,
  and for collecting charging and accounting information.
The MSC may be connected to other MSCs or to the PSTN.

## Slide 28: Mobile communication overview
Each cell has a number of channels associated with it.
When a Mobile Station (MS) becomes 'active' it registers with the nearest BS.
The corresponding MSC stores the information about that MS and its position.
This information is used to direct incoming calls to the MS.
If during a call the MS moves to an adjacent cell then a change of frequency will necessarily occur - since adjacent cells never use the same channels. This procedure is called hand over and is the key to Mobile communications.

## Slide 29: History of Wireless Technologies Development (1980-200?)

## Slide 30: Simple Reference Model for mobile computing

## Slide 31: Networking Approaches in mobile Computing

## Slide 32: The Future
With the emphasis increasingly on compact, small mobile computers, it may also be possible to have all the practicality of a mobile computer in the size of a hand held organizer or even smaller.
With the rapid technological advancements in Artificial Intelligence, Integrated Circuitry and increases in Computer Processor speeds, the future of mobile computing looks increasingly exciting.
Use of Artificial Intelligence may allow mobile units to be the ultimate in personal secretaries,
  which can receive emails and paging messages, understand what they are about, and change the individuals personal schedule according to the message.
The working lifestyle will change, with the majority of people working from home, rather than commuting. This may be beneficial to the environment as less transportation will be utilized.

## Slide 33: The Future
As shown in the figure, trends are very much towards ubiquitous or mobile computing.
Interactive television, Video Image Compression, mobility in the home, ie. home shopping etc.this mobility may be pushed to extreme.
The future of Mobile Computing is very promising indeed, although technology may go too far, causing big changes to society.

## Slide 34: Quiz
Next Lecture