## Slide 1: CT1306
Rehab AlFallaj

## Slide 2: Dynamic Routing Protocols
Routing Protocols
Dynamic Routing Protocols
Interior Gateway Protocols
Exterior Gateway Protocols
Static Routing Protocols
Static
Distance victor
RIP
IGRP
Link State Protocols
OSPF
ISIS
Border Gateway Protocols
Default

## Slide 3: Static Routing Protocols
Is a form of routing that occurs when a router uses a manually-configured routing entry, usually manually configured by a network administrator.
Advantages:
  Fixed.
  Do not change if the network is changed or reconfigured.
  Security.
  Control of resources.

## Slide 4: Static Routing Protocols
Disadvantages:
  Time-consuming.
  Error-prone,
  Administrator intervention is required to maintain changing route information.
  Does not scale well with growing networks; maintenance becomes cumbersome.
  Requires complete knowledge of the whole network for proper implementation.

## Slide 5: Static Routing Protocols
When to use static routing:
In stub networks.
To provide a gateway of last resort.
Create a backup route in case a primary route link fails

## Slide 6: Static Routing Protocols
ip routenetworkmask {next-hop-ip | exit-intf }
Default Static Route used when the routing table does not contain a path for a destination network.
ip route 0.0.0.0 0.0.0.0 {exit-intf | next-hop-ip}

## Slide 7: Dynamic Routing Protocols
Used by routers to share information about the reachability and status of remote networks.
Performs network discovery and maintaining routing tables.

## Slide 8: Dynamic Routing Protocols
Open Shortest Path First:
Router(config)# router ospf process_ID
Router(config-router)# network IP_address wildcard_mask area area_#

## Slide 9: Open Shortest Path First Components of OSPF
OSPF Routers Exchange Packets - These packets are used to discover neighboring routers and also to exchange routing information to maintain accurate information about the network.
Notes: 9
8.1.1.3