## Slide 1: Interactions of Radiation With Matter

## Slide 2: Objectives
We have focused in previous lectures on the source of radiation and the types of radiation. We are now in a position to consider what happens when this radiation interacts with matter (mechanisms of energy transfer and its effects on the physical-chemical- and biological level)

## Slide 3: Objectives
Our main reason for doing this is to find out what happens to the radiation as it passes through matter and also to set ourselves up for considering how it interacts with living tissue and understand the chain of events leading to radiation injury. This knowledge also forms the bases of radiation therapy and diagnostic radiology.

## Slide 4: Objectives
Also, Since all radiation detectors are made from some form of matter it is useful to first of all know how radiation interacts so that we can exploit the effects in the design of such detectors and know how it works.

## Slide 5: Ionizing radiation
Ionizing radiation is radiation that has sufficient energy to remove electrons from atoms, creating ions.
Ionizing radiation can be classified into two groups: photons (gamma and X-rays) and particles (alpha, beta, and neutrons(

## Slide 6: A -Basic Concepts Of Interaction of photons with matter
Three possible occurrences when x or gamma photons in the primary beam pass through matter:
  No interaction at all
    Known as transmission
  Absorption
  Scatter
    The latter two are methods of attenuation

## Slide 7: Attenuation Of An X-Ray Photon

## Slide 8: The Three main Interactions Of X and Gamma Rays With Matter
Photoelectric effect
  Very important in diagnostic radiology
Compton scatter
  Very important in diagnostic radiology
Pair production
  Very important in therapeutic & diagnostic radiology

## Slide 9: Photoelectric Effect
All of the energy of the incoming photon is totally transferred to the atom
  Following interaction, the photon ceases to exist
The incoming photon interacts with an orbital electron in an inner shell – usually K
The orbital electron is dislodged
To dislodge the electron, the energy of the incoming photon must be equal to, or greater than the electron’s energy

## Slide 10: Photoelectric Effect
The incoming photon gives up all its energy, and ceases to exist
The ejected electron is now a photoelectron
This photoelectron now contains the energy of the incoming photon minus the binding energy of the electron shell
This photoelectron can interact with other atoms until all its energy is spent

## Slide 11: Photoelectric Effect
A vacancy now exists in the inner shell
To fill this gap, an electron from an outer shell drops down to fill the gap
Once the gap is filled, the electron releases its energy in the form of a characteristic photon
This process continues, with each electron emitting characteristic photons, until the atom is stable
The characteristic photon produces relatively low energies and is generally absorbed in tissue

## Slide 12: Photoelectric absorption (I-131)

## Slide 13: The Byproducts of the Photoelectric Effect
Photoelectrons
Characteristic photons

## Slide 14: The Probability of Occurrence
Depends on the following:
  The energy of the incident photon(E)
  The atomic number of the irradiated object(Z)
  It increases as the photon energy decreases, and the atomic number of the irradiated object increases
  The probability of photoelectric absorption, is roughly proportional to (Z/E)3
  This type of interaction is prevalent in the diagnostic keV range – 30 - 150

## Slide 15: What Does This All Mean?
Bones are more likely to absorb radiation(Higher Z)
  This is why they appear white on the film
Soft tissue allows more radiation to pass through than bone (Lower Z)
  These structures will appear gray on the film
Air-containing structures allow more radiation to pass through
  These structures will appear black on the film

## Slide 16: Compton Scattering
An incoming photon is partially absorbed in an outer shell electron
The electron absorbs enough energy to break the binding energy, and is ejected
The ejected electron is now a Compton electron
Not much energy is needed to eject an electron from an outer shell
The incoming photon, continues on a different path with less energy as scattered radiation

## Slide 18: Byproducts Of Compton Scatter
Compton scattered electron
  Possesses kinetic energy and is capable of ionizing atoms
  Finally recombines with an atom that has an electron deficiency
Scattered x-ray photon with lower energy
  Continues on its way, but in a different direction
  It can interact with other atoms, either by photoelectric or Compton scattering
  It may emerge from the patient as scatter

## Slide 19: Probability Of Compton Scatter Occurring
Increases as the incoming photon energy increases up to certain limit then decreases as the photon energy increases.
Independent on Z of the absorber.
The Compton process is most important for energy absorption for soft tissues in the range from 100 keV to 2MeV.

## Slide 20: Pair Production
Incoming photon must have an energy of at least 1.02 MeV
This process is a conversion of energy into matter and then matter back into energy
Two electrons are produced in this interaction

## Slide 21: Pair Production
An incoming photon of 1.02 MeV or greater interacts with the nucleus of an atom
The incoming photon disappears
The transformation of energy results in the formation of two particles
Negatron
  Possesses negative charge
Positron
  Possesses a positive charge

## Slide 22: Pair Production

## Slide 23: Positrons
Considered antimatter
Do not exist freely in nature
Cannot exist near matter
Will interact with the first electron they encounter
An electron and the positron destroy each other during interaction
  Known as the annihilation reaction
This converts matter back into energy
Both the positron and electron disappear
Two gamma photons are released with an energy of .51 MeV

## Slide 24: Pair Production
The produced gamma photons may interact with matter through pair production or Compton scatter
Pair production is used for positron emission tomography, a nuclear medicine imaging procedure
It is also used in radiation therapy

## Slide 25: Pair production probability
· Increases with increasing photon energy
· Increases with atomic number approximately as Z2

## Slide 26
Z of absorber
Photon Energy, in Mev

## Slide 27: B -Interactions Of Particulate Radiation With Matter
Alpha particles ionize by attracting an electron from an atom
Beta particles ionize by repelling an electron from an atom

## Slide 28: Particle interactions
Energetic charged particles interact with matter by electrical forces and lose kinetic energy via:
  Excitation
  Ionization
  Radiative losses

## Slide 29: Charged Particle Tracks
Electrons follow tortuous paths in matter as the result of multiple scattering events
  Ionization track is sparse and nonuniform
Larger mass of heavy charged particle results in dense and usually linear ionization track
Path length is actual distance particle travels; range is actual depth of penetration in matter

## Slide 30: Path lengths vs. ranges

## Slide 31: Linear Energy Transfer
Amount of energy deposited per unit path length is called the linear energy transfer (LET)
Expressed in units of eV/cm
LET of a charged particle is proportional to the square of the charge and inversely proportional to its kinetic energy(velocity)
High LET radiations (alpha particles, protons, etc.) are more damaging to tissue than low LET radiations (electrons, gamma and x-rays)

## Slide 32: Specific Ionization
Number of primary and secondary ion pairs produced per unit length of charged particle’s path is called specific ionization
  Expressed in ion pairs (IP)/mm
Increases with electrical charge of particle
Decreases with increase incident particle velocity

## Slide 33: Bremsstrahlung(Radiative losses)
Probability of bremsstrahlung production per atom is proportional to the square of Z of the absorber
Energy emission via bremsstrahlung varies inversely with the square of the mass of the incident particle (Z/M)2
  Protons and alpha particles produce less than one-millionth the amount of bremsstrahlung radiation as electrons of the same energy

## Slide 34: Bremsstrahlung

## Slide 35: Question 1
What are the factors affecting The Probability of Occurrence of :
Photoelectric effect
Compton scattering
Pair production
Bremsstrahlung

## Slide 36: Question 2
What are the byproducts of :
Photoelectric effect
Compton scattering
Pair production
Bremsstrahlung

## Slide 37: Question 3
Give the scientific reason for:
Bones appear more clear than soft tissues in the radiographic film?
Lead is used for sheading gamma emitters?
Plastic is preferred than lead for sheading Beta emitters?