## Slide 1: Lecture 9: Voice Over IP (VoIP): Internet Telephony
Dr. Najla Al-nabhan
<number>

## Slide 2: VoIP Definition
The use of IP networks, namely the LAN and WAN, to carry voice
<number>

## Slide 3: Internet Telephony
The use of the Internet that was originally designed to carry computer data to carry voice
  A packet switched network
Voice was originally carried over circuit switched networks
  PSTN
<number>

## Slide 4: Related Issues
Voice over Frame Relay
Voice over ATM
<number>

## Slide 5: Further Evolution
Media transmission over IP
  Audio
  Image
  Video
<number>

## Slide 6: VoIP Basic Functions
Signaling
Database services
  Mapping addresses (IP to Phone numbers) etc.
Call connect and disconnect (bearer control)
CODEC operations
  For encapsulating voice into data packets
<number>

## Slide 7: VoIP Components
Servers
  For processing IP calls and manage interaction with private branch exchange (PBX) etc.
End-point devices such as phones
Media and VoIP gateways
IP network
Source: Juniper Networks
<number>
Notes: A PBX (private branch exchange) is a telephone system within an enterprise that switches calls between enterprise users on local lines while allowing all users to share a certain number of external phone lines.
<number>

## Slide 8: Overcoming the Challenges
Latency
Jitter
Bandwidth
Packet loss
Reliability
Scalability
Security
Features
Interoperability
Switch over cost
<number>

## Slide 9: Latency
Latency is the time taken for a packet to arrive at its destination
  Packet switching overhead
  Congestion
Latency may result in voice synchronization problems
<number>

## Slide 10: Jitter
Jitter in IP networks is the variation in the latency on a packet flow between two systems, when some packets take longer to travel from one system to the other.
Jitter results from network congestion and route changes.
Example: When someone is sending VoIP communication (let’s say one frame every 10 ms) those packets can stuck somewhere in between inside the network and not arrive at expected time to the destination.
<number>

## Slide 11: Bandwidth
When bandwidth is shared between voice and computer data, certain bandwidth may have to be allocated for voice communication on a network
<number>

## Slide 12: Packet Loss
Packet loss in unavoidable
It can be minimally tolerated in voice transmission
  It should not, in the first place, distort the audio
<number>

## Slide 13: Reliability
Because the computer network is used, the reliability of the network will have an impact on the telephony service
  In the analog telephone industry, reliability of 99.999 percent uptime is required
  The above is known as five nines
VoIP networks can achieve over 98 percent reliability ?
<number>

## Slide 14: Scalability
Ability to add more telephony equipment as the company grows
  Network bandwidth and other issues may have an effect on scalability
<number>

## Slide 15: Security
As VoIP uses the Internet, for example, it is vulnerable to the same type as security risks
  Hacking
  Denial of service
  Eavesdropping
<number>

## Slide 16: Features
IP telephony need to match and, in the long run, exceed the features provided by the PSTN
  Call waiting
  Three way calling etc.
<number>

## Slide 17: Interoperability
IP telephony equipment manufactured by different vendors must be able to talk to each other
  Standardized protocols are needed
<number>

## Slide 18: Migration Cost
The cost of migrating from legacy PBX to IP PBX
<number>

## Slide 19: Facing the Challenges
Many of the challenges listed have now been addressed by effective network performance management and standardized protocols
<number>

## Slide 20: Network Performance Management
Addresses the following issues:
  Latency
  Reliability
  Security
<number>

## Slide 21: Other Terminology
FXS
  Foreign Exchange Station
FXO
  Foreign Exchange Office
<number>

## Slide 22: FXS
A device that connects on one side to an analog equipment and other side to the Internet
A simple example is the ATA (Analog Telephone Adapter) that connects an analog phone to the Interent
<number>

## Slide 23: FXO
An interface between the PSTN and the local equipment that would also connect to the Internet
An example use would be to have a telephone that connects to the Internet and, at the same time, has a connection to the PSTN as well
  There are equipment that will automatically switch to the PSTN if for some reason the VoIP connection does not function
<number>

## Slide 24
<number>

## Slide 25: Modes of Internet Telephony
PC-to-PC
PC-to-Phone
Phone-to-Phone
Note: In the above listing phones can be either analog or digital phones.
<number>

## Slide 26: Case 1: PC to PC Connection
Made over the internet for voice connection
Sample product:
  Net2Phone
  NetMeeting
Calls are free
Vendors of PC to PC Connection
  Skype
  Earthlink
<number>

## Slide 27: Case 2: PC to Phone Connection
Made over the Internet for connecting PC to phones
Sample Product:
  Net2Phone
Need to pay for the calls but they are relatively inexpensive
  Cheaper compared to phone to phone calls made over the Internet
Vendors
  Net2Phone
<number>

## Slide 28: Procedure
1. Download Net2Phone FREE software 2. Create a Username and Password 3. Select the amount of money you want to add to your account 4. Login to the software 5. Make PC2Phone calls and send faxes
- Net2Phone
<number>

## Slide 29: Dialing from the PC
<number>

## Slide 30: Features
PC2PC
PC2Phone
PC2Fax
Instant messaging
<number>

## Slide 31: Case 3: Phone to Phone Connection
Phone to phone calls are made over the Internet
A special phone will connect to a hub or switch on the network
<number>

## Slide 32: Typical Layout
ATA
<number>

## Slide 33: Connections
<number>

## Slide 34: Analog Telephone Adapter (ATA) Manufacturers
CISCO
AT&T
Linksys
<number>

## Slide 35: A Note on Implementation Problems
Some of the adapters may not work properly when used in conjunction with a NAT
Some vendors may lock the ATA meaning that it would only work with their service
  A fee may have to be paid to unlock the ATA
<number>

## Slide 36: Soft Phones
Soft phones do not require an ATA for connection
They connect through the computer
  It can be used for example with a notebook computer to facilitate mobility
<number>

## Slide 37: Residential Broadband Phone Companies
Vonage
AT&T CallVantage
VoicePulse
Packet8
VocalTec
<number>

## Slide 38: IP Telephony Standards and Protocols
H.323
  ITU standard
SIP
  IETF standard
MGCP
  IETF standard
H.248
  ITU standard
Megaco
  IETF standard
<number>

## Slide 39: H.323
An ITU recommendation applicable to “Packet-based multimedia communications systems”. - CISCO
H.323 defines a distributed architecture for creating multimedia applications, including VoIP – CISCO
Older and more established protocol
<number>

## Slide 40: H.323 Components
Source: CISCO
<number>

## Slide 41: Summary
Implementations based on the three different protocols will be in use
All three will be implemented with IP as the common core
H.323 is an older implementation protocol for VOIP.
Reference:
  © N. Ganesan, Ph.d.
<number>