## Slide 1: Oxygen Therapy
Prepared by
Dr. Irene Roco

## Slide 2: Oxygen therapy
is the administration of oxygen as a medical intervention, which can be for a variety of purposes in both chronic and acute patient care
Oxygen is often prescribed for people to prevent hypoxia because of the following conditions:
difficulty ventilating all areas of their lungs
Impaired gas exchange
Heart failure
Prescribed by the physician who specifies the following:
Concentration
liter per minute
Method of delivery

## Slide 3: Oxygen supply
Piped in wall outlets – at the client’s bedside
Portable (Tanks or cylinders) – for transporting oxygen dependent clients, in home use;
Humidifier – add water vapor to inspired air because Oxygen is a dry gas that dehydrates respiratory mucous membrane
Prevents mucous membrane from drying and becoming irritated
Loosens secretions for easier expectoration

## Slide 4: Safety Precautions for Oxygen Administration
Teach family members to smoke only outside away from the client and oxygen equipment.
Set up “No Smoking: and “oxygen in Use” signs at the site of administration and at the door, according to agency policy.
Instruct the client and visitors about the hazard of smoking with oxygen in use
Provide cotton gown and blankets . Synthetics and wool may generate sparks of static electricity

## Slide 5: Safety Precautions for Oxygen Administration
Avoid the use of volatile, flammable materials such as oils, greases, alcohol, ether and acetone near clients receiving oxygen
Remove matches, lighters, ashtrays, and any friction-type or battery operated toys or devices from bedside
Be sure that electric monitoring equipment , suction machines, and portable diagnostic machines are electrically grounded.
Locate fire extinguishers and oxygen meter turn-off lever.

## Slide 6: Various devices used for administration of oxygen.
Pressure regulator - used to control the high pressure of oxygen delivered from a cylinder (or other source) to a lower pressure. This lower pressure is then controlled by a flowmeter.
Flowmeter – controls the lower pressure which may be preset or selectable, and this controls the flow in a measure such as litres per minute (lpm).

## Slide 7: Oxygen Delivery System
1. Nasal cannula (NC)
is a thin tube with two small nozzles that protrude into the patient's nostrils.
Most common and inexpensive device
provides oxygen at low flow rates, 2–6 litres per minute (LPM), delivering a concentration of 24–45%.
allows the patient to continue to talk, eat and drink while still receiving the therapy.
associated with greater overall comfort, and improved oxygenation and respiratory rates than with face mask oxygen.

## Slide 8: Oxygen Delivery System
1. Nasal cannula (NC)
Limitation:
Unable to deliver higher concentration of oxygen
Can be drying and irritating to mucous membrane

## Slide 9: Oxygen Delivery System
2. Simple face mask
covers the patient’s nose and mouth.
Exhalation ports at the sides of the mask allow exhaled CO2 to escape
often used at between 5 and 8 LPM, with a concentration of oxygen to the patient of between 40 – 60%.

## Slide 10: Oxygen Delivery System
3. Air-entrainment masks, also known as Venturi masks,
Has a wide bore tubing and color coded jet adapters ( blue adapter – 24% at 4-10 lpm; green adapter – 35% at 8lpm)
can accurately deliver a predetermined oxygen concentration to the trachea up to 24 - 50% at 4- 10 lpm .
4. Partial rebreathing mask – has a reservoir bag, which increases the provided oxygen rate to 60–90% oxygen at 6 to 10 LPM.

## Slide 11: Oxygen Delivery System
5. Non-rebreather masks ( reservoir mask), - draw oxygen from an attached reservoir bags, with one-way valves that direct exhaled air out of the mask.
Delivers the highest oxygen concentration when properly fitted and used at flow rates of 8-10 LPM or higher, they deliver close to 100% oxygen. This type of mask is indicated for acute medical emergencies.

## Slide 12: Oxygen Delivery System
Face Tent
Can replace oxygen mask when masks are poorly tolerated by clients
Provides oxygen concentration at 30 – 50% with flow rates of 4- 8 LPM

## Slide 13: Oxygen Delivery System
7. Bag-valve-mask (BVM) - a malleable bag attached to a face mask (or invasive airway such as an endotracheal tube or laryngeal mask airway), usually with a reservoir bag attached, which is manually manipulated by the healthcare professional to push oxygen (or air) into the lungs.
Used in many emergency medical service and first aid personnel

## Slide 14: Oxygen Delivery System
 | Characteristic | Concentration | LPM
1. Nasal Cannula | provides oxygen at low flow rates | 24–45%. | , 2–6 litres per minute (LPM),
2. Simple face mask |  | 40 – 60%. | 5 - 8 LPM
3. Air-entrainment masks also known as Venturi masks, |  | blue adapter – 24% green adapter – 35% At trachea : 24 - 50% | 4-10 lpm; 8 lpm 4- 10 lpm .
4. Partial rebreathing mask – | has a reservoir bag | 60–90% | 6 to 10 LPM.
5. Non-rebreather masks ( reservoir mask), | Delivers the highest oxygen concentration | Close to 100% | of 8-10 LPM or higher, they deliver close to
6. Face Tent |  | 30 – 50% | 4- 8 LPM or higher

## Slide 15: Let’s Review!

## Slide 16: References:
Kozier & Erb’s Fundamentals of Nursing . Eighth Edition