## Slide 1: Synchronous Sequential Logic
Verilog provides certain syntax, which turns into synchronous sequential circuits
  In always statements, signals keep their old value until an event in the sensitivity list takes place
  Statement inside always is executed only when the event specified in the sensitivity list occurs
  Note that always statement could generate combinational logic, depending on your description
always @ (sensitivity list)
begin
statement;
statement;
…
end

## Slide 2: D Flip-Flop
As studied, flip-flop samples input at the edge of the clock
  always @(posedge clk) samples input at the rising edge of the clock (clk)
  always @(negedge clk) samples input at the falling edge of the clock (clk)
Any output assigned in an always statement must be declared reg
  Note that a variable declared reg is not necessarily to be a registered output
    We’ll see it later…
<= or = can be used inside the always statement
  <= is called nonblocking assignment
  = is called blocking assignment
  We are going to discuss about this later
module flipflop(input clk,
input [3:0] d,
output reg [3:0] q);
always @ (posedge clk)
begin
q <= d; // pronounced “q gets d”
end
endmodule

## Slide 3: D Flip-Flop Simulation
module Dflipflop(input clk,
input [3:0] d,
output reg [3:0] q);
always @(posedge clk)
begin
q <= d;
end
endmodule

## Slide 4: D Flip-Flop with Sync and Async Reset
module ff_asyncR(input clk,
input reset,
input [3:0] d,
output reg [3:0] q);
// asynchronous reset
// sensitivity list has both clk and reset
always @ (posedge clk, posedge reset)
begin
if (reset) q <= 4'b0;
else q <= d;
end
endmodule
module ff_syncR(input clk,
input reset,
input [3:0] d,
output reg [3:0] q);
// synchronous reset
// sensitively list has only clk
always @(posedge clk)
begin
if (reset) q <= 4'b0;
else q <= d;
end
endmodule
DFF with Synchronous Reset
DFF with Asynchronous Reset

## Slide 5: D Flip-Flop with Sync Reset
module ff_syncR(input clk,
input reset,
input [3:0] d,
output reg [3:0] q);
// synchronous reset
always @(posedge clk)
begin
if (reset) q <= 4'b0;
else q <= d;
end
endmodule

## Slide 6: D Flip-Flop with Enable
module ff_en(input clk,
input reset,
input en,
input [3:0] d,
output reg [3:0] q);
// asynchronous reset and enable
always @(posedge clk, posedge reset)
begin
if (reset) q <= 4'b0;
else
begin
if (en) q <= d;
end
end
endmodule

## Slide 7: D Latch
As studied, a D-latch is
  transparent when the clock is high
  opaque when the clock is low (retaining its old value)
Try to avoid using latches unless you have a good reason to use them because latches may transfer unwanted input (such as glitches) to output
  Instead, use flip-flops
module latch(input clk,
input [3:0] d,
output reg [3:0] q);
always @ (clk, d)
begin
if (clk) q <= d;
end
endmodule

## Slide 8: D Latch Simulation
module latch(input clk,
input [3:0] d,
output reg [3:0] q);
always @(clk, d)
begin
if (clk) q <= d;
end
endmodule

## Slide 9: Useful Behavioral Statements
Keywords that must be inside always statements
  if / else
  case, casez
Again, variables assigned in an always statement must be declared as reg even if they’re not actually intended to be registers
  In other words, all signals on the left side of <= and = inside always should be declared as reg

## Slide 10: Combinational Logic using always
The always statement can also describe combinational logic (not generating flip-flops)
// combinational logic using an always statement
module gates(input [3:0] a, b,
output reg [3:0] y1, y2, y3, y4, y5);
always @ (*) // need begin/end because there is
begin // more than one statement in always
y1 = a & b; // AND
y2 = a | b; // OR
y3 = a ^ b; // XOR
y4 = ~(a & b); // NAND
y5 = ~(a | b); // NOR
end
endmodule
This hardware could be described with assign statements using fewer lines of code, so it’s better to use assign statements in this case.

## Slide 11: Combinational Logic using case
module sevenseg(input [3:0] data, output reg [6:0] segments);
always @(*)
begin
case (data)
// abc_defg
0: segments = 7'b111_1110;
1: segments = 7'b011_0000;
2: segments = 7'b110_1101;
3: segments = 7'b111_1001;
4: segments = 7'b011_0011;
5: segments = 7'b101_1011;
6: segments = 7'b101_1111;
7: segments = 7'b111_0000;
8: segments = 7'b111_1111;
9: segments = 7'b111_1011;
default: segments = 7'b000_0000; // required
endcase
end
endmodule
  What kind of circuit would it generate?

## Slide 12: Combinational Logic using case
In order for a case statement to imply combinational logic, all possible input combinations must be described by the HDL
  Remember to use a default statement when necessary, that is, when all the possible combinations are not listed in the body of the case statement
  Otherwise, what kind of circuit do you think the statement would generate?

## Slide 13: Combinational Logic using casez
The casez statement is used to describe truth tables with don’t cares
  don’t cares are indicated with ? in the casez statement
module priority_casez(input [3:0] a,
output reg [3:0] y);
always @(*)
begin
casez(a) // ? = don’t care
4'b1???: y = 4'b1000; // only y[3] = 1
4'b01??: y = 4'b0100; // only y[2] = 1
4'b001?: y = 4'b0010; // only y[1] = 1
4'b0001: y = 4'b0001; // only y[0] = 1
default: y = 4'b0000;
endcase
end
endmodule

## Slide 14: Priority Circuit Simulation
module priority_casez(input [3:0] a,
output reg [3:0] y);
always @(*)
begin
casez(a)
4'b1???: y = 4'b1000;
4'b01??: y = 4'b0100;
4'b001?: y = 4'b0010;
4'b0001: y = 4'b0001;
default: y = 4'b0000;
endcase
end
endmodule

## Slide 15: Parameterized Modules
HDLs permit variable bit widths using parameterized modules
  So far, all of our modules have had fixed-width inputs and outputs
  Verilog allows a #(parameter …)statement to define parameters before the inputs and outputs
module mux2
#(parameter width = 8) // name and default value
(input [width-1:0] d0, d1,
input s,
output [width-1:0] y);
assign y = s ? d1 : d0;
endmodule
Instance with 8-bit bus width (uses default):
mux2 #(8) mux1(d0, d1, s, out);
Instance with 12-bit bus width:
mux2 #(12) lowmux(d0, d1, s, out);

## Slide 16: Blocking and Nonblocking Statements
In the always statement,
  = indicates blocking statement
  <= indicates nonblocking statement
Blocking statements are evaluated in the order in which they appear in the code
  Like one would expect in a standard programming language such as C language
Nonblocking statements are evaluated concurrently
  All of the statements are evaluated concurrently before any of the signals on the left hand sides are updated

## Slide 17: Blocking vs Nonblocking Example
module sync_nonblocking
(input clk,
input d,
output reg q);
reg n1;
always @(posedge clk)
begin
n1 <= d; // nonblocking
q <= n1; // nonblocking
end
endmodule
module sync_blocking
(input clk,
input d,
output reg q);
reg n1;
always @(posedge clk)
begin
n1 = d; // blocking
q = n1; // blocking
end
endmodule
What kinds of circuit would be generated?

## Slide 18: Blocking vs Nonblocking Example
1-bit full adder
Cout = AB + (A + B)Cin
= G + PCin
+
S = A B Cin
Cout = AB + ACin + BCin
+
Let P = A B
Let G = AB
+
S = P Cin
+

## Slide 19: Full Adder with Blocking Statements
Like a high-level language, the blocking statements are evaluated in the order they appear in the body of the module
  Suppose that all the inputs and internal nodes are initially 0
  At some time later, a changes to 1
p ← 1 ^ 0 = 1
g ← 1 • 0 = 0
s ← 1 ^ 0 = 1
cout ← 0 + 1 • 0 = 0
module fulladder(input a, b, cin,
output reg s, cout);
reg p, g;
always @(*)
begin
p = a ^ b; // blocking
g = a & b; // blocking
s = p ^ cin; // blocking
cout = g | (p & cin); // blocking
end
endmodule

## Slide 20: Full Adder with Nonblocking Statements
Nonblocking statements are evaluated concurrently
  Suppose that all the inputs and internal nodes are initially 0
  At some time later, a changes to 1
module fulladder(input a, b, cin,
output reg s, cout);
reg p, g;
always @(*)
begin
p <= a ^ b; // nonblocking
g <= a & b; // nonblocking
s <= p ^ cin; // nonblocking
cout <= g | (p & cin); // nonblocking
end
endmodule
p ← 1 ^ 0 = 1, g ← 1 • 0 = 0, s ← 0 ^ 0 = 0, cout ← 0 + 0 • 0 = 0
p ← 1 ^ 0 = 1, g ← 1 • 0 = 0, s ← 1 ^ 0 = 1, cout ← 0 + 1 • 0 = 0
It makes simulation slow though it synthesizes to the same hardware
Also kind of hard to figure out what the circuit is doing… This kinds of coding should be avoided

## Slide 21: Blocking and Nonblocking Recap
Some statements generates completely different logic as shown in the flip-flop case
Some statements generates the same logic no matter which statement you use as we have seen in the full-adder case
  But, it affects the simulation time
So, choose wisely which statement you have to use

## Slide 22: Rules for Signal Assignment
Use continuous assignment statements to model simple combinational logic
assign y = a & b;
Use always @(*) and blocking assignments to model more complicated combinational logic where the always statement is helpful
Use always @(posedge clk) and nonblocking assignments to model synchronous sequential logic
always @(posedge clk)
q <= d; // nonblocking statement
Do not make assignments to the same signal in more than one always statement or continuous assignment statement

## Slide 23
Backup Slides

## Slide 24: N: 2N Decoder Example
module decoder #(parameter N = 3)
(input [N-1:0] a,
output reg [2**N-1:0] y);
always @(*)
begin
y = 0;
y[a] = 1;
end
endmodule