## Slide 1: Topics
We are going to discuss the following topics for roughly 3 weeks from today
  Introduction to Hardware Description Language (HDL)
  Combinational Logic Design with HDL
  Synchronous Sequential Logic Design with HDL
    Finite State Machine (FSM) Design

## Slide 2: Introduction
In old days (~ early 1990s), hardware engineers used to draw schematic of digital logic (combinational and sequential logics), based on Boolean equations
But, it is not virtually possible to draw schematic as the hardware complexity increases
As the hardware complexity increases, there has been a necessity of designing hardware in a more efficient way

## Slide 3: Examples
Core i7
  Number of transistors in Core i7 is roughly 1 billion
  Assuming that the gate count is based on 2-input NAND gate, (which is composed of 4 transistors), do you want to draw 250 million gates by hand? Absolutely NOT!
Midterm Exam
  Even a simple FSM design problem in the midterm exam took you more than 30 minutes
  Even worse, many of you got your answer wrong in the exam!
Notes: `

## Slide 4: Introduction
Hardware description language (HDL)
  Allows hardware designers to specify logic function using language
    So, hardware designer only needs to specify the target functionality (such as Boolean equations and FSM) with language
  Then, a computer-aided design (CAD) tool produces the optimized digital circuit with logic gates
    Nowadays, most commercial designs are built using HDLs
module example(
input a, b, c,
output y);
assign y = ~a & ~b & ~c |
a & ~b & ~c |
a & ~b & c;
endmodule
HDL-based Design
CAD Tool
Optimized Gates

## Slide 5: HDLs
Two leading HDLs
  VHDL
    Developed in 1981 by the Department of Defense
    Became an IEEE standard (1076) in 1987
  Verilog-HDL
    Developed in 1984 by Gateway Design Automation
    Became an IEEE standard (1364) in 1995
    We are going to use Verilog-HDL in this class
      The book on the right is a good reference (but not required to purchase)
IEEE: Institute of Electrical and Electronics Engineers is a professional society responsible for many computing standards including WiFi (802.11), Ethernet (802.3) etc

## Slide 6: Hardware Design with HDL
3 steps to design hardware with HDL
  Hardware design with HDL
    Describe target hardware with HDL
      When describing circuits using an HDL, it’s critical to think of the digital logic the code would produce
  Simulation
    Validate the design
      Inputs are applied to the design
      Outputs checked for correctness
      Millions of dollars saved by debugging in simulation instead of hardware
  Synthesis
    Transforms HDL code into a netlist, describing the hardware
      Netlist is a text file describing a list of logic gates and the wires connecting them

## Slide 7: CAD tools for Simulation
There are renowned CAD companies that provide HDL simulators
  Cadence
    www.cadence.com
  Synopsys
    www.synopsys.com
  Mentor Graphics
    www.mentorgraphics.com
    We are going to use ModelSim Altera Starter Edition for simulation
      http://www.altera.com/products/software/quartus-ii/modelsim/qts-modelsim-index.html

## Slide 8: CAD tools for Synthesis
The same companies (Cadence, Synopsys, and Mentor Graphics) provide synthesis tools, too
  They are extremely expensive to purchase though
We are going to use a synthesis tool from Altera
  Altera Quartus-II Web Edition (free)
    Synthesis, place & route, and download to FPGA
    http://www.altera.com/products/software/quartus-ii/web-edition/qts-we-index.html

## Slide 9: Verilog Modules
Verilog Module
  A block of hardware with inputs and outputs
    Examples: AND gate, multiplexer, priority encoder etc
  A Verilog module begins with the module name and a list of the inputs and outputs
  assign statement is used to describe combinational logic
  ~ indicates NOT
  & indicates AND
  | indicates OR
module example(input a, b, c,
output y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule

## Slide 10: Synthesis
Transforms HDL code into a netlist, that is, collection of gates and their connections
module example(input a, b, c,
output y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule

## Slide 11: Digital Design w/ Verilog HDL
Combinational Logic
  Continuous assignment statement
    It is used to describe simple combinational logic
    assign
  always statement
    It is used to describe complex combinational logic
    always @(*)
Synchronous Sequential Logic
  FSM is composed of flip-flops and combinational logics
  Flip-flops are described with always statement
    always @(posedge clk)
    always @(negedge clk)

## Slide 12: Verilog Syntax
Verilog is case sensitive.
  So, reset and Reset are NOT the same signal.
Verilog does not allow you to start signal or module names with numbers
  For example, 2mux is NOT a valid name
Verilog ignores whitespace such as spaces, tabs and line breaks
  Proper indentation and use of blank lines are helpful to make your design readable
Comments come in single-line and multi-line varieties like C-language
  // : single line comment
  /* */ : multiline comment

## Slide 13: Continuous Assignment Statement
Statements with assign keyword
  Examples:
    assign y = ~(a & b); // NAND gate
    assign y = a ^ b; // XOR gate
It is used to describe combinational logic
Anytime the inputs on the right side of the “=“ changes in a statement, the output on the left side is recomputed
assign statement should not be used inside the always statement

## Slide 14: Bitwise Operators
Bitwise operators perform a bit-wise operation on two operands
  Take each bit in one operand and perform the operation with the corresponding bit in the other operand
module gates(input [3:0] a, b,
output [3:0] y1, y2, y3, y4, y5);
/* Five different two-input logic
gates acting on 4 bit busses */
assign y1 = a & b; // AND
assign y2 = a | b; // OR
assign y3 = a ^ b; // XOR
assign y4 = ~(a & b); // NAND
assign y5 = ~(a | b); // NOR
endmodule

## Slide 15: Wait! What is Bus?
Bus is a medium that transfers data between computer components
In hardware design, a collection of bits is called bus
  Example: A[3:0]: 4-bit bus (composed of A[3], A[2], A[1], A[0])
    A[5:0]: 6-bit bus
CPU
North Bridge
South Bridge
A[31:0]
Address Bus
D[63:0]
Data Bus
Main Memory

## Slide 16: Bus Representation
Why uses a[3:0] to represent a 4-bit bus?
  How about a[0:3]?
  How about a[1:4] or a[4:1]?
In digital world, we always count from 0
  So, it would be nice to start the bus count from 0
  If you use a[0:3],
    a[0] indicates MSB
    a[3] indicates LSB
  If you use a[3:0],
    a[3] indicates MSB
    a[0] indicates LSB
    We are going to follow this convention in this course

## Slide 17: Reduction Operators
Reduction operations are unary
  Unary operation involves only one operand, whereas binary operation involves two operands
They perform a bit-wise operation on a single operand to produce a single bit result
As you might expect, |(or), &(and), ^(xor), ~&(nand), ~|(nor), and ~^(xnor) reduction operators are available
module and8(input [7:0] a,
output y);
assign y = &a;
// &a is much easier to write than
// assign y = a[7] & a[6] & a[5] & a[4] &
// a[3] & a[2] & a[1] & a[0];
endmodule

## Slide 18: Examples
& 4’b1001 =
& 4’bx111 =
~& 4’b1001 =
~& 4’bx001 =
| 4’b1001 =
~| 4’bx001 =
^ 4’b1001 =
~^ 4’b1101 =
^ 4’b10x1 =
0
x
1
1
1
0
0
0
x

## Slide 19: Conditional Assignment
The conditional operator ? : chooses between a second and third expression, based on a first expression
  The first expression is the condition
    If the condition is 1, the operator chooses the second expression
    If the condition is 0, the operator chooses the third expression
  Therefore, it is a ternary operator because it takes 3 inputs
  It looks the same as the C-language and Java, right?
module mux2(input [3:0] d0, d1,
input s,
output [3:0] y);
assign y = s ? d1 : d0;
// if s is 1, y = d1
// if s is 0, y = d0
endmodule
What kind of hardware do you think this would generate?

## Slide 20: Internal Variables
It is often convenient to break a complex design into intermediate designs
The keyword wire is used to represent internal variable whose value is defined by an assign statement
  For example, in the schematic below, you can declare p and g as wires

## Slide 21: Internal Variables Example
module fulladder(input a, b, cin, output s, cout);
wire p, g; // internal nodes
assign p = a ^ b;
assign g = a & b;
assign s = p ^ cin;
assign cout = g | (p & cin);
endmodule

## Slide 22: Logical & Arithmetic Shifts
Logical shift
Arithmetic shift

## Slide 23: Logical & Arithmetic Shifts
Logical shift (<<, >>)
  Every bit in the operand is simply moved by a given number of bit positions, and the vacant bit-positions are filled in with zeros
Arithmetic shift (<<<, >>>)
  Like logical shift, every bit in the operand is moved by a given number of bit positions
  Instead of being filled with all 0s, when shifting to the right, the leftmost bit (usually the sign bit in signed integer representations) is replicated to fill in all the vacant positions
    This is sign extension
  Arithmetic shifts can be useful as efficient ways of performing multiplication or division of signed integers by powers of two
    a <<< 2 is equivalent to a x 4 ?
    a >>> 2 is equivalent to a/4?
      Take floor value if the result is not an integer. The floor value of X (or X) is the greatest integer number less than or equal to X
      Examples:5/2 = 2, -3/2 = -2

## Slide 24: Operator Precedence
The operator precedence for Verilog is much like you would expect in other programming languages
  In particular, AND has precedence over OR
  You may use parentheses if the operation order is not clear
~ | NOT
*, /, % | mult, div, mod
+, - | add,sub
<<, >> | logical shift
<<<, >>> | arithmetic shift
<, <=, >, >= | comparison
==, != | equal, not equal
&, ~& | AND, NAND
^, ~^ | XOR, XNOR
¦, ~¦ | OR, XOR
?: | ternary operator
Highest
Lowest

## Slide 25: Number Representation
In Verilog, you can specify base and size of numbers
  Format: N’Bvalue
    N: size (number of bits)
    B: base (b: binary, d: decimal, o: octal, h: hexadecimal)
When writing a number, specify both base and size
Number | # Bits | Base | Decimal Equivalent | Stored
3’b101 | 3 | binary | 5 | 101
8’b11 | 8 | binary | 3 | 00000011
8’b1010_1011 | 8 | binary | 171 | 10101011
3’d6 | 3 | decimal | 6 | 110
6’o42 | 6 | octal | 34 | 100010
8’hAB | 8 | hexadecimal | 171 | 10101011

## Slide 26: Replication Operator
Replication operator is used to replicate a group of bits
  For instance, if you have a 1-bit variable and you want to replicate it 3 times to get a 3-bit variable, you can use the replication operator
wire [2:0] y;
assign y = {3{b[0]}};
// the above statement produces:
// y = b[0] b[0] b[0]

## Slide 27: Concatenation Operator
Concatenation operator { , } combines (concatenates) the bits of 2 or more operands
wire [11:0] y;
assign y = {a[2:1], {3{b[0]}}, a[0], 6’b100_010};
// the above statement produces:
// y = a[2] a[1] b[0] b[0] b[0] a[0] 1 0 0 0 1 0
// underscores (_) are used for formatting only to make it easier to read. Verilog ignores them.

## Slide 28: Tristate buffer and Floating output (Z)
Synthesis:
Verilog:
module tristate(input [3:0] a,
input en,
output [3:0] y);
assign y = en ? a : 4'bz;
endmodule

## Slide 29: Verilog Module Description
Two general styles of describing module functionality
  Behavioral modeling
    Express the module’s functionality descriptively
  Structural modeling
    Describe the module’s functionality from combination of simpler modules

## Slide 30: Behavioral Modeling Example
Behavioral modeling
  Express the module’s functionality descriptively
module example(input a, b, c,
output y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule

## Slide 31: Structural Modeling Example
Structural modeling
  Describe the module’s functionality from combination of simpler modules
module myinv(input a, output y);
assign y = ~a ;
endmodule
module myand3(input a, b, c, output y);
assign y = a & b & c;
endmodule
module myor3(input a, b, c, output y);
assign y = a | b | c;
endmodule
// Behavioral model
module example(input a, b, c,
output y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule
module example_structure (input a, b, c, output y);
wire inv_a, inv_b, inv_c;
wire and3_0, and3_1, and3_2;
myinv inva (.a (a), .y (inv_a));
myinv invb (.a (b), .y (inv_b));
myinv invc (.a (c), .y (inv_c));
myand3 and3_y0 (.a (inv_a), .b (inv_b), .c (inv_c), .y (and3_0));
myand3 and3_y1 (.a (a), .b (inv_b), .c (inv_c), .y (and3_1));
myand3 and3_y2 (.a (a), .b (inv_b), .c (c), .y (and3_2));
myor3 or3_y (.a (and3_0), .b (and3_1), .c (and3_2), .y (y));
endmodule

## Slide 32: Simulation
module example(input a, b, c,
output y);
assign y = ~a & ~b & ~c | a & ~b & ~c | a & ~b & c;
endmodule