## Slide 1: LAB 8 LIPASE
Quantitative turbid-metric determination of Pancreatic Lipase in serum or plasma
Daheeya ALEnazi

## Slide 2: Principle
Triglycerides + H2O Lipase mono + di-glycerides + Fatty acids
Serum is incubated at 37C with an olive oil substrate buffered at pH 9.0. triglycerides will hydrolysed in presence of the olive oil by pancreatic lipase this cause :
a decrease in the turbidity of the reaction mixture.
*The decrease in absorbance is measured and reflects the activity of lipase in the sample.

## Slide 3: Clinical Diagnosis
Elevation of LPS is used for:
Diagnosis of pancreatic disease such as acute and chronic pancreatitis and obstruction of the pancreatic duct.

## Slide 4: Procedure
 | blank | Test
WR-ml | 3 | 3
Incubate at 37 C for 5 min. |  | 
Sample-µl | -- | 100
Read Abs. at 400nm against D.W as AO for Blank and test Incubate at 37 C for 5 min. Read Abs A1 for blank and test. Calculate A . |  | 
 | blank | Test
WR-ml | 3 | 3
Incubate at 37 C for 5 min. |  | 
Sample-µl | -- | 100

## Slide 5: Calculation and normal range
Test (A0 – A1) – blank (A0 – A1) x 3000 = lipase activity in U/L
blank (A0)
Reference values:
ADULTS: 10 – 150 U/L