## Slide 2: Mass Spectroscopy

## Slide 3: Mass Spectrometry
Most useful tool for molecular structure determination if you can get it into gas phase
Molecular weight of parent and fragments that can give hints as to the structure of the molecule

## Slide 4: Early Use of Mass Spectroscopy
Quantitative methods for determination of the components in complex hydrocarbon mixtures
Later used for the identification and structural analysis of complex compounds
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Principles of measurements
As an identification method:
  When a given molecular species is impacted with an electron beam, a family of positive particles are produced
  The mass distribution of the particles are characteristic of the parent species
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: How does it work?
Sample is volatized and allowed to leak slowly into an ion chamber
Molecules of sample are ionized to mostly positive ions by electron beam
Positive ions are separated from negative ions
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: How does it work?
Positive ions are accelerated into separation chamber
The fast moving particles are subjected to a strong magnetic field in which they travel in a curved path
The radius depends upon their velocity and mass as well as the field strength
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: How does it work?
ions pass through an exit slit and fall upon a collector electrode
the ion current that results is amplified and recorded as a function of field strength or accelerating potential
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Magnetic sector MS

## Slide 10: Time of flight MS

## Slide 12
Portable TOF/MS

## Slide 13
ICP/MS

## Slide 14
Quadrupoles

## Slide 15
Quadrupole MS
Liquid Chrom
GC

## Slide 16: MS Instrumentation - Sample introduction
Need high vacuum - 10 torr( torr=1 mm Hg)
Oil diffusion pumps, turbomolecular pump, diffusion pump
Gas injection through pinhole
Liquids that vaporize into vacuum
Direct ionization of solids

## Slide 17: Sample ionization
General ionization that causes fragmentation (electron impact)
Gentle ionization that favors intensity of molecular ion (chemical ionization with gaseous ions)
Gentle ionization for molecules that are not in the gas phase (eg biological molecules) (Fast Atom Bombardment)

## Slide 18: Ionization of inorganic solids
Spark source (like atomic emission)
ICP/MS
Glow discharges (hollow cathode lamps)
Laser spallation

## Slide 19: Mass analyzer - separation based on mass to charge ratio
Magnetic sector (single focus)
Double focus (electrostatic field to select energy and magnetic field for m/e)
Quadrupole (1 to 3)
Time of flight (pulsed ioization)
Fourier transform (ion cyclotron resonance)

## Slide 20: Magnetic sector MS
large
slow scans (change magnetic field with electromagnet)
finite spread of energies from source limit resolution
R= m/m : capable of R= 600 to 2000 which means looking at m/e of 600 with unit mass resolution

## Slide 21: Double focus MS
Very large with electrostatic analyzer to eliminate differences in KE of ions
R= 40,000 is possible which means for m/e of 100 the mass differences of 0.0025 can be measured
Isotopic differences: C3H7 = 43.0892
C2H3O= 43.0456
C2H5N= 43.0688

## Slide 22: Quadrupole MS
Electrical fields applied pairwise
DC voltage and RF oscillating voltage changed so only one value of m/e moves in a stable path through the field
Scans over 1000 mass units/sec
R= 10,000 possible
R= 500 typical

## Slide 24
Ion Source
Quad 1
Quad 2 Collision chamber
Quad 3 Analyzer
Detector

## Slide 25: MS Pumps
Mechanical pumps of large capacity (for ion sources)
Turbomolecular pumps are expensive ($7000) but smaller and less problem than diffusion pumps

## Slide 26: Ion Trap MS (like ion cyclotron)

## Slide 27: Time of Flight MS
Fast scans of pulses of ions
eV=1/2 mv2 How long does it take for ions to travel 1 meter.
R=400 at best
Can store up to 20,000 spectra/sec.

## Slide 28: FT-MS or ICR-MS
Simultaneous measurement, multiplex, mass accuracy, high throughput
R= 800,000 possible but expensive as you need superconducting magnet
Different ions rotate at different velocities so we measure the frequencies
m/e=H/2f

## Slide 29: Triple Quadropole (MS-MS)
Select an ion, fragment it, and then analyze the fragments
Detector
Source
Select ion
Collision
Chamber
Analyze