## Slide 1
Mechanical ventilator

## Slide 2: Mechanical Ventilation
Ventilators deliver gas to the lungs using positive pressure at a certain rate. The amount of gas delivered can be limited by time, pressure or volume. The duration can be cycled by time, pressure or flow.
Notes: Most ventilators used in pediatrics are time cycled and operate either in a pressure limited or volume limited mode. Flow cycled ventilators are available but not commonly used.
As almost all of my experience is with servo’s I do not know of any time-limited vents….what would be the difference between a flow-limited and time-cycled vent and a time-limited flow cycled vent? Should we clean up this slide and just say you can limit by pressure or volume and cycle by flow or time?

## Slide 3
Initiation and maintenance of positive pressure ventilation (PPV) or improve Oxygenation, maintains or improve ventilation and provide respiratory muscle rest.
Purpose

## Slide 4
Indication
Acute Respiratory Failure
Hypoxemia
Neuromuscular Disorders
Pulmonary edema
central nervous system Disorders
Over Sedation
reduce ICP
Aspiration
ARDS
Pulmonary embolism
Left ventricular failure.

## Slide 5: Types of Artificial Airways
ETT
Tracheostomy

## Slide 6: Basic Concepts in Mechanical Ventilation
Flow
Pressure
Time
Volume
Respiratory rate
FIO2
PEEP
PIP
MAP

## Slide 7: FLOW.. FLOW.. FLOW..
The amount of air over a specific period of time
Constant flow a device which presents a constant of gas past the patient airway.

## Slide 8: Pressure.. Pressure.. Pressure..
May be inward atmospheric
May be outward (mechanical ventilation)

## Slide 9: Time.. Time.. Time ..Time
The time taken to inhale and exhale, including any pause before the next breathing.

## Slide 10: Volume.. Volume.. Volume
Tidal volume: the amount of gas in any breath
(5-7ml/kg of body weight)
Minute volume: the total amount of gas breathed over one minutes.

## Slide 11: FIO2..FIO2..FIO2
Fraction of inspired Oxygen
% percent of O2 delivered to the patient
Preset on the ventilator and will be mixed with air to be delivered via the ventilator.

## Slide 12: PEEP..PIP..MAP
PEEP:
Positive end expiratory pressure, a pressure designed to maintain patent airway
PIP:
Peak inspiratory pressure
The highest pressure attained in breath
MAP:
Mean airway pressure

## Slide 13
Type of ventilators

## Slide 14: Inflate the lungs by exerting positive pressure on the airway, similar to a bellows mechanism, forcing the alveoli to expand during inspiration. Requires use of artificial airway.
Applies negative pressure around the chest wall.
No artificial air way is necessary.
- pressure
+ pressure

## Slide 15
Mechanical ventilation
Modes
Negative Pressure
Ventilation
Positive Pressure
Ventilation
Pressure Mode
Volume Mode
Control ventilation (CV),
Controlled Mandatory
Ventilation, CMV
Assist Control AC
Assisted Mandatory
Ventilation AMV
Synchronized Intermittent mandatory
Ventilation / SIMV
Intermittent mandatory ventilation IMV
Pressure support
Ventilation
PSV
Pressure –controlled
Ventilation
PCV

## Slide 16: Volume controlled ventilation
Set volume delivered to the patients
Volume delivered are preset
Fully support patient ventilator requirement

## Slide 17: Assist control A /C
Inspiratory cycle is activated by the patient
Also ventilator cycles at rate predetermine by the operator.
Should the pt stop breathing, or breathe so weakly that the ventilator cannot function as an assistor, this mandatory baseline rate will prevent a pnea.

## Slide 18: Synchronized intermittent Mandatory ventilation (SIMV)
Patient can breath spontaneously through the ventilator circuitry.
The pt may initiate the mandatory breath with own inspiratory effort ,and the ventilator breath will be synchronized with the pt effort.
Provide good ventilatory support +allow respiratory muscle exercise
Can be used in weaning

## Slide 19: Pressure Support
Breath must be initiated from patient
Ventilator will then provide gas flow to patients
Overcome ETT resistance
Provide variable level of support to patients
Weaning mode

## Slide 20
Airway:
Inspiration.
Decreased clearance of secretions.
Nosocomial or ventilator-acquired pneumonia
complication

## Slide 21
Endotracheal tube:
-Tube kinked or plugged.
-Tracheal stenosis .
-lung atelectasis.
-Sinusitis.
-Otitis media
-Laryngeal edema

## Slide 22
Mechanical:
-hypoventilation with atelectasis
-hyperventilation with hypocapnia and respiratory alkalosis
-barotraumas ,pneumothorax
-Alarm "turn off".
-Failure of alarms or ventilator.
-Inadequate nebulization or humidification.
-Overheated inspired air, resulting in hyperthermia