## Slide 1: IE 469 Manufacturing Systems 469 صنع نظم التصنيع
II - Modeling Systems Tutorial

## Slide 2: Problem #1
Question 1
A production line is used to produce a product. Number of products at the start of the line is 400 units per week. The line consists of four stations. It is arranged such that an inspection station (I) is placed after three process stations (S1, S2, S3). The processing time of stations (S1, S2, S4, I) are (8, 10, 13, 8) minute respectively. Inspection station (I) has defect rate of 10%. 4% of the defects are scraped and the reminders are returned to station (S2).
Find :
(a) Determine the effective arrival rate at each station.
(b) Determine the number of machines at each station.
(c) Find the average work in process.
(d) Find the throughput time.
400
4%
S1
S2
I
S3
6%
Question Graph (NOT GIVEN!):

## Slide 3: Problem #1 Solution
 | S1 | S2 | S3 | I
Arrival Rate, λ unit/hr | 10 | 10 | 10 | 10
Service Rate, m unit/hr | 7.5 | 6 | 4.615385 | 7.5
Arrival Rate, λ’ unit/hr | 10 | 10.6383 | 10.6383 | 10.6383
Utilization Ratio, r=λ’/ m | 1.333333 | 1.77305 | 2.304965 | 1.41844
Number of machines, n | 2 | 2 | 3 | 2
At this stage a decision to be taken; 1st alternative to have single production line with multi station at all staion, OR 2nd two have two production lines [each produce half the weekly production at 200. in this case the solution will be: |  |  |  | 
Arrival Rate, λ = Rp, unit/hr | 5 | 5 | 5 | 5
Arrival Rate, λ’ = λ/(1-p), unit/hr | 5 | 5.319149 | 5.319149 | 5.319149
Service Rate, m =1/Tp, unit/hr | 7.5 | 6 | 4.615385 | 7.5
Utilization Ratio, r=λ’/ m | 0.666667 | 0.886525 | 1.152482 | 0.70922
Number of machines, n =int(ρ)+1 | 1 | 1 | 2 | 1
Utilization Ratio, r=λ’/n m | 0.666667 | 0.886525 | 0.576241 | 0.70922
Po =probability | 0.333333 | 0.113475 | 0.268841 | 0.29078

## Slide 4: Problem #1 Solution
v= λ’/ l | 1 | 1.06383 | 1.06383 | 1.06383
Lq = length of queue | 1.333333 | 6.925975 | 0.57293 | 1.729805
L =System Queue , unit | 2 | 7.8125 | 1.7254 | 2.439024
Total Queue in system =ΣL, units | 13.98 |  |  | 
Wq =queue throughput, | 0.27 | 1.30 | 0.11 | 0.33
W = System Throughput, hr | 0.4 | 1.46875 | 0.324377 | 0.458537
v*w | 0.4 | 1.5625 | 0.345082 | 0.487805
W=Snw, hr | 2.7954 |  |  | 

## Slide 5: Problem #2
Product | Demand / Week | Routing Data [Centers, Process Time in hr] |  |  | 
 |  | 1 | 2 | 3 | 4
1 | 15 | C3, 1 | C2, 2 | C1, 1 | C4, 2
2 | 10 | C4, 3 | C1, 3 |  | C3, 1
3 | 6 | C4, 4 | C3, 2 | C1, 2 | 
4 | 10 | C3, 2 |  | C2, 2 | C1, 1
5 | 8 | C3, 3 | C2, 1 | C1, 2 | 
Question 2
Five parts are processed using four machining centers (C1, C2, C3, and C4) as indicated in Table (1).
(a) Determine the effective arrival rate at each center.
(b) Determine the average processing time at each center.
(c) Determine number of machines in each center
(d) Find the average number of jobs in process.
(e) Find the throughput time for each parts.

## Slide 6: Problem #2 Solution
a- Calculate Arrival Rate |  |  |  | 
Product, (i) | Effective arrival Rate |  |  | 
 | λ’ C1 | λ’ C2 | λ’ C3 | λ’ C4
1 | 15 | 15 | 15 | 15
2 | 10 | 0 | 10 | 10
3 | 6 | 0 | 6 | 6
4 | 10 | 10 | 10 | 0
5 | 8 | 8 | 8 | 0
Sum | 49 | 33 | 49 | 31
Process time data, Tp , Hr |  |  |  | 
Product,(i) | Machine centers |  |  | 
 | C1 | C2 | C3 | C4
1 | 1 | 2 | 1 | 2
2 | 3 | 0 | 1 | 3
3 | 2 | 0 | 2 | 4
4 | 1 | 2 | 2 | 0
5 | 2 | 1 | 3 | 0

## Slide 7: Problem #2 Solution
c) Number of machines |  |  |  |  |  |  |  |  | 
Station | λ | m | M(c)=l/μ | r | Po | L | Lq | W | Wq
C1 | 49 | 23.61 | 3 | 0.692 | 0.099 | 3.152 | 1.077 | 0.064 | 0.022
C2 | 33 | 22.76 | 2 | 0.725 | 0.159 | 3.057 | 1.607 | 0.093 | 0.049
C3 | 49 | 24.2 | 3 | 0.675 | 0.107 | 2.973 | 0.948 | 0.061 | 0.019
C4 | 31 | 14.76 | 3 | 0.7 | 0.096 | 3.249 | 1.149 | 0.105 | 0.037
b- Calculate Process Times (λ’i x Tp)/(Sum (λ’i) x 40) |  |  |  | 
Product,(i) | Average Process Time |  |  | 
 | m-1 C1 | m-1 C2 | m-1 C3 | m-1 C4
1 | 15 | 30 | 15 | 30
2 | 30 | 0 | 10 | 30
3 | 12 | 0 | 12 | 24
4 | 10 | 20 | 20 | 0
5 | 16 | 8 | 24 | 0
Sum m-1 | 0.0423 | 0.043939 | 0.0413 | 0.0677
m | 23.614 | 22.75862 | 24.1975 | 14.762

## Slide 8: Problem #2 Solution
e) Throughput time for each product (Troughput time, Wp = Σprocess time+ΣWq)
d) Number of products in the system

## Slide 9: Problem #3
Question 3
A five departments manufacturing system is used to produce five parts according the data given in table (2). Find
(a) Determine the effective arrival rate at each department.
(b) Determine the number of machines at each station.
(c) Find the average work in process.
(d) Find the throughput time.
TABLE (2) |  |  |  |  |  |  |  |  |  |  | 
Part | Weekly Demand | Process Sequence |  |  |  | Operation Time,hr |  |  |  |  | 
 |  |  |  |  |  | Load | Process Station |  |  |  | Unload
 |  |  |  |  |  | A | B | C | D | E | A
1 | 6 | A > C > B > D > A |  |  |  | 0.2 | 2 | 1.5 | 2.1 | 0 | 0.2
2 | 7 | A > B > D > E > A |  |  |  | 0.2 | 2.8 | 0 | 2.2 | 1.5 | 0.2
3 | 3 | A > C > D > E > A |  |  |  | 0.2 | 0 | 1.5 | 1.8 | 2 | 0.2
4 | 5 | A > C >E > B > A |  |  |  | 0.2 | 1.5 | 0 | 0 | 2.2 | 0.2
5 | 4 | A > B > E > C > A |  |  |  | 0.2 | 2.5 | 2 | 0 | 1.8 | 0.2
Ʃ | 25 |  |  |  |  |  |  |  |  |  | 

## Slide 10: Problem #3 Solution
a) Arrival rate calculation |  |  |  |  |  | 
demand of part (i) at department (k), λ’ |  |  |  |  |  | 
 | P1 | P2 | P3 | P4 | P5 | ld=Σ(lki)
A | 6 | 7 | 3 | 5 | 4 | 25
B | 6 | 7 | --- | 5 | 4 | 22
C | 6 | --- | 3 | --- | 4 | 13
D | 6 | 7 | 3 | --- | --- | 16
E | --- | 7 | 3 | 5 | 4 | 19
operation time of part (i) at department (k) , Tki |  |  |  |  | 
 | P1 | P2 | P3 | P4 | P5
A | 0.4 | 0.4 | 0.4 | 0.4 | 0.4
B | 2 | 2.8 | --- | 1.5 | 2.5
C | 1.5 | --- | 1.5 | --- | 2
D | 2.1 | 2.2 | 1.8 | --- | ---
E | --- | 1.5 | 2 | 2.2 | 1.8
ΣTo | 6 | 6.9 | 5.7 | 4.1 | 6.7

## Slide 11: Problem #3 Solution
b) Service rate calculation |  |  |  |  |  |  |  |  | 
Calculate the operation time (service time) for a department, md-1 =S(λki/λd)*(Tki/40), |  |  |  |  |  |  |  |  | 
 | P1 | P2 | P3 | P4 | P5 | Ʃ(OT&AR) |  | μd-1 | μd
A | 2.4 | 2.8 | 1.2 | 2 | 1.6 | 10 |  | 0.0100 | 100.0
B | 12 | 19.6 | 0 | 7.5 | 10 | 49.1 |  | 0.0558 | 17.923
C | 9 | 0 | 4.5 | 0 | 8 | 21.5 |  | 0.0413 | 24.186
D | 12.6 | 15.4 | 5.4 | 0 | 0 | 33.4 |  | 0.0522 | 19.162
E | 0 | 10.5 | 6 | 11 | 7.2 | 34.7 |  | 0.0457 | 21.902
 | λ | μ | C | ρ | Po | L | Lq | W | Wq
A | 25 | 100.0 | 1 | 0.250 | 0.750 | 0.33333 | 0.0833 | 0.013 | 0.0033
B | 22 | 17.923 | 2 | 0.614 | 0.239 | 1.96932 | 0.7418 | 0.090 | 0.0337
C | 13 | 24.186 | 1 | 0.538 | 0.463 | 1.16216 | 0.6247 | 0.089 | 0.0481
D | 16 | 19.162 | 1 | 0.835 | 0.165 | 5.06061 | 4.2256 | 0.316 | 0.2641
E | 19 | 21.902 | 1 | 0.868 | 0.133 | 6.54717 | 5.6797 | 0.345 | 0.2989

## Slide 12: Problem #3 Solution
Throughput for each product |  | 
 | TP= ΣTo/40 | Tp+ΣWq
W1 | 0.150 | 0.499
W2 | 0.173 | 0.773
W3 | 0.143 | 0.757
W4 | 0.103 | 0.438
W5 | 0.168 | 0.552
Average work in process
L | ƩL
0.33333 | 15.0726
1.96932 | 
1.16216 | 
5.06061 | 
6.54717 |