## Slide 1: CHAPTER OBJECTIVES
Review important principles of statics
Use the principles to determine internal resultant loadings in a body
Introduce concepts of normal and shear stress
Discuss applications of analysis and design of members subjected to an axial load or direct shear

## Slide 2: CHAPTER OUTLINE
Introduction
Equilibrium of a deformable body
Stress
Average normal stress in an axially loaded bar
Average shear stress
Allowable stress
Design of simple connections

## Slide 3: 1.1 INTRODUCTION
Mechanics of materials
A branch of mechanics
It studies the relationship of
  External loads applied to a deformable body, and
  The intensity of internal forces acting within the body
Are used to compute deformations of a body
Study body’s stability when external forces are applied to it

## Slide 4: 1.1 INTRODUCTION
Historical development
Beginning of 17th century (Galileo)
Early 18th century (Saint-Venant, Poisson, Lamé and Navier)
In recent times, with advanced mathematical and computer techniques, more complex problems can be solved

## Slide 5: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
External loads
Surface forces
  Area of contact
  Concentrated force
  Linear distributed force
  Centroid C (or geometric center)
Body force (e.g., weight)

## Slide 6: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Support reactions
for 2D problems

## Slide 7: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Equations of equilibrium
For equilibrium
  balance of forces
  balance of moments
Draw a free-body diagram to account for all forces acting on the body
Apply the two equations to achieve equilibrium state
∑ F = 0
∑ MO = 0

## Slide 8: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Internal resultant loadings
Define resultant force (FR) and moment (MRo) in 3D:
  Normal force, N
  Shear force, V
  Torsional moment or torque, T
  Bending moment, M

## Slide 9: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Internal resultant loadings
For coplanar loadings:
  Normal force, N
  Shear force, V
  Bending moment, M

## Slide 10: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Internal resultant loadings
For coplanar loadings:
  Apply ∑ Fx = 0 to solve for N
  Apply ∑ Fy = 0 to solve for V
  Apply ∑ MO = 0 to solve for M

## Slide 11: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Procedure for analysis
Method of sections
  Choose segment to analyze
  Determine Support Reactions
  Draw free-body diagram for whole body
  Apply equations of equilibrium

## Slide 12: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Procedure for analysis
Free-body diagram
  Keep all external loadings in exact locations before “sectioning”
  Indicate unknown resultants, N, V, M, and T at the section, normally at centroid C of sectioned area
  Coplanar system of forces only include N, V, and M
  Establish x, y, z coordinate axes with origin at centroid

## Slide 13: 1.2 EQUILIBRIUM OF A DEFORMABLE BODY
Procedure for analysis
Equations of equilibrium
  Sum moments at section, about each coordinate axes where resultants act
  This will eliminate unknown forces N and V, with direct solution for M (and T)
  Resultant force with negative value implies that assumed direction is opposite to that shown on free-body diagram

## Slide 14: EXAMPLE 1.1
Determine resultant loadings acting on cross section at C of beam.

## Slide 15: EXAMPLE 1.1 (SOLN)
Support reactions
Consider segment CB
Free-body diagram:
Keep distributed loading exactly where it is on segment CB after “cutting” the section.
Replace it with a single resultant force, F.

## Slide 16: EXAMPLE 1.1 (SOLN)
Intensity (w) of loading at C (by proportion)
w/6 m = (270 N/m)/9 m
w = 180 N/m
F = ½ (180 N/m)(6 m) = 540 N
F acts 1/3(6 m) = 2 m from C.
Free-body diagram:

## Slide 17: EXAMPLE 1.1 (SOLN)
Equilibrium equations:
∑ Fx = 0;
∑ Fy = 0;
∑ Mc = 0;
− Nc = 0
Nc = 0
Vc − 540 N = 0
Vc = 540 N
−Mc − 504 N (2 m) = 0
Mc = −1080 N·m
+
+
+

## Slide 18: EXAMPLE 1.1 (SOLN)
Equilibrium equations:
Negative sign of Mc means it acts in the opposite direction to that shown below

## Slide 19: EXAMPLE 1.5
Mass of pipe = 2 kg/m, subjected to vertical force of 50 N and couple moment of 70 N·m at end A. It is fixed to the wall at C.
Determine resultant internal loadings acting on cross section at B of pipe.

## Slide 20: EXAMPLE 1.5 (SOLN)
Support reactions:
Consider segment AB, which does not involve support reactions at C.
Free-body diagram:
Need to find weight of each segment.

## Slide 21: EXAMPLE 1.5 (SOLN)
WBD = (2 kg/m)(0.5 m)(9.81 N/kg)
= 9.81 N
WAD = (2 kg/m)(1.25 m)(9.81 N/kg)
= 24.525 N

## Slide 22: EXAMPLE 1.5 (SOLN)
Equilibrium equations:
∑ Fx = 0;
∑ Fy = 0;
(FB)x = 0
(FB)y = 0
∑ Fz = 0;
(FB)z − 9.81 N − 24.525 N − 50 N = 0
(FB)z = 84.3 N

## Slide 23: EXAMPLE 1.5 (SOLN)
Equilibrium equations:
∑ (MB)x = 0;
(Mc)x + 70 N·m − 50 N (0.5 m) − 24.525 N (0.5 m) − 9.81 N (0.25m) = 0
(MB)x = − 30.3 N·m
∑ (MB)y = 0;
(Mc)y + 24.525 N (0.625·m) + 50 N (1.25 m) = 0
(MB)y = − 77.8 N·m
∑(MB)z = 0;
(Mc)z = 0

## Slide 24: EXAMPLE 1.5 (SOLN)
NB = (FB)y = 0
VB = √ (0)2 + (84.3)2 = 84.3 N
TB = (MB)y = 77.8 N·m
MB = √ (30.3)2 + (0)2 = 30.3 N·m
The direction of each moment is determined using the right-hand rule: positive moments (thumb) directed along positive coordinate axis
Equilibrium equations:

## Slide 25: 1.3 STRESS
Concept of stress
To obtain distribution of force acting over a sectioned area
Assumptions of material:
  It is continuous (uniform distribution of matter)
  It is cohesive (all portions are connected together)

## Slide 26: 1.3 STRESS
Concept of stress
Consider ΔA in figure below
Small finite force, ΔF acts on ΔA
As ΔA → 0, Δ F → 0
But stress (ΔF / ΔA) → finite limit (∞)

## Slide 27: 1.3 STRESS
Normal stress
Intensity of force, or force per unit area, acting normal to ΔA
Symbol used for normal stress, is σ (sigma)
Tensile stress: normal force “pulls” or “stretches” the area element ΔA
Compressive stress: normal force “pushes” or “compresses” area element ΔA
σz =
lim
ΔA →0
ΔFz
ΔA

## Slide 28: 1.3 STRESS
Shear stress
Intensity of force, or force per unit area, acting tangent to ΔA
Symbol used for normal stress is τ (tau)
τzx =
lim
ΔA →0
ΔFx
ΔA
τzy =
lim
ΔA →0
ΔFy
ΔA

## Slide 29: 1.3 STRESS
General state of stress
Figure shows the state of stress acting around a chosen point in a body
Units (SI system)
Newtons per square meter (N/m2) or a pascal (1 Pa = 1 N/m2)
kPa = 103 N/m2 (kilo-pascal)
MPa = 106 N/m2 (mega-pascal)
GPa = 109 N/m2 (giga-pascal)

## Slide 30: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Examples of axially loaded bar
Usually long and slender structural members
Truss members, hangers, bolts
Prismatic means all the cross sections are the same

## Slide 31: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Assumptions
Uniform deformation: Bar remains straight before and after load is applied, and cross section remains flat or plane during deformation
In order for uniform deformation, force P be applied along centroidal axis of cross section

## Slide 32: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Average normal stress distribution
σ = average normal stress at any point on cross sectional area
P = internal resultant normal force
A = x-sectional area of the bar
FRz = ∑ Fxz
∫ dF = ∫A σ dA
P = σ A
+
P
A
σ =

## Slide 33: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Equilibrium
Consider vertical equilibrium of the element
∑ Fz = 0
σ (ΔA) − σ’ (ΔA) = 0
σ = σ’
Above analysis applies to members subjected to tension or compression.

## Slide 34: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Maximum average normal stress
For problems where internal force P and x-sectional A were constant along the longitudinal axis of the bar, normal stress σ = P/A is also constant
If the bar is subjected to several external loads along its axis, change in x-sectional area may occur
Thus, it is important to find the maximum average normal stress
To determine that, we need to find the location where ratio P/A is a maximum

## Slide 35: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Maximum average normal stress
Draw an axial or normal force diagram (plot of P vs. its position x along bar’s length)
Sign convention:
  P is positive (+) if it causes tension in the member
  P is negative (−) if it causes compression
Identify the maximum average normal stress from the plot

## Slide 36: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Procedure for analysis
Average normal stress
Use equation of σ = P/A for x-sectional area of a member when section subjected to internal resultant force P

## Slide 37: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Procedure for analysis
Axially loaded members
Internal Loading:
Section member perpendicular to its longitudinal axis at pt where normal stress is to be determined
Draw free-body diagram
Use equation of force equilibrium to obtain internal axial force P at the section

## Slide 38: 1.4 AVERAGE NORMAL STRESS IN AXIALLY LOADED BAR
Procedure for Analysis
Axially loaded members
Average Normal Stress:
Determine member’s x-sectional area at the section
Compute average normal stress σ = P/A

## Slide 39: EXAMPLE 1.6
Bar width = 35 mm, thickness = 10 mm
Determine max. average normal stress in bar when subjected to loading shown.

## Slide 40: EXAMPLE 1.6 (SOLN)
Internal loading
Normal force diagram
By inspection, largest loading area is BC, where PBC = 30 kN

## Slide 41: EXAMPLE 1.6 (SOLN)
Average normal stress
σBC =
PBC
A
30(103) N
(0.035 m)(0.010 m)
=
= 85.7 MPa

## Slide 42: EXAMPLE 1.8
Specific weight γst = 80 kN/m3
Determine average compressive stress acting at points A and B.

## Slide 43: EXAMPLE 1.8 (SOLN)
Internal loading
Based on free-body diagram,
weight of segment AB determined from
Wst = γstVst

## Slide 44: EXAMPLE 1.8 (SOLN)
Average normal stress
+
∑ Fz = 0;
P − Wst = 0
P − (80 kN/m3)(0.8 m)(0.2 m)2 = 0
P = 8.042 kN

## Slide 45: EXAMPLE 1.8 (SOLN)
Average compressive stress
Cross-sectional area at section:
A = (0.2)m2
8.042 kN
(0.2 m)2
P
A
=
σ =
σ = 64.0 kN/m2