## Slide 1: 1.5 AVERAGE SHEAR STRESS
Shear stress is the stress component that act in the plane of the sectioned area.
Consider a force F acting to the bar
For rigid supports, and F is large enough, bar will deform and fail along the planes identified by AB and CD
Free-body diagram indicates that shear force, V = F/2 be applied at both sections to ensure equilibrium

## Slide 2: 1.5 AVERAGE SHEAR STRESS
Average shear stress over each section is:
τavg = average shear stress at section, assumed to be same at each pt on the section
V = internal resultant shear force at section determined from equations of equilibrium
A = area of section
P
A
τavg =

## Slide 3: 1.5 AVERAGE SHEAR STRESS
Case discussed above is example of simple or direct shear
Caused by the direct action of applied load F
Occurs in various types of simple connections, e.g., bolts, pins, welded material

## Slide 4: 1.5 AVERAGE SHEAR STRESS
Single shear
Steel and wood joints shown below are examples of single-shear connections, also known as lap joints.
Since we assume members are thin, there are no moments caused by F

## Slide 5: 1.5 AVERAGE SHEAR STRESS
Single shear
For equilibrium, x-sectional area of bolt and bonding surface between the two members are subjected to single shear force, V = F
The average shear stress equation can be applied to determine average shear stress acting on colored section in (d).

## Slide 6: 1.5 AVERAGE SHEAR STRESS
Double shear
The joints shown below are examples of double-shear connections, often called double lap joints.
For equilibrium, x-sectional area of bolt and bonding surface between two members subjected to double shear force, V = F/2
Apply average shear stress equation to determine average shear stress acting on colored section in (d).

## Slide 7: 1.5 AVERAGE SHEAR STRESS
Procedure for analysis
Internal shear
Section member at the pt where the τavg is to be determined
Draw free-body diagram
Calculate the internal shear force V
Average shear stress
Determine sectioned area A
Compute average shear stress τavg = V/A

## Slide 8: EXAMPLE 1.10
Depth and thickness = 40 mm
Determine average normal stress and average shear stress acting along (a) section planes a-a, and (b) section plane b-b.

## Slide 9: EXAMPLE 1.10 (SOLN)
Part (a)
Internal loading
Based on free-body diagram, Resultant loading of axial force, P = 800 N

## Slide 10: EXAMPLE 1.10 (SOLN)
Part (a)
Average stress
Average normal stress, σ
σ =
P
A
800 N
(0.04 m)(0.04 m)
= 500 kPa
=

## Slide 11: EXAMPLE 1.10 (SOLN)
Part (a)
Internal loading
No shear stress on section, since shear force at section is zero.
τavg = 0

## Slide 12: EXAMPLE 1.10 (SOLN)
Part (b)
Internal loading
+
∑ Fx = 0;
− 800 N + N sin 60° + V cos 60° = 0
+
∑ Fy = 0;
V sin 60° − N cos 60° = 0

## Slide 13: EXAMPLE 1.10 (SOLN)
Part (b)
Internal loading
Or directly using x’, y’ axes,
∑ Fx’ = 0;
∑ Fy’ = 0;
+
+
N − 800 N cos 30° = 0
V − 800 N sin 30° = 0

## Slide 14: EXAMPLE 1.10 (SOLN)
Part (b)
Average normal stress
σ =
N
A
692.8 N
(0.04 m)(0.04 m/sin 60°)
= 375 kPa
=

## Slide 15: EXAMPLE 1.10 (SOLN)
Part (b)
Average shear stress
τavg =
V
A
400 N
(0.04 m)(0.04 m/sin 60°)
= 217 kPa
=
Stress distribution as shown below:

## Slide 16: 1.6 ALLOWABLE STRESS
When designing a structural member or mechanical element, the stress in it must be restricted to safe level
Choose an allowable load that is less than the load the member can fully support
One method used is the factor of safety (F.S.)
F.S. =
Ffail
Fallow

## Slide 17: 1.6 ALLOWABLE STRESS
If load applied is linearly related to stress developed within member, then F.S. can also be expressed as:
F.S. =
σfail
σallow
F.S. =
τfail
τallow
In all the equations, F.S. is chosen to be greater than 1, to avoid potential for failure
Specific values will depend on types of material used and its intended purpose

## Slide 18: 1.7 DESIGN OF SIMPLE CONNECTIONS
To determine area of section subjected to a normal force, use
A =
P
σallow
A =
V
τallow
To determine area of section subjected to a shear force, use

## Slide 19: 1.7 DESIGN OF SIMPLE CONNECTIONS
Cross-sectional area of a tension member
Condition:
The force has a line of action that passes through the centroid of the x-section.

## Slide 20: 1.7 DESIGN OF SIMPLE CONNECTIONS
Cross-sectional area of a connecter subjected to shear
Assumption:
If bolt is loose or clamping force of bolt is unknown, assume frictional force between plates to be negligible.

## Slide 21: 1.7 DESIGN OF SIMPLE CONNECTIONS
Assumptions:
(σb)allow of concrete < (σb)allow of base plate
Bearing stress is uniformly distributed between plate and concrete
Required area to resist bearing
Bearing stress is normal stress produced by the compression of one surface against another.

## Slide 22: 1.7 DESIGN OF SIMPLE CONNECTIONS
Although actual shear-stress distribution along rod difficult to determine, we assume it is uniform.
Thus use A = V / τallow to calculate l, provided d and τallow is known.
Required area to resist shear caused by axial load

## Slide 23: 1.7 DESIGN OF SIMPLE CONNECTIONS
Procedure for analysis
When using average normal stress and shear stress equations, consider first the section over which the critical stress is acting
Internal loading
  Section member through x-sectional area
  Draw a free-body diagram of segment of member
  Use equations of equilibrium to determine internal resultant force

## Slide 24: 1.7 DESIGN OF SIMPLE CONNECTIONS
Procedure for analysis
Required area
Based on known allowable stress, calculate required area needed to sustain load from A = P/τallow or A = V/τallow

## Slide 25: EXAMPLE 1.13
The two members pinned together at B. If the pins have an allowable shear stress of τallow = 90 MPa, and allowable tensile stress of rod CB is (σt)allow = 115 MPa
Determine to nearest mm the smallest diameter of pins A and B and the diameter of rod CB necessary to support the load.

## Slide 26: EXAMPLE 1.13 (SOLN)
Draw free-body diagram:
σ =
P
A
800 N
(0.04 m)(0.04 m)
= 500 kPa
=
No shear stress on section, since shear force at section is zero
τavg = 0

## Slide 27: EXAMPLE 1.13 (SOLN)
Diameter of pins:
dA = 6.3 mm
AA =
VA
Tallow
2.84 kN
90  103 kPa
=
= 31.56  10−6 m2 = (dA2/4)
dB = 9.7 mm
AB =
VB
Tallow
6.67 kN
90  103 kPa
=
= 74.11  10−6 m2 = (dB2/4)

## Slide 28: EXAMPLE 1.13 (SOLN)
Diameter of pins:
dA = 7 mm
dB = 10 mm
Choose a size larger to nearest millimeter.

## Slide 29: EXAMPLE 1.13 (SOLN)
Diameter of rod:
dBC = 8.59 mm
ABC =
P
(σt)allow
6.67 kN
115  103 kPa
=
= 58  10−6 m2 = (dBC2/4)
dBC = 9 mm
Choose a size larger to nearest millimeter.

## Slide 30: CHAPTER REVIEW
Internal loadings consist of
  Normal force, N
  Shear force, V
  Bending moments, M
  Torsional moments, T
Get the resultants using
  method of sections
  Equations of equilibrium

## Slide 31: CHAPTER REVIEW
Assumptions for a uniform normal stress distribution over x-section of member (σ = P/A)
  Member made from homogeneous isotropic material
  Subjected to a series of external axial loads that,
  The loads must pass through centroid of x-section

## Slide 32: CHAPTER REVIEW
Determine average shear stress by using τ = V/A equation
  V is the resultant shear force on x-sectional area A
  Formula is used mostly to find average shear stress in fasteners or in parts for connections

## Slide 33: CHAPTER REVIEW
Design of any simple connection requires that
  Average stress along any x-section not exceed a factor of safety (F.S.) or
  Allowable value of σallow or τallow
  These values are reported in codes or standards and are deemed safe on basis of experiments or through experience