## Slide 1: CHAPTER OBJECTIVES
Define concept of normal strain
Define concept of shear strain
Determine normal and shear strain in engineering applications

## Slide 2: CHAPTER OUTLINE
Deformation
Strain

## Slide 3: 2.1 DEFORMATION
Deformation
Occurs when a force is applied to a body
Can be highly visible or practically unnoticeable
Can also occur when temperature of a body is changed
Is not uniform throughout a body’s volume, thus change in geometry of any line segment within body may vary along its length

## Slide 4: 2.1 DEFORMATION
To simplify study of deformation
Assume lines to be very short and located in neighborhood of a point, and
Take into account the orientation of the line segment at the point

## Slide 5: 2.2 STRAIN
Normal strain
Defined as the elongation or contraction of a line segment per unit of length
Consider line AB in figure below
After deformation, Δs changes to Δs’

## Slide 6: 2.2 STRAIN
Normal strain
Defining average normal strain using avg (epsilon)
As Δs → 0, Δs’ → 0
avg =
Δs − Δs’
Δs
 =
Δs − Δs’
Δs
lim
B→A along n

## Slide 7: 2.2 STRAIN
Normal strain
If normal strain  is known, use the equation to obtain approx. final length of a short line segment in direction of n after deformation.
Hence, when  is positive, initial line will elongate, if  is negative, the line contracts
Δs’ ≈ (1 + ) Δs

## Slide 8: 2.2 STRAIN
Units
Normal strain is a dimensionless quantity, as it’s a ratio of two lengths
But common practice to state it in terms of meters/meter (m/m)
 is small for most engineering applications, so is normally expressed as micrometers per meter (μm/m) where 1 μm = 10−6
Also expressed as a percentage, e.g., 0.001 m/m = 0.1 %

## Slide 9: 2.2 STRAIN
Shear strain
Defined as the change in angle that occurs between two line segments that were originally perpendicular to one another
This angle is denoted by γ (gamma) and measured in radians (rad).

## Slide 10: 2.2 STRAIN
Shear strain
Consider line segments AB and AC originating from same point A in a body, and directed along the perpendicular n and t axes
After deformation, lines become curves, such that angle between them at A is θ’

## Slide 11: 2.2 STRAIN
Shear strain
Hence, shear strain at point A associated with n and t axes is
If θ’ is smaller than /2, shear strain is positive, otherwise, shear strain is negative
γnt =

2
lim
B→A along n
C →A along t
θ’
−

## Slide 12: 2.2 STRAIN
Cartesian strain components
Using above definitions of normal and shear strain, we show how they describe the deformation of the body
Divide body into small elements with undeformed dimensions of Δx, Δy and Δz

## Slide 13: 2.2 STRAIN
Cartesian strain components
Since element is very small, deformed shape of element is a parallelepiped
Approx. lengths of sides of parallelepiped are
(1 + x) Δx (1 + y)Δy (1 + z)Δz

## Slide 14: 2.2 STRAIN
Cartesian strain components
Approx. angles between the sides are

2
− γxy

2
− γyz

2
− γxz
Normal strains cause a change in its volume
Shear strains cause a change in its shape
To summarize, state of strain at a point requires specifying 3 normal strains; x, y, z and 3 shear strains of γxy, γyz, γxz

## Slide 15: 2.2 STRAIN
Small strain analysis
Most engineering design involves applications for which only small deformations are allowed
We’ll assume that deformations that take place within a body are almost infinitesimal, so normal strains occurring within material are very small compared to 1, i.e.,  << 1.

## Slide 16: 2.2 STRAIN
Small strain analysis
This assumption is widely applied in practical engineering problems, and is referred to as small strain analysis
E.g., it can be used to approximate sin θ = θ, cos θ = θ and tan θ = θ, provided θ is small