## Slide 1: CHAPTER OBJECTIVES
Determine deformation of axially loaded members
Develop a method to find support reactions when it cannot be determined from equilibrium equations
Analyze the effects of thermal stress, stress concentrations, inelastic deformations, and residual stress

## Slide 2: CHAPTER OUTLINE
Saint-Venant’s Principle
Elastic Deformation of an Axially Loaded Member
Principle of Superposition
Statically Indeterminate Axially Loaded Member
Force Method of Analysis for Axially Loaded Member
Thermal Stress
Stress Concentrations
*Inelastic Axial Deformation
*Residual Stress

## Slide 3: 4.1 SAINT-VENANT’S PRINCIPLE
Localized deformation occurs at each end, and the deformations decrease as measurements are taken further away from the ends
At section c-c, stress reaches almost uniform value as compared to a-a, b-b
c-c is sufficiently far enough away from P so that localized deformation “vanishes”, i.e., minimum distance

## Slide 4: 4.1 SAINT-VENANT’S PRINCIPLE
General rule: min. distance is at least equal to largest dimension of loaded x-section. For the bar, the min. distance is equal to width of bar
This behavior discovered by Barré de Saint-Venant in 1855, this the name of the principle
Saint-Venant Principle states that localized effects caused by any load acting on the body, will dissipate/smooth out within regions that are sufficiently removed from location of load
Thus, no need to study stress distributions at that points near application loads or support reactions

## Slide 5: 4.2 ELASTIC DEFORMATION OF AN AXIALLY LOADED MEMBER
Relative displacement (δ) of one end of bar with respect to other end caused by this loading
Applying Saint-Venant’s Principle, ignore localized deformations at points of concentrated loading and where x-section suddenly changes

## Slide 6: 4.2 ELASTIC DEFORMATION OF AN AXIALLY LOADED MEMBER
Use method of sections, and draw free-body diagram
σ =
P(x)
A(x)
 =
dδ
dx
σ = E
Assume proportional limit not exceeded, thus apply Hooke’s Law
P(x)
A(x)
= E
dδ
dx
( )
dδ =
P(x) dx
A(x) E

## Slide 7: 4.2 ELASTIC DEFORMATION OF AN AXIALLY LOADED MEMBER
δ =
∫0
P(x) dx
A(x) E
L
δ = displacement of one pt relative to another pt
L = distance between the two points
P(x) = internal axial force at the section, located a distance x from one end
A(x) = x-sectional area of the bar, expressed as a function of x
E = modulus of elasticity for material
Eqn. 4-1

## Slide 8: 4.2 ELASTIC DEFORMATION OF AN AXIALLY LOADED MEMBER
Constant load and X-sectional area
For constant x-sectional area A, and homogenous material, E is constant
With constant external force P, applied at each end, then internal force P throughout length of bar is constant
Thus, integrating Eqn 4-1 will yield
δ =
PL
AE
Eqn. 4-2

## Slide 9: 4.2 ELASTIC DEFORMATION OF AN AXIALLY LOADED MEMBER
Constant load and X-sectional area
If bar subjected to several different axial forces, or x-sectional area or E is not constant, then the equation can be applied to each segment of the bar and added algebraically to get
δ =
PL
AE


## Slide 10: 4.2 ELASTIC DEFORMATION OF AN AXIALLY LOADED MEMBER
Sign convention
Sign | Forces | Displacement
Positive (+) | Tension | Elongation
Negative (−) | Compression | Contraction

## Slide 11: 4.2 ELASTIC DEFORMATION OF AN AXIALLY LOADED MEMBER
Procedure for analysis
Internal force
Use method of sections to determine internal axial force P in the member
If the force varies along member’s strength, section made at the arbitrary location x from one end of member and force represented as a function of x, i.e., P(x)
If several constant external forces act on member, internal force in each segment, between two external forces, must then be determined

## Slide 12: 4.2 ELASTIC DEFORMATION OF AN AXIALLY LOADED MEMBER
Procedure for analysis
Internal force
For any segment, internal tensile force is positive and internal compressive force is negative. Results of loading can be shown graphically by constructing the normal-force diagram
Displacement
When member’s x-sectional area varies along its axis, the area should be expressed as a function of its position x, i.e., A(x)

## Slide 13: 4.2 ELASTIC DEFORMATION OF AN AXIALLY LOADED MEMBER
Procedure for analysis
Displacement
If x-sectional area, modulus of elasticity, or internal loading suddenly changes, then Eqn 4-2 should be applied to each segment for which the qty are constant
When substituting data into equations, account for proper sign for P, tensile loadings +ve, compressive −ve. Use consistent set of units. If result is +ve, elongation occurs, −ve means it’s a contraction

## Slide 14: EXAMPLE 4.1
Composite A-36 steel bar shown made from two segments AB and BD. Area AAB = 600 mm2 and ABD = 1200 mm2.
Determine the vertical displacement of end A and displacement of B relative to C.

## Slide 15: EXAMPLE 4.1 (SOLN)
Internal force
Due to external loadings, internal axial forces in regions AB, BC and CD are different.
Apply method of sections and equation of vertical force equilibrium as shown. Variation is also plotted.

## Slide 16: EXAMPLE 4.1 (SOLN)
Displacement
From tables, Est = 210(103) MPa.
Use sign convention, vertical displacement of A relative to fixed support D is
δA =
PL
AE

[+75 kN](1 m)(106)
[600 mm2 (210)(103) kN/m2]
=
[+35 kN](0.75 m)(106)
[1200 mm2 (210)(103) kN/m2]
+
[−45 kN](0.5 m)(106)
[1200 mm2 (210)(103) kN/m2]
+
= +0.61 mm

## Slide 17: EXAMPLE 4.1 (SOLN)
Displacement
Since result is positive, the bar elongates and so displacement at A is upward
Apply Equation 4-2 between B and C,
δA =
PBC LBC
ABC E
[+35 kN](0.75 m)(106)
[1200 mm2 (210)(103) kN/m2]
=
= +0.104 mm
Here, B moves away from C, since segment elongates

## Slide 18: 4.3 PRINCIPLE OF SUPERPOSITION
After subdividing the load into components, the principle of superposition states that the resultant stress or displacement at the point can be determined by first finding the stress or displacement caused by each component load acting separately on the member.
Resultant stress/displacement determined algebraically by adding the contributions of each component

## Slide 19: 4.3 PRINCIPLE OF SUPERPOSITION
Conditions
The loading must be linearly related to the stress or displacement that is to be determined.
The loading must not significantly change the original geometry or configuration of the member
When to ignore deformations?
Most loaded members will produce deformations so small that change in position and direction of loading will be insignificant and can be neglected
Exception to this rule is a column carrying axial load, discussed in Chapter 13

## Slide 20: 4.4 STATICALLY INDETERMINATE AXIALLY LOADED MEMBER
For a bar fixed-supported at one end, equilibrium equations is sufficient to find the reaction at the support. Such a problem is statically determinate
If bar is fixed at both ends, then two unknown axial reactions occur, and the bar is statically indeterminate
+↑ F = 0;
FB + FA − P = 0

## Slide 21: 4.4 STATICALLY INDETERMINATE AXIALLY LOADED MEMBER
To establish addition equation, consider geometry of deformation. Such an equation is referred to as a compatibility or kinematic condition
Since relative displacement of one end of bar to the other end is equal to zero, since end supports fixed,
δA/B = 0
This equation can be expressed in terms of applied loads using a load-displacement relationship, which depends on the material behavior

## Slide 22: 4.4 STATICALLY INDETERMINATE AXIALLY LOADED MEMBER
For linear elastic behavior, compatibility equation can be written as
Assume AE is constant, solve equations simultaneously,
= 0
FA LAC
AE
FB LCB
AE
−
LCB
L
FA = P
( )
LAC
L
FB = P
( )

## Slide 23: 4.4 STATICALLY INDETERMINATE AXIALLY LOADED MEMBER
Procedure for analysis
Equilibrium
Draw a free-body diagram of member to identigy all forces acting on it
If unknown reactions on free-body diagram greater than no. of equations, then problem is statically indeterminate
Write the equations of equilibrium for the member

## Slide 24: 4.4 STATICALLY INDETERMINATE AXIALLY LOADED MEMBER
Procedure for analysis
Compatibility
Draw a diagram to investigate elongation or contraction of loaded member
Express compatibility conditions in terms of displacements caused by forces
Use load-displacement relations (δ=PL/AE) to relate unknown displacements to reactions
Solve the equations. If result is negative, this means the force acts in opposite direction of that indicated on free-body diagram

## Slide 25: EXAMPLE 4.5
Steel rod shown has diameter of 5 mm. Attached to fixed wall at A, and before it is loaded, there is a gap between the wall at B’ and the rod of 1 mm.
Determine reactions at A and B’ if rod is subjected to axial force of P = 20 kN.
Neglect size of collar at C. Take Est = 200 GPa

## Slide 26: EXAMPLE 4.5 (SOLN)
Equilibrium
Assume force P large enough to cause rod’s end B to contact wall at B’. Equilibrium requires
δB/A = 0.001 m
− FA − FB + 20(103) N = 0
+ F = 0;
Compatibility
Compatibility equation:

## Slide 27: EXAMPLE 4.5 (SOLN)
FA (0.4 m) − FB (0.8 m) = 3927.0 N·m
Compatibility
Use load-displacement equations (Eqn 4-2), apply to AC and CB
δB/A = 0.001 m =
FA LAC
AE
FB LCB
AE
−
Solving simultaneously,
FA = 16.6 kN FB = 3.39 kN