## Slide 1: CHAPTER OBJECTIVES
Discuss effects of applying torsional loading to a long straight member
Determine stress distribution within the member under torsional load
Determine angle of twist when material behaves in a linear-elastic and inelastic manner
Discuss statically indeterminate analysis of shafts and tubes
Discuss stress distributions and residual stress caused by torsional loadings

## Slide 2: CHAPTER OUTLINE
Torsional Deformation of a Circular Shaft
The Torsion Formula
Power Transmission
Angle of Twist
Statically Indeterminate Torque-Loaded Members
*Solid Noncircular Shafts
*Thin-Walled Tubes Having Closed Cross Sections
Stress Concentration
*Inelastic Torsion
*Residual Stress

## Slide 3: 5.1 TORSIONAL DEFORMATION OF A CIRCULAR SHAFT
Torsion is a moment that twists/deforms a member about its longitudinal axis
By observation, if angle of rotation is small, length of shaft and its radius remain unchanged

## Slide 4: 5.1 TORSIONAL DEFORMATION OF A CIRCULAR SHAFT
By definition, shear strain is
Let x  dx and   = d
BD =  d = dx 
 = (/2)  lim ’
CA along CA
BA along BA
 = 
d
dx
Since d / dx =  / = max /c
 = max

c
( )
Equation 5-2

## Slide 5: 5.2 THE TORSION FORMULA
For solid shaft, shear stress varies from zero at shaft’s longitudinal axis to maximum value at its outer surface.
Due to proportionality of triangles, or using Hooke’s law and Eqn 5-2,
 =  max

c
( )
...
 =
 max
c
∫A 2 dA

## Slide 6: 5.2 THE TORSION FORMULA
The integral in the equation can be represented as the polar moment of inertia J, of shaft’s x-sectional area computed about its longitudinal axis
 max =
Tc
J
 max = max. shear stress in shaft, at the outer surface
T = resultant internal torque acting at x-section, from method of sections & equation of moment equilibrium applied about longitudinal axis
J = polar moment of inertia at x-sectional area
c = outer radius pf the shaft

## Slide 7: 5.2 THE TORSION FORMULA
Shear stress at intermediate distance, 
 =
T
J
The above two equations are referred to as the torsion formula
Used only if shaft is circular, its material homogenous, and it behaves in an linear-elastic manner

## Slide 8: 5.2 THE TORSION FORMULA
Solid shaft
J can be determined using area element in the form of a differential ring or annulus having thickness d and circumference 2 .
For this ring, dA = 2 d
J = c4

2
J is a geometric property of the circular area and is always positive. Common units used for its measurement are mm4 and m4.

## Slide 9: 5.2 THE TORSION FORMULA
Tubular shaft
J = (co4  ci4)

2

## Slide 10: 5.2 THE TORSION FORMULA
Absolute maximum torsional stress
Need to find location where ratio Tc/J is maximum
Draw a torque diagram (internal torque  vs. x along shaft)
Sign Convention: T is positive, by right-hand rule, is directed outward from the shaft
Once internal torque throughout shaft is determined, maximum ratio of Tc/J can be identified

## Slide 11: 5.2 THE TORSION FORMULA
Procedure for analysis
Internal loading
Section shaft perpendicular to its axis at point where shear stress is to be determined
Use free-body diagram and equations of equilibrium to obtain internal torque at section
Section property
Compute polar moment of inertia and x-sectional area
For solid section, J = c4/2
For tube, J = (co4  ci2)/2

## Slide 12: 5.2 THE TORSION FORMULA
Procedure for analysis
Shear stress
Specify radial distance , measured from centre of x-section to point where shear stress is to be found
Apply torsion formula,  = T /J or max = Tc/J
Shear stress acts on x-section in direction that is always perpendicular to 

## Slide 13: EXAMPLE 5.3
Shaft shown supported by two bearings and subjected to three torques.
Determine shear stress developed at points A and B, located at section a-a of the shaft.

## Slide 14: EXAMPLE 5.3 (SOLN)
Internal torque
Bearing reactions on shaft = 0, if shaft weight assumed to be negligible. Applied torques satisfy moment equilibrium about shaft’s axis.
Internal torque at section a-a determined from free-body diagram of left segment.

## Slide 15: EXAMPLE 5.3 (SOLN)
Internal torque
 Mx = 0;
4250 kN·mm  3000 kN·mm  T = 0
T = 1250 kN·mm
Section property
J = /2(75 mm)4 = 4.97 107 mm4
Shear stress
Since point A is at  = c = 75 mm
B = Tc/J = ... = 1.89 MPa

## Slide 16: EXAMPLE 5.3 (SOLN)
Shear stress
Likewise for point B, at  = 15 mm
B = T /J = ... = 0.377 MPa
Directions of the stresses on elements A and B established from direction of resultant internal torque T.

## Slide 17: 5.3 POWER TRANSMISSION
Power is defined as work performed per unit of time
Instantaneous power is
Since shaft’s angular velocity  = d/dt, we can also express power as
P = T (d/dt)
P = T
Frequency f of a shaft’s rotation is often reported. It measures the number of cycles per second and since 1 cycle = 2 radians, and  = 2f T, then power
P = 2f T
Equation 5-11

## Slide 18: 5.3 POWER TRANSMISSION
Shaft Design
If power transmitted by shaft and its frequency of rotation is known, torque is determined from Eqn 5-11
Knowing T and allowable shear stress for material, allow and applying torsion formula,
J
c
T
allow
=

## Slide 19: 5.3 POWER TRANSMISSION
Shaft Design
For solid shaft, substitute J = (/2)c4 to determine c
For tubular shaft, substitute J = (/2)(co2  ci2) to determine co and ci

## Slide 20: EXAMPLE 5.5
Solid steel shaft shown used to transmit 3750 W from attached motor M. Shaft rotates at  = 175 rpm and the steel allow = 100 MPa.
Determine required diameter of shaft to nearest mm.

## Slide 21: EXAMPLE 5.5 (SOLN)
Torque on shaft determined from P = T,
Thus, P = 3750 N·m/s
Thus, P = T, T = 204.6 N·m
( )
 = = 18.33 rad/s
175 rev
min
2 rad
1 rev
1 min
60 s
( )
= =
J
c
 c4
2 c2
T
allow
. . .
c = 10.92 mm
Since 2c = 21.84 mm, select shaft with diameter of d = 22 mm

## Slide 22: 5.4 ANGLE OF TWIST
Angle of twist is important when analyzing reactions on statically indeterminate shafts
 =
T(x) dx
J(x) G
∫0
L
 = angle of twist, in radians
T(x) = internal torque at arbitrary position x, found from method of sections and equation of moment equilibrium applied about shaft’s axis
J(x) = polar moment of inertia as a function of x
G = shear modulus of elasticity for material

## Slide 23: 5.4 ANGLE OF TWIST
Constant torque and x-sectional area
 =
TL
JG
If shaft is subjected to several different torques, or x-sectional area or shear modulus changes suddenly from one region of the shaft to the next, then apply Eqn 5-15 to each segment before vectorially adding each segment’s angle of twist:
 =
TL
JG


## Slide 24: 5.4 ANGLE OF TWIST
Sign convention
Use right-hand rule: torque and angle of twist are positive when thumb is directed outward from the shaft

## Slide 25: 5.4 ANGLE OF TWIST
Procedure for analysis
Internal torque
Use method of sections and equation of moment equilibrium applied along shaft’s axis
If torque varies along shaft’s length, section made at arbitrary position x along shaft is represented as T(x)
If several constant external torques act on shaft between its ends, internal torque in each segment must be determined and shown as a torque diagram

## Slide 26: 5.4 ANGLE OF TWIST
Procedure for analysis
Angle of twist
When circular x-sectional area varies along shaft’s axis, polar moment of inertia expressed as a function of its position x along its axis, J(x)
If J or internal torque suddenly changes between ends of shaft,  = ∫ (T(x)/J(x)G) dx or  = TL/JG must be applied to each segment for which J, T and G are continuous or constant
Use consistent sign convention for internal torque and also the set of units

## Slide 27: EXAMPLE 5.9
50-mm-diameter solid cast-iron post shown is buried 600 mm in soil. Determine maximum shear stress in the post and angle of twist at its top. Assume torque about to turn the post, and soil exerts uniform torsional resistance of t N·mm/mm along its 600 mm buried length. G = 40(103) GPa

## Slide 28: EXAMPLE 5.9 (SOLN)
Internal torque
From free-body diagram
 Mz = 0; TAB = 100 N(300 mm) = 30  103 N·mm

## Slide 29: EXAMPLE 5.9 (SOLN)
Internal torque
Magnitude of the uniform distribution of torque along buried segment BC can be determined from equilibrium of the entire post.
 Mz = 0;
100 N(300 mm)  t(600 mm) = 0
t = 50 N·mm

## Slide 30: EXAMPLE 5.9 (SOLN)
Internal torque
Hence, from free-body diagram of a section of the post located at position x within region BC, we have
 Mz = 0;
TBC  50x = 0
TBC = 50x

## Slide 31: EXAMPLE 5.9 (SOLN)
Maximum shear stress
Largest shear stress occurs in region AB, since torque largest there and J is constant for the post. Applying torsion formula
max = = ... = 1.22 N/mm2
TAB c
J

## Slide 32: EXAMPLE 5.9 (SOLN)
Angle of twist
Angle of twist at the top can be determined relative to the bottom of the post, since it is fixed and yet is about to turn. Both segments AB and BC twist, so
A = +
TAB LAB
JG
TBC dx
JG
∫
0
LBC
. . .
A = 0.00147 rad

## Slide 33: 5.5 STATICALLY INDETERMINATE TORQUE-LOADED MEMBERS
A torsionally loaded shaft is statically indeterminate if moment equation of equilibrium, applied about axis of shaft, is not enough to determine unknown torques acting on the shaft

## Slide 34: 5.5 STATICALLY INDETERMINATE TORQUE-LOADED MEMBERS
From free-body diagram, reactive torques at supports A and B are unknown, Thus,
 Mx = 0; T  TA  TB = 0
Since problem is statically indeterminate, formulate the condition of compatibility; end supports are fixed, thus angle of twist of both ends should sum to zero
A/B = 0

## Slide 35: 5.5 STATICALLY INDETERMINATE TORQUE-LOADED MEMBERS
Assume linear-elastic behavior, and using load-displacement relationship,  = TL/JG, thus compatibility equation can be written as
TA LAC
JG
TB LBC
JG
 = 0
Solving the equations simultaneously, and realizing that L = LAC + LBC, we get
TA = T
LBC
L
( )
TB = T
LAC
L
( )

## Slide 36: 5.5 STATICALLY INDETERMINATE TORQUE-LOADED MEMBERS
Procedure for analysis
Equilibrium
Draw a free-body diagram
Write equations of equilibrium about axis of shaft
Compatibility
Express compatibility conditions in terms of rotational displacement caused by reactive torques
Use torque-displacement relationship, such as  = TL/JG
Solve equilibrium and compatibility equations for unknown torques

## Slide 37: EXAMPLE 5.11
Solid steel shaft shown has a diameter of 20 mm. If it is subjected to two torques, determine reactions at fixed supports A and B.

## Slide 38: EXAMPLE 5.11 (SOLN)
Equilibrium
From free-body diagram, problem is statically indeterminate.
 Mx = 0;
 TB + 800 N·m  500 N·m  TA = 0
Compatibility
Since ends of shaft are fixed, sum of angles of twist for both ends equal to zero. Hence,
A/B = 0

## Slide 39: EXAMPLE 5.11 (SOLN)
1.8TA  0.2TB = 750
Compatibility
The condition is expressed using the load-displacement relationship,  = TL/JG.
. . .
Solving simultaneously, we get
TA = 345 N·m TB = 645 N·m

## Slide 40: *5.6 SOLID NONCIRCULAR SHAFTS
Shafts with noncircular x-sections are not axisymmetric, as such, their x-sections will bulge or warp when it is twisted
Torsional analysis is complicated and thus is not considered for this text.

## Slide 41: *5.6 SOLID NONCIRCULAR SHAFTS
Results of analysis for square, triangular and elliptical x-sections are shown in table

## Slide 42: EXAMPLE 5.13
6061-T6 aluminum shaft shown has x-sectional area in the shape of equilateral triangle. Determine largest torque T that can be applied to end of shaft if allow = 56 MPa, allow = 0.02 rad, Gal = 26 GPa.
How much torque can be applied to a shaft of circular x-section made from same amount of material?

## Slide 43: EXAMPLE 5.13 (SOLN)
By inspection, resultant internal torque at any x-section along shaft’s axis is also T. Using formulas from Table 5-1,
allow = 20T/a3; ... T = 179.2 N·m
allow = 46TL/a3Gal; ... T = 24.12 N·m
By comparison, torque is limited due to angle of twist.

## Slide 44: EXAMPLE 5.13 (SOLN)
Circular x-section
We need to calculate radius of the x-section.
Acircle = Atriangle; ... c = 14.850 mm
Limitations of stress and angle of twist require
allow = Tc/J; ... T = 288.06 N·m
allow = TL/JGal; ... T = 33.10 N·m
Again, torque is limited by angle of twist.
Comparing both results, we can see that a shaft of circular x-section can support 37% more torque than a triangular one