## Slide 1: CHAPTER OBJECTIVES
Determine stress in members caused by bending
Discuss how to establish shear and moment diagrams for a beam or shaft
Determine largest shear and moment in a member, and specify where they occur
Consider members that are straight, symmetric x-section and homogeneous linear-elastic material

## Slide 2: CHAPTER OBJECTIVES
Consider special cases of unsymmetrical bending and members made of composite materials
Consider curved members, stress concentrations, inelastic bending, and residual stresses

## Slide 3: CHAPTER OUTLINE
Shear and Moment Diagrams
Graphical Method for Constructing Shear and Moment Diagrams
Bending Deformation of a Straight Member
The Flexure Formula
Unsymmetrical Bending
*Composite Beams
*Reinforced Concrete Beams
*Curved Beams
Stress Concentrations
*Inelastic Bending
*Residual Stress

## Slide 4: 6.1 SHEAR AND MOMENT DIAGRAMS
Members that are slender and support loadings applied perpendicular to their longitudinal axis are called beams

## Slide 5: 6.1 SHEAR AND MOMENT DIAGRAMS
In order to design a beam, it is necessary to determine the maximum shear and moment in the beam
Express V and M as functions of arbitrary position x along axis.
These functions can be represented by graphs called shear and moment diagrams
Engineers need to know the variation of shear and moment along the beam to know where to reinforce it

## Slide 6: 6.1 SHEAR AND MOMENT DIAGRAMS
Shear and bending-moment functions must be determined for each region of the beam between any two discontinuities of loading

## Slide 7: 6.1 SHEAR AND MOMENT DIAGRAMS
Beam sign convention
Although choice of sign convention is arbitrary, in this course, we adopt the one often used by engineers:

## Slide 8: 6.1 SHEAR AND MOMENT DIAGRAMS
IMPORTANT
Beams are long straight members that carry loads perpendicular to their longitudinal axis. They are classified according to how they are supported
To design a beam, we need to know the variation of the shear and moment along its axis in order to find the points where they are maximum
Establishing a sign convention for positive shear and moment will allow us to draw the shear and moment diagrams

## Slide 9: 6.1 SHEAR AND MOMENT DIAGRAMS
Procedure for analysis
Support reactions
Determine all reactive forces and couple moments acting on beam
Resolve all forces into components acting perpendicular and parallel to beam’s axis
Shear and moment functions
Specify separate coordinates x having an origin at beam’s left end, and extending to regions of beam between concentrated forces and/or couple moments, or where there is no discontinuity of distributed loading

## Slide 10: 6.1 SHEAR AND MOMENT DIAGRAMS
Procedure for analysis
Shear and moment functions
Section beam perpendicular to its axis at each distance x
Draw free-body diagram of one segment
Make sure V and M are shown acting in positive sense, according to sign convention
Sum forces perpendicular to beam’s axis to get shear
Sum moments about the sectioned end of segment to get moment

## Slide 11: 6.1 SHEAR AND MOMENT DIAGRAMS
Procedure for analysis
Shear and moment diagrams
Plot shear diagram (V vs. x) and moment diagram (M vs. x)
If numerical values are positive, values are plotted above axis, otherwise, negative values are plotted below axis
It is convenient to show the shear and moment diagrams directly below the free-body diagram

## Slide 12: EXAMPLE 6.6
Draw the shear and moment diagrams for beam shown below.

## Slide 13: EXAMPLE 6.6 (SOLN)
Support reactions: Shown in free-body diagram.
Shear and moment functions
Since there is a discontinuity of distributed load and a concentrated load at beam’s center, two regions of x must be considered.
0 ≤ x1 ≤ 5 m,
+↑  Fy = 0; ... V = 5.75 N
+  M = 0; ... M = (5.75x1 + 80) kN·m

## Slide 14: EXAMPLE 6.6 (SOLN)
Shear and moment functions
5 m ≤ x2 ≤ 10 m,
+↑  Fy = 0; ... V = (15.75  5x2) kN
+  M = 0; ... M = (5.75x22 + 15.75x2 +92.5) kN·m
Check results by applying w = dV/dx and V = dM/dx.

## Slide 15: EXAMPLE 6.6 (SOLN)
Shear and moment diagrams

## Slide 16: 6.2 GRAPHICAL METHOD FOR CONSTRUCTING SHEAR AND MOMENT DIAGRAMS
A simpler method to construct shear and moment diagram, one that is based on two differential equations that exist among distributed load, shear and moment

## Slide 17: 6.2 GRAPHICAL METHOD FOR CONSTRUCTING SHEAR AND MOMENT DIAGRAMS
Regions of distributed load
dV
dx
= w(x)
dM
dx
= V
Slope of shear diagram at each point
Slope of moment diagram at each point
= distributed load intensity at each point
= shear at each point

## Slide 18: 6.2 GRAPHICAL METHOD FOR CONSTRUCTING SHEAR AND MOMENT DIAGRAMS
Regions of distributed load
V = ∫ w(x) dx
M = ∫ V(x) dx
Change in shear
Change in moment
= area under distributed loading
= area under shear diagram

## Slide 19: 6.2 GRAPHICAL METHOD FOR CONSTRUCTING SHEAR AND MOMENT DIAGRAMS
Regions of concentrated force and moment

## Slide 20: 6.2 GRAPHICAL METHOD FOR CONSTRUCTING SHEAR AND MOMENT DIAGRAMS
Regions of concentrated force and moment

## Slide 21: 6.2 GRAPHICAL METHOD FOR CONSTRUCTING SHEAR AND MOMENT DIAGRAMS
Procedure for analysis
Support reactions
Determine support reactions and resolve forces acting on the beam into components that are perpendicular and parallel to beam’s axis
Shear diagram
Establish V and x axes
Plot known values of shear at two ends of the beam

## Slide 22: 6.2 GRAPHICAL METHOD FOR CONSTRUCTING SHEAR AND MOMENT DIAGRAMS
Procedure for analysis
Shear diagram
Since dV/dx = w, slope of the shear diagram at any point is equal to the (-ve) intensity of the distributed loading at that point
To find numerical value of shear at a point, use method of sections and equation of equilibrium or by using V = ∫ w(x) dx, i.e., change in the shear between any two points is equal to (-ve) area under the load diagram between the two points

## Slide 23: 6.2 GRAPHICAL METHOD FOR CONSTRUCTING SHEAR AND MOMENT DIAGRAMS
Procedure for analysis
Shear diagram
Since w(x) must be integrated to obtain V, then if w(x) is a curve of degree n, V(x) will be a curve of degree n+1
Moment diagram
Establish M and x axes and plot known values of the moment at the ends of the beam
Since dM/dx = V, slope of the moment diagram at any point is equal to the shear at the point

## Slide 24: 6.2 GRAPHICAL METHOD FOR CONSTRUCTING SHEAR AND MOMENT DIAGRAMS
Procedure for analysis
Moment diagram
At point where shear is zero, dM/dx = 0 and therefore this will be a point of maximum or minimum moment
If numerical value of moment is to be determined at the point, use method of sections and equation of equilibrium, or by using M = ∫ V(x) dx, i.e., change in moment between any two pts is equal to area under shear diagram between the two pts

## Slide 25: 6.2 GRAPHICAL METHOD FOR CONSTRUCTING SHEAR AND MOMENT DIAGRAMS
Procedure for analysis
Moment diagram
Since V(x) must be integrated to obtain M, then if V(x) is a curve of degree n, M(x) will be a curve of degree n+1

## Slide 26: EXAMPLE 6.11
Draw the shear and moment diagrams for beam shown below.

## Slide 27: EXAMPLE 6.11 (SOLN)
Support reactions:
See free-body diagram.
Shear diagram
From behavior of distributed load, slope of shear diagram varies from zero at x = 0 to 2 at x = 4.5. Thus, its parabolic shape.
Use method of sections to find point of zero shear:
+↑  Fy = 0; ... x = 2.6 m

## Slide 28: EXAMPLE 6.11 (SOLN)
Moment diagram
From shear diagram, slope of moment diagram begin at +1.5, then decreases positively till it reaches zero at 2.6 m. Then it increases negatively and reaches 3 at x = 4.5 m. Moment diagram is a cubic function of x.
M = 2.6 kN·m
+  M = 0; . . .

## Slide 29: 6.3 BENDING DEFORMATION OF A STRAIGHT MEMBER
When a bending moment is applied to a straight prismatic beam, the longitudinal lines become curved and vertical transverse lines remain straight and yet undergo a rotation

## Slide 30: 6.3 BENDING DEFORMATION OF A STRAIGHT MEMBER
A neutral surface is where longitudinal fibers of the material will not undergo a change in length.

## Slide 31: 6.3 BENDING DEFORMATION OF A STRAIGHT MEMBER
Thus, we make the following assumptions:
  Longitudinal axis x (within neutral surface) does not experience any change in length
  All cross sections of the beam remain plane and perpendicular to longitudinal axis during the deformation
  Any deformation of the cross-section within its own plane will be neglected
In particular, the z axis, in plane of x-section and about which the x-section rotates, is called the neutral axis

## Slide 32: 6.3 BENDING DEFORMATION OF A STRAIGHT MEMBER
For any specific x-section, the longitudinal normal strain will vary linearly with y from the neutral axis
A contraction will occur () in fibers located above the neural axis (+y)
An elongation will occur (+) in fibers located below the axis (y)
 = (y/c)max
Equation 6-8

## Slide 33: 6.4 THE FLEXURE FORMULA
Assume that material behaves in a linear-elastic manner so that Hooke’s law applies.
A linear variation of normal strain must then be the consequence of a linear variation in normal stress
Applying Hooke’s law to Eqn 6-8,
 = (y/c)max
Equation 6-9

## Slide 34: 6.4 THE FLEXURE FORMULA
By mathematical expression, equilibrium equations of moment and forces, we get
Equation 6-11
∫A y dA = 0
Equation 6-10
max
c
M = ∫A y2 dA
The integral represents the moment of inertia of x-sectional area, computed about the neutral axis. We symbolize its value as I.

## Slide 35: 6.4 THE FLEXURE FORMULA
Hence, Eqn 6-11 can be solved and written as
Equation 6-12
Mc
I
max =
max = maximum normal stress in member, at a pt on x-sectional area farthest away from neutral axis
M = resultant internal moment, computed about neutral axis of x-section
I = moment of inertia of x-sectional area computed about neutral axis
c = perpendicular distance from neutral axis to a pt farthest away from neutral axis, where max acts

## Slide 36: 6.4 THE FLEXURE FORMULA
Normal stress at intermediate distance y can be determined from
Equation 6-13
My
I
 = 
 is -ve as it acts in the -ve direction (compression)
Equations 6-12 and 6-13 are often referred to as the flexure formula.

## Slide 37: 6.4 THE FLEXURE FORMULA
IMPORTANT
X-section of straight beam remains plane when beam deforms due to bending.
The neutral axis is subjected to zero stress
Due to deformation, longitudinal strain varies linearly from zero at neutral axis to maximum at outer fibers of beam
Provided material is homogeneous and Hooke’s law applies, stress also varies linearly over the x-section

## Slide 38: 6.4 THE FLEXURE FORMULA
IMPORTANT
For linear-elastic material, neutral axis passes through centroid of x-sectional area. This is based on the fact that resultant normal force acting on x-section must be zero
Flexure formula is based on requirement that resultant moment on the x-section is equal to moment produced by linear normal stress distribution about neutral axis

## Slide 39: 6.4 THE FLEXURE FORMULA
Procedure for analysis
Internal moment
Section member at pt where bending or normal stress is to be determined and obtain internal moment M at the section
Centroidal or neutral axis for x-section must be known since M is computed about this axis
If absolute maximum bending stress is to be determined, then draw moment diagram in order to determine the maximum moment in the diagram

## Slide 40: 6.4 THE FLEXURE FORMULA
Procedure for analysis
Section property
Determine moment of inertia I, of x-sectional area about the neutral axis
Methods used are discussed in Textbook Appendix A
Refer to the course book’s inside front cover for the values of I for several common shapes

## Slide 41: 6.4 THE FLEXURE FORMULA
Procedure for analysis
Normal stress
Specify distance y, measured perpendicular to neutral axis to pt where normal stress is to be determined
Apply equation  = My/I, or if maximum bending stress is needed, use max = Mc/I
Ensure units are consistent when substituting values into the equations

## Slide 42: EXAMPLE 6.16
Beam shown has x-sectional area in the shape of a channel. Determine the maximum bending stress that occurs in the beam at section a-a.

## Slide 43: EXAMPLE 6.16 (SOLN)
Internal moment
Beam support reactions need not be determined. Instead, use method of sections, the segment to the left of a-a. Note that resultant internal axial force N passes through centroid of x-section.
The resultant internal moment must be computed about the beam’s neutral axis a section a-a.

## Slide 44: EXAMPLE 6.16 (SOLN)
Internal moment
To find location of neutral axis, x-sectional area divided into 3 composite parts as shown. Then using Eqn. A-2 of Appendix A:
y = = ... = 59.09 mm
 y A
 A

## Slide 45: EXAMPLE 6.16 (SOLN)
Internal moment
Apply moment equation of equilibrium about neutral axis,
+  MNA = 0; 24 kN(2 m) + 1.0 kN(0.05909 m)  M = 0
M = 4.859 kN·m

## Slide 46: EXAMPLE 6.16 (SOLN)
Section property
Moment of inertia about neutral axis is determined using parallel-axis theorem applied to each of the three composite parts of the x-sectional area.
I = [1/12(0.250 m)(0.020 m)3 + (0.250 m)(0.020 m)(0.05909 m  0.010 m)2] + 2[1/12(0.015 m)(0.200 m)3 + (0.015 m)(0.200 m)(0.100 m  0.05909 m)2]
I = 42.26(10-6) m4

## Slide 47: EXAMPLE 6.16 (SOLN)
Maximum bending stress
It occurs at points farthest away from neutral axis. At bottom of beam, c = 0.200 m  0.05909 m = 0.1409 m. Thus,
At top of beam, ’ = 6.79 MPa. In addition, normal force of N = 1 kN and shear force V = 2.4 kN will also contribute additional stress on x-section.
Mc
I
max = = = 16.2 MPa
4.859 kN·m(0.1409 m)
42.26(10-6) m4

## Slide 48: 6.5 UNSYMMETRICAL BENDING
A condition for flexure formula is the symmetric x-sectional area of beam about an axis perpendicular to neutral axis
However, the flexure formula can also be applied either to a beam having x-sectional area of any shape OR to a beam having a resultant moment that acts in any direction

## Slide 49: 6.5 UNSYMMETRICAL BENDING
Moment applied along principal axis
Consider a beam with unsymmetrical shape
Establish coordinate system as per usual and that resultant moment M acts along +z axis
Conditions:
  Stress distribution acting over entire x-sectional area to be a zero force resultant,
  Resultant internal moment about y axis to be zero
  Resultant internal moment about z axis to be equal to M

## Slide 50: 6.5 UNSYMMETRICAL BENDING
Moment applied along principal axis
Express the 3 conditions mathematically by considering force acting on differential element dA located at (0, y, z). Force is dF =  dA, therefore
FR = Fy; 0 = ∫A  dA
(MR)y =  My; 0 = ∫A z  dA
(MR)z =  Mz; 0 = ∫A y  dA
Equation 6-14
Equation 6-15
Equation 6-16

## Slide 51: 6.5 UNSYMMETRIC BENDING
Moment applied along principal axis
Eqn 6.14 is satisfied since z axis passes through centroid of x-sectional area
If material has linear-elastic behavior, then we can substitute  = (y/c)max into Eqn 6-16 and after integration, we get
∫A yz dA = 0

## Slide 52: 6.5 UNSYMMETRIC BENDING
Moment applied along principal axis
∫A yz dA = 0
This integral is the product of inertia for the area. It will be zero if y and z axes are chosen as principal axes of inertia for the area.
Thus, Eqns 6-14 to 6-16 will always be satisfied regardless of the direction of applied moment M

## Slide 53: 6.5 UNSYMMETRIC BENDING
Moment arbitrarily applied
If a member is loaded such that resultant internal moment does not act about one of the principal axes of x-section, resolve the moment into components directed along the principal axes
Use flexure formula to determine normal stress caused by each moment component
Use principle of superposition to determine resultant normal stress at the pt

## Slide 54: 6.5 UNSYMMETRIC BENDING
Moment arbitrarily applied
Resultant general normal stress at any pt on x-section is
Mzy
Iz
 = +
Myz
Iy
 = normal stress at the pt
y, z = coordinates of pt measured from x, y, z axes having origin at centroid of x-sectional area and forming a right-handed coordinate system
Equation 6-17

## Slide 55: 6.5 UNSYMMETRIC BENDING
Moment arbitrarily applied
Resultant general normal stress at any pt on x-section is
Mzy
Iz
 = +
Myz
Iy
My, Mz = resultant internal moment components along principal y and z axes. Positive if directed along +y and +z axes. Can also be stated as My = M sin  and Mz = M cos  , where  is measured positive from +z axis toward +y axis
Iy, Iz = principal moments of inertia computed about the y and z axes, respectively
Equation 6-17

## Slide 56: 6.5 UNSYMMETRIC BENDING
Moment arbitrarily applied
=
+

## Slide 57: 6.5 UNSYMMETRIC BENDING
Orientation of neutral axis
Angle  of neutral axis can be determined by applying Eqn 6-17 with  = 0, since no normal stress acts on neutral axis. Finally, we get
Iz
Iy
tan  = tan 
For unsymmetrical bending, angle  defining direction of moment M is not equal to angle , angle defining inclination of neutral axis unless Iz = Iy.
Thus,     90o
Equation 6-19

## Slide 58: 6.5 UNSYMMETRIC BENDING
IMPORTANT
Flexure formula applied only when bending occurs about axes that represent the principal axes of inertia for x-section
These axes have their origin at centroid and are orientated along an axis of symmetry and perpendicular to it
If moment applied about arbitrary axis, then resolve moment into components along each of the principal axes, and stress at a pt is determined by superposition of stress caused by each moment component.

## Slide 59: EXAMPLE 6.20
Z-section shown is subjected to bending moment of M = 20 kN·m. Using methods from Appendix A, the principal axes y and z are oriented as shown such that they represent the maximum and minimum principal moments of inertia, Iy = 0.960(10-3) m4 and Iz = 7.54(10-3) m4 respectively.
Determine normal stress at point P and orientation of neutral axis.

## Slide 60: EXAMPLE 6.20 (SOLN)
Internal moment components
To use Eqn 6-19, z axis needs to be principal axis for the maximum moment of inertia, as most of the area if located furthest away from this axis
My = 20 kN·m sin 57.1o = 16.79 kN·m
Mz = 20 kN·m cos 57.1o = 10.86 kN·m

## Slide 61: EXAMPLE 6.20 (SOLN)
Bending stress
The y and z coordinates of P must be determined first. Note that y’, z’ coordinates of P are (0.2 m, 0.35 m). Using colored and shaded triangles from construction shown below,
yP = 0.35 sin 32.9o  0.2 cos 32.9o = 0.3580 m
zP = 0.35 cos 32.9o  0.2 sin 32.9o = 0.1852 m

## Slide 62: EXAMPLE 6.20 (SOLN)
Bending stress
Applying Eqn 6-17, we have
Mzy
Iz
 = + = ... = 3.76 MPa
Myz
Iy

## Slide 63: EXAMPLE 6.20 (SOLN)
Orientation of neutral axis
Angle =57.1o is shown, Thus,
Iz
Iy
tan  = tan 
 = 85.3o
. . .
Neutral Axis