## Slide 1: *6.6 COMPOSITE BEAMS
Beams constructed of two or more different materials are called composite beams
Engineers design beams in this manner to develop a more efficient means for carrying applied loads
Flexure formula cannot be applied directly to determine normal stress in a composite beam
Thus a method will be developed to “transform” a beam’s x-section into one made of a single material, then we can apply the flexure formula

## Slide 2: *6.6 COMPOSITE BEAMS
Trial-and-error procedure requires the stress distribution produce a zero resultant force on x-section and moment of stress distribution about neutral axis must be equal to M
A simpler way to satisfy the conditions is to “transform” the beam into one made of a single material

## Slide 3: *6.6 COMPOSITE BEAMS
Height remains the same, but upper portion of beam widened to carry equivalent load to that carried by material 1.
n =
E1
E2
Equation 6-20
Dimensionless factor n, is called the transformation factor. It indicates that x-section, with a width b on original beam, be increased to a width of b2 = nb in region where material 1 is being transformed into material 2.

## Slide 4: *6.6 COMPOSITE BEAMS

## Slide 5: *6.6 COMPOSITE BEAMS
Once “transformed”, the normal-stress distribution over the transformed x-section will be linear as shown below.

## Slide 6: *6.6 COMPOSITE BEAMS
For “transformed” material, stress on transformed section has to be multiplied by transformation factor n (or n’)
 = n’
Equation 6-21

## Slide 7: *6.6 COMPOSITE BEAMS
IMPORTANT
Composite beams made from different materials to efficiently carry a load
Application of flexure formula requires material to be homogeneous, and x-section of beam must be transformed into a single material

## Slide 8: *6.6 COMPOSITE BEAMS
IMPORTANT
Transformation factor is a ratio of the moduli of different materials that make up the beam. It converts dimensions of x-section of composite beam into a beam of single material.
Stress in transformed section must be multiplied by transformation factor to obtain stress in actual beam

## Slide 9: EXAMPLE 6.22
Composite beam as shown. If allowable normal stress for steel is (allow)st = 168 MPa and for wood is (allow)w = 21 MPa, determine maximum bending moment beam can support, with and without reinforcement.
Est = 200 GPa, Ew = 12 GPa, Moment of inertia of steel beam is Iz = 7.93  106 mm4, x-sectional area is A = 5493.75 mm2

## Slide 10: EXAMPLE 6.22 (SOLN)
Without board
Neutral axis coincides with the z axis. Direct application of flexure formula to steel beam yields
Mc
Iz
(allow)st =
M = 12.688 kN·m
. . .

## Slide 11: EXAMPLE 6.22 (SOLN)
With board
Easier to transform wood to equivalent amount of steel. Thus, n = Ew/Est.
12(103) MPa
200(103) MPa
bst = nbw = (300 mm) = 18 mm

## Slide 12: EXAMPLE 6.22 (SOLN)
With board
Neutral axis is at
Moment of inertia about neutral axis is
 y A
 A
y = = ... = 13.57 mm
I = ... = 13.53(106) mm4

## Slide 13: EXAMPLE 6.22 (SOLN)
With board
Maximum normal stress in steel will occur at bottom of the beam. Here c = 105 mm + 13.57 mm = 118.57 mm. Therefore,
Mc
I
(allow)st =
M = 19.17 kN·m
. . .

## Slide 14: EXAMPLE 6.22 (SOLN)
With board
Maximum normal stress in wood occur at top of the beam. Here c’ = 105 mm  13.57 mm = 91.43 mm. Since w = nst, maximum moment based on allowable stress for wood is
M’c’
I
(allow)w = n
M’ = 51.79 kN·m
. . .

## Slide 15: EXAMPLE 6.22 (SOLN)
With board
By comparison, maximum moment limited by allowable steel in the steel. Thus, M = 19.17 kN·m.
Note also that by using board as reinforcement, one provides an additional 51% moment capacity for the beam

## Slide 16: *6.7 REINFORCED CONCRETE BEAMS
Steel reinforcing rods is placed in concrete to resist tension cracking
The rods are placed farthest away from beam’s neutral axis. However, they also need concrete coverage to prevent corrosion or loss of strength in case of fire

## Slide 17: EXAMPLE 6.23
If reinforced concrete beam is subjected to bending moment of M = 60 kN·m, determine the normal stress in each of the steel reinforcing rods and maximum normal stress in the concrete.
Take Est = 200 GPa and Econc = 25 GPa.

## Slide 18: EXAMPLE 6.23 (SOLN)
Section properties
Total area of steel, Ast = 2[(12.5 mm)2] = 982 mm2 will be transformed into an equivalent area of concrete.
A’ = nAst = ... = 7856 mm2
Centroid must lie on the neutral axis, thus  yA = 0
(h’)2 + 52.37h’  20949.33 = 0
Solving for positive root, h’ = 120.90 mm

## Slide 19: EXAMPLE 6.23 (SOLN)
Section properties
Using computed value of h’, moment of inertia of transformed section about neutral axis is
I = ... = 788.67  106 mm4

## Slide 20: EXAMPLE 6.23 (SOLN)
Normal stress
Apply flexure formula to transformed section, maximum normal stress in concrete is
(conc)max = ... = 9.20 MPa
Normal stress resisted by “concrete” strip, is
’conc = ... = 21.23 MPa
Normal stress in each of the rods is
’st = n’conc = ... = 169.84 MPa

## Slide 21: *6.8 CURVED BEAMS
Flexure formula only applies to members that are straight as normal strain varies linearly from the neutral axis
Thus another equation needs to be formulated for curved beam, i.e., a member that has a curved axis and is subjected to bending

## Slide 22: *6.8 CURVED BEAMS
Assumptions for analysis:
  X-sectional area is constant and has an axis of symmetry that is perpendicular to direction of applied moment M
  Material is homogeneous and isotropic and behaves in linear-elastic manner under loading
  X-sections of member remain plane after moment applied and distortion of x-section within its own will be neglected

## Slide 23: *6.8 CURVED BEAMS
By first principles:
 = Ek ( )
R  r
r
Equation 6-22

## Slide 24: *6.8 CURVED BEAMS
Equation 6-23
R =
A
dA
r
∫A
R = location of neutral axis, specified from center of curvature O’ of member
A = x-sectional area of the member
R = arbitrary position of the area element dA on x-section specified from center of curvature P’ of member
Location of neutral axis:

## Slide 25: *6.8 CURVED BEAMS
Common x-sections to use in integral in Eqn 6-23
R =
A
dA
r
∫A

## Slide 26: *6.8 CURVED BEAMS
Normal stress in curved beam:
 =
M(R  r)
Ar(r  R)
Equation 6-24
 =
My
Ae(R  y)
Equation 6-25
The above equations represent 2 forms of the curved-beam formula, used to determine the normal-stress distribution in a member

## Slide 27: *6.8 CURVED BEAMS
Normal stress in curved beam:
The stress distribution is as shown, hyperbolic, and is sometimes called circumferential stress
Radial stress will also be created as a result
If radius of curvature is greater than 5 times the depth of member, flexure formula can be used to determine the stress instead

## Slide 28: *6.8 CURVED BEAMS
IMPORTANT
Curved beam formula used to determine circumferential stress in a beam when radius of curvature is less than five times the depth of the beam
Due to beam curvature, normal strain in beam does not vary linearly with depth as in the case of straight beam. Thus, neutral axis does not pass through centroid of section
Ignore radial stress component of bending, if x-section is a solid section and not made from thin plates

## Slide 29: *6.8 CURVED BEAMS
Procedure for analysis
Section properties
Determine x-sectional area A and location of centroid r, measured from centre of curvature
Compute location of neutral axis, R using Eqn 6-23 or Table 6-2. If x-sectional area consists of n “composite” parts, compute ∫ dA/r for each part.
From Eqn 6-23, for entire section,
In all cases, R < r
R =
A
dA
r
∫A

## Slide 30: *6.8 CURVED BEAMS
Procedure for analysis
Normal stress
Normal stress located at a pt r away from the centre of curvature is determined Eqn 6-24. If distance y to pt is measured from neutral axis, then compute e = r  R and use Eqn 6-25
Since r  R generally produces a very small number, it is best to calculate r and R with sufficient capacity so that subtraction leads to e with at least 3 significant figures

## Slide 31: *6.8 CURVED BEAMS
Procedure for analysis
Normal stress
Positive stress indicates tensile stress, negative means compressive stress
Stress distribution over entire x-section can be graphed, or a volume element of material can be isolated and used to represent stress acting at the pt on x-section where it has been calculated

## Slide 32: EXAMPLE 6.24
Steel bar with rectangular x-section is shaped into a circular arc. Allowable normal stress is allow = 140 MPa. Determine maximum bending moment M that can be applied to the bar. What would this moment be if the bar was straight?

## Slide 33: EXAMPLE 6.24 (SOLN)
Internal moment
Since M tends to increase bar’s radius of curvature, it is positive.
Section properties
Location of neutral axis is determined using Eqn 6-23.
dA
r
∫A
(20 mm) dr
r
∫90 mm
110 mm
= = 4.0134 mm
Similar result can also be obtained from Table 6-2.

## Slide 34: EXAMPLE 6.24 (SOLN)
Section properties
We do not know if normal stress reaches its maximum at the top or bottom of the bar, so both cases must be compute separately.
Since normal stress at bar top is  = 140 MPa
 =
M(R  ro)
Aro(r  R)
. . .
M = 0.199 kN·m

## Slide 35: EXAMPLE 6.24 (SOLN)
Section properties
Likewise, at bottom of bar,  = +140 MPa
 =
M(R  ri)
Ari(r  R)
. . .
M = 0.174 kN·m
By comparison, maximum that can be applied is 0.174 kN·m, so maximum normal stress occurs at bottom of the bar.

## Slide 36: EXAMPLE 6.24 (SOLN)
Section properties
Compressive stress at top of bar is then
 = 122.5 N/mm2
By comparison, maximum that can be applied is 0.174 kN·m, so maximum normal stress occurs at bottom of the bar.

## Slide 37: EXAMPLE 6.24 (SOLN)
If bar was straight?
 = Mc/I
This represents an error of about 7% from the more exact value determined above.
M = 0.187 kN·m
. . .

## Slide 38: 6.9 STRESS CONCENTRATIONS
Flexure formula can only be used to determine stress distribution within regions of a member where x-sectional area is constant or tapers slightly
If x-section suddenly changes, normal-stress and strain distributions become nonlinear and they can only be obtained via experiment or mathematical analysis using the theory of elasticity

## Slide 39: 6.9 STRESS CONCENTRATIONS
Common discontinuities include members having notches on their surfaces, holes for passage of fasteners or abrupt changes in outer dimensions of member’s x-section
The maximum normal stress at the discontinuities occur at the smallest x-sectional area

## Slide 40: 6.9 STRESS CONCENTRATIONS
For design, we only need to know the maximum normal stress developed at these sections, not the actual stress distribution
Thus, the maximum normal stress due to bending can be obtained using the stress-concentration factor K
 = K
Mc
I
Equation 6-26

## Slide 41: 6.9 STRESS CONCENTRATIONS
IMPORTANT
Stress concentrations in members subjected to bending occur at pts of x-sectional change, such as notches and holes, because here the stress and strain become nonlinear.
The more severe the change, the larger the stress distribution
For design/analysis, not necessary to know the exact stress distribution around x-sectional change
The maximum normal stress occurs at the smallest x-sectional area

## Slide 42: 6.9 STRESS CONCENTRATIONS
IMPORTANT
The maximum normal stress can be obtained using stress concentration factor K, which is determined through experiment and is a function of the geometry of the member
If material is brittle or subjected to fatigue loading, stress concentrations in the member need to be considered in design

## Slide 43: EXAMPLE 6.26
Transition in x-sectional area of steel bar is achieved using shoulder fillets as shown. If bar is subjected to a bending moment of 5kN·m, determine the maximum normal stress developed in the steel. Y = 500 MPa.

## Slide 44: EXAMPLE 6.26 (SOLN)
Moment creates largest stress in bar at base of fillet. Stress concentration factor can be determined from the graph.
r/h = ... = 0.2
w/h = ... = 1.5
From above values, we get K = 1.45

## Slide 45: EXAMPLE 6.26 (SOLN)
Applying Eqn 6-26:
Result indicates that steel remains elastic since stress is below yield stress.
Normal stress distribution is nonlinear.
 = K = ... = 340 MPa
Mc
I
However, by Saint-Venant’s principle, the localized stresses smooth out and become linear when one moves at a distance of 80 mm or more to right of transition.

## Slide 46: EXAMPLE 6.26 (SOLN)
Thus, the flexure formula gives max = 234 MPa.
Note that choice of a larger-radius fillet will significantly reduce max, since as r increase, K will decrease.

## Slide 47: *6.10 INELASTIC BENDING
Linear normal-strain distribution
Based on geometric considerations, it was shown in section 6.3 that normal strains that develop in the material always vary linearly from zero at neutral axis of x-section to a maximum at the farthest pt from the neutral axis
Resultant force equals zero
Since there is only a resultant internal moment acting on the x-section, resultant force caused by stress distribution must be equal to zero.
FR =  Fx; ∫A  dA = 0
Equation 6-27

## Slide 48: *6.10 INELASTIC BENDING
Resultant moment
Resultant moment at section must be equivalent to moment caused by the stress distribution about the neutral axis
Maximum elastic moment
Since each of the forces acts through the centroid of the volume of its associated triangular stress block, we have
(MR)z =  Mz; M = ∫A y ( dA)
Equation 6-28
MY = (1/6)(bh2Y)
Equation 6-29

## Slide 49: *6.10 INELASTIC BENDING
Plastic moment
From first principles, we derive the plastic moment
Its value is unique only for the rectangular section shown below, since analysis depends on geometry of the x-section
MP = (3/2) MY
Equation 6-32

## Slide 50: *6.10 INELASTIC BENDING
Plastic moment
Beams used in steel buildings are sometimes designed to resist a plastic moment. The codes usually list a design property called the shape factor:
The k-value specifies the additional moment capacity a beam can support beyond its maximum elastic moment.
k = MP/MY
Equation 6-33

## Slide 51: *6.10 INELASTIC BENDING
Ultimate moment
Trial-and-error procedure is used to solve such a problem:
  For given moment M, assume location of neutral axis and slope of “linear” strain distribution
  Graphically establish the stress distribution on member’s x-section using - curve to plot values of stress and strain.

## Slide 52: *6.10 INELASTIC BENDING
Ultimate moment
Trial-and-error procedure is used to solve such a problem:
  Determine the volumes enclosed by tensile and compressive stress “blocks”. They need to be equal, otherwise, adjust the location neutral axis till they are equal
  Once tensile force = compressive force, compute their corresponding moments. Moment arms are measured from the neutral axis to the centroids of the volumes defined by the stress distributions

## Slide 53: *6.10 INELASTIC BENDING
IMPORTANT
Normal strain distribution over x-section of a beam is based only on geometric considerations and has been found to always remain linear, regardless of load applied
Normal stress distribution must be determined from the material behavior, or stress/strain diagram once the strain is established
Location of neutral axis is determined from the condition that resultant force on the x-section is zero

## Slide 54: *6.10 INELASTIC BENDING
IMPORTANT
Resultant internal moment on x-section must be equal to moment of stress distribution about the neutral axis
Perfectly plastic behavior assumes normal stress distribution is constant over the x-section, and beam continue to bend, with no increase in moment. This moment is called the plastic moment.

## Slide 55: EXAMPLE 6.28
T-beam has dimensions as shown. If it is made of an elastic perfectly plastic material having tensile and compressive yield stress of Y = 250 MPa, determine the plastic moment that can be resisted by the beam.

## Slide 56: EXAMPLE 6.28 (SOLN)
“Plastic” stress distribution acting over beam’s x-sectional area is shown. The x-section is not symmetric with respect to horizontal axis, thus neutral axis will not pass through centroid of x-section.
To determine location of neutral axis, we require the stress distribution to produce a zero resultant force on the x-section.

## Slide 57: EXAMPLE 6.28 (SOLN)
Assuming d  120 mm, we have
∫A  dA = 0; T C1  C2 = 0
d = 0.110 m
< 0.120 m (OK!)
. . .
Using this result, forces acting on each segment:
T = ... = 412.5 kN
C1 = ... = 37.5 kN
C2 = ... = 375 kN

## Slide 58: EXAMPLE 6.28 (SOLN)
Hence, resulting plastic moment about the neutral axis is
MP = ... = 29.4 kN·m

## Slide 59: *6.11 RESIDUAL STRESS
Like the case for torsion, residual stress is important when considering fatigue and other types of mechanical behavior
A method is developed here to determine residual stress for a member subjected to bending
Plastic moment, modulus of rupture and principles of superposition is used in the method

## Slide 60: EXAMPLE 6.30
Steel wide-flange beam shown is subjected to a fully plastic moment of MP. If moment is removed, determine the residual-stress distribution in the beam. Material is elastic perfectly plastic and has a yield stress of Y = 250 MPa.

## Slide 61: EXAMPLE 6.30 (SOLN)
Normal stress distribution caused by MP is shown in (b). When MP is removed, material responds elastically. The assumed elastic stress distribution is shown in (c). Modulus of rupture r, is calculated from the flexure formula.

## Slide 62: EXAMPLE 6.30 (SOLN)
Using MP = 188 kN·m and I = 82.44  106 mm4.
max =
Mc
I
... allow = 285.1 MPa
As expected, r < 2Y.
Superposition of stresses gives residual-stress distribution as shown. Note that point of zero normal stress was determined by proportion,
281.51 MPa
125 mm
2501 MPa
y
=
y = 109.61 mm

## Slide 63: CHAPTER REVIEW
Shear and moment diagrams are graphical representations of internal shear and moment within a beam.
They can be constructed by sectioning the beam an arbitrary distance x from the left end, finding V and M as functions of x, then plotting the results
Another method to plot the diagrams is to realize that at each pt, the slope of the shear diagram is a negative of the distributed loading, w = dV/dx; and slope of moment diagram is the shear, V = dM/dx.

## Slide 64: CHAPTER REVIEW
Also, the (-ve) area under the loading diagram represents the change in shear, V = ∫ w dx.
The area under the shear diagram represents the change in moment, M = ∫ V dx. Note that values of shear and moment at any pt can be obtained using the method of sections
A bending moment tends to produce a linear variation of normal strain within a beam.
Provided that material is homogeneous, Hooke’s law applies, and moment applied does not cause yielding, then equilibrium is used to relate the internal moment in the beam to its stress distribution

## Slide 65: CHAPTER REVIEW
That results in the flexure formula,  = Mc/I, where I and c are determined from the neutral axis that passes through the centroid of the x-section
If x-section of beam is not symmetric about an axis that is perpendicular to neutral axis, then unsymmetrical bending occurs
Maximum stress can be determined from formulas, or problem can be solved by considering the superposition of bending about two separate axes

## Slide 66: CHAPTER REVIEW
Beams made from composite materials can be “transformed” so their x-section is assumed to be made from a single material
A transformation factor, n = E1/E2 is used to do this.
Once the “transformation” is done, the stress in the beam can be determined in the usual manner of the flexure formula
Curved beams deform such that normal strain does not vary linearly from the neutral axis

## Slide 67: CHAPTER REVIEW
Provided that material of the curved beam is homogeneous, linear elastic and x-section has axis of symmetry, then curved beam formula can be used to determine the bending stress,  = My/[Ae(R y)]
Stress concentrations occur in members having a sudden change in their x-section, such as holes and notches.
The maximum bending stresses in such locations is determined using a stress concentration factor K, that is found empirically,  = Kavg.

## Slide 68: CHAPTER REVIEW
If bending moment causes material to exceed its elastic limit, then normal strain remains linear, however stress distribution varies in accordance with shear strain diagram and balance of force and moment equilibrium. Thus plastic and ultimate moments can be determined.
If an applied plastic or ultimate moment is released, it will cause the material to respond elastically, thereby inducing residual stresses in the beam