## Slide 1: Multifocal Intraocular Lenses
Abdullah Al-assiri
Mansour Farooqui
Abdulrahman Al-Muammar
Saudi Ophthalmology Meeting 2009

## Slide 2: Course Outline
Part I
  Optical principles of multifocal lenses
  Designs of multifocal lenses
  Patient selection
  Intraocular lenses calculation
Part II
  Visual results following implantation of multifocal lenses
    Personal data
    Literature review
Part III
  Multifocal IOLs and pupil size
  Multifocal IOLs and preoperative corneal astigmatism
  Multifocal IOLs and posterior capsular opacification
  Postoperative residual refractive error
  Controversial issues

## Slide 3: Multifocal IOLs and pupil size
Preoperative evaluation and inclusion/exclusion criteria for MIOL must include pupil size
Pupil size affects various visual functions in pseudophakic patients with MIOLs including
  Glare and haloes disability
  Binocular vision
  Contrast sensitivity
  Far and near VA

## Slide 4: Multifocal IOLs and pupil size
Previous studies have shown that pupil size decreases as age increases in a linear fashion to all luminance level
Winn et al, Invest Ophthalmol Vis Sci 1994
Nakamura found that photopic and scotopic pupil sizes decreased with age up to 60 years
Nakamura et al, J Cataract Refract Surg 2009

## Slide 5: Multifocal IOLs and pupil size
Kurz measured monocular and binocular pupil sizes and reported that pupil diameters were larger when the measurement was monocular
Kurz et al, J Cataract Refract Surg 2004

## Slide 6: Multifocal IOLs and pupil size
Postoperative pupil size cannot always be predicted from the preoperative diameter because the pupil can be substantially impaired by cataract surgery
Koch et al,J Cataract Refract Surg 1996
Newer phacoemulsification surgical techniques have shown unchanged pupils after surgery
Hayashi at al, J Cataract Refract Surg 2004

## Slide 7: Multifocal IOLs and pupil size
Pupil size under mesopic and photopic conditions must be determined prior to surgery

## Slide 8
Restor
Rezoom
Tecnis

## Slide 9: Pre-existing astigmatism
Approximately 30% of cataract surgical patients will have pre-existing astigmatism
Routine corneal topography to qualify the type of astigmatism and to quantify the amount of astigmatism should be done preoperatively
Irregular astigmatism should eliminate patients as candidates for MIOLs

## Slide 10: Pre-existing astigmatism
Surgeons using MIOL should manage pre-existing regular astigmatism in order to allow patients to gain the full benefit of MIOL technology
Available options are
  < 0.75 D Cyl, perform on axis incision
  0.75-1.5 D Cyl, perform intraoperative limbal relaxing incision
  > 1.5 D Cyl, perform intraoperative limbal relaxing incision + pot-op laser refractive surgery
  WWW.LRIcalculator.com
  Astigmatic keratotomy

## Slide 11: Decrease postoperative visual acuity
Most common causes of decrease visual acuity after MIOLs implantation are
  Residual refractive error
  Posterior capsular opacification
  Cystoid macular edema
  Ocular surface disease
  Poor adaptation
  Buznego et al, curr Opinion in ophthalmology 2009

## Slide 12: Surgical tips
Surgical tips for MIOLs implantation
    Well dilated pupil
    Proper capsulorrhexis size with good centration
    Proper cortical cleaning
    Lens implantation

## Slide 13: Effect of posterior capsular opacification in patients with MIOLs
Posterior capsular opacification (PCO) causes forward and backward light scattering and reduces visual acuity and contrast sensitivity
Since MIOLS reduces contrast sensitivity, it is not known if this can be exacerbated by the development of PCO, which may lead to an increased rate of Nd:YAG capsulotomy

## Slide 14: Effect of posterior capsular opacification in patients with MIOLs
Incidence of PCO with MIOLs is about 10 %
De Vries at al, J Cataract Refract surg 2008
Elgohary found that the effect of PCO on visual function in patients with monofocal and multifocal IOLs is comparable
Elgohary et al, Eye 2008

## Slide 15: Effect of posterior capsular opacification in patients with MIOLs
Recent literatures didn’t report complication with Nd:YAG capsulotomy in patients with MIOLS
Surgeons should proceed with capsulotomy only if the possibility of IOL exchange has been excluded

## Slide 16: Postoperative residual refractive error
Emmetropia is critical to a good performance of multifocal IOLs
Not all patients achieve emmetropia with lens surgery alone
Laser refractive surgery can be done to correct residual error

## Slide 17: Postoperative residual refractive error
Knorz had reported good outcome using wavefront-guided ablation in patients with diffractive multifocal IOLs
Knorz et al, J Refract surg 2008
Campbell performed wavefront measurements in an artificial eye and found that diffractive IOLs could be measured reliably whereas refractive multifocal IOLs could not
Campbell, J Refract Surg 2008

## Slide 18: Controversial issues
Neuroadaptation
  MIOLS by definition, deliver more than one simultaneous image to the visual cortex
  Surgeons must consider patients ability to neuroadapt

## Slide 19: Controversial issues
Mixing and Matching MIOLs
  Mixing different MIOLs designs is not generally agreed upon concept
  Bilateral implantation of the same design and mixing different designs are viable option
  Decision regarding which MIOL should be used for the second eye should be based on the result of the first eye

## Slide 20: Controversial issues
Patients with Unilateral cataract
Patients with monofocal IOL in the first eye
Time between first and second eye surgery

## Slide 21: Controversial issues
Complicated surgery in the second eye
Patients who may have diabetes or glaucoma after cataract surgery
Future vitreo-retina surgery
Lim et al, Ophthalmology 2000
Pediatric cataract surgery
Jacobi et al, Ophthalmology 2001

## Slide 22
Thank you for your attention