## Slide 1: Chapter 1: Planning Maintenance for Complex Networks
CCNP TSHOOT: Maintaining and Troubleshooting IP Networks
Eng. AbdulMalik Rahhal
Notes: <number>
Cisco Networking Academy Program
CCNP TSHOOT: Maintaining and Troubleshooting IP Networks
Chapter 1: Planning Maintenance for Complex Networks

## Slide 2: Chapter 1 Objectives
This chapter covers the following topics:
  • Applying maintenance methodologies
  • Maintenance processes and procedures
  • Network maintenance tools, applications, and resources
Notes: <number>
High-level assessment claims:
Describe Maintenance Models and Methodologies
Describe the network maintenance plan
Describe the disaster recovery process
Describe common network maintenance tools, applications and resources
Describe the importance of network monitoring and performance measurement
Explain how to work with backup and restore services

## Slide 3: 1- Maintenance Models and Methodologies
The objective of network maintenance is to keep the network available with minimum service disruption and at acceptable performance levels.
A network engineer’s job description can include tasks related to:
  Device installation and maintenance: Includes tasks such as installing devices and software, as well as creating and backing up configurations and software.
  Failure response: Includes tasks such as supporting users that experience network problems, troubleshooting device or link failures, replacing equipment, and restoring backups.
Notes: <number>

## Slide 4: 1- Maintenance Models and Methodologies
A network engineer’s job description can include tasks related to:
  Network performance: Includes tasks such as capacity planning, performance tuning, and usage monitoring.
  Business procedures: Includes tasks such as documenting, compliance auditing, and service level agreement (SLA) management.
  Security: Includes tasks such as following and implementing security procedures and security auditing.
Notes: <number>

## Slide 5: 1- Maintenance Models and Methodologies
Method of performing network maintenance:
Interrupt driven maintenance : is the most basic method of performing network maintenance. For example is that a company’s network engineer reviews and improves the security of the network only when security concerns or incidents are reported.
structured network maintenance : Structured network maintenance predefines and plans much of the processes and procedures. This proactive approach not only reduces the frequency and quantity of user, application, and business problems, it also renders the responses to incidents more efficiently.

## Slide 6: Benefits of Structured Maintenance over Interrupt-driven Maintenance
Proactive vs. reactive
Reduced network downtime: Discover and prevent problems before they happen. Maximize mean time between failures (MTBF). Minimize mean time to repair (MTTR).
More cost effective: Performance monitoring and capacity planning for budgeting and future networking needs. Choosing proper equipment for better price/performance ratio over the lifetime of equipment.
Notes: <number>

## Slide 7: Benefits of Structured Maintenance over Interrupt-driven Maintenance
Better alignment with business objectives : Time and resources are allocated to processes based on importance to the business instead of prioritizing tasks and assigning budgets based on incidents. For example, upgrades and major maintenance jobs are not scheduled during critical business hours.
Improved network security : Attention to network security is part of structured network maintenance. Up-to-date prevention and detection mechanisms can notify staff through logs and alarms. Monitoring allows you to observe network vulnerabilities and needs, and justify plans for strengthening network security
Notes: <number>

## Slide 8: Maintenance Models and Organizations
IT Infrastructure Library (ITIL): This is a framework of best practices for IT Service Management. ITIL describes best practices that help in providing high quality IT services that are aligned with business needs and processes. Developed by the UK Office of Government Commerce (OGC).
ISO – FCAPS categories (FCAPS is first letter of each):
  Fault management
  Configuration management
  Accounting management
  Performance Management
  Security Management
Notes: <number>

## Slide 9: Maintenance Models and Organizations
ITU-T - Telecommunications Management Network (TMN): The ITU-T integrated and refined the FCAPS model to create this approach, which defines a framework for the management of telecommunications networks.
Cisco Lifecycle Services Phases - PPDIOO: A model that helps businesses successfully deploy, operate, and optimize Cisco technologies in their network. PPDIOO = Prepare, Plan, Design, Implement, Operate, and Optimize (PPDIOO) Network maintenance tasks are usually considered part of the Operate and Optimize phases of the cycle.
Notes: <number>

## Slide 10: The Configuration Management element of the FCAPS model
Notes: <number>
Example procedures and tools for the Configuration Management element of FCAPS

## Slide 11: Network Maintenance Processes and Procedures
A network maintenance plan includes procedures for the following tasks:
Accommodating Adds, Moves, and Changes: Affects users, computers, printers, servers and phones and potential changes in configuration and cabling.
Installation and configuration of new devices: Includes adding ports, link capacity and network devices. Can be handled by a different group within an organization, by an external party, or by internal staff.
Replacement of failed devices: Done through service contracts or by in-house support engineers.
Backup of device configurations and software: Good backups of both software and configurations can simplify and reduce the time the recovery process takes for failed devices.
Notes: <number>

## Slide 12: Network Maintenance Processes and Procedures
Troubleshooting link and device failures: Diagnosing and resolving failures related to network components, links, or service provider connections are essential tasks within a network engineer’s job.
Software upgrading or patching: Requires that you stay informed of available software upgrades or patches and use them if necessary. These can address critical performance or security vulnerabilities.
Network monitoring: Monitoring operation of the devices and user activity can be performed using simple mechanisms such as router and firewall logs or by using sophisticated network monitoring applications.
Performance measurement and capacity planning: This can help determine when to upgrade links or equipment and justify the cost. Facilitates planning for upgrades (capacity planning) to help prevent bottlenecks, congestion and failures.
Writing and updating documentation: Current network documentation is used for reference during implementation, administration, and troubleshooting is a mandatory network maintenance task.
Notes: <number>

## Slide 13: Network Maintenance Tools, Applications, and Resources
Console
SSH
Telnet
HTTP
HTTPS
Telnet
SSH
NTP
Syslog
TFTP
FTP
SCP
HTTP(S)
Time
Logging
Backups
CLI mgmt
GUI mgmt
Notes: <number>
CLI management: Cisco IOS Software includes a command-line interface (CLI) to configure and monitor routers and switches. This includes show and debug commands, Embedded Event Manager (EEM) commands, and IP Service Level Agreement (SLA) commands. The CLI is accessed through the serial console of the device or remotely using Telnet or Secure Shell (SSH) protocols.
GUI management: Free GUI-based device management tools include Cisco Configuration Professional (CCP), Secure Device Manager (SDM), Cisco Configuration Assistant (CCA), and Cisco Network Assistant (CNA).
Backups: You can use TFTP, FTP, HTTP, or Secure Copy Protocol (SCP) server to create backups of the software and configurations of routers and switches.
Logging: Basic logging can send router or switch log messages to a syslog server. Syslog is a standard service on most UNIX-based operating systems. Several free Windows-based syslog servers are available for download from the Internet. Examples are Kiwi and TFTPD32.
Time: To synchronize clocks on all of your network devices, it is useful to have a Network Time Protocol (NTP) server on your network. There are many public timeservers available on the Internet and NTP is supported by the Cisco IOS.

## Slide 14: NTP Example
service timestamps debug datetime msec localtime show-timezone
service timestamps log datetime localtime show-timezone
!
clock timezone PST -8
clock summer-time PDT recurring 2 Sun Mar 2:00 1 Sun Nov 2:00
!
ntp server 10.1.220.3
(Selected output from the running config)
Notes: <number>
In the example, the clock of this device is synchronized to a single timeserver with IP address 10.1.220.3. The time zone set to Pacific Standard Time (PST), which has an -8 hour offset to Universal Time Coordinated (UTC). The clock is configured to change to daylight savings time on the 2nd Sunday in March at 2:00 am and back to standard time on the first Sunday in November at 2:00 am.
The logging for system logging is configured to use the local date and time in the time stamps and to include the time zone in the time stamp. For log entries generated by debugs, the settings are similar, but milliseconds are included in the timestamps for greater accuracy.
For more details about the configuration of NTP, consult the “Configuring NTP” section of the Cisco IOS network management configuration guide: http://tinyurl.com/yezfkr3

## Slide 15: Cisco Configuration and Documentation Tools
Dynamic Configuration Tool
  Aids in creating hardware configurations
  Verifies compatibility of hardware and software selected
  Produces a Bill of Materials (BoM) with part numbers
Cisco Feature Navigator
  Quickly finds Cisco IOS Software release for required features
SNMP Object Navigator
  Translates SNMP Object Identifiers (OID) into object names
  Allows download of SNMP MIB files
  Verify supported MIBs for a Cisco IOS Software version
Cisco Power Calculator
  Calculates power supply requirements a PoE hardware configuration
  Requires CCO login
Notes: <number>
Dynamic Configuration Tool: Aids in creating hardware configurations. It verifies compatibility of hardware and software selected, produces a Bill of Materials (BoM) that lists the necessary part numbers.
https://apps.cisco.com/qtc/config/html/configureHomeGuest.html
Cisco Feature Navigator: This tool allows you to quickly find the right Cisco IOS Software release for the features you want to run on your network.
http://tools.cisco.com/ITDIT/CFN/
SNMP Object Navigator: The Simple Network Management Protocol (SNMP) Navigator translates SNMP Object Identifiers (OID) into object names. This tool also allows you to download SNMP Management Information Base (MIB) files and to verify the supported MIBs in a particular Cisco IOS Software version.
http://tools.cisco.com/Support/SNMP/do/BrowseOID.do?local=en
Cisco Power Calculator: This tool calculates the power supply requirements for a particular Power over Ethernet (PoE) hardware configuration. Requires CCO login.
Cisco Tool Index (to the above tools and more): http://www.cisco.com/en/US/products/prod_tools_index.html

## Slide 16: Logging Services
Events on networking devices can be logged.
  Various events
  Various levels of severity
Events are logged to:
  Console (default)
    Console display
    Buffer
  Server
Examples
  Interfaces up or down
  Configuration changes
  Routing protocol adjacencies
<number>

## Slide 17: Logging Services
Logging severity levels on Cisco Systems devices are as follows:
  (0) Emergencies
  (1) Alerts
  (2) Critical
  (3) Errors
  (4) Warnings
  (5) Notifications
  (6) Informational
  (7) Debugging
By default, all messages from level 0 to 7 are logged to the console
<number>

## Slide 18: Logging Services
Buffer
  logging buffered [buffer-size|level]
    May or may not be the default
  By default, messages of all severity levels are logged to buffer.
  show logging Displays the content of the buffer
    The buffer is circular, meaning that when the buffer has reached its maximum capacity, the oldest messages will be discarded to allow the logging of new messages.
<number>

## Slide 19: Logging Services
Console
  You can also adjust the logging severity level of the console.
  By default, all messages from level 0 to 7 are logged to the console;
  You can configure the severity level as an optional parameter:
  logging console level
  Limits the logging of messages displayed on the console terminal to the specified level and (numerically) lower levels.
  You can enter the level number or level name.
<number>

## Slide 20: Logging Services
Server
  logging ip-address command
    Some IOS version it is logging host
  By default, only messages of severity level 6 or lower will be logged to the syslog server.
  This can be changed by entering the logging trap level command.
<number>

## Slide 21: Network Monitoring and Performance Measurement Tools
Capacity planning: Measure average and peak loads on the network to create a baseline of the traffic levels and utilization. Repeat the measurements over time to monitor trends and predict when you need to upgrade links or equipment.
Diagnosing performance problems: Performance problems are difficult to troubleshoot because they are hard to quantify and very often intermittent. Problems could be related to an application, software, a server, or the network in between. Awareness of the network loads on the path between the client and the server is important to isolate the problem.
SLA compliance: SLAs can guarantee a level of service to others to you from a service provider. A method is required to measure whether the service guarantees defined in the SLA are met.
Notes: <number>

## Slide 22: Implementing Backup and Restore Services using FTP
Copy using FTP with specified username and password
Copy using FTP with stored username and password
R1(config)# ip ftp username backup
R1(config)# ip ftp password san-fran
R1(config)# exit
R1# copy startup-config ftp://10.1.152.1/R1-test.cfg
Address or name of remote host [10.1.152.1]?
Destination filename [R1-test.cfg]?
Writing R1-test.cfg !
2323 bytes copied in 0.304 secs (7641 bytes/sec)
R1# copy startup-config ftp://backup:san-fran@10.1.152.1/R1-test.cfg
Address or name of remote host [10.1.152.1]?
Destination filename [R1-test.cfg]?
Writing R1-test.cfg !
2323 bytes copied in 0.268 secs (8668 bytes/sec)
Notes: SCP, HTTP and HTTPS use a similar syntax, replacing the URL prefix ftp:// with scp://, http:// or https://
Specifying the username and password on the command line cumbersome and the password is displayed in clear text.
In the second example, the username and password is specified in the configuration.
<number>

## Slide 23: Implementing Backup and Restore Services using Archive
Setting up the configuration archive
show archive command output
R1(config)# archive
R1(config-archive)# path flash:/config-archive/$h-config
R1(config-archive)# write-memory
R1(config-archive)# time-period 10080
R1# show archive
There are currently 3 archive configurations saved.
The next archive file will be named flash:/config-archive/R1-config-4
Archive # Name
0
1 flash:/config-archive/R1-config-1
2 flash:/config-archive/R1-config-2
5 flash:/config-archive/R1-config-3 <- Most Recent
Notes: The archive command enters config-archive configuration mode.
The only mandatory parameter is the base file path.
The configuration path can include the variables $h for the device’s hostname and $t to for time and date stamp.
Adding the write-memory option triggers an archive copy of the running configuration to be created any time the running configuration is copied to NVRAM.
Archives can be made periodically by specifying the time-period option followed by a time period, specified in minutes.
Use the show archive command to verify archive to be created as demonstrated in Example 1-6.
<number>

## Slide 24: Implementing Backup and Restore Services using configure replace
R1# configure terminal
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)# hostname TEST
TEST(config)# ^Z
TEST# configure replace flash:config-archive/R1-config-3 list
This will apply all necessary additions and deletions
to replace the current running configuration with the
contents of the specified configuration file, which is
assumed to be a complete configuration, not a partial
configuration. Enter Y if you are sure you want to proceed. ? [no]: yes
!Pass 1
!List of Commands:
no hostname TEST
hostname RO1
end
Total number of passes: 1
Rollback Done
Notes: The slide shows a simple example where the hostname of a device is changed and then the configuration is rolled back to the most current archived configuration.
The command option list is added to the configure replace command in order to show the configuration commands that are being applied by the configuration replacement.

## Slide 25: Disaster Recovery Tools
Successful disaster recovery is dependent on the existence of the following:
Up to date configuration backups
Up to date software backups
Up to date hardware inventories
Configuration and software provisioning tools
Notes: <number>
As parts of the fundamental network maintenance toolkit, TFTP, FTP, SCP, HTTP and HTTPS servers are useful for creating backups of the configuration and operating system of a router or switch. Additional software can be used to extend the functionality of the toolkit and perform the following tasks:
  Automatic backup scheduling
  Configuration file comparison and change tracking
  Template creation and editing
  Pushing configurations to multiple devices
  Hardware inventory tracking
  CiscoWorks Resource Manager Essentials (RME), which is part of the CiscoWorks LAN Management Solutions (LMS), is a prime example of software that provides these functions.

## Slide 26: Chapter 1 Summary
Advantages of a structured network maintenance model over interrupt-driven include reduced network downtime and higher network security.
Examples of structured network maintenance methodologies include ITIL, FCAPS, TMN and Cisco Lifecycle Services (PPDIOO).
Network maintenance plans include procedures for adds/moves/changes, software upgrades and replacement of failed devices.
Network maintenance planning includes maintenance scheduling, documentation development, templates/procedures/conventions definition and disaster recovery planning.
Network documentation includes network drawings, connections, equipment lists, IP address administration, device configurations and design documentation.
When a device fails, disaster recovery requires that replacement hardware, software, configuration files and transfer tools be available.
Notes: <number>
Acronyms:
ITIL: IT Infrastructure Library (from UK Office of Government Commerce - OGC).
FCAPS: Fault, Configuration, Accounting, Performance, and Security Management (from ISO)
TMN: Telecommunications Management Network (from ITU-T)
PPDIOO: Prepare, Plan, Design, Implement, Operate, and Optimize (from Cisco)

## Slide 27: Chapter 1 Summary – Cont.
The basic components of a network maintenance toolkit include CLI and GUI device management tools as well as backup, log and time servers.
Cisco web-based tools and resources: Dynamic Configuration Tool, Cisco Feature Navigator, SNMP Object Navigator and Cisco Power Calculator.
Main motivations for measuring network performance are capacity planning, diagnosing performance problems and SLA compliance.
TFTP, FTP, SCP, HTTP, and HTTPS can be used to transfer files between network and backup devices. FTP, SCP, HTTP, and HTTPS are more secure than TFTP as they require authentication. SCP and HTTPS are most secure because they also incorporate encryption.
The configuration archiving feature can be helpful in creating configuration archives, either locally on a remote server (introduced with IOS Release 12.3(7)T).
Notes: <number>

## Slide 28: Chapter 1 Labs
There are no labs for this chapter.

## Slide 29
Notes: <number>