## Slide 1: Chapter 3: Using Maintenance & Troubleshooting Tools and Applications
CCNP TSHOOT: Maintaining and Troubleshooting IP Networks
Notes: <number>
Cisco Networking Academy Program
CCNP TSHOOT: Maintaining and Troubleshooting IP Networks
Chapter 3: Using Maintenance and Troubleshooting Tools and Applications

## Slide 2: Chapter 3 Objectives
Use Cisco IOS commands to gather information in support of diagnostic processes.
Identify tools used for specific maintenance and troubleshooting processes.
Notes: <number>

## Slide 3: Using Cisco IOS Software for Maintenance and Troubleshooting
Notes: <number>

## Slide 4: Collecting and Filtering Information Using IOS show Commands
R1# show ip route 10.1.193.2
Routing entry for 10.1.193.0/30
Known via "connected", distance 0, metric 0 (connected, via interface)
Redistributing via eigrp 1
Routing Descriptor Blocks:
* directly connected, via Serial0/0/1
Route metric is 0, traffic share count is 1
R1# show ip route 10.1.193.10
% subnet not in table
Filtering show ip route command output
Notes: To limit the output of the show ip route command, you can enter a specific IP address on the command line as an option. You can also limit output to a specific routing protocol or type of route.
Note that if gateway of last resort (default route) is present in the IP routing table, but no entry matches the IP address entered, the router responds with the % Subnet not in table message even though packets for that destination are forwarded using the gateway of last resort.
<number>

## Slide 5: Collecting and Filtering Information Using IOS show Commands – Cont.
R1# show ip route
< output omitted >
192.168.1.0/30 is subnetted, 1 subnets
C 192.168.1.0 is directly connected, Loopback0
R1# show ip route 192.168.1.0
Routing entry for 192.168.1.0/30, 1 known subnets
Attached (1 connections)
C 192.168.1.0 is directly connected, Loopback0
R1# show ip route 192.168.1.0 255.255.255.252
Routing entry for 192.168.1.0/30
Known via "connected", distance 0, metric 0 (connected, via interface)
Routing Descriptor Blocks:
* directly connected, via Loopback0
Route metric is 0, traffic share count is 1
Using show ip route with network addresses
Notes: Care must be taken when using the show ip route command with network addresses.
Ideally, both the network address and the network mask should be specified in the command.
If the netmask argument is omitted, the behavior of the command is more complicated. The command always tries to display the longest-prefix-matching routing table entry. However, that means that if there are several networks with the same address but different netmasks present in the routing table, the command will display details only about a single entry that matches the original address argument in the longest prefix length. In addition, if the address argument is by itself a major network address (i.e. a valid classful address) then the command will search the routing table only for classful network and supernets of the given network having the same address.
  This behavior may result in displaying the parent route instead of a child route, as indicated in the example.
For these reasons, when using the show ip route command with a network address, it is highly recommended to specify the network using both its address and network mask to avoid the unintuitive behavior of the show ip route command.
<number>

## Slide 6: Collecting and Filtering Information Using IOS show Commands – Cont.
R1# show processes cpu | include IP Input
71 3149172 7922812 397 0.24% 0.15% 0.05% 0 IP Input
S1# show ip interface brief | exclude unassigned
Interface IP-Address OK? Method Status Protocol
Vlan128 10.1.156.1 YES NVRAM up up
S1# show running-config | begin line vty
line vty 0 4
transport input telnet ssh
line vty 5 15
transport input telnet ssh
!
End
R1# show processes cpu| include IP Input
^
% Invalid input detected at '^' marker.
Using pipes with include, exclude and begin
Notes: A more generic way of filtering is to use the a pipe operator “|” with Cisco IOS show commands, followed by one of the keywords include, exclude, or begin, and then a regular expression. Regular expressions are patterns that can be used to match strings in a piece of text. The pattern to be matched is case sensitive.
The first example shows only the IP Input CPU process for R1.
The second example shows only switch S1 interfaces that have an IP addressed assigned.
The third example shows the running config for switch S1 beginning with the first output line that contains the character string “line vty”.
The fourth example illustrates that, when using the pipe operator, there must always be at least one space preceding and following it, otherwise it will not be accepted by the IOS CLI.
<number>

## Slide 7: Collecting and Filtering Information Using IOS show Commands – Cont.
R1# show running-config | section router eigrp
router eigrp 1
network 10.1.192.2 0.0.0.0
network 10.1.192.10 0.0.0.0
network 10.1.193.1 0.0.0.0
no auto-summary
R1# show processes cpu | include ^CPU|IP Input
CPU utilization for five seconds: 1%/0%; one minute: 1%; five minutes: 1%
71 3149424 7923898 397 0.24% 0.04% 0.00% 0 IP Input
Using pipes with section and ^
Notes: Cisco IOS Software Release (12.3(2)T) introduced the section option, to display a specific section of lines from the configuration that matches a particular regular expression and any following associated lines.
In the first example, the command show running-config | section router eigrp displays the EIGRP configuration section only. Using section router without the eigrp keyword will display all router sections configured (EIGRP, RIP, OSPF, etc.) .
In the second example, the show processes cpu | include ^CPU|IP Input, the ^CPU only matches lines that start with the characters “CPU”. Lines that do not start with the "CPU" characters do not match the ^CPU regular expression, even if they actually contain the string "CPU" somewhere else.
The same line uses the pipe operator “|” as part of a regular expression to signify a logical “OR” to also include lines that contain the string “IP Input”.
<number>

## Slide 8: Collecting and Filtering Information Using IOS show Commands – Cont.
R1# show tech-support | redirect tftp://192.168.37.2/show-tech.txt
R1# show ip interface brief | tee flash:show-int-brief.txt
Interface IP-Address OK? Method Status Protocol
FastEthernet0/0 10.1.192.2 YES manual up up
FastEthernet0/1 10.1.192.10 YES manual up up
Loopback0 10.1.220.1 YES manual up up
R1# dir flash:
Directory of flash:/
1 -rw- 23361156 Mar 2 2009 16:25:54 -08:00 c1841-advipservicesk9mz.1243.bin
2 -rw- 680 Mar 7 2010 02:16:56 -08:00 show-int-brief.txt
Using the redirect and tee options
Notes: In the first example, the output from the show tech-support command, which is normally very lengthy, is redirected to a TFTP server with IP address 192.168.37.2 and at the same time the file is named show-tech.txt. If the redirect option is used multiple times with the same file name, it overwrites the previous file. The redirect option does not display the output on the console.
In the second example, the tee option displays the output on the console, and sends it to a file named show-int-brief.txt. This file is listed in the output of the dir flash: command.
<number>

## Slide 9: Collecting and Filtering Information Using IOS show Commands – Cont.
R1# show version | append flash:show-commands.txt
R1# show ip interface brief | append flash:show-commands.txt
R1# more flash:show-commands.txt
Cisco IOS Software, 1841 Software (C1841-ADVIPSERVICESK9-M), Version 12.4(23), RELEASE SOFTWARE (fc1)
Technical Support: http://www.cisco.com/techsupport
Copyright (c) 1986-2008 by Cisco Systems, Inc.
Compiled Sat 08-Nov-08 20:07 by prod_rel_team
ROM: System Bootstrap, Version 12.3(8r)T9, RELEASE SOFTWARE (fc1)
R1 uptime is 3 days, 1 hour, 22 minutes
< output omitted >
Interface IP-Address OK? Method Status Protocol
FastEthernet0/0 10.1.192.2 YES manual up up
FastEthernet0/1 10.1.192.10 YES manual up up
Using the append option and the more command
Notes: The append option is similar to the redirect option, but it allows you to append the output to a file instead of replacing that file.
The use of this command option makes it easy to collect the output of several show commands in a text file.
A prerequisite for this option is that the file system that you are writing to must support “append” operations, so for instance, a TFTP server cannot be used in this case.
In this example, the content of the file is displayed using the more command.
<number>

## Slide 10: Collecting and Filtering Information Using IOS show Commands – Cont.
Parameter | Description
repeat repeat-count | Number of ping packets that are sent to the destination address. The default is 5.
size datagram-size | Size of the ping packet (in bytes). Default: 100 bytes.
source [address ¦ interface] | The interface or IP address of the router to use as a source address for the probes.
df-bit | Enables the "do-not-fragment" bit in the IP header.
ping ip-address | hostname [repeat repeat-count size datagram-size source [address | interface] df-bit]
Router#
Notes: repeat repeat-count: The Cisco IOS ping by default sends out five ICMP echo request packets. The repeat option allows you to specify how many echo-request packets are sent. This is useful when you are troubleshooting a packet loss situation. For example, if you see a pattern where every other packet is lost, resulting in 50 percent packet loss, you might have a load balancing situation with packet loss on one path.
size datagram-size: This option allows you to specify the total size of the ping packet (including headers) in bytes that will be sent. In combination with the repeat option, you can send a steady stream of large packets and generate some load, as with a large repeat count, a size set to 1500 bytes, and the timeout option set to 0 seconds. When used with the don’t fragment (df-bit) option, the size option allows you to determine the maximum transmission unit (MTU) along the path to a particular destination IP address.
source [address | interface]: This option allows you to set the source IP address or interface of the ping packet. The IP address has to be one of the local device’s own IP addresses. If this option is not used, the router will select the IP address of the egress interface as the source of the ping packets
df-bit: This option sets the Don’t-Fragment bit in the IP header to indicate that routers should not fragment this packet. If it is larger than the MTU of the outbound interface, the router should drop the packet and send an ICMP Fragmentation needed and DF bit set message back to the source. This option can be very useful when you are troubleshooting MTU related problems.
<number>

## Slide 11: Testing Network Connectivity Using Cisco IOS Commands – Cont.
R1# ping 10.1.156.1
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 10.1.156.1, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 1/2/4 ms
R1# ping 10.1.156.1 source FastEthernet 0/0
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 10.1.156.1, timeout is 2 seconds:
Packet sent with a source address of 10.1.192.2
.....
Success rate is 0 percent (0/5)
Using the ping extended option: source
Notes: The first example is a standard ping, where the IP address of the egress interface is used as the source address.
The second example is an extended ping, where the IP address of interface Fa0/0 is used as the source address. The actual ip address can be substituted for the interface designation.
The failure of the second ping suggests that the destination 10.1.156.1 or some router(s) along the path towards it are unable to route ICMP echo-reply packets back to the source IP address 10.1.192.2
<number>

## Slide 12: Testing Network Connectivity Using Cisco IOS Commands – Cont.
R1# ping 10.1.221.1 size 1476 df-bit
Type escape sequence to abort.
Sending 5, 1476-byte ICMP Echos to 10.1.221.1, timeout is 2 seconds:
Packet sent with the DF bit set
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 184/189/193 ms
R1# ping 10.1.221.1 size 1477 df-bit
Type escape sequence to abort.
Sending 5, 1477-byte ICMP Echos to 10.1.221.1, timeout is 2 seconds:
Packet sent with the DF bit set
M.M.M
Success rate is 0 percent (0/5)
Using the ping extended option: df-bit
Notes: The example shows successful ping results when packet size of 1476 bytes is used, however, ping packets with a size of 1477 bytes are not successful.
The ‘M’ in the output of the ping command signifies that an ICMP Fragmentation needed and DF bit set message was received.
From this, you can conclude that somewhere along the path to the destination there must be a host that has an MTU of 1476 bytes.
A possible explanation for this could be usage of a Generic Routing Encapsulation (GRE) tunnel, which typically has an MTU of 1476 bytes (1500 bytes default MTU minus 24 bytes for the GRE and IP headers).
<number>

## Slide 13: Testing Network Connectivity Using Cisco IOS Commands – Cont.
Explanation of ping results characters
! Each exclamation point indicates receipt of a reply.
. Each period indicates a timeout waiting for a reply.
U A destination unreachable ICMP message was received.
Q Source quench (destination too busy).
M Could not fragment (MTU related).
? Unknown packet type.
& Packet lifetime exceeded
Notes: <number>
Note: The Source Quench message is possible but improbable to see in today's networks. The ICMP Source Quench message has not been widely supported. The IOS 12.4T Command Reference to the ping command does not mention the 'Q' result code.

## Slide 14: Testing Network Connectivity Using Cisco IOS Commands – Cont.
R1# ping
Protocol [ip]:
Target IP address: 10.1.221.1
Repeat count [5]: 1
Datagram size [100]:
Timeout in seconds [2]:
Extended commands [n]: y
Source address or interface:
Type of service [0]:
Set DF bit in IP header? [no]: yes
Validate reply data? [no]:
Data pattern [0xABCD]:
Loose, Strict, Record, Timestamp, Verbose[none]:
Sweep range of sizes [n]: y
Sweep min size [36]: 1400
Sweep max size [18024]: 1500
Sweep interval [1]:
Type escape sequence to abort.
Sending 101, [1400..1500]-byte ICMP Echos to 10.1.221.1, timeout is 2 seconds:
<output omitted>
Using the ping extended prompt mode
Notes: This example shows using the extended ping prompted mode to set a sweep range ping packet sizes.
You must be in privileged EXEC mode to use extended ping prompted mode.
<number>

## Slide 15: Diagnosing Hardware Issues Using Cisco IOS Commands – Cont.
R1# show interfaces FastEthernet 0/0
FastEthernet0/0 is up, line protocol is up
<output omitted>
Last input 00:00:00, output 00:00:01, output hang never
Last clearing of "show interface" counters never
Input queue: 0/75/1120/0 (size/max/drops/flushes); Total output drops: 0
Queueing strategy: fifo
Output queue: 0/40 (size/max)
5 minute input rate 2000 bits/sec, 3 packets/sec
5 minute output rate 0 bits/sec, 1 packets/sec
110834589 packets input, 1698341767 bytes
Received 61734527 broadcasts, 0 runts, 0 giants, 565 throttles
30 input errors, 5 CRC, 1 frame, 0 overrun, 25 ignored
0 watchdog
0 input packets with dribble condition detected
35616938 packets output, 526385834 bytes, 0 underruns
0 output errors, 0 collisions, 1 interface resets
0 babbles, 0 late collision, 0 deferred
0 lost carrier, 0 no carrier
0 output buffer failures, 0 output buffers swapped out
Checking interfaces with the show interfaces command
Notes: The output of this command lists a number of key statistics:
Input queue drops: Input queue drops signify that at some point more traffic was delivered to the router than it could process. This may not indicate a problem, as it could be normal during traffic peaks. It could be an indication that the CPU is not able to process packets in time.
Output queue drops: Seeing output drops is normal when the aggregate input traffic rate is higher than the output traffic rate on an interface. However, even if this is considered normal behavior, it leads to packet drops and queuing delays. Applications that are sensitive to delay and packet loss, such as voice over IP, will have serious quality issues in those situations. This counter is a good indicator that you need to implement a congestion management mechanism to provide good quality of service (QoS) to your applications.
Input errors: This counter indicates the number of errors such as cyclic redundancy check (CRC) errors, experienced during reception of frames. High numbers of CRC errors could indicate cabling problems, interface hardware problems, or in an Ethernet based network, duplex mismatches.
Output errors: This counter indicates the number of errors such as collisions, during transmission of frames. In most Ethernet-based networks today, full-duplex transmission is the norm and half-duplex is the exception. In full-duplex operation collisions cannot occur, therefore collisions, and especially late collisions, often indicate duplex mismatches.
<number>

## Slide 16: Diagnosing Hardware Issues Using Cisco IOS Commands – Cont.
Additional hardware commands and tools:
show controllers
show platform
show inventory
show diag
Generic Online Diagnostics (GOLD)
Time Domain Reflectometer
Notes: <number>

## Slide 17
Using Specialized Maintenance and Troubleshooting Tools
Notes: <number>

## Slide 18: Using Traffic Capturing Tools
Sample screen shot from a protocol analyzer
Notes: In the sample screen from the Wireshark protocol analyzer (also referred to as a packet sniffer), the first four packets shown on the screen are the 4-way DHCP exchange resulting in an IP address lease from a DHCP server to a DHCP client. The next three packets are gratuitous ARPs from an IP device.
<number>

## Slide 19: Using Traffic Capturing Tools – Cont.
Switched Port Analyzer (SPAN)
Notes: The figure shows a switch that is configured to send traffic from the source interface Fa0/7 to the destination interface Fa0/8 using the SPAN feature. The objective is to capture all the traffic sent or received by the server connected to interface Fa0/7, in order to troubleshoot a problem with that server. A packet sniffer is connected to interface Fa0/8. The switch is instructed to copy all the traffic that it sends and receives on interface Fa0/7 to interface Fa0/8. This is done using the monitor session session# commands shown on the top of the Figure.
The configuration of the SPAN session is verified using the show monitor command. The output of this command shows that both incoming and outgoing traffic are sent from Fa0/7 to Fa0/8. Also, the frame type of native indicates Ethernet frames rather than 802.1Q frames. The last line indicating ingress as disabled, means that on the destination interface Fa0/8 (where the sniffer is connected), ingress traffic is not accepted as per the current configuration.
<number>

## Slide 20: Using Traffic Capturing Tools – Cont.
Remote Switched Port Analyzer (RSPAN)
Notes: In the figure, special purpose SPAN VLAN number 100 is created the remote-span command within the VLAN configuration mode and this VLAN needs to be defined on all switches and allowed on all the trunks within the path between the source and destination switches.
On the source switch, the RSPAN VLAN is configured as the destination for the SPAN session through use of the monitor session session# destination remote vlan vlan# command and in a similar way the destination switch is configured to use the RSPAN VLAN as the source of the SPAN session through use of the monitor session session# source remote vlan vlan# command.
<number>

## Slide 21: Using Traffic Capturing Tools – Cont.
Remote Switched Port Analyzer (RSPAN) – Cont.
Notes: The show monitor command is used to verify the configuration of RSPAN on the source and destination switches.
Notice that on the source switch (SW1) the session is identified as a Remote Source Session, while on the destination switch (SW2) it is marked as a Remote Destination Session.
<number>

## Slide 22: Gathering Information with SNMP
A Simple SNMP Configuration Example
Notes: In the example shown, the read-only community string is set to cisco and the read-write community is set to san-fran.
The location is set to “TSHOOT Lab Facility”, the contact is set to support@mgmt.tshoot.local, and ifindex is set to persistent.
<number>

## Slide 23: Gathering Information with NetFlow
A Simple NetFlow Configuration Example
Notes: To export NetFlow information to a collector, you must first enable NetFlow accounting (collection) on the desired router interfaces. This is done using the ip flow ingress interface configuration mode IOS command.
The figure shows a router with its Fa0/0 and Fa0/1 interfaces enabled to collect NetFlow information for ingress traffic.
The definition of a flow is unidirectional, so if you want to account for both inbound and outbound traffic, the feature needs to be turned on for both interfaces.
The Cisco IOS router command ip flow ingress replaces the old ip route-cache flow command.
The NetFlow information is exported to a collector with the IP address 10.1.152.1 (at UDP port 9996), the packet format version is 5, and interface loopback 0’s IP address is used as the source of the outgoing IP packet.
<number>

## Slide 24: Enabling Network Event Notification – SNMP
Enabling SNMP trap notification
Notes: The figure shows a router configured with the commands that enable SNMP trap notification.
In the first step one or more trap receivers are defined and in the second step sending traps is enabled.
By default, Cisco routers send SNMP version 1 traps. Version 2c is configured here.
To enable a router to send specific traps, each trap must be specified.
All trap types can be enabled with the single snmp-server enable traps command (does not appear in the configuration, because it executes a macro that enables all available categories of traps.)
The output of the show running-config | include traps command shows traps enabled.
SNMP and syslog both act on predefined triggers and send predefined messages. Both protocols allow for a limited amount of filtering, but it is not possible to define entirely new event triggers or messages.
<number>

## Slide 25
Notes: <number>