## Slide 1: Chapter 4: Maintaining and Troubleshooting Campus Switched Solutions
CCNP TSHOOT: Maintaining and Troubleshooting IP Networks
Notes: <number>
Cisco Networking Academy Program
CCNP TSHOOT: Maintaining and Troubleshooting IP Networks
Chapter 4: Maintaining and Troubleshooting Campus Switched Solutions

## Slide 2: Topics
Troubleshooting VLANs
  LAN Switching Process
Troubleshooting Spanning Tree
  Etherchannel Operations
Troubleshooting Switched Virtual Interfaces and Inter-VLAN Routing
Troubleshooting First-Hop Redundancy Protocols
<number>

## Slide 3: Troubleshooting VLANs
<number>

## Slide 4: LAN Switch Operation
A good understanding of the processes involved in Layer 2 switching is essential to any engineer that is involved in network troubleshooting.
Many times we try to memorize situations instead of understanding and analyzing network operations.
To focus just on Layer 2 switching, assume that the two hosts reside on a common subnet (VLAN).
Host A pings Host B
<number>

## Slide 5
Host A Needs to determine if 10.1.1.2 is on its subnet or another subnet.
How does Host A knows its own network address?
  IP Address AND Subnet Mask
How does Host A know Host B’s network address?
  Host B’s IP Address AND Host A’s Subnet Mask
Why does Host A use it’s own Subnet Mask and not that of Host B?
  Does not know Host B’s Subnet Mask
  If Host B is in same subnet as Host A they will have the same mask
Host A compares the network address from both AND operations
  Same network address: Need MAC Address of 10.1.1.2
  Different network addresses: Need MAC Address of Default Gateway
<number>

## Slide 6: LAN Switch Operation
Host A and Host B are on the same subnet
Host A will examine its Address Resolution Protocol (ARP) cache to find the MAC address of Host B.
  If there is an entry for 10.1.1.2 and its MAC Address:
    No ARP process needed
    Encapsulate the IP packet in an Ethernet frame with Destination MAC address of Host B
<number>

## Slide 7
If Host A does not have an ARP cache entry for 10.1.1.2:
  Sends out ARP Request (broadcast)
  ARP Request: Contains IP address of 10.1.1.2 but no MAC Address
Switch C:
  Learns
    Checks the VLAN of the incoming port (VLAN 10)
    Records (or resets 5 minute timer) for Source MAC address and Port Number
<number>

## Slide 8
Switch C:
  Forward
    The MAC address table never contains an entry for the broadcast MAC address (FFFF:FFFF:FFFF).
    Switch C will flood the frame on all ports:
      All access ports in that VLAN (VLAN 10)
      All trunks that this VLAN is allowed, active, and not pruned on
      Except the port it came in from
Switches D and E repeat this process as they receive the frame
<number>

## Slide 9
Host B receives the ARP request:
  Records the Host A’s IP address and MAC address in its own ARP cache
  Sends an ARP Reply (unicast) back to Host A
<number>

## Slide 10
Because all switches now have an entry in their MAC address table for the MAC address of Host A they will:
  Learns
    Record Host B’s MAC address and corresponding interface and VLAN in their MAC address table (if they did not already have that entry)
  Forwards
    Forward the frame containing the ARP reply on the path to Host A only
    No flooding
<number>

## Slide 11
Host A receives the ARP reply:
  Records the IP and MAC address of Host B in its ARP cache
  Now it is ready to send the original IP packet.
Host A encapsulates the IP packet (ICMP echo request) in a unicast frame destined for Host B and sends it out.
  Note that the Ethernet type field of 0x0800 (IP packet)
The switches examine their MAC address tables:
  Learn: Resets 5 minute timer Host A’s source MAC address
  Forward: Finds Host B’s MAC address and forward it towards Host B (no flooding)
<number>

## Slide 12
Host B receives the packet
  Responds to Host A (sends an ICMP echo reply packet)
The switches examine their MAC address tables:
  Learn: Resets 5 minute timer Host B’s source MAC address
  Forward: Finds Host A’s MAC address and forward it towards Host A (no flooding)
<number>

## Slide 13
Host A receives the packet
  Ping program displays output
  The end.
Question: If everything works as shown why might this first ping fail?
  Sometimes the very first ICMP echo request times out due to the requirement for an ARP Request
Although this process might seem trivial, listing the steps clearly shows that even for the simplest communication, an elaborate chain of events take place.
If at any point this chain is broken due to faulty cabling, failing devices, or misconfiguration, the communication will fail.
Important to leverage your knowledge of these processes to diagnose and solve problems in a switched environment.
<number>

## Slide 14
Firewall (host or switch)
Physical problems
Bad, missing, or miswired cables
Bad ports
Power failure
Device problems
Software bugs
Performance problems
Misconfiguration
Missing or wrong VLANs
Misconfigured VTP settings
Wrong VLAN setting on access ports
Missing or misconfigured trunks
Native VLAN mismatch
VLANs not allowed on trunk
<number>
Some possible issues that could cause the communication to fail

## Slide 15: Verifying Layer 2 Forwarding
A common method to troubleshoot Layer 2 switching problems is to follow the path of the frames through the switches.
  Takes time and effort
Objective: To confirm that frames have passed through the switches and to verify how each switch made its forwarding decisions.
  Find the point where the trail stops.
  Possible to start at the endpoints.
<number>

## Slide 16
MAC Address Table – key data structure
Find the entry for a particular MAC address in this table it proves:
  Proves within the last five minutes this switch received frames from that source
But nothing about a particular frame.
Useful command:
  clear mac-address-table - Verify that the MAC address is learned again when you reinitiate the connection
<number>

## Slide 17
Many possible findings and conclusions :
  Frames are not received on the correct VLAN:
    Possible VLAN or trunk misconfiguration.
  Frames are received on a different port than you expected:
    Possible physical problem, spanning tree issues or duplicate MAC addresses.
  The MAC address is not registered in the MAC address table:
    Most likely problem is upstream from this switch.
<number>

## Slide 18
show vlan:
  Verifies VLAN existence and port-to-VLAN associations.
  Lists all VLANS that were created on the switch (either manually or through the VLAN Trunking Protocol [VTP]).
  Note: Trunks are not listed because they do not belong to any VLAN, in particular.
<number>

## Slide 19
show interfaces trunk:
Displays all interfaces that are configured as trunks.
Displays for each trunk which VLANs are allowed and what the native VLAN is.
<number>

## Slide 20
traceroute mac:
You specify a source and destination MAC address
Shows a list of switch hops that a frame from that source MAC address to that destination MAC address.
Discovers the Layer 2.
This command requires that Cisco Discovery Protocol (CDP) is enabled on all the switches in the network (or at least within the path).
<number>

## Slide 21
Troubleshooting Spanning Tree

## Slide 22: L2 Loops
<number>
Switch (Bridge) loops can occur any time there is a redundant path or loop in the bridge network.
The switches will flip flop the MAC address table entries (creating extremely high CPU utilization).
Unicasts, unknown unicasts and broadcasts are all problems.
Notes: <number>

## Slide 23: Two-key STP Concepts
<number>
STP calculations make extensive use of two key concepts in creating a loop-free topology:
  Bridge ID
  Path Cost
Link Speed | Cost (Revised IEEE Spec) | Cost (Previous IEEE Spec)
10 Gbps | 2 | 1
1 Gbps | 4 | 1
100 Mbps | 19 | 10
10 Mbps | 100 | 100
Notes: <number>

## Slide 24: Five-Step STP Decision Sequence
<number>
When creating a loop-free topology, STP always uses the same five-step decision sequence:
Five-Step decision Sequence
Step 1 - Lowest BID
Step 2 - Lowest Path Cost to Root Bridge
Step 3 - Lowest Sender BID
Step 4 – Lowest Port Priority
Step 5 - Lowest Port ID
Bridges use Configuration BPDUs during this five-step process.
We will assume all BPDUs are configuration BPDUs
Notes: <number>

## Slide 25: Elect one Root Bridge Lowest BID wins!
<number>
Who wins?
Notes: <number>

## Slide 26: Elect one Root Bridge Lowest BID wins!
<number>
Who wins?
My BID is 32768.0001.C945.A573
My BID is 32768.0005.5E0D.9315
My BID is 32768.0060.47B0.5850
My BID is 32768.0003.E461.46EC
My BID is 32768.0001.964E.7EBB
I win!
Root Bridge
Notes: <number>

## Slide 27: Elect Root Ports
<number>
STP Convergence Step 1 Elect one Root Bridge Step 2 Elect Root Ports Step 3 Elect Designated Ports
Next, each switch determines its Root Port:
  It’s port closest to the Root Bridge
Bridges use the cost to determine closeness.
Every non-Root Bridge will select one Root Port!
Specifically, bridges track the Root Path Cost, the cumulative cost of all links to the Root Bridge.
I will select one Root Port that is closest, best path to the root bridge.
Notes: <number>

## Slide 28
<number>
Root Bridge, Access2 sends out BPDUs, containing a Root Path Cost of 0.
Switches receive these BPDUs and adds the Path Cost of the FastEthernet interface to the Root Path Cost contained in the BPDU.
This value is used internally and used in BPDUs to other switches.
Root Bridge
BPDU
Cost=0
BPDU
Cost=0+19=19
BPDU
Cost=0+19=19
BPDU
Cost=0+19=19
0
0
0
19
19
19
Path Cost
Notes: <number>

## Slide 29
<number>
Switches now send BPDUs with their Root Path Cost out other interfaces.
Switches receive BPDU and add their path cost.
Root Bridge
BPDU
Cost=4+19=23
BPDU
Cost=4+19=23
19
19
0
0
0
19
BPDU
Cost=19
BPDU
Cost=19
Path Cost
Notes: <number>

## Slide 30
<number>
Root Bridge
BPDU
Cost=4+19=23
BPDU
Cost=4+19=23
19
19
0
0
0
19
BPDU
Cost=19
BPDU
Cost=19
This process continues…
Notes: <number>

## Slide 31
<number>
This process continues…
Root Bridge
19
19
19
23
23
BPDU
Cost=4+19=23
0
0
0
BPDU
Cost=4+19=23
BPDU
Cost=19
BPDU
Cost=19+19=38
19
Path Cost
Notes: <number>

## Slide 32
<number>
Final Results
Ports show BPDU Received Root Path Cost + Path Cost = Root Path Cost of Interface, after the “best” BPDU is received on that port from the neighboring switch.
This is the cost of reaching the Root Bridge from this interface towards the neighboring switch.
Now let’s see how this is used!
Root Bridge
19
19
0
0
0
19+4=23
23+4=27
19+19=38
19+4=23
19+4=23
19+4=23
19+4=23
19+4=23
19
23+4=27
19+19=38
Path Cost
Notes: <number>

## Slide 33
<number>
Next:
Elect Root Ports
Elect Designated Ports
Non-Designated Ports: All other ports
Elect Root Ports
Every non-Root bridge must select one Root Port.
A bridge’s Root Port is the port closest to the Root Bridge.
Bridges use the cost to determine closeness.
Root Bridge
19
19
0
0
0
23
27
38
23
23
23
23
23
19
27
38
Path Cost
These values would be the Root Path Cost if this interface was used to reach the Root Bridge.
Notes: <number>

## Slide 34
<number>
Elect Root Ports: (Review)
Ports show Root Path Cost of Interface, after the “best” BPDU is received on that port from the neighboring switch.
This is the cost of reaching the Root Bridge from this interface towards the neighboring switch.
Distribution 1 “thought process”
If I go through Core it costs 27.
If I go through D2 it costs 38.
If I go through A1 it costs 23.
If I go through A2 it costs 19. This is the best path to the Root!
Path Cost
Notes: <number>

## Slide 35
<number>
Elect Root Ports
Every non-Root bridge must select one Root Port.
A bridge’s Root Port is the port closest to the Root Bridge.
Bridges use the Root Path Cost to determine closeness.
Root Bridge
19
19
0
0
0
23
27
38
23
23
23
23
23
19
27
38
?
?
RP
RP
RP
Notes: <number>

## Slide 36
<number>
Elect Root Ports
Core switch has two equal Root Path Costs to the Root Bridge.
Five-step decision process.
Dist 1 switch has a lower Sender BID than Dist 2.
Core chooses the Root Port of G 0/1.
Five-Step decision Sequence
Step 1 - Lowest BID
Step 2 - Lowest Path Cost to Root Bridge
Step 3 - Lowest Sender BID
Step 4 - Lowest Port Priority
Step 5 - Lowest Port ID
Root Bridge
19
19
0
0
0
23
27
38
23
23
23
23
23
19
27
38
?
?
Lower BID
My BID is 32768.0005.5E0D.9315
My BID is 32768.0060.47B0.5850
RP
RP
RP
RP
Notes: <number>

## Slide 37: Elect Designated Ports
<number>
STP Convergence Step 1 Elect one Root Bridge Step 2 Elect Root Ports Step 3 Elect Designated Ports
A Designated Port functions as the single bridge port that both sends and receives traffic to and from that segment and the Root Bridge.
Each segment in a bridged network has one Designated Port, chosen based on cumulative Root Path Cost to the Root Bridge.
The switch containing the Designated Port is referred to as the Designated Bridge for that segment.
To locate Designated Ports, lets take a look at each segment.
Segment’s perspective: From a device on this segment, “Which switch should I go through to reach the Root Bridge?”
Notes: <number>

## Slide 38
<number>
A Designated Port is elected for every segment.
Segment’s perspective: From a device on this segment, “Which switch should I go through to reach the Root Bridge?”
“I’ll decide using the advertised Root Path Cost from each switch!”
Root Bridge
19
19
0
0
0
23
19
19
23
19
19
19
19
19
19
19
RP
RP
RP
RP
?
?
?
?
?
?
?
?
Notes: <number>

## Slide 39
<number>
Because Access 2 has the lower Root Path Cost it becomes the Designated Port for that segment.
Root Bridge
19
19
0
0
0
23
19
19
23
19
19
19
19
19
19
19
RP
RP
RP
RP
?
What is my best path to the Root Bridge, 19 via Access 1 or 0 via Access 2?
My designated port will be 0 via Access 2 (Fa0/5). It’s the best path, lowest Root Path, to the Root Bridge.
DP
Notes: <number>

## Slide 40
<number>
Because Access 2 has the lower Root Path Cost it becomes the Designated Port for those segments.
Root Bridge
19
19
0
0
0
23
19
19
23
19
19
19
19
19
19
19
RP
RP
RP
RP
DP
?
DP
?
DP
Notes: <number>

## Slide 41
<number>
Segment between Distribution 1 and Access 1 has two equal Root Path Costs of 19.
Using the Lowest Sender ID (first two steps are equal), Access 1 becomes the best path and the Designated Port.
Five-Step decision Sequence
Step 1 - Lowest BID
Step 2 - Lowest Path Cost to Root Bridge
Step 3 - Lowest Sender BID
Step 4 - Lowest Port Priority
Step 5 - Lowest Port ID
Root Bridge
19
19
0
0
0
23
19
19
23
19
19
19
19
19
19
19
RP
RP
RP
RP
DP
DP
DP
What is my best path to the Root Bridge, 19 via Distribution 1 or 19 via Access 1? They are the same! Who has the lowest BID?
?
32768.0005.5E0D.9315
32768.0003.E461.46EC
DP
Lower BID
Notes: <number>

## Slide 42
<number>
After this process is finished…
All other ports, those ports that are not Root Ports or Designated Ports, become Non-Designated Ports.
Non-Designated Ports are put in blocking mode.
This is the loop prevention part of STP.
Root Bridge
19
19
0
0
0
23
19
19
23
19
19
19
19
19
19
19
RP
RP
RP
RP
DP
DP
DP
DP
DP
DP
NDP
X
NDP
X
DP
NDP
X
NDP
X
Notes: <number>

## Slide 43: show spanning-tree
<number>
Core# show spanning-tree
VLAN0001
Spanning tree enabled protocol ieee
Root ID Priority 32769
Address 0001.964E.7EBB
Cost 4
Port 25(GigabitEthernet0/1)
Hello Time 2 sec Max Age 20 sec Forward Delay 15 sec
Bridge ID Priority 32769 (priority 32768 sys-id-ext 1)
Address 0001.C945.A573
Hello Time 2 sec Max Age 20 sec Forward Delay 15 sec
Aging Time 20
Interface Role Sts Cost Prio.Nbr Type
---------------- ---- --- --------- -------- --------------------------------
Gi0/1 Root FWD 4 128.25 P2p
Gi0/2 Altn BLK 4 128.26 P2p
Path Cost
Notes: <number>

## Slide 44: show spanning-tree detail
<number>
Core# show spanning-tree detail
VLAN0001 is executing the ieee compatible Spanning Tree Protocol
Bridge Identifier has priority of 32768, sysid 1, 0001.C945.A573
Configured hello time 2, max age 20, forward delay 15
Current root has priority 32769
Root port is 25 (GigabitEthernet0/1), cost of root path is 4
Topology change flag not set, detected flag not set
Number of topology changes 0 last change occurred 00:00:00 ago
from FastEthernet0/1
Times: hold 1, topology change 35, notification 2
hello 2, max age 20, forward delay 15
Timers: hello 0, topology change 0, notification 0, aging 300
Path Cost
Notes: <number>

## Slide 45: STP Convergence: Summary
<number>
Recall that switches go through three steps for their initial convergence:
STP Convergence Step 1 Elect one Root Bridge Step 2 Elect Root Ports Step 3 Elect Designated Ports
Also, all STP decisions are based on a the following predetermined sequence:
Five-Step decision Sequence
Step 1 - Lowest BID
Step 2 - Lowest Path Cost to Root Bridge
Step 3 - Lowest Sender BID
Step 4 – Lowest Port Priority
Step 5 - Lowest Port ID
Notes: <number>

## Slide 46: Example 2- Spanning Tree Operation
Elect a Root Bridge/Switch.
Select a Root Port on each Bridge/Switch (except on the Root bridge/switch).
Elect a Designated device/port on each network segment.
Ports that are neither Root Port nor a Designated Port go into Blocking state.
Notes: Refer to next 4 slides for additional detail on the process.
<number>

## Slide 47: Example 2- Spanning Tree Operation – Cont.
1. Elect a Root Bridge/Switch.
Notes: 1. Elect a Root Bridge/Switch - This is based on the lowest Bridge-ID (Bridge-ID is comprised of bridge/switch priority and lowest MAC address).
<number>

## Slide 48: Example 2- Spanning Tree Operation – Cont.
2. Select a Root Port on each bridge/switch.
Notes: 2. Select a Root Port on each Bridge/Switch (except on the Root bridge/switch). This is based on the least cost to Root. Ties are broken based on the lowest upstream Bridge-ID. Further ties are broken based on the lowest Port-ID.
Note: A commonly misunderstood detail is that when using the upstream Bridge ID (BID) and Port ID (PID) to break ties when selecting a Root Port, it is the sender's BID and PID that are used to break the ties, not the receiver's.
<number>

## Slide 49: Spanning Tree Operation – Cont.
3. Elect a Designated device/port on each network segment.
Notes: 3. Elect a Designated device/port on each network segment.
This is based on the least cost to Root. Ties are broken based on the lowest Bridge-ID. Further ties are broken based on the lowest Port-ID.
<number>

## Slide 50: Spanning Tree Operation – Cont.
4. Place ports in Blocking state.
Notes: 4. Ports that ended up as neither a Root Port nor a Designated Port go into Blocking state, and the Root Ports and Designated Ports go over Listening and Learning states, finally entering the Forwarding state.
<number>

## Slide 51: Spanning Tree Operation – Cont.
Sample output from the show spanning-tree vlan command.
Notes: show spanning-tree [vlan vlan-id]: This command, without specifying any additional options, is useful if you want a quick overview of the status of the Spanning Tree Protocol for all VLANs that are defined on a switch. If you are interested in only a particular VLAN, you can limit the scope of this command by specifying the VLAN number as an option. The figure shows sample output from this command.
<number>

## Slide 52: Spanning Tree Operation – Cont.
Sample output from the show spanning-tree interface command.
Notes: In the example, port 88 (TenGigabitEthernet9/1) is a root port and the upstream switch’s port is the Designated Port. This is also reflected by the fact that this switch is receiving BPDUs (it received 670 BPDUs), but not transmitting them (it sent 10 BPDUs during initial spanning tree convergence and stopped after that).
You can also see that the upstream switch is the Root Bridge. This can be concluded from the fact that the Designated Bridge ID and the Root Bridge ID are the same. This is further confirmed by the fact that the designated path cost is reported as a cost of 0.
<number>

## Slide 53: Spanning Tree Failures
STP is a reliable but not an absolutely failproof protocol.
If STP fails there are usually major negative consequences.
With Spanning Tree, there are two different types of failures.
  Type 1 - STP may erroneously block certain ports that should have gone to the forwarding state. You may lose connectivity to certain parts of the network, but the rest of the network is unaffected.
  Type 2 - STP erroneously moves one or more ports to the Forwarding state. The failure is more disruptive as bridging loops and broadcast storms can occur.

## Slide 54: Spanning Tree Failures – Cont.
Type 2 failures can cause these symptoms.
  The load on all links in the switched LAN will quickly start increasing.
  Layer 3 switches and routers report control plane failures such as continual HSRP, OSPF and EIGRP state changes or that they are running at a very high CPU utilization load.
  Switches will experience very frequent MAC address table changes.
  With high link loads and CPU utilization devices typically become unreachable, making it difficult to diagnose the problem while it is in progress.
Eliminate topological loops and troubleshoot issues.
  Physically disconnect links or shut down interfaces.
  Diagnose potential problems.
  A unidirectional link can cause STP problems. You may be able to identify and remove a faulty cable to correct the problem.
Notes: <number>

## Slide 55: Spanning Tree Failures – Cont.
DSW2# show etherchannel 1 detail
Group state = L2
Ports: 2 Maxports = 8
Port-channels: 1 Max Port-channels = 1
Protocol: -
Minimum Links: 0
Ports in the group:
-------------------
Port: Fa0/5
------------
Port state = Up Cnt-bndl Suspend Not-in-Bndl
Channel group = 1 Mode = On Gcchange = -
Port-channel = null GC = - Pseudo port-channel = Po1
Port index = 0 Load = 0x00 Protocol = -
Age of the port in the current state: 0d:00h:25m:13s
Probable reason: vlan mask is different
<output omitted>
Using the show etherchannel 1 detail command
Notes: The output shown in the example indicates that the cause of the problem is the “VLAN mask”, which means that there must be a mismatch between the VLANs allowed on the port-channel versus the VLANs allowed on the physical interfaces.
<number>

## Slide 56: EtherChannel Operation
EtherChannel bundles multiple physical Ethernet links (100 Mbps,1 Gbps, 10 Gbps) into a single logical link.
Traffic is distributed across multiple physical links as one logical link.
This logical link is represented in Cisco IOS syntax as a “Port-channel” (Po) interface.
STP and routing protocols interact with this single port-channel interface.
Packets and frames are routed or switched to the port-channel interface.
A hashing mechanism determines which physical link will be used to transmit them.
Notes: <number>

## Slide 57: EtherChannel Problems
Three common EtherChannel problems:
Inconsistencies between the physical ports that are members of the channel
Inconsistencies between the ports on the opposite sides of the EtherChannel link
Uneven distribution of traffic between EtherChannel bundle members
Notes: Inconsistencies between the physical ports that are members of the channel:
The physical links in an EtherChannel must have the same operational characteristics (speed, duplex, trunk or access port status, native VLAN when trunking, and same access VLAN when they are access ports).
If one physical link changes such that a mismatch with the other physical links is created, this port will be suspended and removed from the EtherChannel bundle until consistency is restored.
Inconsistencies between the ports on the opposite sides of the EtherChannel link:
If one switch is configured to bundle these links into an EtherChannel and the switch on the other side is not, the switch that is configured for EtherChannel will detect this and move the port to an error-disabled state.
The use of a Link Aggregation Control Protocol (LACP) or the Port Aggregation Protocol (PAgP) prevents this situation from happening because both sides must first agree to form the channel.
Uneven distribution of traffic between EtherChannel bundle members:
The Cisco EtherChannel hash algorithm results in a value between 0 and 7. An eight-port EtherChannel will be equally balanced across all eight links.
However, if the channel consists of six links, the distribution will be 2:2:1:1:1:1 instead, meaning that the first two links in the channel will each handle twice as much traffic as the other links.
Another factor in EtherChannel load balancing is which header fields are used as the base of the hash value. When only the destination MAC address is used as the input for the hash calculation, if 90% of all frames are destined for a single MAC address (for instance, the MAC address of the default gateway), then all of that traffic would end up on the same physical link.
If you see an uneven distribution of traffic over the links in the channel, you should examine the hashing method and the traffic mix to determine the cause.
<number>

## Slide 58: EtherChannel Diagnostic Commands
DSW2# show etherchannel summary
Flags: D - down P - bundled in port-channel
I - stand-alone s - suspended
H - Hot-standby (LACP only)
R - Layer3 S - Layer2
U - in use f - failed to allocate aggregator
M - not in use, minimum links not met
u - unsuitable for bundling
w - waiting to be aggregated
d - default port
Number of channel-groups in use: 2
Number of aggregators: 2
Group Port-channel Protocol Ports
------+-------------+-----------+-------------------------
1 Po1(SD) - Fa0/5(s) Fa0/6(s)
2 Po2(SU) - Fa0/3(P) Fa0/4(P)
Using the show etherchannel summary command
Notes: The output from this command presents a concise overview of all links that are configured for EtherChannel, the status of the individual physical interfaces, as well as the logical Port-channel interfaces.
Note the letters “SD” beside the Po1 interface. “S” means that it is configured as a Layer 2 interface, but “D” means that Port-channel 1 (Po1) is down.
The small letter “s” is present beside the physical interfaces Fa0/5 and Fa0/6. Small “s”, marking the physical interfaces, indicates that those interfaces have been suspended.
Note: Po1 and Po2 were created without using PAgP or LACP, as evidenced by the empty name in the Protocol column. Configuring EtherChannels without a signalling protocol is generally not recommended.
<number>

## Slide 59: EtherChannel Diagnostics
ASW1# show spanning-tree vlan 17
MST0
Spanning tree enabled protocol mstp
Root ID Priority 32768
Address 001e.79a9.b580
This bridge is the root
Hello Time 2 sec Max Age 20 sec Forward Delay 15 sec
Bridge ID Priority 32768 (priority 32768 sys-id-ext 0)
Address 001e.79a9.b580
Hello Time 2 sec Max Age 20 sec Forward Delay 15 sec
Interface Role Sts Cost Prio.Nbr Type
------------------- ---- --- --------- -------- ------------------------------
Fa0/7 Desg FWD 200000 128.9 P2p Edge
Po1 Desg BLK 100000 128.56 P2p
Po2 Desg BKN*100000 128.64 P2p Bound(PVST) *PVST_Inc
Using the show spanning-tree command to examine STP
Notes: The output of this command has two elements that clearly point to a spanning tree configuration issue with Po2. The “BKN*” and “*PVST_Inc” elements in the output, point towards a spanning-tree inconsistency, while the “Bound (PVST)” element points toward a boundary between two different Spanning Tree varieties. In this case other switches run Rapid PVST+ and this should not be running MST. Please note that the third line in the example indicates that this switch is running MST.
<number>

## Slide 60: Troubleshooing First Hop Redundancy Protocols

## Slide 61: First Hop Redundancy Protocols (FHRPs)
FHRP is an important element in building highly available networks.
Clients and servers normally point to a single default gateway and lose connectivity to other subnets if their gateway fails.
FHRPs provide redundant default gateway functionality that is transparent to the end hosts.
These protocols provide a virtual IP address and the corresponding virtual MAC address.
Examples of FHRPs include:
  Hot Standby Router Protocol (HSRP) – Cisco
  Virtual Router Redundancy Protocol (VRRP) – IETF standard
  Gateway Load Balancing Protocol (GLBP) – Cisco
The mechanisms of these protocols revolve around these functions:
  Electing a single router that controls the virtual IP address
  Tracking availability of the active router
  Determining if control of the virtual IP and MAC addresses should be handed over to another router
Notes: These protocols provide a redundant default gateway on a subnet and do this in such a way that actions such as failover and load balancing remain entirely transparent to the hosts.
These protocols provide a virtual IP address and the corresponding virtual MAC address that can be used as the default gateway by the hosts on the subnet.
This virtual IP and MAC address is not bound to any particular router, but can be controlled by a router within a group of routers participating in the protocol's scheme.
Under normal circumstances, at any given moment, the active router, has control over the virtual IP and MAC address.
<number>

## Slide 62: Using First Hop Redundancy
Sample HSRP Configuration
Notes: The example shows two routers R1 and R2 with IP addresses 10.1.1.1 and 10.1.1.2 on their FastEthernet interfaces, respectively, configured with HSRP.
Routers R1 and R2 have been configured for the same HSRP group (group 1) and virtual IP address (10.1.1.254).
Both routers have been configured for preemption. This will allow either of them to take over the role of active router when its priority is the highest of the routers in the group.
R1 has been configured with a priority of 110, which is higher than the default priority of 100.
This will cause R1 to be elected as the active router, while R2 will be elected as the standby router.
This means that R1 will be in control of the virtual IP and MAC address and will forward packets sent to the virtual router’s IP and MAC address.
If R1 goes down, R2 will take over control of the virtual IP and MAC address and will forward packets from hosts on the subnet.
<number>

## Slide 63: Verifying HSRP Operation
Sample output from the show standby brief command
Notes: The figure shows a sample output from this command for routers R1 and R2 that participate in HSRP group 1. For each interface, this command shows the configured HSRP group, the IP addresses for the active and standby router, the virtual IP address, configured priority, and the preemption option.
<number>

## Slide 64: Chapter 4 Summary
Commonly used diagnostic commands for the Layer 2 switching process, VLANs and trunks are as follows:
  show mac address-table
  show vlan
  show interfaces trunk
  show interfaces switchport
  show platform forward interface
  traceroute mac
Important commands for gathering information about the status of STP and the corresponding topology are:
  show spanning-tree [vlan vlan-id]
  show spanning-tree interface interface-id detail
Notes: <number>

## Slide 65: Chapter 4 Summary – Cont.
Building the spanning tree has the following 4 main steps:
Elect a Root Bridge/Switch
  This is based on the lowest Bridge-ID.
Select a Root Port on each non-Root Bridge/Switch
  This is based on the least cost to Root.
  Ties are broken based on the lowest upstream Bridge-ID.
  Further ties are broken based on the lowest upstream Port-ID.
Elect a Designated port on each network segment
  This is based on the least cost to Root.
  Ties are broken based the on the lowest upstream Bridge-ID.
  Further ties are broken based on the lowest upstream Port-ID.
Ports that ended up as neither a Root port nor a Designated port go into Blocking state, and the Root Ports and Designated ports move through Listening, Learning and Forwarding states.
Notes: <number>

## Slide 66: Chapter 4 Summary – Cont.
The consequences and corresponding symptoms of broadcast (or unknown MAC) storms are:
The load on all links in the switched LAN will quickly start increasing as more and more frames enter the loop.
If the Spanning Tree failure has caused more than one bridging loop to form, traffic will increase exponentially.
When control plane traffic starts entering the loop, the devices that are running these protocols will quickly start getting overloaded and their CPU will approach 100% utilization.
Switches will experience very frequent MAC address table changes.
Due to the combination of very high load on all links and the CPU running at maximum load on Layer 3 switches or routers, these devices typically become unreachable, making it nearly impossible to diagnose the problem while it is in progress.
Notes: <number>

## Slide 67: Chapter 4 Summary – Cont.
Three common EtherChannel problems are:
Inconsistencies between the physical ports that are members of the channel (a %EC-5-CANNOT_BUNDLE2 log message is generated)
Inconsistencies between the ports on the opposite sides of the EtherChannel link (The switch will generate a %SPANTREE-2-CHNL_MISCFG message)
Uneven distribution of traffic between EtherChannel bundle members
Notes: <number>

## Slide 68: Chapter 4 Summary – Cont.
Similarities between multilayer switches and routers include:
Both routers and multilayer switches use routing protocols or static routes to maintain information about the reachability and direction to network destinations (prefixes), and record this information in a routing table.
Both routers and multilayer switches perform the same functional packet switching actions:
    Receive a frame, strip off the Layer 2 header.
    Perform a Layer 3 lookup to determine the outbound interface and next hop.
    Encapsulate the packet in a new Layer 2 frame and transmit the frame.
Notes: <number>

## Slide 69: Chapter 4 Summary – Cont.
Differences between multilayer switches and routers include:
Routers connect heterogeneous networks and support a wide variety of media and interfaces.
Multilayer switches typically connect homogenous networks. Modern LAN switches are mostly Ethernet.
Multilayer switches utilize specialized hardware to achieve wire-speed Ethernet-to-Ethernet packet switching.
Low- to mid-range routers use multi-purpose hardware to perform the packet switching process.
On average, the packet switching throughput of routers is lower than the packet switching throughput of multilayer switches.
Routers usually support a wider range of features, mainly because switches need specialized hardware to be able to support certain data plane features or protocols.
On routers, you can often add features through a software update.
Notes: <number>

## Slide 70: Chapter 4 Summary – Cont.
There are two main commands to check the CEF data structures:
  show ip cef
  show adjacency
To extract information about the forwarding behavior of switches from the TCAMs on some of the common Cisco Catalyst series switches you can use the following commands:
  show platform
  show mls cef
Notes: <number>

## Slide 71: Chapter 4 Summary – Cont.
A multilayer switch provides three different core functions in a single device:
Layer 2 switching within each VLAN
Routing and multilayer switching between the local VLANs
Routing and multilayer switching between the local VLANs and one or more routed interfaces
Notes: <number>

## Slide 72: Chapter 4 Summary – Cont.
The main differences between SVIs and router interfaces are as follows:
A routed port is not a Layer 2 port. This means that on a routed port typical Layer 2 protocols that are enabled by default, such as Spanning Tree Protocol and Dynamic Trunking Protocol (DTP), are not active.
There is a direct relationship between the status of a routed port and the availability of the corresponding directly-connected subnet. When/if the port goes down, the corresponding connected route will immediately be removed from the routing table.
The status of an SVI is directly related to its associated VLAN, wheras a routed port is not associated with a VLAN.
Notes: <number>

## Slide 73: Chapter 4 Summary – Cont.
Among first hop redundancy protocols, VRRP is the only standards based protocol, the only one that has the preempt option enabled by default, and also the only one that allows the virtual IP address to also be a real address assigned to one of the participating routers.
VRRP's default hello timer is 1 second as compared to HSRP and GLBP's 3 second default hello timer.
Among HSRP, VRRP, and GLBP, only GLBP makes use of multiple routers in the group to do simultaneous forwarding (load balancing).
With respect to debug, VRRP does not have the terse option, but HSRP and GLBP do.
Notes: <number>

## Slide 74: Chapter 4 Labs
Lab 4-1 Layer 2 Connectivity and Spanning Tree
Lab 4-2 Layer 3 Switching and First-Hop Redundancy

## Slide 75
Notes: <number>