## Slide 1: Ch. 5 Maintaining and Troubleshooting Routing Solutions
Notes: <number>

## Slide 2: Materials
<number>
Book:
  Troubleshooting and Maintaining Cisco IP Networks (TSHOOT) Foundation Learning Guide: Foundation learning for the CCNP TSHOOT 642-832
  By Amir Ranjbar
  Book
    ISBN-10: 1-58705-876-6
    ISBN-13: 978-1-58705-876-9
  eBook
    ISBN-10: 1-58714-170-1
    ISBN-13: 978-1-58714-170-6
Notes: <number>

## Slide 3: Troubleshooting Routing
Network Layer Connectivity
EIGRP
OSPF
Route Redistribution
Note: You always have the option of reviewing my CCNP ROUTE PowerPoints or attending the lectures for a review.
  At the time of this presentation we will be discussing Manipulating Routing Updates with route maps and distribution lists in my CIS 185 ROUTE class on Tuesday.
<number>

## Slide 4: Network Connectivity
Just like we did when we looked at Layer 2 connectivity
To troubleshoot Layer 3 connectivity, you need to have a good understanding of the processes that are involved in routing a packet from a host through multiple routers to the final destination.
Lack of network layer connectivity indicates that the problem is at or below network layer.
<number>

## Slide 5
Which decisions does Host A make to successfully send a packet destined for Host B to the first hop Router C?
  What information does it need?
    Addressing; ARP Cache
  Which actions does it perform?
    DHCP Request; Host or GW Address; DNS Query; ARP Request; Layer 2 encapsulation
Which decisions does Router C make to successfully send the packet from Host A destined for Host B to the next hop Router D?
  TTL – ICMP Time Exceeded; ; CEF or layer 3; Longest prefix match; Layer 2 Next-hop address; layer 2 encapsulation; Fragmentation
Which decisions does Router D make to successfully send the packet from Host A destined for Host B to the next hop Router E? (Same questions)
Which decisions does Router E make to successfully send the packet from Host A destined for Host B to its final destination, Host B? (Same questions)
Are there any differences in the processes and information required in order to successfully transmit return packets from Host B back to Host A?
<number>

## Slide 6: Alex Zinin’s Routing Table Principles
<number>
Principle 1: Every router makes its decision alone, based on the information it has in its own routing table.
R1 makes forwarding decisions based solely on the information in the routing table.
R1 does not consult the routing tables in any other routers.
Making each router aware of remote networks is the responsibility of the network administrator.
I know about my remote networks but it is not my responsibility if R2 and R3 know about their remote networks.
Notes: <number>
Principle 1: Every router makes its decision alone, based on the information it has in its own routing table.
R1 has three static routes in its routing table and makes forwarding decisions based solely on the information in the routing table.
R1 does not consult the routing tables in any other routers, nor does it know whether those routers have routes to other networks.
Making each router aware of remote networks is the responsibility of the network administrator.

## Slide 7: Alex Zinin’s Routing Table Principles
<number>
Principle 2: The fact that one router has certain information in its routing table does not mean that other routers have the same information.
Just because I know how to get to R3’s LAN, 192.168.2.0/24 and I send that packet to R2, doesn’t mean R2 knows how to get there.
???
Notes: <number>
Principle 2: The fact that one router has certain information in its routing table does not mean that other routers have the same information.
R1 does not know what information other routers have in their routing table.
For example, R1 has a route to the 192.168.2.0/24 network through Router R2.
Any packets that match this route belong to the 192.168.2.0/24 network and will be forwarded to Router R2.
R1 does not know whether R2 has a route to the 192.168.2.0/24 network.
Again, the network administrator would be responsible for ensuring that the next-hop router also has a route to this network.
Using Principle 2, you still need to configure the proper routing on the other routers (R2 and R3) to make sure that they have routes to these three networks.

## Slide 8: Alex Zinin’s Routing Table Principles
<number>
Principle 3: Routing information about a path from one network to another does not provide routing information about the reverse, or return, path.
And if the packet for R3’s LAN reaches 192.168.2.0/24, I don’t know if R3 has a route back to 172.16.3.0/24 for any return traffic.
???
Notes: <number>
Principle 3: Routing information about a path from one network to another does not provide routing information about the reverse, or return, path.
Most of the communication over networks is bidirectional.
This means that packets must travel in both directions between the end devices involved.
A packet from PC1 can reach PC3 because all the routers involved have routes to the destination network 192.168.2.0/24.
However, the success of any returning packets going from PC3 to PC1 depends on whether the routers involved have a route to the return path, PC1’s 172.16.3.0/24 network.
Using Principle 3 as guidance, you will configure proper static routes on the other routers to make sure that they have routes back to the 172.16.3.0/24 network.

## Slide 9
To forward packets, a router combines information from various control plane data structures.
  The most important of these data structures is the routing table.
  Other structures include:
    LSDB or topology table
    Neighbor table
    ARP or Frame Relay Map table
Unlike switches, which flood unknown frames, routers drop any packet for which they cannot find a matching entry in the routing table.
Searches for longest possible prefix match of the destination IP address.
Associated with this entry is an egress interface - most cases, a next-hop IP address.
<number>

## Slide 10
The mapping between the next hop-IP address and the Layer 2 address or identifier is stored in a data structure that is specific for that Layer 2 protocol.
  Ethernet: ARP cache
  Frame Relay: Frame Relay map table (except for point-to-point)
A routing table lookup may need to be followed up by a lookup in a Layer 3 to Layer 2 mapping table to construct a frame, encapsulate the packet, and transmit it.
<number>

## Slide 11: Troubleshooting EIGRP
<number>

## Slide 12
At a high level, each routing protocol consists of the following elements and processes: (RIP is a notable exception to some of these.)
Reception of routing information from neighbors:
  Neighbor relationships
Routing protocol data structures:
  Neighbor table, topology table
Route injection or redistribution:
  Directly connected, dynamic routes, static routes
Route selection and installation:
  Best path, equal cost load balancing, unequal cost load balancing
Transmission of routing information to neighbors:
  Summarization, Broadcast, Multicast, LSAs, Route updates, ACKs
<number>

## Slide 13
To diagnose and resolve problems related to EIGRP you must be able to:
  Apply your knowledge of EIGRP data structures
    Neighbor table, Topology Table
  Apply your knowledge of EIGRP processes
    DUAL, adjacency process, summarization, load balancing
  Use Cisco IOS commands to gather information from the EIGRP data structures and track the flow of EIGRP routing information
Note: As we will see these procedures can be applied to other routing protocols as well.
<number>

## Slide 14
EIGRP stores its operational data, configured parameters, and statistics in three main data structures:
Interface table:
  Lists all interfaces that have been enabled for the processing of EIGRP packets
  Passive interfaces are not listed in this table.
<number>
R3# show ip eigrp interfaces
IP-EIGRP interfaces for process 1
Xmit Queue Mean Pacing Time Multicast Pending
Interface Peers Un/Reliable SRTT Un/Reliable Flow Timer Routes
Se0/1 1 0/0 60 0/15 299 0
Se0/0 1 0/0 607 0/15 3031 0
Se0/2 1 0/0 29 0/15 143 0
Se0/3 1 0/0 24 0/17 50 0
R3#

## Slide 15
Neighbor table:
  Keeps track of all active EIGRP neighbors.
  Neighbors are added to this table on the reception of hello packets
  Neighbors are removed when:
    Hold-time expires
    Interface goes down or is removed from the interface table
<number>
R3# show ip eigrp neighbors
IP-EIGRP neighbors for process 1
H Address Interface Hold Uptime SRTT RTO Q Seq Type
(sec) (ms) Cnt Num
3 10.0.0.18 Se0/3 13 00:17:37 24 200 0 5
2 10.0.0.14 Se0/2 14 00:17:50 29 200 0 4
1 10.0.0.5 Se0/0 14 00:23:35 607 3642 0 13
0 10.0.0.9 Se0/1 12 00:24:01 60 360 0 21
R3#

## Slide 16
Topology table:
  Holds all the routes that were received from neighboring routers, locally injected, or redistributed into EIGRP.
  EIGRP will select the best path from among the available possible paths
  EIGRP’s best path selection is based on the Diffusing Update Algorithm (DUAL).
<number>
R3# show ip eigrp topology
<output omitted>
P 10.0.0.0/30, 2 successors, FD is 2681856
via 10.0.0.9 (2681856/2169856), Serial0/1
via 10.0.0.5 (2681856/2169856), Serial0/0
<output omitted>
P 172.16.0.0/16, 1 successors, FD is 2172416
via 10.0.0.14 (2172416/28160), Serial0/2
via 10.0.0.18 (2312192/28160), Serial0/3
successor
feasible successor
Feasible distance
Feasible distance: if this router was the successor.
FS if Reported Distance is less than Feasible distance

## Slide 17: Initial Route Discovery
<number>
A
B
Hello, I am Router A. Is anyone there?
Hello, I am Router B.
Here is all my routing information.
I’m using split horizon.
Thanks for the information!
That is very nice of you.
Here is all my routing information.
I’m also using split horizon.
Thanks for the information!
We’ve reached convergence.
EIGRP
Neighbor
Table
EIGRP
Neighbor
Table
EIGRP
Topology
Table
EIGRP
Topology
Table
IP
Routing
Table
IP
Routing
Table
Updated
Updated
Updated
Updated
Updated
Updated
Successor
Successor

## Slide 18
After the initial updates have been exchanged, routing updates will only be exchanged as a result of changes on the networks.
Changes can be caused by changes in connectivity, such as:
  Loss of a link or neighbor
  Configuration events
<number>

## Slide 19
debug ip routing:
  Not specific to EIGRP
  Displays any changes that are made to the routing table, such as installation or removal of routes.
<number>
R2# debug ip routing
IP routing debugging is on
R2# conf t
R2(config)# int fa0/0
R2(config-if)# ip address 172.16.1.1 255.255.255.0
R2(config-if)# no shutdown
%LINK-3-UPDOWN: Interface FastEthernet0/0, changed state to up
%LINEPROTO-5-UPDOWN: Line protocol on Interface FastEthernet0/0, changed state to up
RT: add 172.16.1.0/24 via 0.0.0.0, connected metric [0/0]
RT: interface FastEthernet0/0 added to routing table

## Slide 20
debug eigrp packets:
  Displays the transmission and reception of EIGRP packets.
  Note: Cisco Press Implementing Cisco IP Routing (ROUTE) by Diane Teare provides detailed explanation of the output.
<number>

## Slide 21
debug ip eigrp:
  Displays EIGRP routing events, such as updates, queries, and replies sent to or received from neighbors.
  Focuses on the routing information contained in the packets and the actions that EIGRP takes as a result of the information received.
  Note: Cisco Press Implementing Cisco IP Routing (ROUTE) by Diane Teare provides detailed explanation of the output.
<number>

## Slide 22: Troubleshooting Example: Routing Problem in an EIGRP Network
<number>

## Slide 23
Traffic path unexpectedly goes through BRO2
<number>

## Slide 24
ping from BRO1 to CRO1 succeeds, you can conclude that the WAN link is operational at Layers 3 and below
<number>

## Slide 25
Two likely reasons why the traffic is routed through router BRO2 instead of directly across the WAN to router CRO1:
  BRO1 has not learned about the direct route to router CRO1.
  BRO1 selects the route through router BRO2 as the best route.
Let’s look at the EIGRP topology table
<number>

## Slide 26
The topology table lists all routes that were received, so you can see if the direct route to CRO1 is missing.
  Note: This command displays all entries in the topology table for this destination, not just feasible successors – similar to “all-links” option.
  No direct route!
Need to determine whether the route was not learned because:
  A neighbor relationship with CRO1 was never established
  The relationship was established but the specific route was not exchanged.
Good next step is to display the neighbor table
<number>

## Slide 27
CRO1 is not listed as a neighbor on router BRO1.
Could be one or the other routers is not:
  Sending Hello packets
  Ignoring Hello packets
Let’s look at the EIGRP interfaces to make sure the serial interface is configured for EIGRP.
<number>

## Slide 28
Does not list the serial interface of router BRO1.
So, even if hello packets are received on the serial interface, router BRO1 does not process them.
Two conditions need to be met for an interface to be added to the EIGRP interface table:
  The interface has to be up and its IP address must match one of the configured network statements.
  The interface should not be configured as a passive interface.
Let’s look at the running-config…
<number>

## Slide 29
Problem with one of the network statements.
The statement network 10.1.194.1 0.0.0.0 matches IP address 10.1.194.1 the IP address of router CRO1
  Does not match the serial interface of BRO1
Replaced it with the statement network 10.1.194.2 0.0.0.0 or some other network statement
<number>

## Slide 30
The interface table now lists subinterface Serial 0/0/0.111 in addition to subinterface FastEthernet 0/1.30.
  This means that EIGRP packets are now processed on interface Serial 0/0/0.111.
IP address of router CRO1 (10.1.194.2) is now listed in the neighbor table on the WAN interface.
<number>

## Slide 31
The EIGRP topology table now lists two entries for network 10.1.220.1/32.
Note: BR02 is listed but is not a Feasible Successor (RD is not less than FD)
<number>
Successor

## Slide 32
show ip route command with network 10.1.220.1 confirms that the path through router CRO1 has been installed in the routing table
traceroute command confirms that this path is now used to forward packets to the loopback of CRO1.
<number>

## Slide 33: Troubleshooting OSPF
<number>

## Slide 34
To diagnose and resolve problems related to OSPF you must be able to:
  Apply your knowledge of OSPF data structures
  Apply your knowledge of OSPF processes within an area
  Apply your knowledge of OSPF processes between areas
  Use Cisco IOS commands to gather information from the OSPF data structures and track the flow of OSPF routing information
<number>

## Slide 35
OSPF stores its operational data, configured parameters, and statistics in four main data structures:
Interface table:
  Lists all interfaces that have been enabled for OSPF.
  When an interface is configured as a passive interface, it is still listed in the OSPF interface table, but no neighbor relationships are established on this interface.
<number>
R1# show ip ospf interface serial 0/0/0
Serial0/0/0 is up, line protocol is up
Internet Address 192.168.10.1/30, Area 0
Process ID 1, Router ID 10.1.1.1, Network Type POINT_TO_POINT, Cost: 64
Transmit Delay is 1 sec, State POINT_TO_POINT,
Timer intervals configured, Hello 10, Dead 40, Wait 40, Retransmit 5
<output omitted>

## Slide 36
Neighbor table:
  Keeps track of all active OSPF neighbors.
  OSPF goes through a number of states while establishing a neighbor relationship (also known as adjacency)
  Lists the current state for each individual neighbor
<number>
R1# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
10.3.3.3 1 FULL/ - 00:00:30 192.168.10.6 Serial0/0/1
10.2.2.2 1 FULL/ - 00:00:33 192.168.10.2 Serial0/0/0

## Slide 37
Link-state database:
  This is the main data structure that OSPF uses to store all its network topology information.
  Contains a wealth of network topology information
  One of the most important data structures to gather information from when troubleshooting OSPF problems.
<number>

## Slide 38
Routing information base:
  After executing the SPF algorithm, the results of this calculation are stored in the RIB (Routing Information Base).
  Routes might be added to or deleted from the RIB without the need for a SPF recalculation.
  From the RIB, OSPF offers its routes to the IP routing table.
Note: The collection of best paths is known as the OSPF RIB.
  There is not a separate physical data structure called the OSPF RIB.
  Many writings refer to the IP routing table as the RIB to allow it to be distinguished from the FIB that CEF creates.
<number>
R33# show ip route
33.0.0.0/32 is subnetted, 1 subnets
C 33.33.33.33 is directly connected, Loopback0
172.16.0.0/24 is subnetted, 2 subnets
C 172.16.1.0 is directly connected, FastEthernet0/0
O 172.16.2.0 [110/2] via 172.16.1.1, 00:02:13, FastEthernet0/0
172.30.0.0/24 is subnetted, 2 subnets
C 172.30.1.0 is directly connected, FastEthernet0/1
O 172.30.2.0 [110/2] via 172.16.1.3, 00:02:23, FastEthernet0/0
O*IA 0.0.0.0/0 [110/2] via 172.16.1.1, 00:02:13, FastEthernet0/0

## Slide 39
Two routers will become neighbors only if the following parameters match in the Hello packets:
Hello and dead timers:
  Use the same Hello and dead time.
  Broadcast and point-to-point type networks are 10-second Hello and 40-second dead time.
OSPF area number:
  Both consider that link to be in the same area.
IP subnet and subnet mask:
  If they are on the same subnet.
  The exception to this rule is on a point-to-point link, where the subnet mask is not verified.
<number>
R1# show ip ospf neighbor
Neighbor ID Pri State Dead Time Address Interface
10.3.3.3 0 FULL/ - 00:00:35 192.168.10.6 Serial0/0/1
10.2.2.2 0 FULL/ - 00:00:36 192.168.10.2 Serial0/0/0

## Slide 40: Troubleshooting Example: Routing Problem in an OSPF Network
<number>

## Slide 41
CR01# show ip route 10.1.152.0
Examine the routing table on router CRO1, you only find a single entry, the path through router CSW1.
Should be two equal cost paths
<number>

## Slide 42
This result is unexpected because there are two equal cost paths are available to CRO1:
  via CSW1
  via CSW2
Ping CSW2
Because this ping succeeds, conclude that the Fast Ethernet link between router CRO1 and router CSW2 is operational at Layers 3 and below.
Need to find out why the second, equal cost path through router CSW2 is not installed in the routing table
There are two main reasons why this could be happening.
  CSW2 is not advertising subnet 10.1.152.0/24 to area 0
  Cost to reach subnet 10.1.152.0/24 through router CSW2 from router CRO1 is considered to be worse than the cost through router CSW1.
<number>

## Slide 43
Therefore, the preference for the path to 10.1.152.0/24 via CSW1 must be based on the topology within area 0.
Given that router CRO1 has a direct connection in area 0 to both router CSW1 and CSW2, there are only two plausible explanations for the fact that router CRO1 is not using the path via router CSW2.
  Either the direct path to router CSW2 is not used because routers CSW2 and CRO1 have not become neighbors
  The path is not used because the cost for interface FastEthernet 0/1 is higher than the cost for interface FastEthernet 0/0
<number>

## Slide 44
To verify if router CRO1 has established, a proper neighbor relationship with router CSW1, the show ip ospf neighbor
There could be several reasons why router CSW2 is not listed as a neighbor of CRO1:
  CSW2 is not sending Hellos
  Hellos are received, but ignored due to mismatched Hello parameters.
  Hellos are sent, but not received, because interface FastEthernet 0/1 has not been activated for OSPF and therefore does not listen to the OSPF multicast group 224.0.0.5
<number>
Note: Unlike the show ip eigrp interfaces command,
the show ip ospf interface command will
display interfaces that are enabled for OSPF,
but configured as passive interfaces.

## Slide 45
The is a problem with one of the network statements.
The statement network 10.1.192.9 0.0.0.0 area 0 matches IP address 10.1.192.9, which is not one of router CRO1’s IP addresses, but an IP address of router CSW2.
network statement needs to be replaced with the statement network 10.1.192.10 0.0.0.0 area 0 or some other network statement
<number>

## Slide 46
After change, verify interface and neighbor relationship
<number>

## Slide 47
Verify route
<number>

## Slide 48: Troubleshooting the book 
Through no fault of the author the diagram in the book is incorrect.
Why is this diagram incorrect given this output?
CR01 cannot receive LSA 3’s from CSW2 unless:
  Establishes a neighbor adjacency with CSW2
  CSW2 forwards the LSA3 to CSW1 within area 0 (CR01’s area)
<number>

## Slide 49: Troubleshooting Route Redistribution
<number>

## Slide 50
Ideally, no more than one interior (intra-AS) routing protocol is used within an organization.
Reasons for running multiple routing protocols:
  Company mergers and different IGPs are used
  Company has different divisions with the network under separate control for business or political reasons
  Company has connections between business partners
  To allow multivendor interoperability (OSPF on non-Cisco, EIGRP on Cisco, for instance)
Improper route redistribution can lead to:
  Suboptimal routing
  Routing feedback (routing loops)
<number>

## Slide 51
There are two ways for routes to be injected in a routing protocol:
  Directly connected:
    Enabling the routing protocol on an interface.
    These routes are considered internal by the routing protocol.
  External:
    Networks from a different source that are present in the routing table
    Because these routes were not originated by the routing protocol, they are considered external.
<number>
Router(config-router)# redistribute protocol [protocol options]
Router(config-router)# network network-address [protocol options]

## Slide 52
There are two important conditions that must be met for a prefix learned from one protocol (using redistribution) to be successfully advertised through another protocol:
  The route needs to be installed in the routing table doing the redistribution.
  A proper seed metric is assigned to the redistributed route (except for OSPF which defaults to 20)
      <number>

## Slide 53: Example
So far…
R2 summary:
router eigrp 1
network 172.30.0.0
auto-summary
redistribute ospf 1
default-metric 1000 33 255 1 1500
redistribute connected metric 1000 33 255 1 1500
!
router ospf 1
network 10.0.0.0 0.0.0.255 area 0
network 172.16.0.0 0.0.0.3 area 0
redistribute eigrp 1 subnets
redistribute connected
1000 33 255 1
BW=20
BW=20
OSPF learned networks are distributed
into the EIGRP domain
Use the metrics for BW DLY RLY Load
Distribute any directly connected networks
and use these metrics for BW DLY RLY Load
EIGRP learned networks are distributed
into the OSPF domain, default metric of 20
Distribute any directly connected networks
and use default metric of 20

## Slide 54: Using Route Maps to Avoid Route Feedback
Multi-point boundary routers may cause suboptimal routing or routing loops.
RIPv2 on Router C advertises network 192.168.1.0.
Routers A and B redistribute the network into OSPF.
OSPF then advertises the route to its neighbor OSPF routers as an OSPF external route.
The route passes through the OSPF AS and eventually makes its way back to the other edge router.
Router B (or A) then redistributes 192.168.1.0 from OSPF back into the original RIPv2 network; this is a routing feedback loop.
Depending upon the metrics this may result in suboptimal routing or even a routing loop!
<number>
OSPF
RIPv2
192.168.1.0/24
C
D
A
B
0 E2 192.168.1.0/24
E

## Slide 55
To prevent the routing feedback loop, a route map called OSPF_into_RIP has been applied to Routers A and B when redistributing OSPF routes into RIP.
The decision to filter a route or allow the route through is based on the deny or permit in the route-map command, and not the deny or permit in the ACL or prefix list.
<number>
router ospf 10
redistribute rip subnets
router rip
redistribute ospf 10 route-map OSPF_into_RIP
route-map OSPF_into_RIP deny 10
match ip address 1
route-map OSPF_into_RIP permit 20
access-list 1 permit 192.168.1.0 0.0.0.255
192.168.1.0/24 network will not be redistributed into RIP
All other routes will be redistributed into RIP

## Slide 56: Using Route Maps With Tags (Reminder from Rick )
route tag – A unitless 32-bit integer that most routing protocols can assign to any given route.
Tag follows the route advertisement, even through the redistribution process.
Another router may use an IOS tool such as route-maps to match routes with a given route tag to make a decision.
Can be used to help to solve the domain loop problem.
<number>
router eigrp 100
redistribute rip metric 1000 100 255 1 1500 route-map into-eigrp
route-map into-eigrp deny 10
match tag 40
route-map into-eigrp permit 20
set tag 20

## Slide 57
<number>
EIGRP
RIPv2
R2
R1
172.16.0.0/16
10.0.0.0/8
Tag 40
Tag 20
Tag 20
Tag 40
router eigrp 100
redistribute rip metric 1000 100 255 1 1500 route-map into-eigrp
router rip
redistribute eigrp 100 metric 3 route-map into-rip
route-map into-eigrp permit 20
set tag 20
route-map into-rip permit 20
set tag 40
Routes redistributed into EIGRP are tagged with the value 20
Routes redistributed into RIP are tagged with the value 40
BUT BEFORE we tag and allow a route into the domain we want to deny any routes that the other router already tagged and allowed in from the other domain.

## Slide 58
<number>
router eigrp 100
redistribute rip metric 1000 100 255 1 1500 route-map into-eigrp
router rip
redistribute eigrp 100 metric 3 route-map into-rip
route-map into-eigrp deny 10
match tag 40
route-map into-eigrp permit 20
set tag 20
route-map into-rip deny 10
match tag 20
route-map into-rip permit 20
set tag 40
EIGRP
RIPv2
R2
R1
172.16.0.0/16
10.0.0.0/8
Tag 40
Tag 40
Tag 40
Tag 40
Updates with the tag 40 are not allowed to go back into EIGRP
X
X
All other updates get a tag 20 are allowed into EIGRP

## Slide 59
<number>
router eigrp 100
redistribute rip metric 1000 100 255 1 1500 route-map into-eigrp
router rip
redistribute eigrp 100 metric 3 route-map into-rip
route-map into-eigrp deny 10
match tag 40
route-map into-eigrp permit 20
set tag 20
route-map into-rip deny 10
match tag 20
route-map into-rip permit 20
set tag 40
EIGRP
RIPv2
R2
R1
172.16.0.0/16
11.0.0.0/8
10.0.0.0/8
Tag 20
Tag 20
Tag 20
Tag 20
Updates with the tag 20 are not allowed to go back into RIP
X
X
All other updates get a tag 40 are allowed into RIP

## Slide 60
Notice that the route tags do not appear on the routes within the R1 and R2 routers, because these routers learn about all routes from both RIP and EIGRP directly.
<number>
R3
11.0.0.0.0/8

## Slide 61
However, show ip route output from router R3, an internal router in the EIGRP network.
Notice that router R3 does see network 11.0.0.0 with a tag of 20; this tag is carried with the route as R3 advertises it to other routers in the EIGRP network, including R1 and R2.
When routers R1 and R2 see the tag of 20, they do not redistribute the 11.0.0.0 route back into RIP.
<number>
R3
11.0.0.0.0/8

## Slide 62: Troubleshooting BGP
<number>

## Slide 63
BGP is classified as an EGP or an inter-autonomous-system (inter-AS) routing protocol.
BGP does not use metrics such as bandwidth, delay or path cost to find the best paths within an AS
It is used to:
  Exchange routing information with external networks (other autonomous systems)
  Selection of guaranteed loop-free path using policies (attributes)
<number>

## Slide 64
Specifics of BGP
Reception of routing information from neighbors:
  Neighbors need not be directly connected.
  Neighbors are manually configured, not automatically discovered through a hello protocol.
Routing protocol data structures:
  BGP has two main data structures.
    Neighbor table to keep track of the state of configured neighbors.
    BGP table, which BGP uses to store all the prefixes, including those received from the neighbors.
<number>
ISP1#show ip bgp
Network Next Hop Metric LocPrf Weight Path
* 128.107.0.0/19 10.1.1.5 0 0 100 i
*> 10.1.1.1 0 0 100 I
* 200.0.0.0 10.1.1.5 0 100 2 i
*> 10.1.1.1 0 100 2 i
# show ip bgp neighbors
BGP neighbor is 129.213.1.1, remote AS 200, external link BGP version 4, remote router ID 175.220.12.1 BGP state = Established, table version = 3, up for 0:10:59 Last read 0:00:29, hold time is 180, keepalive interval is 60 seconds Minimum time between advertisement runs is 30 seconds Received 2828 messages, 0 notifications, 0 in queue Sent 2826 messages, 0 notifications, 0 in queue Connections established 11; dropped 10

## Slide 65
Route injection or redistribution:
  BGP does not automatically inject any routes into the BGP table
  Learned via:
    Redistribute into IGP (ex: OSPF or EIGRP)
    Configure iBGP: subject to BGP synchronization rule
BGP synchronization rule states that a BGP router E1 should not advertise to external neighbors (ISP1) destinations (200.0.0.0) learned from inside BGP neighbors (E2) unless those destinations are also known via an IGP (OSPF).
See my BGP presentations for more information.
<number>

## Slide 66
Route selection and installation: BGP has a complex decision algorithm to compare paths received from different neighbors and select the best one for each prefix.
<number>

## Slide 67
Transmission of routing information to neighbors:
  Paths that are selected as best in the BGP table can be advertised to other BGP routers.
  Several rules, such as the one commonly referred to as IBGP split-horizon rule
  BGP Split Horizon Rule - Routes learned via IBGP peers are not propagated to other IBGP peers.
<number>

## Slide 68: BGP FSM
<number>
BGP FSM includes six states:
  Idle
  Connect
  Active
  OpenSent
  Open Confirm
  Established
Note: Curved arrows should show pointing back to the same state.
Notes: <number>

## Slide 69: Troubleshooting Example: Routing Problem in a BGP Network
<number>

## Slide 70
When a traceroute command is executed on router IRO1 to determine the path that is used to reach IP address 192.168.224.1, which belongs to an IP address block that is owned by ISP1
Traffic path goes through router IRO2
<number>

## Slide 71
The successful ping to ISP1’s access router verifies that the link between router IRO1 and ISP1 access router is operational at Layers 3 and below.
Need to find out why the direct path to Internet service provider 1 is not being used to route traffic to IP address 192.168.224.1.
There are two likely reasons:
  IRO1 has not learned about the prefix directly from ISP1 at all
  IRO1 router has learned about the route, but it “incorrectly” prefers the path through router IRO2
Let’s look at the routing table…
<number>

## Slide 72
Output shows that the route to network 192.168.224.0/19 is:
  The best match for destination IP address 192.168.224.1 and that this route is an internal BGP path and its source is the router with IP address 10.1.220.4, which is IRO2.
However, the IP routing table does not show if the path through IRO2 is used because:
  No other path is available, or
  The path through IRO2 was selected as the best path.
Need to look at the BGP table…
<number>

## Slide 73
Output shows that:
  The only the path through router IRO2 is present in the BGP table and (no other BGP learned paths are available)
  The path through IRO2 is the best (only) path
ISP1 is not present in the BGP table can have several different causes:
  ISP1 might not advertise the route
  ISP1 advertises it, but router IRO1 rejects or ignores the advertisement
  IRO1 and ISP1 have not successfully established a peering relationship and no routes have been exchanged at all
<number>

## Slide 74
Output reveals:
  IRO1 peering to IP address 10.1.220.4 (IRO2) has been established and 6 prefixes have been received from the neighbor
  But peering to IP address 192.168.224.244 is in the “Active” state.
This means that this router is trying to establish a TCP session to neighbor 192.168.224.244, but has not succeeded yet.
In the Active state, the BGP process is trying to initiate a TCP connection with the neighbor.
<number>

## Slide 75
Ping to the IP address 192.168.224.244 which is the configured neighbor address for ISP1 fails.
Two possible causes ping not succeeding:
  The IP address 192.168.224.244 is not the correct IP address and/or
  IP address 192.168.224.254 should have been used for the peering to ISP1 instead
Note: It is possible that we could ping ISP1 but still not able to establish a BGP peering because of something like a wrong AS in the neighbor statement.
<number>

## Slide 76
Change neighbor command to correct IP Address
Neighbor is now sending Prefixes to IRO1
New best path via ISP1
<number>

## Slide 77
Output shows that router IRO2 has received a path to 192.168.224.0/19 from router IRO1 and installed it in its BGP table.
IRO2 selects the path through (learned from) IRO1 as the best path to prefix 192.168.22.0/19 in AS 65525.
<number>

## Slide 78
Output confirms that the path through neighbor 192.168.224.254 (ISP1) has been installed in the routing table
The result of the traceroute command confirms this.
<number>

## Slide 79
To summarize, each routing protocol consists of the following elements and processes: (RIP is a notable exception to some of these.)
Reception of routing information from neighbors:
  Neighbor relationships
Routing protocol data structures:
  Neighbor table, topology table
Route injection or redistribution:
  Directly connected, dynamic routes, static routes
Route selection and installation:
  Best path, equal cost load balancing, unequal cost load balancing
Transmission of routing information to neighbors:
  Summarization, Broadcast, Multicast, LSAs, Route updates, ACKs
<number>

## Slide 80: CIS 188 CCNP TSHOOT (Troubleshooting) Ch. 5 Maintaining and Troubleshooting Routing Solutions
Rick Graziani
Cabrillo College
graziani@cabrillo.edu
Fall 2010
Notes: <number>