## Slide 1: Chapter 6: Troubleshooting Addressing Services
CCNP TSHOOT: Maintaining and Troubleshooting IP Networks
Notes: <number>
Cisco Networking Academy Program
CCNP TSHOOT: Maintaining and Troubleshooting IP Networks
Chapter 6: Troubleshooting Addressing Services

## Slide 2: Chapter 6 Objectives
Describe common issues related to NAT/PAT and DHCP.
Identify common IPv6 routing and tunneling issues.
Notes: <number>

## Slide 3: Common IPv4 Addressing Service Issues

## Slide 4: NAT/PAT Operation Review
Network Address Translation (NAT) was designed for IP version 4 (IPv4) address conservation.
Also used for address hiding, with security implications.
Usually operates at the border of a network and translates source address of exiting IP packets that are private addresses to public addresses before packets are forwarded out.
The packet header information and the corresponding translated IP address are kept in a NAT table.
NAT does the reverse for the destination address of the responding IP packets based on the content of the NAT table.
NAT can also be used to renumber global address space when switching between service providers.

## Slide 5: NAT/PAT Operation Review – Cont.
NAT operates at the border of the network and generally translates the source IP address of exiting packets and the destination IP address of incoming IP packets.
Notes: <number>

## Slide 6: NAT/PAT Operation Review – Cont.
Three main categories of NAT:
Static NAT:
  Inside local (locally significant) and inside global (globally significant) addresses are mapped one to one.
  Useful when an inside device must be accessible from the outside network (such as a web server).
  In troubleshooting, IP address changes might affect an existing static configuration.
Dynamic NAT:
  Translates addresses utilizing the same basic technology as static NAT.
  Local addresses are translated to a group or pool of global addresses.
  Issues can be related to the size of the global pool (requires one-to-one translation).
  Some inside hosts may not obtain a valid global address, causing connectivity problems.
  Subject to management, tracking, and audit issues due to the dynamic nature of the translation.
NAT overloading:
  Special type of dynamic NAT in which addresses are translated in a many-to-many fashion.
  Also known as PAT, or Port Address Translation, because global addresses can be reused.
  The differentiator for multiple inside local addresses sharing the same global address is a port number.
  NAT overloading suffers from some application support issues.
Notes: <number>

## Slide 7: NAT/PAT Operation Review – Cont.
Advantages and disadvantages of implementing NAT:
Advantages | Disadvantages
Conserves registered addresses | Translation introduces processing delays
Hides the actual address of internal hosts and services | Loss of end-to-end IP reachability
Increases flexibility when connecting to Internet | Certain applications will not function with NAT enabled
Eliminates address renumbering as the network changes from one ISP to another | Considerations are needed when working with VPNs

## Slide 8: Troubleshooting NAT/PAT Issues
Some important NAT issues and considerations to keep in mind are:
Diagrams for the NAT configuration are helpful and should be a standard practice.
Do not start configuring without a diagram that shows or explains each item involved.
ACLs are used to tell the NAT device "what source IP addresses are to be translated“
IP NAT pools are used to specify "to what those addresses translate", as packets go from IP NAT inside to IP NAT outside.
Marking the IP NAT inside interfaces and the IP NAT outside interfaces correctly is important.
NAT packets still have to obey routing protocols and reachability rules.
Make sure that every router knows how to reach the desired destinations.
Make sure the public addresses to which addresses translate are advertised to the outside neighbors and autonomous systems.
Notes: <number>

## Slide 9: Troubleshooting NAT/PAT Issues – Cont.
The following commands can help determine if NAT is functioning correctly:
clear ip nat translation:
  Removes NAT entries from the NAT table.
  Specific entries can cleared with additional parameters.
  Clearing all translations can cause disruption until new translations are re-created.
show ip nat translations:
  Displays all the translations (static and dynamic) that are currently installed and active on the router.
show ip nat statistics:
  Displays NAT statistics such as number of translations (static, dynamic, extended), number of expired translations, number of hits (match), number of misses (no match).
Notes: <number>

## Slide 10: Troubleshooting NAT/PAT Issues – Cont.
Helpful NAT-related debug commands:
debug ip nat:
  Displays information about each packet that the router translates.
debug ip nat detailed:
  Generates a description of each packet considered for translation.
  Also displays information about certain errors or exception conditions, such as the failure to allocate a global address.
debug ip packet [access-list]:
  Displays general IP debugging information and IP security option (IPSO) security transactions.
  If a communication session is closing when it should not be, an end-to-end connection problem can be the cause.
  Useful for analyzing messages traveling between the local and remote hosts.
  Captures packets that are process switched including received, generated, and forwarded packets.
  IP packets that are switched in the fast path are not captured.
  The access-list option allows you to narrow down the scope of debugging.
Notes: An access list can be used to narrow down the scope of the debug ip packet and filter the output to what the access permits. Some commands do not have the access list option.
<number>

## Slide 11: Troubleshooting NAT/PAT Issues – Cont.
Limiting debug output with the debug condition command:
debug condition interface interface:
  Called conditionally triggered debugging.
  Generates debugging messages for packets entering or leaving on the specified interface.
  Will not generate debugging output for packets for a different interface.
  First define the condition with the debug condition command. For example, define a condition of interface serial 0/0.
  This definition means that all debug output will be limited to that particular interface.
  The condition remains defined and applied until it is removed.
  Check the active debug conditions using the show debug condition command.
Notes: A more recent approach is to use conditionally triggered debugs.
To use conditional debug, first define your condition with the debug condition command. For example, we can define a condition of interface serial 0/0 by typing debug condition interface serial 0/0.
This definition means that all debug output will be limited to that particular interface. The condition remains there until it is removed.
You can check the active debug conditions using the show debug condition command.
<number>

## Slide 12: NAT/PAT Troubleshooting Example 1: Routing Issue
Router R1 can ping R4, but router R1 cannot ping R3.
There are no routing protocols running in any of the routers.
R1 uses R2 as its gateway of last resort.
The objective is to restore end-to-end connectivity from R1 to all destinations.

## Slide 13: NAT/PAT Troubleshooting Example 1 – Cont.
R2# sh ip nat statistics
Total active translations: 1 (1 static, 0 dynamic, 0 extended)
Outside interfaces:
FastEthernet0/1, Serial0/1/0
Inside interfaces:
FastEthernet0/0
Hits: 39 Misses: 6
CEF Translated packets: 45, CEF Punted packets: 49
Expired translations: 6
Dynamic mappings:
-- Inside Source
[Id: 1] access-list 10 pool NAT_OUT refcount 0
pool NAT_OUT: netmask 255.255.255.0
start 172.16.6.129 end 172.16.6.240
type generic, total addresses 112, allocated 0 (0%), misses 0
Appl doors: 0
Normal doors: 0
Queued Packets: 0
Notes: In the example output, the outside and inside NAT interfaces are listed per R2's current configuration: Fa0/0 is correctly configured as inside interface, while S0/1/0 and Fa0/1 are correctly configured as outside interfaces.
Notice that this command also shows the full NAT configuration. In this instance, we have both dynamic and static NAT configured. The only indication that there are static translations configured is the reference to “1 static” in the “Total active translations” line.
In order to see the static translation, the show ip nat translations command is used.
<number>

## Slide 14: NAT/PAT Troubleshooting Example 1 – Cont.
R2# sh ip nat translations
Pro Inside global Inside local Outside local Outside global
--- 172.16.6.1 10.10.10.1 --- ---
Notes: The only entry in the NAT translation table is the static translation for 10.10.10.1 into 172.16.6.1. The address 10.10.10.1 is the IP address of R1's Fa0/0 interface.
This translation may be causing the problem. Typical issues with static translations occur when there is no route back to the statically translated address, or when the statically selected global address overlaps with an available address in the dynamic address pool.
<number>

## Slide 15: NAT/PAT Troubleshooting Example 1 – Cont.
R3# debug ip icmp
ICMP packet debugging is on
R1# ping 172.16.11.3
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 172.16.11.3, timeout is 2 seconds:
.....
Success rate is 0 percent (0/5)
R3#
*Aug 23 13:54:00.556: ICMP: echo reply sent, src 172.16.11.3, dst 172.16.6.1
*Aug 23 13:54:02.552: ICMP: echo reply sent, src 172.16.11.3, dst 172.16.6.1
*Aug 23 13:54:04.552: ICMP: echo reply sent, src 172.16.11.3, dst 172.16.6.1
*Aug 23 13:54:06.552: ICMP: echo reply sent, src 172.16.11.3, dst 172.16.6.1
*Aug 23 13:54:07.552: ICMP: echo reply sent, src 172.16.11.3, dst 172.16.6.1
Notes: As the next step, verify whether packets leaving R1 actually reach R3 or not. This can help us discover if the problem is with NAT or if it is a routing problem.
In order to find out if packets reach R3 and do not return, or if they never reach R3, use icmp debugging on R3 with the debug ip icmp command.
Next, we ping R3 from R1 and observe the out of the debug on R3.
Based on the output of the debug ip icmp command shown, the icmp echo requests reach R3, but R3’s icmp echo replies do not reach R1.
<number>

## Slide 16: NAT/PAT Troubleshooting Example: – Cont.
R3# show ip route 172.16.6.0 255.255.255.0
% Subnet not in table
R3# configure terminal
R3(config)# ip route 172.16.6.0 255.255.255.0 172.16.11.2
R3(config)# exit
R1# ping 172.16.11.3
Type escape sequence to abort.
Sending 5, 100-byte ICMP Echos to 172.16.11.3, timeout is 2 seconds:
!!!!!
Success rate is 100 percent (5/5), round-trip min/avg/max = 1/2/4 ms
R1#
Notes: The NAT translation is working but there is a routing issue on R3 toward the 172.16.6.0 destination. This is verified using the show ip route command on R3.
Because there are no routing protocols in use, the routing problem can only be fixed by entering a static route in R3’s routing table, so that it sends packets destined to 172.16.6.0/24 to R2; this is done and shown in the example.
Following the addition of the static route to R3’s routing table, we can check to see if the connectivity problem between R1 and R3 has been corrected. The ping result from R1 to R3 is shown in the output of the example.
The source of problem was discovered and corrected. The problem was not directly a NAT problem; it was a routing issue. When NAT is deployed, a set of inside local addresses are normally translated to a set of inside global addresses. The inside global addresses may not be assigned to any physical networks, yet they need to be advertised so that outside devices know about those addresses and know how to forward packets to those networks.
<number>

## Slide 17
Reviewing DHCP Operation

## Slide 18: DHCP Overview
DHCP is a client-server protocol. The DHCP client acquires IP configuration parameters such as IP address, subnet mask, and default gateway, from a DHCP server.
The DHCP server is typically centrally located and operated by the network administrator.
The DHCP client initially does not have an IP configuration and must find a DHCP server to obtain its IP configuration based on broadcast communication.
Most enterprise networks are divided into subnets. Each subnet usually maps to a virtual LAN (VLAN) and routers or multilayer switches route between the subnets.
Because routers do not pass broadcasts by default, a DHCP server would be needed on each subnet.
To address this issue, a router interface can be configured with a feature called DHCP Relay Agent, using the ip helper-address server-address command.
When configured with this command, the router interface will forward client DHCP messages to the configured server-address. When the server sends its reply back to the router interface, the router interface forwards it to the client subnet.

## Slide 19: DHCP Overview: Client–Server Communication
Notes: The client starts with a DHCP DISCOVER message with the source IP address 0.0.0.0; this address is referred to as the alien address.
One or more servers reply with a DHCP OFFER.
The client responds, typically to the first offer, using the DHCP REQUEST message. Multiple offer messages could be sent, but only one will be accepted by the client, indicated by the request message.
The request message is a broadcast, and reaches all offering servers. The servers whose offers are not selected withdraw their offer by putting the offered IP address back into the pool of available addresses.
The selected server responds with a DHCP ACK, and confirms the transaction by delivering all configured parameters.
<number>

## Slide 20: DHCP Overview: Client–Server Communication – DHCP Packets (Message Types)
Packet Type | Description
DHCP discover | Client looking for available DHCP servers. It is a UDP broadcast (source port is 68, and the destination port is 67).
DHCP offer | This is the server’s response to the client’s discover message. This is also a UDP broadcast (source port is 67, and the destination port is 68).
DHCP request | This is client’s response to one specific DHCP offer.
DHCP decline | Client-to-server communication, indicating that the IP address is already in use.
DHCP ack | Server-to-client communication. This is the server’s response to a client request. This message includes all configuration parameters.
DHCP nack | Server-to-client communication. This is the server’s negative response to a client’s request, indicating the original offer is no longer available.
DHCP release | Client-to-server communication. The client relinquishes its IP address and other parameters.
DHCP inform | Client-to-server communication. Using this message, the client asks for local configuration parameters such as DNS server’s IP address, but it has its IP address externally configured.
Notes: The table lists various DHCP packets (message types) involved in DHCP transactions, some issued by servers, and some issued by clients.
<number>

## Slide 21: Common DHCP Troubleshooting Issues: Three DHCP Roles a Router May Take
Notes: In branch office scenarios, it is typical to have Cisco IOS routers or firewalls acting as the DHCP server. In that case, troubleshooting DHCP is critical because it will affect the operations of all hosts in the branch, including IP phones and video devices.
In some other scenarios, the routers may act as DHCP clients. An example of that is a branch or home office router using broadband connectivity such as DSL or cable and obtaining IP address and IP parameters from the service provider's DHCP server.
The router may also act as a broker for DHCP transactions, located in the path of DHCP requests. This is a typical scenario in networks where DHCP servers are centralized and serve multiple network segment and the router acts as a DHCP relay agent.
In all three scenarios, typical DHCP issues can come from multiple sources. It is crucial to apply a structured troubleshooting method and to know the inner workings of the protocol.
<number>

## Slide 22: DHCP Troubleshooting Issues – Cont.
Configuration issues can result in many symptoms:
  Clients not obtaining IP information from the server
  Client requests not reaching the server across a DHCP relay agent
  Clients failing to obtain DHCP options and extensions
Address pool issues:
  Poor capacity planning and security issues might result in DHCP scope exhaustion.
  When using static and dynamic IP address assignments, an IP address that is already in use can be granted.
  Multiple DHCP servers, or even rogue DHCP servers can result in duplicate IP addresses
  assigned to hosts.
Management issues:
  Due to the “pull” nature of DHCP.
  There are no provisions in the protocol to allow the DHCP server to push configuration parameters or control messages to DHCP clients.
  A good example, with critical implications in IP address renumbering, is that IP addresses must be renewed from the client side. There is no server-side, push-type renewal process.
  This means that during renumbering, all clients would need to reboot or manually renew their IP addresses. Otherwise, you need to wait until the clients leases expire, which might not be a viable option.

## Slide 23: DHCP Troubleshooting Issues: DHCP Relay Agent
The Cisco IOS command that makes a router a DHCP relay agent is ip helper-address.
This is an interface configuration command that makes the router forward the BootP/DHCP requests from clients to the DHCP server.
If the DHCP server's IP address changes, all interfaces of all routers must be reconfigured with the new IP helper-address (DHCP server's new IP address).
Enabling a router interface with the ip helper-address command makes the interface forward UDP broadcasts for six protocols (not just DHCP) to the IP address configured using the ip helper-address command.
  TFTP (port 69)
  DNS (port 53)
  Time Service (port 37)
  NetBIOS Name Service and Datagram Service (ports 137 and 138)
  TACACS (port 49)
  DHCP/BOOTP Client and Server (ports 67 and 68)
If other protocols do not require this service, forwarding their requests must be disabled manually on all routers using the Cisco IOS no ip forward-protocol udp port-number command in global configuration mode.
Notes: <number>

## Slide 24: DHCP Troubleshooting Issues: DHCP Parameters and Options
DHCP Option | Code | Description
Subnet Mask | 1 | Specifies the subnet mask for the client to use (as per RFC 950)
Router | 3 | The list of routers the client can use (usually, in order of preference)
Domain Name Server | 6 | The list of DNS servers the client can use (usually, in order of preference)
ARP Cache Timeout | 35 | Specifies the timeout (seconds) for ARP cache entries
IP Address Lease Time | 51 | Specifies the period over which the IP address is leased (it must be renewed)
Relay Agent Information | 82 | Information about the port from which the DHCP request originates
TFTP Server IP Address | 150 | Typically used by devices such as IP Phones to download their configuration files
Notes: DHCP troubleshooting includes vendor-specific and function-specific DHCP options.
DHCP options have historically been an integral part of the protocol, because they are
used to deliver parameters in addition to the traditional IP address, subnet mask, default
gateway, and DNS server address.
Some options aim at tuning the DHCP operation, or even the TCP/IP operation.
Some DHCP options are required for certain other protocols or applications to function
properly.
The table lists some important DHCP configured parameters and options.
<number>

## Slide 25: DHCP Troubleshooting Issues
Troubleshooting can be related to DHCP security efforts.
Automatic addressing is accomplished through DHCP.
Security is accomplished through DHCP snooping.
Some specific issues related to DHCP snooping:
  Improper configuration of the DHCP snooping trust boundaries
  Failure to configure DHCP snooping on certain VLANs
  Improper configuration of the DHCP snooping rate limits
  Performance degradation
Poor planning of DHCP snooping can result in DHCP transactions being blocked or affected.

## Slide 26: DHCP Troubleshooting Issues – Cont.
DHCP troubleshooting questions to ask:
Where are the DHCP servers and clients located?
Are DHCP relay agents configured?
What are the DHCP pool sizes? Are they sufficient?
Are there any DHCP option compatibility issues?
Are there any ACLs or firewalls filtering UDP port 67 or UDP port 68?
Are there any active DHCP DoS attacks?
Is forwarding disabled on the router acting as DHCP Relay Agent for any UDP ports (using the Cisco IOS no ip forward-protocol udp port command)?
Is the ip helper-address command applied to correct router interfaces?
Is DHCP snooping configured?

## Slide 27: DHCP Troubleshooting Commands
show ip dhcp server statistics: Displays counts for server statistics and messages sent and received for an IOS-based DHCP server.
show ip dhcp binding: Displays DHCP binding information for IP address assignment and subnet allocation.
show ip dhcp conflict: Displays address conflicts found by a Cisco IOS DHCP server when addresses are offered to the client.
show ip dhcp pool name: Displays the subnets allocated and the current utilization level for the pool or all the pools if the name argument is not used.
show ip dhcp database: Displays server database agent information:
  URL: Specifies the remote file used to store automatic DHCP bindings
  Read/written: The last date and time bindings were read/written from the file
  server
  Status: Indication of whether the last read or write of host bindings was successful
  Delay: The amount of time (in seconds) to wait before updating the database
  Timeout: The amount of time (in seconds) before the file transfer is aborted
  Failures/Successes: The number of failed/successful file transfers
Notes: show ip dhcp conflict: Displays address conflicts found by a Cisco IOS DHCP server when addresses are offered to the client. The server uses ping to detect conflicts. The client uses gratuitous ARP to detect clients. If an address conflict is detected, the address is removed from the pool and the address is not assigned until an administrator resolves the conflict.
<number>

## Slide 28: DHCP Troubleshooting Commands – Cont.
debug ip udp:
  Displays UDP packets sent and received.
  Can use considerable CPU cycles on the device.
debug ip dhcp server [packets | events]:
  Enables DHCP server debugging.
  The events option reports server events such as address assignments and database updates.
  The packets option decodes DHCP receptions and transmissions.
clear ip dhcp binding {* | address}:
  Deletes an address binding from the DHCP server database.
  The address denotes the IP address of the client.
  If the asterisk (*) character is used as the address parameter, DHCP clears all automatic bindings.
clear ip dhcp conflict {* | address}:
  Clears an address conflict for a specific entry with the address option.
  Clears all address conflicts with the asterisk (*) option.
Notes: <number>

## Slide 29: DHCP Troubleshooting Example 1: Problems After a Security Audit
Router R1 provides DHCP services to clients in the 10.1.1.0 subnet.
The DHCP clients are R2 and R3.
A security audit has been recently performed in router R1.
It is reported that R1 is no longer providing reliable DHCP services.
The clients are unable to renew their IP addresses.
Notes: Note: In the example, routers R2 and R3 are configured as DHCP clients to demonstrate how a Cisco router can be a DHCP server or client. More commonly, DHCP clients are end user devices such as PCs and IP phones.
<number>

## Slide 30: DHCP Troubleshooting Example 1 – Cont.
R2# show ip int brief
Interface IP-Address OK? Method Status Protocol
FastEthernet0/0 unassigned YES DHCP up up
FastEthernet0/1 unassigned YES NVRAM administratively down down
Serial0/0/0 unassigned YES NVRAM administratively down down
Serial0/0/1 unassigned YES NVRAM administratively down down
R3# show ip int brief
Interface IP-Address OK? Method Status Protocol
FastEthernet0/0 unassigned YES DHCP up up
FastEthernet0/1 unassigned YES NVRAM administratively down down
Serial0/0/0 unassigned YES NVRAM administratively down down
Serial0/0/1 unassigned YES NVRAM administratively down down
Notes: As the first step, determine if the problem affects all clients in the LAN, or if only specific clients.
Check R2 and R3 to make sure they are configured as a DHCP clients. The output of the show ip interfaces brief command shows that interface Fa0/0 on both routers is configured as a DHCP client and it shows an “unassigned” IP address.
Because multiple clients are having the same problem, it is reasonable to suspect the problem originates elsewhere. We can check the configuration of the DHCP server next.
<number>

## Slide 31: DHCP Troubleshooting Example 1 – Cont.
R3# debug dhcp detail
DHCP client activity debugging is on (detailed)
R3#
*Aug 23 17:32:37.107: Retry count: 1 Client-ID: cisco-0019.5592.a442-Fa0/0
*Aug 23 17:32:37.107: Client-ID hex dump: 636973636F2D303031392E353539322E
*Aug 23 17:32:37.107: 613434322D4551302F30
*Aug 23 17:32:37.107: Hostname: R3
*Aug 23 17:32:37.107: DHCP: SDiscover: sending 291 byte length DHCP packet
*Aug 23 17:32:37.107: DHCP: SDiscover 291 bytes
*Aug 23 17:32:37.107: B cast on FastEthernet0/0 interface from 0.0.0.0
*Aug 23 17:32:40.395: DHCP: SDiscover attempt #2 for entry:
*Aug 23 17:32:40.395: Temp IP addr: 0.0.0.0 for peer on Interface: FastEthernet0/0
*Aug 23 17:32:40.395: Temp sub net mask: 0.0.0.0
*Aug 23 17:32:40.395: DHCP Lease server: 0.0.0.0, state: 1 Selecting
*Aug 23 17:32:40.395: DHCP transaction id: 13BA
*Aug 23 17:32:40.395: Lease: 0 secs, Renewal: 0 secs, Rebind: 0 secs
*Aug 23 17:32:40.395: Next timer fires after: 00:00:04
*Aug 23 17:32:40.395: Retry count: 2 Client-ID: cisco-0019.5592.a442-Fa0/0
*Aug 23 17:32:40.395: Client-ID hex dump: 636973636F2D303031392E353539322E
*Aug 23 17:32:40.395: 613434322D4551302F30
<output omitted>
*Aug 23 17:32:44.395: Hostname: R3
*Aug 23 17:32:44.395: DHCP: SDiscover: sending 291 byte length DHCP packet
*Aug 23 17:32:44.395: DHCP: SDiscover 291 bytes
*Aug 23 17:32:44.395: B cast on FastEthernet0/0 interface from 0.0.0.0
*Aug 23 17:32:48.395: DHCP: Qscan: Timed out Selecting state
%Unknown DHCP problem... No allocation possible
*Aug 23 17:32:57.587: DHCP: waiting for 60 seconds on interface FastEthernet0/0
Notes: To investigate the interaction between the clients and server, check whether the clients are issuing DHCP discovery messages.
The debug dhcp detail command on R3 reveals that DHCP discovery messages are generated out of interface Fa0/0, but no DHCP offers are received from the DHCP server.
Also, this client is making multiple requests, and after three attempts, it times out with the Timed out selecting state message, followed by No allocation possible.
Using the same debug command on the second client, R2, provides the same results.
<number>

## Slide 32: DHCP Troubleshooting Example 1 – Cont.
R1# show ip int brief
Interface IP-Address OK? Method Status Protocol
FastEthernet0/0 10.1.1.1 YES manual up up
FastEthernet0/1 unassigned YES NVRAM administratively down down
Serial0/0/0 unassigned YES NVRAM administratively down down
Serial0/0/1 unassigned YES NVRAM administratively down down
Notes: Next, check router R1, the DHCP server.
Apply a bottom-up approach and use the show ip int brief command to verify that Layers 1 and 2 are operational on the documented DHCP server.
R1's Fa0/0 interface is UP, with the IP address 10.1.1.1/24.
<number>

## Slide 33: DHCP Troubleshooting Example 1 – Cont.
R1# show ip dhcp server statistics
Memory usage 9106
Address pools 1
Database agents 0
Automatic bindings 0
Manual bindings 0
Expired bindings 0
Malformed messages 0
Secure arp entries 0
Message Received
BOOTREQUEST 0
DHCPDISCOVER 1
DHCPREQUEST 1
DHCPDECLINE 0
DHCPRELEASE 0
DHCPINFORM 0
Message Semt
BOOTREPLY 0
DHCPOFFER 1
DHCPACK 1
DHCPNAK 0
R1# sh ip dhcp pool
Pool vlan10 :
Utilization mark (high/low) : 100/0
Subnet size (first/next) : 0/0
Total addresses : 254
Leased addresses : 0
Pending event : none
1 subnet is currently in the pool :
Current index IP address range Leased addresses
10.1.1.12 10.1.1.1 -10.1.1.254 0
Notes: Next, check the DHCP server information.
The command show ip dhcp server statistics displays useful counters. Changes on those counters are a signal of good operation.
The output of this command on R1 shows one address pool configured as part of the service and very few DHCP messages sent and received. So it is not very active.
Verify the address pool (scope) configuration to detemine if it is either misconfigured or exhausted, using the show ip dhcp pool command.
The results show one address pool, vlan10. The number of leased addresses is 0, meaning that there are no leased addresses. There 254 addresses in this pool, but none are allocated at the moment.
Both the DHCP server and the DHCP clients have the correct configurations, and are operationally UP at physical and data-link layers.
<number>

## Slide 34: DHCP Troubleshooting Example 1 – Cont.
R1# show ip sockets
Proto Remote Port Local Port In Out Stat TTY OutputIF
88 --listen-- 10.1.1.1 10 0 0 0 0
17 --listen-- 10.1.1.1 161 0 0 1001 0
17 --listen-- 10.1.1.1 162 0 0 1011 0
17 --listen-- 10.1.1.1 57767 0 0 1011 0
17 --listen-- --any-- 161 0 0 20001 0
17 --listen-- --any-- 162 0 0 20011 0
17 --listen-- --any-- 60739 0 0 20011 0
R1#
Note: There is no entry for UDP port 67 (DHCP server)
Notes: The show ip socket on R1 shows that port 67 is now an active port.
Note: The show ip sockets command has been replaced by the show udp and show sockets commands as of Cisco IOS Software Release 12.4(11)T.
<number>

## Slide 35: DHCP Troubleshooting Example 1 – Cont.
R1# conf t
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)# service dhcp
R1(config)# end
R1#
R1# show ip sockets
Proto Remote Port Local Port In Out Stat TTY OutputIF
88 --listen-- 10.1.1.1 10 0 0 0 0
17 --listen-- 10.1.1.1 161 0 0 1001 0
17 --listen-- 10.1.1.1 162 0 0 1011 0
17 --listen-- 10.1.1.1 57767 0 0 1011 0
17 --listen-- --any-- 161 0 0 20001 0
17 --listen-- --any-- 162 0 0 20011 0
17 --listen-- --any-- 60739 0 0 20011 0
17 0.0.0.0 0 10.1.1.1 67 0 0 2211 0
R1#
Notes: <number>

## Slide 36: DHCP Troubleshooting Example 2: Duplicate Client IP Addresses
In this scenario, the IP address of router R1 Fa0/0 was previously 10.1.1.100.
It has been changed to 10.1.1.1 to comply with a new network policy. This policy states that all branch routers will have the first IP address on any subnet
After the change, some DHCP clients are reporting duplicated IP addresses. Users state that this happens sporadically, a few times a week.
Notes: Note: In the previous scenario the IP address of R1 Fa0/0 was 10.1.1.1 but assume it was 10.1.1.100 for the purposes of this scenario.
<number>

## Slide 37: DHCP Troubleshooting Example 2 – Cont.
R1# show running-config | beg ip dhcp pool
ip dhcp pool vlan10
network 10.1.1.0 255.255.255.0
default-router 10.1.1.1
lease 3
Notes: The change in IP address happened at the router acting as the DHCP server (R1).
The IP address duplication happens sporadically, and one host at a time.
Check the lease times to see whether they match the frequency of the symptoms.
If the lease time of a Cisco IOS DHCP server is set to default values, there is no command to display it.
If it has been changed you can use the show running-config | begin ip dhcp pool command to see the DHCP parameters configured.
The output of this command in the example shows the vlan10 DHCP pool with a lease time of 3 days.
The DHCP pool seems to be correct.
<number>

## Slide 38: DHCP Troubleshooting Example 2 – Cont.
R1# show ip dhcp conflict
IP address Detection method Detection time VRF
10.1.1.1 Gratuitous ARP Aug 23 2009 06:28 PM
10.1.1.3 Gratuitous ARP Aug 23 2009 06:29 PM
10.1.1.3 Gratuitous ARP Aug 23 2009 06:29 PM
10.1.1.4 Gratuitous ARP Aug 23 2009 06:29 PM
10.1.1.5 Gratuitous ARP Aug 23 2009 06:29 PM
10.1.1.6 Gratuitous ARP Aug 23 2009 06:29 PM
10.1.1.7 Gratuitous ARP Aug 23 2009 06:29 PM
10.1.1.8 Gratuitous ARP Aug 23 2009 06:29 PM
10.1.1.9 Gratuitous ARP Aug 23 2009 06:29 PM
10.1.1.10 Gratuitous ARP Aug 23 2009 06:29 PM
10.1.1.11 Gratuitous ARP Aug 23 2009 06:29 PM
10.1.1.12 Gratuitous ARP Aug 23 2009 06:29 PM
10.1.1.13 Gratuitous ARP Aug 23 2009 06:29 PM
--More--
Notes: Based on the reported symptoms, check whether there are statically assigned IP addresses conflicting with some of the addresses that are being delivered to the clients as part of the DHCP dynamic address pool.
The show ip dhcp conflict command verifies whether the DHCP server has found overlap or duplication in the IP addresses that it has assigned, as shows in the example.
One of the many conflicting addresses is 10.1.1.1, which is the new IP address of router R1 (the DHCP server itself) on interface Fa0/0.
Note: The DHCP server will not provide its own IP address to its clients.
<number>

## Slide 39: DHCP Troubleshooting Example 2 – Cont.
R1# sh run | inc excluded
ip dhcp excluded-address 10.1.1.100
R1#
Notes: Many devices such as servers and printers have static ip addresses.
If their addresses are not excluded from the dhcp dynamic pool, there will be conflict problems.
To check and verify which IP addresses are being excluded on R1, the dhcp server, use the show running | include excluded command.
As shown in the output, the only ip address excluded from the dhcp dynamic pool is 10.1.1.100, which is R1’s old address.
The static addresses assigned to devices such as printers and servers are not excluded and are handed out to dhcp clients, resulting in address conflicts.
<number>

## Slide 40: DHCP Troubleshooting Example 2 – Cont.
R1# conf t
Enter configuration commands, one per line. End with CNTL/Z.
R1(config)# no ip dhcp excluded-address 10.1.1.100
R1(config)# ip dhcp excluded-address 10.1.1.1 10.1.1.20
R1(config)# end
R1#
Note: Configure R1 to exclude the range of addresses that are to be reserved for static assignment.
Notes: To correct the R1 configuration, put the 10.1.1.100 address back in the pool, because it need not be excluded any more.
Also exclude the range of addresses that are meant to be statically assigned.
This range is 10.1.1.1 to 10.1.1.20.
Note: To ensure that the users will receive unique addresses from the DHCP server and will not incur any more address conflicts, renew IP address leases on all DHCP clients, especially those that have experienced conflicts before.
<number>

## Slide 41: DHCP Troubleshooting Example 3: Relay Agent Issue
R4 is a centrally located DHCP server.
The DHCP clients in network segment 10.1.1.0 are unable to obtain IP address and other parameters.
R2 is a DHCP client that is having trouble acquiring ip address.
R1 is supposed to act as a relay agent and forward DHCP messages between local clients and the DHCP server (R4).
Notes: Based on the symptoms and the network topology, there are several possible causes:
The clients could be misconfigured or faulty.
The relay agent could be not configured or misconfigured.
The server could be misconfigured or exhausted (or faulty/disabled)
There could be network problems or filtering/security barriers.
<number>

## Slide 42: DHCP Troubleshooting Example 3 – Cont.
R1# debug ip udp
UDP packet debugging is on
R1#
R1#
*Aug 23 19:01:05.303: UDP: rcvd src-0.0.0.0(68), dst=255.255.255.255(67),
length=584
*Aug 23 19:01:05.303: UDP: broadcast packet dropped, src=0.0.0.0,
dst=192.168.1.255
*Aug 23 19:01:08.911: UDP: rcvd src-0.0.0.0(68), dst=255.255.255.255(67),
length=584
*Aug 23 19:01:08.911: UDP: broadcast packet dropped, src=0.0.0.0,
dst=192.168.1.255
*Aug 23 19:01:12.911: UDP: rcvd src-0.0.0.0(68), dst=255.255.255.255(67),
length=584
*Aug 23 19:01:12.911: UDP: broadcast packet dropped, src=0.0.0.0,
dst=192.168.1.255
<output omitted>
Notes: It is simple to check the relay agent. If there is no problem with the relay agent, check the DHCP server.
A quick way to verify DHCP relay agent operations is to use the debug ip udp command on R1
As can be seen from the output R1 is receiving DHCP requests (from R2).
The UDP/IP packets shown have a source address of 0.0.0.0, destination address of 255.255.255.255 with source UDP port of 68 (DHCP client) and destination UDP port of 67 (DHCP server).
<number>

## Slide 43: DHCP Troubleshooting Example 3 – Cont.
R1(config)# int fa0/0
R1(config-if)# ip helper-address 192.168.1.4
R1(config-if)# end
Note: Configure R1 with a helper address to forward DHCP requests to R4.
Notes: The problem could be that the R1 Fa0/0 interface facing the DHCP client is missing the ip helper-address command pointing to 192.168.1.4.
Checking the configuration reveals that this command is missing and needs to be added as shown.
<number>

## Slide 44: DHCP Troubleshooting Example 3 – Cont.
R4# debug ip udp
UDP packet debugging is on
R4#
*Aug 23 19:31:39.303: UDP: sent src=0.0.0.0(67), dst=255.255.255.255(68),length=308
*Aug 23 19:31:39.303: UDP: rcvd src=0.0.0.0(68), dst=255.255.255.255(67),length=584
*Aug 23 19:31:39.303: UDP: sent src=0.0.0.0(67), dst=255.255.255.255(68),length=308
*Aug 23 19:31:40.159: UDP: rcvd src=0.0.0.0(68), dst=192.168.1.4(67), length=584
*Aug 23 19:31:44.159: UDP: rcvd src=0.0.0.0(68), dst=192.168.1.4(67), length=584
*Aug 23 19:31:46.307: UDP: rcvd src=10.1.1.11(53470), dst=255.255.255.255(69),length=30
*Aug 23 19:31:49.307: UDP: rcvd src=10.1.1.11(53470), dst=255.255.255.255(69),length=30
<output omitted>
*Aug 23 19:32:28.439: UDP: rcvd src=10.1.1.11(53470), dst=255.255.255.255(69),length=29
*Aug 23 19:32:31.439: UDP: rcvd src=10.1.1.11(53470), dst=255.255.255.255(69),length=29
*Aug 23 19:32:35.439: UDP: rcvd src=10.1.1.11(53470), dst=255.255.255.255(69),length=29
*Aug 23 19:32:37.011: UDP: rcvd src=0.0.0.0(68), dst=192.168.1.4(67), length=584
Notes: debug ip udp on R4 shows DHCP requests are being forwarded by R1.
Finally, you verify that DHCP clients, such as R2, in the 10.1.1.0 subnet, are acquiring IP address and other parameters from the DHCP server.
<number>