## Slide 1: CIS 188 CCNP TSHOOT Ch. 2: Troubleshooting Processes for Complex Enterprise Networks
Rick Graziani
Cabrillo College
graziani@cabrillo.edu
Fall 2010
Notes: <number>

## Slide 2: Troubleshooting Principles
Troubleshooting is the process that leads to the diagnosis and, if possible, resolution of a problem.
Usually triggered when a person reports a problem.
Networks usually work great until you start connecting computers to it.
Many of these principles apply to many areas of IT, not just networking.
    Systems analysis
    Desktop support
<number>

## Slide 3: Troubleshooting Principles
First step: Define the problem.
Second step: Diagnosing the problem
Eventually this process should lead to a hypothesis for the root cause of the problem
<number>
Diagnosis

## Slide 4: Troubleshooting Principles
Gathering information: Interviewing all parties (user) involved and any other means to gather relevant information.
Analyzing information: Comparing the symptoms against your knowledge of the system, processes, and baselines.
  Separate normal behavior from abnormal behavior.
Eliminating possible causes: By analyzing information possible problem causes are eliminated.
Formulating a hypothesis: one or more potential problem causes remain
  Each potential problem is assessed and the most likely cause proposed as the hypothetical cause of the problem.
Testing the hypothesis: Proposing a solution based on this hypothesis, implementing that solution and verifying if this solved the problem.
<number>
Diagnosis

## Slide 5: Ad Hoc Method
Ad Hoc is a non-structured approach.
More of a random approach.
Let’s try this…
Disadvantages
  Very inefficient.
  Handing the job over to someone else is very hard to do
<number>

## Slide 6: Shoot-from-the-hip Method
Commonly deployed both by inexperienced and experienced network engineers
May seem like random troubleshooting on the surface, it is not.
Guiding principle for this method is:
  Knowledge of common symptoms and their corresponding causes
  Or simply extensive relevant experience
<number>

## Slide 7: Structured Troubleshooting Approaches
Commonly use approaches:
  Top-down
  Bottom-up
  Divide and conquer
  Follow-the-path
  Spot the differences
  Move the problem
Different situations mean different approaches
Sometimes you will use one approach to narrow down the problem then switch to a different approach to solve it.
  Follow the path to find the bad router
  Spot the differences to find the problem
<number>

## Slide 8: Top-Down Troubleshooting Method
Starts with the client.
Uses OSI Model starting at the Application Layer
Problem: User at Branch Office using Outlook can’t access Mail server at Central Office.
  Is this an application issue? Can users ping, telnet or HTTP outside the branch?
  Can they access the Mail server using their Web interface?
    If they can’t then it’s most likely not an application issue.
    If it is, look at their Outlook configuration.
  Can they telnet to a Central Office server (TCP)?
  Is port 25 blocked by the branch or elsewhere?
<number>

## Slide 9: Bottom-Up Troubleshooting Method
Starts with the network.
Uses OSI Model starting at the Physical Layer
A benefit of this method is that all of the initial troubleshooting takes place on the network.
So access to clients, servers, or applications is not necessary until a very late stage in the troubleshooting process.
<number>

## Slide 10: Divide-and-Conquer Troubleshooting Method
Highly effective approach.
Usually faster elimination of potential problems the top-down or bottom-up.
Example: Start with a ping and go from there.
  Doesn’t work check firewall (blocking ICMP), IP addressing, data link layer, physical layer.
  Does work check firewall (port blocking), IP fragmentation, TCP issues, application issues.
<number>

## Slide 11: Follow-the-Path Troubleshooting Method
Discovers the actual traffic path all the way from source to destination.
Next, the scope of troubleshooting is reduced to just the links and devices that are actually in the forwarding path.
The principle of this approach is to eliminate the links and devices that are irrelevant to the troubleshooting task at hand.
<number>

## Slide 12: Spot-the-Differences Troubleshooting Method
Comparing working and non-working situations and spotting significant differences:
  Configurations
  Software versions
  Hardware or other device properties
  Links
  Processes
Problem is that it might lead to a working situation, without clearly revealing the root cause of the problem
Helpful when are lacking in some area of expertise. (And we all are!)
Copy a config from a working device to a similar device that is not working.
  Is the problem really fixed?
(What’s-in-Common Method – When several devices are not working.)
<number>

## Slide 13: Move-the-Problem Troubleshooting Method
Great for quick problem isolation
Swap devices and see if the problem stays in place or moves with the device.
Example: One user in the office can’t access the network.
  Swap switch ports with a known-working host and see if the problem moves with the device.
<number>

## Slide 14: Implementing Troubleshooting Procedures
The generic troubleshooting process is comprised of the following tasks:
  1. Defining the problem
  2. Gathering information
  3. Analyzing the information
  4. Eliminating possible problem causes
  5. Formulating a hypothesis about the likely cause of the problem
  6. Testing that hypothesis
  7. Solving the problem
Every problem is different and there is not a single script to solve all possible problems.
Troubleshooting is a skill that requires relevant knowledge and experience.
With more experience you can adopt more of a shoot from the hip approach
<number>

## Slide 15: Defining the Problem
Troubleshooting starts here
Someone reports a problem
Reported problem can unfortunately be vague or even misleading
  “I can’t get to the Internet.” or “My Internet is broken.”
  Maybe they can they just can’t access their email via the browser.
The problem has to be first verified, and then defined by you (the support engineer, not the user.
A good problem description consists of accurate descriptions of symptoms and not of interpretations or conclusions.
You must determine if this problem is your responsibility or if it needs to be escalated to another department or person.
  Network infrastructure issue, database issue, server issue?
<number>

## Slide 16: Gathering and Analyzing Information
Select a troubleshooting method
Identify who you will talk to and/or what devices you need to examine
Determine how you will gather this information (assemble a toolkit).
  CLI
  GUI management devices
  Syslog
Get access to devices you need to examine
Gather the information
  At some point you may need to escalate the issue
<number>

## Slide 17: Eliminating Possible Problem Causes
Detective work – Who done it?
Use the facts and evidence to progressively eliminate possible causes and eventually identify the root of the problem.
Interpret the raw information from:
  show and debug commands
  packet captures
  device logs
Might need to:
  research commands, protocols, and technologies (always learning!)
  consult network documentation
<number>

## Slide 18: Formulating/Testing a Hypothesis
Formulating and proposing a hypothesis.
  Propose causes
  Eliminate Causes
Example:
  Propose Cause: A very high CPU load on your multilayer switches can be a sign of a bridging loop.
  Eliminate Cause: A successful ping from a client to its default gateway rules out Layer 2 problems between them.
<number>

## Slide 19: Solving the Problem
Propose Hypothesis
Based on experience, you might even be able to assign a certain measure of probability to each of the remaining potential causes.
May need a workaround if the user(s) affected by the problem can’t afford to wait long for the other group to fix the problem.
After a hypothesis is proposed the next step is to come up with a possible solution (or workaround) to that problem.
Next step: Assess the impact of the change on the network and balance that against the urgency of the problem.
<number>

## Slide 20: Solving the Problem
Test the Hypothesis
If solution does not fix the problem you need to have a way to undo your changes and revert to the original situation
  Rollback plan
  Give yourself time for the rollback! – “Drop-dead time”
<number>

## Slide 21: Solving the Problem
Problem solved after you have verified that the symptoms have disappeared.
  Create backups of any changed configurations or upgraded software
  Document all changes
    Normal documentation
    Trouble-ticket database (quick resolution for the next time this occurs)
  Communicate that the problem has been solved.
    Original user that reported the problem
    Others involved in the troubleshooting process
    Other team members
<number>

## Slide 22: Integrating Troubleshooting into the Network Maintenance Process
Documentation
To troubleshoot effectively you need to have access to documentation that is up to date and accurate.
  Good baseline information so you know what kind of behavior is considered abnormal
  Access to logs that are properly time stamped to find out when particular events have happened
  Good diagrams
  Good IP Addressing scheme
  Recent configurations, software, version and license information
Wrong or outdated is often worse than having no documentation at all
Assuming that people will forget to update the documentation, is to schedule regular checks of the documentation (outside audits)
<number>

## Slide 23: Integrating Troubleshooting into the Network Maintenance Process
Creating a Baseline
Critical to troubleshooting is to be able to compare what is normal behavior and what is not normal behavior on the network.
show processes cpu - Notice that the average CPU load over the past five seconds was 97% and over the last one minute was around 39%.
  Is this high or normal on this router?
Basic performance statistics like CPU load and memory usage: Collected on a regular basis using SNMP and graphed for visual inspection.
Accounting of network traffic: Remote Monitoring (RMON), Network Based Application Recognition (NBAR), or NetFlow statistics can be used.
Measurements of network performance characteristics: The IP SLA feature in Cisco IOS can be used to measure critical performance indicators like delay and jitter across the network infrastructure.
<number>

## Slide 24: Communication and Change Control
Communication is an essential part of the troubleshooting process.
Defining the Problem: Asking good questions, clarifying and listening carefully.
Gathering information: Often dependent upon for collecting information.
Analyzing information and Eliminating possible causes: You won’t know it all and you will need to rely on others’ expertise.
  Second opinion or different viewpoint is always a good idea.
Formulating and testing hypothesis: changes may be disruptive and users may be impacted. Communicate the impact the change will make to the users. Other team members may also be working on the problem and want to make sure you are not creating new problems
  Solving the problem: Communicate that the problem has been solved. To the original user, others involved in the troubleshooting, other team members
<number>

## Slide 25: Change Control
Change control is one of the most fundamental processes in network maintenance.
You can reduce the frequency and duration of unplanned outages and thereby increase the overall uptime of your network by:
  Strictly controlling when changes are made
  Defining what type of authorization is required
  What actions need to be taken as part of that process
Always an aspect of balancing urgency, necessity, impact, and risk.
The troubleshooting process can benefit tremendously from having well-defined and well-documented change processes.
Uncommon for devices or links to simply fail from one moment to the next. In many cases, problems are triggered or caused by some sort of change.
  But it does happen.
<number>

## Slide 26: CIS 188 CCNP TSHOOT Ch. 2: Troubleshooting Processes for Complex Enterprise Networks
Rick Graziani
Cabrillo College
graziani@cabrillo.edu
Fall 2010
Notes: <number>