## Slide 1: Network Layer IPv6
Slides were original prepared by Dr. Tatsuya Suda

## Slide 2: Contents
6. IPv6

## Slide 3: 2. IPv6
IPv4 (the standard IP protocol) is limited
  IP is running out of addresses
    32 bits is not enough
  Real-time traffic and mobile users are also becoming more common
    IPv4 cannot support various QoS requirements
IP version 6 (Also called IPng, or IP next generation)

## Slide 4
IPv6 is
  A revision of IPv4

## Slide 5: IPv6: The Changes
Large address space:
  128-bit addresses (16 bytes)
  Allows up to 340,282,366,920,938,463,463,374,607,431,768,211,456 unique addresses
    3,911,873,538,269,506,102 addresses for each m2 (meter x meter) of the surface of the planet Earth
Fixed length headers
  Improves the speed of packet processing in routers

## Slide 6
Support for “flows”
  Flows help support real-time service in the Internet
  A “flow” is a number in the IPv6 header that can be used by routers to see which packets belong to the same stream
  Guarantees can then be assigned to certain flows
  Example:
    Packets from flow 10 should receive rapid delivery
    Packets from flow 12 should receive reliable delivery

## Slide 7: Other changes from IPv4
Removal of redundant features
  Fragmentation
  Broadcast
Checksum
  removed entirely to reduce processing time at each hop
Options
  allowed, but outside of header, indicated by “Next Header” field

## Slide 8
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 9: 3. IPv6: Header
Version Traffic Class Flow Label
Payload Length Next Header Hop Limit
Source Address
Destination Address
0
7
15
31
23

## Slide 10
Version (4-bit)
  Internet Protocol version number = 6.
Traffic Class (8-bit)
  Traffic class field for prioritizing types of traffic. Still Experimental.
Flow Label (20-bit)
  Allows a host to label sequences of packets for which it requests special handling by the IPv6 routers.
Payload Length (16-bit unsigned integer)
  Length of the IPv6 payload, i.e., the rest of the packet following this IPv6 header, in octets.

## Slide 11
Next Header (8-bit selector)
  identifies upper layer protocol for data
  Identifies the type of header immediately following the IPv6 header (protocol field in IPv4)
Hop Limit (8-bit unsigned integer)
  Decremented by 1 by each node that forwards the packet. The packet is discarded if Hop Limit is decremented to zero.
Source Address (128-bit address)
  Source address of the originator of the packet.
Destination Address (128-bit address)
  Destination Address of the intended recipient of the packet

## Slide 12: IPv6: Addressing Architecture
Three types of address:
  Unicast
  Anycast
  Multicast
    No Broadcast Addresses- Superseded by Multicast functionality
A prefix determines the type of address

## Slide 13: IPv6: Path MTU
Fragmentation only done end-to-end
Hosts compute MTU (Maximum Transfer Unit) for the entire path to destination by increasing the estimate periodically, and revising it down when they receive Packet Too Big messages en route
IPv6 informs upper-layer protocols (e.g., TCP) what the MTU to a destination should be

## Slide 14: IPv6: Neighbor Discovery
Replaces IPv4’s ARP (Address Resolution Protocol)
Uses multicasts to well-known addresses to find routers and other nodes sharing network links

## Slide 15: IPv6: References
Internet Standards
  RFC2640: Internet Protocol, Version 6 (IPv6) Specification
  RFC2463: Internet Control Message Protocol (ICMPv6) for the Internet Protocol Version 6 (IPv6)
  RFC1981: Path MTU Discovery for IP version 6
  RFC2462: IPv6 Stateless Address Autoconfiguration
  RFC2461: Neighbor Discovery for IP Version 6 (IPv6)

## Slide 16: 5. ICMPv6
Internet Control Message Protocol for IPv6
Handles special Internet control functions
Difference from ICMPv4
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 17
Responsibilities:
  Reporting unreachable destinations
  Reporting IP packet header problems
  Reporting routing problems
  Reporting echoes (pings)

## Slide 18: 6. Transition From IPv4 To IPv6
Not all routers can be upgraded simultaneous
  no “flag days”
  How will the network operate with mixed IPv4 and IPv6 routers?
Tunneling: IPv6 carried as payload in IPv4 datagram among IPv4 routers
Translator: gateway that translates IPv4 addresses and IPv6 addresses

## Slide 19: Tunneling
A
B
E
F
IPv6
IPv6
IPv6
IPv6
tunnel
Logical view:
Physical view:
A
B
E
F
IPv6
IPv6
IPv6
IPv6
IPv4
IPv4

## Slide 20: Tunneling
A
B
E
F
IPv6
IPv6
IPv6
IPv6
tunnel
Logical view:
Physical view:
A
B
E
F
IPv6
IPv6
IPv6
IPv6
IPv4
IPv4
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
Flow: X
Src: A
Dest: F
data
Src:B
Dest: E
A-to-B:
IPv6
E-to-F:
IPv6
B-to-C:
IPv6 inside
IPv4
B-to-C:
IPv6 inside
IPv4
Notes: <number>

## Slide 21: Adoption
Was formalized by IETF in 1998; However:
  6/2014 percentage of adoption is around 4%
  16% of the networks can support IPV6
Was used in 2008 summer Olympics:
  From data networking, cameras, taxis
Verizon Wireless (telecom company in USA), 33% of users use IPV6
2011, all major operating systems on personal compute and servers have IPV6 support