## Slide 1: Quantitative Determination of Protein by the Biuret &Lowery Reactions
CLS 331
Exp.no.5

## Slide 2
Introduction
There are many methods for the determination of the amount of protein in a natural product.
A particular method is chosen in accordance with materials to be analysed and the type of information needed.

## Slide 3
Some common methods:
Kjeldahl analysis
For total nitrogen after appropriate extraction and precipitation.
2. Biuret assay
Using a known protein to establish a standard curve.
3. Lowry method
Based on the presence of tyrosine and tryptophan in proteins

## Slide 4
The Biuret assay (sensitivity 0.25 -200 mg) and Lowry method (sensitivity 1 -200 ug)
are the most widely used

## Slide 5
The chemical basic for Biuret determination
The biuret test is a chemical test used for detecting the presence of peptide bonds. With it, a violet color complex is being formed between the Cu2+ of the Biuret reagent and the nitrogen atoms involved in the peptide bond (in alkaline solution).
In the presence of peptides, a copper ion forms a violet-coloured complex.

## Slide 6
The Biuret reaction can be used to assay the concentration of proteins because peptide bonds occur with the same frequency per amino acid in the peptide.
The intensity of the color is directly proportional to the protein concentration, according to the Beer-Lambert law.

## Slide 7
The reagent does not in fact contain biuret (NH2CONHCONH2). The test is so named because the substance biuret gives a positive reaction under the same circumstances.

## Slide 8
The biuret reagent is made of potassium hydroxide (KOH) and hydrated copper (II) sulfate, together with potassium sodium tartrate. The reagent turns from blue to violet in the presence of proteins.

## Slide 9
Procedure

## Slide 10
unknown | std5 | std4 | std3 | std2 | std1 | Blank | 
--- | 2ml | 1.5ml | 1ml | 0.75ml | 0.5ml | ----- | Stock st. sol. (protein)
3ml | 3ml | 3ml | 3ml | 3ml | 3ml | 3ml | Biuret reagent
 | ----- | 0.5ml | 1ml | 1.25ml | 1.5ml | 2ml | water
2ml | ------ | ------ | ----- | ------ | ------ | ----- | unknown
Mix the tubes and incubate them at 37C for 10 min.
Cool and then read at 540nm

## Slide 11
The Folin –Lowry method of protein assay
The Lowry protein assay is a biochemical assay for determining the total level of protein in a solution. The total protein concentration is exhibited by a color change of the sample solution in proportion to protein concentration,
This method is about 10 times more sensitive than the Biuret method.

## Slide 12
The reagent, called Folin-Ciocalteu reagent, is quite complex and contains phosphomolybdic acid & tungstate.
The aromatic amino acids, tyrosine, tryptophan present in proteins react with these and produce a dark blue colour.

## Slide 13
The colour formed is due to the reaction of alkaline copper with protein as in the biuret test and the reduction of phosphomolybdate by tyrosine and tryptophan present in the protein.

## Slide 14
Mechanism
First, the proteins are pre- treated with copper ion in alkali solution, and then the aromatic amino acids in the treated sample reduce the Folin reagent.
The end product of this reaction has a blue colour.

## Slide 15
The reaction mechanism involves reduction of the Folin reagent and oxidation of aromatic residues (mainly tryptophan, also tyrosine). The concentration of the reduced Folin reagent is measured by absorbance at 750 nm. As a result, the total concentration of protein in the sample can be deduced from the concentration of Trp and Tyr residues that reduce the Folin reagent.
The reactions result in a strong blue color, which depends partly on the tyrosine and tryptophan content.

## Slide 16
Method

## Slide 17
Mix , allow to stand at room temp. for 10 min or longer
Then, add 0.5ml of diluted Folin-Ciocalteau reagent rapidly with immediate mixing.
Stand at room temp. for 30 min
Read at 750nm
Tube2 | Tube 1 | Blank | 
5ml | 5ml | 5ml | alkaline solution
------- | 1ml | ------ | protein std (5mg/ml)
1ml | ------- | ------- | (Unknown)
------- | -------- | 1ml | water

## Slide 18
Calculation:
Conc. of Unknown = Ab of Unknown X Conc. of Std
Ab of Std