## Slide 1
NUR 422

## Slide 2
1- Definition of suctioning .
2- Sites for suction .
3- Deferent between oropharengyeal / nasopharyngeal suctioning and endotracheal / tracheostomy suctioning .
4- Purposes for suctioning .
5- Indications for suctioning.
6- Choosing the right size catheter.

## Slide 3
7- Setting the correct pressure .
8- The procedure .
9- Documentation.
10- Complications of suctioning .
11- Techniques to minimize or decrease the complications .

## Slide 4
Suctioning Definition
Aspirating secretion through a catheter connected to a suction machine or wall suction outlet.

## Slide 5
Sites for Suctioning
Oropharyngeal
Nasopharyngeal
Endotracheal.
Tracheostomy

## Slide 6
Oropharyngeal /Nasopharyngeal suctioning | Endotracheal/Tracheostomy suctioning
Remove secretion from the upper respiratory tract . | Remove secretion from the trachea and bronchi or the lower respiratory tract .

## Slide 7
Tracheal/ Endotracheal suction
Oral / Nasal suction
1- maintain oral/ nasal hygiene.
2- comfort for the patient.
3- remove blood and vomit in an emergency situation.
Remove pulmonary secretions in patients who are unable to cough and clear their own secretions effectively.
P
U
R
P
O
S
E
S
of
S
u
C
T
I
O
N
I
N
G

## Slide 8
Oropharyngeal and Nasopharyngeal suctioning required for:
1- Patient who has undergone head and neck surgery.
2- Signs of respiratory distress .
3- Evidence of unable to cough up and expectorate secreations .
Indications

## Slide 9
5- Obtain sample of secretion for diagnostic purposes
6- Prevent infection.
Tracheal suctioning required for :
1- Patients unable to clear their secretions themselves.
2- patients with mechanical ventilation.

## Slide 10
 | Size
Adult | #12 to #18
Children | #8 to # 10
Infant | # 5 to #8
Half the diameter (or less) of the tracheal tube.
Choosing the Right Size Catheter

## Slide 11
Tow types of suctioning catheter :
1- Whistle – tipped catheter .
2- Open – tipped catheter .
whistle – tipped catheter | open – tipped catheter
Less irritate the airway | More effective for removing thick mucus plugs .
Choosing the Right Size Catheter Cont’

## Slide 13
 | Wall Unit | Portable Unite
Adult | 100to 120 mm Hg . | 10 to 15 mm Hg
Child | 95 to 110 mm Hg . | 5 to 10 mm Hg
Infant | 50 to 95 mm Hg . | 2 to 5 mm Hg
Setting the Correct Pressure

## Slide 14
The procedure
E
Q
U
I
P
M
E
N
T
1- Towel or moisture – resistant pad .
2- Portable or wall suctioning machine with tubing and collection receptor.
3- sterile deposable container for fluids .
4- Sterile normal saline or water.

## Slide 15
E
Q
U
I
P
M
E
N
T
The procedure Cont’
5- Sterile gloves .
6- Goggles or face shield .
7- Sterile Suction Catheter kit .
8- Water – soluble lubricant .
10- sterile gauzes.
11- Moisture resistant disposable bag.
12- Sputum trap .

## Slide 16
4- position the patient.
Conscious patient | Unconscious patient
Semi – Fowler’s position with: head turned to one side for oral suctioning . For nasal suctioning with the neck hyperextended. | Lateral position and the patient facing you .

## Slide 18
5- prepare the equipment .
6- make approximate measure of the depth for the insertion of the catheter and test the equipment .
7- lubricate and introduce the catheter :

## Slide 19
The procedure Cont’
  For Oropharyngeal suctioning :
    Pull the tongue forward .
    Do not apply suction during insertion .
    Advance the catheter about 10 to 15 cm along on side of the mouth into oropharynx.

## Slide 20
The procedure Cont’
  For Nasopharyngeal suction
    Advance the catheter along the nasal cavity with out suctioning.
    Never force the catheter against an obstruction .

## Slide 21
8- Perform suctioning .
9- clean the catheter and apply suction again :
    Wipe off the catheter with sterile gauze.
    Flash the catheter with sterile water or saline.
    Relubricate the catheter and repeat suctioning until the air passage is clear.

## Slide 22
    Allow 20 t0 30 second intervals between each suction and limit suctioning to 5 minutes in total .
    Alternate nares for repeat suctioning.
    Encourage the client to breath deeply and to cough between suctioning .

## Slide 23
10 – Obtain specimen if required.
11- promote the patient comfort .
12- Dispose of equipment and ensure availability for the next suction .
13- Assess the effectiveness of suctioning .

## Slide 24
11- promote the patient comfort .
12- Dispose of equipment and ensure availability for the next suction .
13- Assess the effectiveness of suctioning .

## Slide 25
Documentation
Record the procedure :
  The amount .
  Consistency .
  Color .
  Odor of the mucus .
  Client breathing status before and after.
If the technique is carried out frequently it may be appropriate to record only once , how ever the frequency of suctioning must be record

## Slide 26
Complications
Trauma to the airway
Hypoxemia
Cardiac dysrhythmia
Nosocomial infection

## Slide 27
1- Suction only as needed .
2- sterile technique .
3- Hyperinflation .
4- Hyperoxygenation .
5- safe catheter size .
6- No saline instillation.

## Slide 28
Thank you for your listening