## Slide 1
HEMODYNAMIC MONITORING

## Slide 2: Outline
Click to add Title
1
Click to add Title
2
Click to add Title
3
Click to add Title
4

## Slide 3: Definition
  Hemodynamic monitoring refers to measurement of pressure, flow and oxygenation of blood within the cardiovascular system.
  OR
  Using invasive technology to provide quantitative information about vascular capacity, blood volume, pump effectiveness and tissue perfusion.

## Slide 4: Indications:
Continuous, real-time blood pressure monitoring
Planned pharmacologic or mechanical cardiovascular manipulation
Repeated blood sampling
Determination of volume responsiveness from systolic pressure or pulse -pressure variation
Supplementary diagnostic information from the arterial waveform
Failure of indirect arterial blood pressure measurement

## Slide 5: SPECIALISED EQUIPMENTS NEEDED FOR INVASIVE MONITORING

## Slide 7: HEMODYNAMIC MONITER

## Slide 10: Type of Invasive monitoring
Invasive
  Arterial pressure monitoring
  Central venous pressure monitoring
  Pulmonary artery pressure monitoring

## Slide 11: Indications for Arterial Catheterization
Need for continuous blood pressure measurement
Hemodynamic instability
Vasopressor requirement
Respiratory failure
Frequent arterial blood gas assessments
Most common locations: radial, femoral, axillary, and dorsalis pedis

## Slide 12: CENTRAL VENOUS PRESSURE MONITORING (CVP)
The CVP, the pressure in the vena cava or right atrium, is used to assess right ventricular function and venous blood return to the right side of the heart. The CVP can be continuously measured by connecting either a catheter positioned in the vena cava or the proximal port of a pulmonary artery catheter to a pressure monitoring system

## Slide 14: Central Venous Pressure Waveform

## Slide 15: Indications for Pulmonary Artery Catheterization
Identification of the type of shock
  Cardiogenic (acute MI)
  Hypovolemic (hemorrhagic)
  Obstructive (PE, cardiac tamponade)
  Distributive (septic)
  Many critically ill patients exhibit elements of more than 1 shock classification
Monitoring the effectiveness of therapy

## Slide 16: Pulmonary Artery Catheter (Swan-Ganz catheter)

## Slide 17: PULMONARY ARTERY Catheter

## Slide 19: Measuring hemodynamic parameters
Before obtaining hemodynamic parameters, the transducer is leveled and zeroed.
1. Explain the procedure to the patient to gain informed consent.
2. If IV fluid is not running, ensure that the CVC is patent by flushing the catheter.
3. Place the patient flat in a supine position if possible.
Zero reference point is: mid-axillary line at the fourth intercostal space
(Phlebostatic axis)

## Slide 20: Methods
Using a manometer
Using a transducer

## Slide 22: Using a transducer
white or proximal lumen is suitable for measuring CVP.
Tape the transducer to the phlebostatic axis or as near to the right atrium as possible

## Slide 23: Continue
Turn the tap off to the patient and open to the air by removing the cap from the three-way port opening the system to the atmosphere.
Press the zero button on the monitor and wait while calibration occurs.

## Slide 24: Continue
When 'zeroed' is displayed on the monitor, replace the cap on the three-way tap and turn the tap on to the patient.
Observe the CVP trace on the monitor. The waveform undulates as the right atrium contracts and relaxes, emptying and filling with blood. (light blue in this image)

## Slide 28: Catheter displacement
If the CVC moves into the chambers of the heart then cardiac arrhythmias may be noted, and should be reported. If the CVC is no longer in the correct position, CVP readings and medication administration will be affected.

## Slide 29: DERIVED PARAMETERS
Cardiac o/p measurements may be combined with systemic arterial, venous, and PAP determinations to calculate a number of variables useful in assessing the overall hemodynamic status of the patient.
They are,
Cardiac index = Cardiac output / Body surface area
Systemic vascular resistance = [(Mean arterial pressure - resistance CVP or RT atrial pressure)/Cardiac output] x 80
Pulmonary vascular resistance = [(PAP - PAWP) / Cardiac vascular resistance output] x 80
Mixed venous oxygen saturation (SvO2)
(SvO2 = SaO2 - [VO2 / (1.36 x Hb x CO)] (6)

## Slide 30: Normal value
Normal value | Parameter
70 -90 mm Hg | Mean Arterial Pressure (MAP)
2.8-4.2 L/min/m2 | Cardiac Index (CI)
4-8 L/min | Cardiac Output (CO)
2-6 mmHg | Central Venous Pressure (CVP)
2-8mm H2O | Atrial Pressure (RA))
Systolic 20-30 mmHg (PAS) Diastolic 8-12 mmHg (PAD) Mean 15-25 mmHg | Pulmonary Artery Pressure (PA)
8-12 mmHg | Pulmonary Capillary Wedge Pressure (PWCP)

## Slide 31: NURSING INTERVENTIONS
Once catheter is inserted, it is secured and a dry, sterile dressing is applied.
Catheter placement is confirmed by a chest x-ray, and the site is inspected daily for signs of infection. The dressing and pressure monitoring system or water manometer are changed according to hospital policy.
In general, the dressing is to be kept dry and air occlusive.
Dressing changes are performed with the use of sterile technique.
CVP catheters can be used for infusing intravenous fluids, administering intravenous medications, and drawing blood specimens in addition to monitoring pressure.

## Slide 32: Continue
the transducer must be positioned at the phlebostatic axis to ensure accurate readings .
The nurse who obtains the wedge reading ensures that the catheter has returned to its normal position in the pulmonary artery by evaluating the pulmonary artery pressure waveform.
The pulmonary artery diastolic reading and the wedge pressure reflect the pressure in the ventricle at end-diastole and are particularly important to monitor in critically ill patients, because they are used to evaluate left ventricular filling pressures (preload)
At end-diastole, when the mitral valve is open, the wedge pressure is the same as the pressure in the left atrium and the left ventricle, unless the patient has mitral valve disease or pulmonary hypertension.
Critically ill patients usually require higher left ventricular filling pressures to optimize cardiac output. These patients may need to have their wedge pressure maintained as high as 18 mm Hg.

## Slide 33: NURSING RESPONSIBILITIES
Site Care and Catheter Safety:
A sterile dressing is placed over the insertion site and the catheter is taped in place. The insertion site should be assessed for infection and the dressing changed every 72 hours and prn.
The placement of the catheter, stated in centimeters, should be documented and assessed every shift.
The integrity of the sterile sleeve must be maintained so the catheter can be advanced or pulled back without contamination.
The catheter tubing should be labeled and all the connections secure.
The balloon should always be deflated and the syringe closed and locked unless you are taking a PCWP measurement

## Slide 34: Patient Activity and Positioning:
Many physicians allow stable patients who have PA catheters, such as post CABG patients, to get out of bed and sit. The nurse must position the patient in a manner that avoids dislodging the catheter.
Proper positioning during hemodynamic readings will ensure accuracy.

## Slide 35: Conclusion
Hemodynamic is the forces involved in blood circulation. Hemodynamic monitoring started with the estimation of heart rate using the simple skill of 'finger on the pulse' and then moved on to more and more sophisticated techniques like stethoscope, sphygmomanometer, ECG etc. The status of critically ill patients can be assessed either from non-invasive single parameter indicators or various invasive techniques that provide multi-parameter hemodynamic measurements. As a result, comprehensive data can be provided for the clinician to proactively address hemodynamic crisis and safely manage the patient instead of reacting to late indicators of hemodynamic instability

## Slide 36
www.themegallery.com
Thank You !