## Slide 1: Reservoirs Heterogeneity Characterization of the Shajara Member: Permo-Carboniferous Unayzah Formation *Al-Khidir, K. E., **Al-Laboun, A. A., ***AlQuraishi, A. A. *M. S. Benzagouta *College of Engineering, Al Amoudi Research Chair in EOR, Department of Petroleum Engineering & Natural Gas King Saud University, ***King Abdulaziz City for Science and Technology Petroleum and Natural Gas Research Institute **College of Science Department of Geology King Saud University.
Notes: <number>

## Slide 2: Introduction
The Unayzah Formation is hydrocarbon bearing in many oil and gas fields in Saudi Arabia. It is composed of continental siliciclastic of Permo-Carboniferous age bounded by two regional unconformities, namely sub-unayzah and sub-Khuff.
Based on Saudi Stratigraphic Code (1983), Unayzah Formation should be raised to a group status and a new Shajara Formation is introduced.
The Shajara Formation is divided into three members from base to top are: Lower Shajara, Middle Shajara, and Upper Shajara Members.
Local unconformities were interpreted as braided fluvial channels.
Notes: <number>

## Slide 3: Objectives
Determination of the thermodynamic model based on Mercury Intrusion techniques .
Determination of fractal Dimension using 3-D Fractal Model for characterizing pore structure and reservoir heterogeneity.
Application is on selected Samples from Shajara Reservoirs.
Notes: <number>

## Slide 4: Reservoir Description
The Permo-Carboniferous Unayzah Formation consists of sandstone and mudstone intervals bounded by two unconformities namely sub Unayzah and Sub Khuff.
Based on Saudi stratigraphic code, Unayzah should be raised to a group status and a new Shajara Formation is introduced.
Lithologically, the Shajara Formation is classified into three members named from bottom to top as Lower Shajara, Middle Shajara and Upper Shajara Members.
Sedimentological Interpretation has revealed a braided fluvial channels.
Notes: <number>

## Slide 5: Type Section of The Shajara Formation N.26° 52 17.4 E. 43° 36 18
Notes: <number>

## Slide 6: Methodology
The Autopore III was used for :
Determination of Pc and pore throat radius and intrusion volume (Hg).
thus, The thermodynamic model equation is applied :
Ln (Pc*Vi /r^2) = Df Ln (Vn^1/3 /r) + C
Where, Vi = cumulative Intrusion Volume Vn =Intrusion Volume
This equation leads to the Determination of Df( Fractal Dimension) which is defined asSimilarity in geometry and difference in Size
Notes: <number>

## Slide 7
Following the thermodynamic equation, the pore size radius was calculated (Washburn,s equation) as:
r = -2*σ*cosθ/Pc, where
r = pore radius in meter (m),
σ = mercury interfacial tension in Newton per meter(0.485 N/m),
θ = mercury contact angle measured in degrees(130°) and,
Pc = capillary pressure in Newton per square meter (N/m^2).
Notes: <number>

## Slide 8: Thermodynamic model for the Lower Shajara Reervoir (3 samples). The obtained straight line plot is assigned for fractal dimension system.
Notes: <number>

## Slide 9: Affirmation of heterogeneity for 3 samples from the Lower Shajara Reservoir. The non-uniformities delineate the heterogeneities.
Notes: <number>

## Slide 10: Thermodynamic model for the Middle Shajara Reservoir (3 samples), the obtained straight line identifies the fractal dimension of the system
Notes: <number>

## Slide 11: Further confirmation of heterogeneity for 3 samples from the Middle Shajara Reservoir
Notes: <number>

## Slide 12: Thermodynamic model for the Upper Shajara Reservoir of the Shajara Formation. The linearity displays the fractal system of the 3 samples
Notes: <number>

## Slide 13: Further confirmation of heterogeneity for 3 samples from the Upper Shajara Reservoir
Notes: <number>

## Slide 14: The 3-D Fractal Model
This method is aimed to be correlated to the thermodynamic model to confirm the Reservoir
Heterogeneity based on Fractal Dimension
The 3 D model is Calculated based on Mercury Saturation and Average Capillary Pressure.
Notes: <number>

## Slide 15: 3-D Fractal Model Equation and Fractal Dimension (Df)
It is based on natural logarithm of mercury saturation (Ln, Hg) divided by average capillary pressure. The latter one was plotted versus Ln(dSHg / dPc).
The slope was determined from the straight line and its value was added to 4 to give the Fractal Dimension Df as follows:
Ln (dSHg / dPc) = (Df -4) Ln ( Pc)
Notes: <number>

## Slide 16: 3-D fractal model of the Lower Shajara Reservoir ( Lower Shajara Member)
Notes: <number>

## Slide 17: 3-D fractal model for the Middle Shajara Reservoir (Middle Shajara Member)
Notes: <number>

## Slide 18: 3-D fractal model of the Upper Shajara Reservoir (Upper Shajara Member).
Notes: <number>

## Slide 19
Table showing porosity and permeability results for the three Shajara Formation reservoirs (Permo-Carboniferous Unayzah Group area, Al-Qasim district).
Reservoirs | Facies | h (feet) | Aver. r(μm) | Φ% | K (mD)
Upper Shajara Reservoir | SJ-13 | 6.5 | 25 | 25 | 973
 | SJ-12 | 13.1 | 68 | 28 | 1440
 | SJ-11 |  | 43 | 36 | 1197
Middle Shajara Reservoir | SJ-9 | 0.9 | 74 | 32 | 1395
 | SJ-8 |  | 29 | 32 | 1344
 | SJ-7 | 13.4 | 46 | 35 | 1472
Lower Shajara Reservoir | SJ-3 | 1.6 | 13 | 34 | 56
 | SJ-2 | 3.9 | 25 | 35 | 1955
 | SJ-1 | 11.8 | 41 | 29 | 1680
Notes: <number>

## Slide 20: Conclusion
Based on Saudi stratigraphic code, the Permo-Carboniferous Unayzah Formation is raised to a group status and a new Shajara is introduced.
The Shajara Formation of the Permo-Carboniferous Unayzah group has been divided here, into three members, from base to top are; Lower, Middle and Upper Shajara Members.
Three fractal dimension units were identified on the basis of unconformities and mudstone of the Middle Shajara Member.
The thermodynamic model and 3-D fractal model of mercury intrusion show their effectiveness, mathematical capabilities and continuity in evaluating the fractal dimensions of the Shajara Reservoirs (Shajara Formation Permo-Carboniferous Unayzah Group).
The Shajara Reservoirs have show their heterogeneities, their bimodality and their megaporous classification.
Notes: <number>

## Slide 21: Conclusion
The results of the fractal dimensions in addition to pore size distribution indicate the heterogeneity of the Shajara Reservoirs which accounts for a wide range of pore sizes.
A plot of incremental pore size distribution reveals bimodal behavior for the samples selected from three Shajara Reservoirs of the Shajara Formation, except sample SJ12 which is characterized by monomodal pore size distribution.
Notes: <number>

## Slide 22: Conclusion
In our case, neither modality nor bimodality have great effect on reservoir quality, but owing to sorting and fluid flow capacity (permeability).
The three Shajara Reservoirs are classified as megaporous, with average pore size of 26 μm for the Lower Shajara Reservoir, 49 μm for the Middle Shajara Reservoir, and 45 μm for the Upper Shajara Reservoir.
Notes: <number>