## Slide 1: Cls 332 lab no.4
MEASUREMENT OF OSMOLALITY USING A DIGITAL MICRO-OSMOMETER

## Slide 3: What is Osmolality??
Osmolality:
Is measurement of concentration: it is the number of moles of particles (solute) per kilogram of water (solvent).
Osmolality is independent of the shape, size or weight of the particles. The properties based on the number of particles is measured are known as Colligative properties. The properties are vapour pressure depression, freezing point depression, boiling point elevation, and osmotic pressure.

## Slide 4
Colligative properties:
(Are those properties of solutions that depend on the number of dissolved particles in solution, but not on the identities of the solutes.)

## Slide 5
For example, the freezing point of salt water is lower than that of pure water, due to the presence of the salt dissolved in the water.
To a good approximation, it does not matter whether the salt dissolved in water is sodium chloride or potassium nitrate; if the molar amounts of solute are the same and the number of ions are the same, the freezing points will be the same .

## Slide 6
Osmolality deals with the concentration of the particles that is dissolved in a fluid. In medical science, osmolality is used to determine several conditions like diabetes, dehydration and shock. For the detection of these conditions, the osmolality of the serum is checked, and is known as plasma osmolality

## Slide 7: Solutes categories
Solutes can be divided into three general categories:
1- Electrolytes.
2- Organic solutions of small molecular weight (urea, glucose, creatinine ).
3- Colloids (chiefly protein).

## Slide 8
Principle of measurement:
There are 4 measurement that depend on colligative properties:
1- Freezing point.
2- Vapor pressure.
3- Osmotic pressure.
4- Boiling point.

## Slide 9
The presence of a solute lowers the freezing point of a solution relative to that of the pure solvent. For example, pure water freezes at 0°C (32°F); if one dissolves 10 grams of sodium chloride in 100 ml of water, the freezing point goes down to −5.9°C (21.4°F).
Freezing Point Depression
Notes: <number>

## Slide 10
The reason that the salt solution has a lower freezing point than the sugar solution is that there are more particles in 10 grams of sodium chloride than in 10 grams of sucrose

## Slide 11
Boiling Point Elevation
The boiling point of a solution is higher than that of the pure solvent.
If 10 grams of sodium chloride are dissolved in 100 ml of water, the boiling point of the solution is 101.7°C which is 1.7°C higher than the boiling point of pure water.

## Slide 12
Vapor Pressure Lowering
The vapor pressure of a liquid is the equilibrium pressure of gas molecules from that liquid (i.e., the results of evaporation) above the liquid itself.

## Slide 13: Osmotic Pressure
Osmosis process would be one that ends with the solute concentrations being equal on both sides of the membrane. Osmotic pressure is the pressure that must be applied on the high concentration side to stop osmosis.
Osmosis is the passage of water from a region of high water concentration through a semi-permeable membrane to a region of low water concentration.

## Slide 14
The freezing point and vapor pressure decrease .
The osmotic pressure and boiling point increase.
So in the present commercial instruments the determination of freezing point lowering is more satisfactory than the other measurement.

## Slide 15: Why?
Using freezing point is:
1- more easier.
2- sample does not destroy.

## Slide 16
Usually osmolality is expressed as Osm/Kg.
To measure osmolality an instrument known as an osmometer is used.

## Slide 17
There are three major types of osmometers:
Freezing Point Osmometers – measure freezing point depression
Vapor Pressure Osmometers – measure vapor pressure of the solution
Membrane Osmometers – measure the osmotic pressure of a solution separated by a semi-permeable membrane

## Slide 18
Osmometer principle:
1- Super cooled the sample by bath containing an antifreeze solution that is maintained at about -5° C
2- Inside the sample there will be thermometer to measure FP.
3- after super cooling we take sample out and the thermometer still inside then we will notice the temp. start getting high .
4- at some point the temp. will stopped increasing and give constant value ....this value is FP.

## Slide 19: Operation of digital micro –osmometer:
Calibration with distalled water:
1- Switch on to warm up for 3 mins.
2- Fill sample vessel with 10 μl disttilled water (volume must be +or – 10 %).
3- Attach sample vessel to measuring head.
4-Slide the measuring head down, insert tube into the cooling cone

## Slide 21
5- Supercooling is reached in about 1.5 mins.
6- At (-1000°c) the freezing needle is automatically inserted into the sample vessel for one second, then its returned back to its original position

## Slide 22
7- During the plateau period, set digital display to zero. as soon as the values rise the plateau has ended.
Plateau temperature: the temperature at which an equilibrium exists between condensation and evaporation.
8-The freezing point is determined and osmolality is shown on the digital display. An audible signal indicates the measurement has been completed. The measurement value is stored in the memory
9- Raise the measuring head, remove sample tube and wipe thermistor with a soft tissue

## Slide 23: Precautions
1- Warm up the instrument 3 mins.
2- Always use the recommended sample vessel.
3- Make the necessary adjustment in the position of thermistor according to the volume of sample and for high accuracy its better to position the thermister for 100 μl volume.
4- Before removal of sample vessel, at the end of the measurements its necessary to warm up frozen solution.
5- To repeat the measurements on the same sample always use a dry or new vessel.