## Slide 1: Particle Size Analysis

## Slide 2: Importance: - The particle size of a drug can affect its physical, chemical, pharmacological properties. - The particle size of a drug can also affect its release from dosage forms. - The particle size of a drug can also affect the formulation of dosage forms

## Slide 3: Effect of milling on crystallinity and dissolution

## Slide 4: Describing Particle Size
The problem is
deciding on the
best way to
describe them
Particles come in
all different
shapes and sizes
Notes: <number>

## Slide 5
Methods for determining particle size
1. Microscopy
2. Sieving
3. Sedimentation techniques
4. Optical and electrical sensing zone method
5. Laser light scattering techniques
(Surface area measurement techniques)

## Slide 6
Nature of the material to be sized, e.g.
estimated particle size and particle size range
solubility
ease of handling
toxicity
flowability
intended use
Cost
capital
running
Specification requirements
Time restrictions

## Slide 7
1. Microscopy
- A very powerful technique as it allows direct observation of particles within the approximate size range 1 -150 microns Optical microscopy
- For submicron particles it is necessary to use either
TEM (Transmission Electron Microscopy) or
SEM (Scanning Electron Microscopy).
TEM and SEM (0.001-5µm)
- Produces a number distribution based on measurement of diameters - or more usually projected area diameters

## Slide 8
Microscopy - Advantages
Allows direct observation of the particles rather than observing a property dependent on particle size.
The dispersion of the sample can be assessed
Initially easy to set up and use
A good back-up with other methods (e.g. Diffraction and S.O.P’s)
Notes: <number>

## Slide 9
Microscopy -Disadvantages
Sampling of the distribution is poor! It is impossible to measure all the particles present!
The result is a number distribution not a volume distribution.
Ignoring one 10um particle is the same as ignoring 1000 1um particles!!
Notes: <number>

## Slide 10
Transmission and Scanning Electron Microscopy
Advantages
Particles are individually examined
Visual means to see sub-micron specimens
Particle shape can be measured
Disadvantages
Very expensive
Time consuming sample preparation
Materials such as emulsions difficult/impossible to prepare
Low throughput - Not for routine use

## Slide 11
Scanning electron microscope

## Slide 12
2. Sedimentation
The particle size is determined by measuring the settling velocity of particles through a liquid medium in a gravitational or centrifugal environment.
Sedimentation rate may be calculated from stokes’s law using the Andreasen pipet which is designed where the sample can be removed from the lower portion at selected time intervals.
- The powder is dispersed in a non-solvent and agitated then 20ml samples is removed over a period of time, each sample is dried and weighed.

## Slide 13
A technique used in the paint and ceramics industries.
Requires particles in a fluid to settle under gravity
Limited particle size range since...
Sedimentation
Notes: <number>

## Slide 14
Sedimentation
Largest particles fall quickly through the medium and can be missed.
Smallest particles are held in suspension for extensive periods
Notes: <number>

## Slide 15
Sedimentation - Advantages
A relatively cheap technique to use if you have the time!
Capable of producing reproducible results if used in the right hands.
Notes: <number>

## Slide 16: Sedimentation.
Notes: <number>

## Slide 17
Sedimentation - Disadvantages
Since Stokes law depends on the viscosity of the fluid, temperature has to be well controlled.
Unable to handle mixtures of different density.
The technique is slow
Tends to underestimate sizes
Notes: <number>

## Slide 18: 3-Electrozone Sensing - (Coulter Counter)
Developed in the 1950’s for counting blood cells which are monodisperse suspensions in a weak electrolyte.
Notes: <number>

## Slide 19: Electrozone Sensing - (Coulter Counter)
Particles are made to flow through a small orifice in a glass tube which has a voltage across it.
As particles pass through the orifice the voltage changes, this is measured by using a pulse height analyser. The height of the pulse is proportional to the size of the particle.
Notes: <number>

## Slide 20
(Coulter Counter)
▪ Instrument measures particle volume which can be expressed as dv : the diameter of a sphere that has the same volume as the particle.
▪ The number and size of particles suspended in an electrolyte is determined by causing them to pass through an orifice an either side of which is immersed an electrode.
▪ The changes in electric impedance (resistance) as particles pass through the orifice generate voltage pulses whose amplitude are proportional to the volumes of the particles.
▪ Volume distribution

## Slide 21: Electrozone Sensing - (Coulter Counter)
Disadvantages
Difficult to measure emulsions
Must measure in Electrolyte
Requires regular calibration
Very poor dynamic size range
Lowest size set by the orifice selected - around 2 microns.
Porous particles give problems
Notes: <number>

## Slide 22: Electrozone Sensing - (Coulter Counter)
Summary
Good technique for blood cells but not suitable for most industrial materials
High resolution for narrow distributions,
Notes: <number>

## Slide 23
4. Sieving
● A widely used method of particle sizing
● Sieve analysis is performed using a nest or stack of sieves where each lower sieve has a smaller aperture size than that of the sieve above it.
● Sieves can be referred to either by their aperture size or by their mesh size (or sieve number).
● The mesh size is the number of wires per linear inch.
  Standard woven wire sieves cover size range of 20um to 125mm.
  Electroformed micromesh sieves at the lower end or range (< 20µm)
  Punch plate sieves at the upper range.
● Punched hole sieves available to cm range
● Micromesh sieves extend the range down to 5um.
● Particles are passed through the series of sieve, the proportion of particles
Passing through or being withheld on each sieve is determined in a specified time.

## Slide 26: Sieving.
Notes: <number>

## Slide 27
Sieving
A widely used method of particle sizing.
Woven wire sieves cover size range of 20um to 125mm.
Punched hole sieves available to cm range
Micromesh sieves extend the range down to 5um.
Notes: <number>

## Slide 28
In practice particles will look more like this and there will always be some that in volume or weight terms are larger than their equivalent sieve measurements.
Shape must be considered for this technique
Sieving...
Notes: <number>

## Slide 29
Sieving - a common question
“ I sieved my material to 110um but laser diffraction tells me I still have particles larger than 110um. How can this be so?
Imagine we have a sieve of 110um hole construction…...
Notes: <number>

## Slide 30
Sieving
100um
100um
Volume of cube = 106 um3.
Diameter of sphere with the same volume as cube =124um
Notes: <number>

## Slide 31
Sieving
The situation gets worse as the shape of the
particle changes
100um
200um
Volume of particle is now 2x106 um3
Diameter of sphere with same volume as particle
is now 156um
Notes: <number>

## Slide 32
Equivalent Spheres
The best way of describing irregularly shaped particles is to compare some aspect of their shape or size to the diameter of a sphere.
Notes: <number>

## Slide 33: Equivalent sphere.
Notes: <number>

## Slide 34
Equivalent spheres
Notes: <number>

## Slide 35
Characterising distributions
Whatever method we choose…...
We need to be aware that different techniques will give different results.
This is because we are measuring a different property of the particle;
e.g. a length or a Stokes’ diameter or a volume.
Notes: <number>

## Slide 36: Graphical data.
Notes: <number>

## Slide 37: 5- Laser MS2000 Measurement.
1. A source of light.
2. A means of passing the light through the particles to allow scattering.
3. A means of measuring the light intensity at a range of scattering angles.
4. A method of analysis which converts the measured scattering to a particle size distribution.
Notes: <number>

## Slide 38
Scattering from particles
Incident light
Small angle scattering
Incident light
Large angle scattering
Notes: <number>
The way in which light interacts with particles is such that large particles cause light to be scattered strongly in the forward direction but very weakly at higher angles. Small particles scatter their light into larger angles but this light is very weak in comparison.
For this reason we find that when measuring large particles we get large amounts of data generated at relatively low obscuration since a lot of light is scattered from the particles. When measuring small particles the scattered light is weak by comparison and so a high obscuration is required in order to generate relatively small amounts of data.