## Slide 1: IE 469 Manufacturing Systems 469 صنع نظم التصنيع
I- Performance Measure Tutorial

## Slide 2
Performance Measure Equations: |  |  | 
MLT = | no*[Tsu+((Q/1-ρ)xTo)+Tno] , hr/order |  | 
 | N x MLT , hr/month |  | 
Production time (Tp) = | [Tsu+QxTo]/Q , hr/pc |  | 
Production rate (Rp) = | 1/TP , pc/hr |  | 
Available Time (AT) = | PlantOperationTime*Weeks*(MTBF-MTTR)/MTBF |  | 
Production Capacity (PC) = | (N/noa)xAT*Rpa , Parts |  | 
Demand parts (D) = | Ʃ (N*Q) |  | 
Utilization (U) = | D/PC |  | 
WIP = | U xPC x MLT/AT = (D/AT) x MLT, pc/month |  | 
Part Cost (Cp) = | Cm + no*(Co x To + Cno) , SR/part |  | 
Holding Cost (Hc) = | [Cm + (no*(Co x To +Cno))/2] x H x (MLT/AT*) ,SR/part |  | 
Equations for Averaging`

## Slide 3: Problem #1
Question 1
A plant contains 24 machines and produces two products according to the data given in table (1). Machine and labor cost= 80 SR/hr, raw material cost 300 SR/part, and holding cost rate = 35%/year.
A) Determine:
a. MLT for each product type.
b. The plant capacity.
c. The utilization.
d. The average WIP for each product type.
e. Products cost
f. Holding cost
B) Comment on your finding of utilization and analyze to improve the system

## Slide 4: Problem #1
Product type |  | P1 | P2 | Using Averaging Equations
Number of order per month, N |  | 20 | 30 | 50
Average quantity per order, units, Q |  | 30 | 20 | 24.00
Average Number of processes, no |  | 10 | 12 | 11.00
Average operating time , To, min |  | 12 | 15 | 13.64
Non operation time per order, Tno, hr |  | 5 | 8 | 6.93
Setup time per order,Tsu, hr |  | 5 | 8 | 6.93
Average mean time to failure, MTTF, hr |  | 240 |  | 
Average mean time to repair, MTTR, hr |  | 10 |  | 
Plant Operation time | 8 hr / day, 6 days / week |  |  | 
Table (1):

## Slide 5: Problem #1 Solution
Solution: A) | P1 | P2 | Average
Plant Capacity: |  |  |  |  | Utilization: | 
Cp = | 779 | pc/month |  |  | U = | 153.96%
B) Hence, Capacity does not meet required production and over time of 53.96% is required |  |  |  |  |  | 
a. MLT = hr/order | 160.00 | 252.00 | 212.43
= N x MLT , hr/month | 3200.00 | 7560.00 | 10621.43
b. Production time Tp = hr/pc | 0.37 | 0.65 | 0.52
c. Production rate Rp = pc/hr | 2.73 | 1.54 | 1.94
d. WIP = pc/month | 1041.67 | 1640.63 | 1383.00
e. Part Cost = SR/part | 460.00 | 540.00 | 500.00
f. Holding Cost = SR/part | 738.89 | 1929.38 | 2581.60
AT= Plant operation time x Availability =(8 hrs x 6 days x 4 weeks)x((240-10)/240) = |  |  |  |  | 184.32 | hr/month
N0. of M/c, N= |  |  |  |  | 24 | Mchines
Production required per month, D= |  |  |  |  | 1200 | pc/month

## Slide 6: Problem #2
Question 2
A manufacturing plant contains 15 machines and produces four products according to the data given in table (1). Determine:
a) MLT for each product type.
b) Average MLT of the plant.
c) The plant capacity. Is this capacity meet production? If not suggest a solution.
d) The plant utilization.
e) WIP for each product type.
f) Average WIP for the plant
g) Part cost for each product type
h) Average holding cost.

## Slide 7: Problem #2
TABLE (1) |  |  |  | 
Product type | P1 | P2 | P3 | P4
Number of order per month | 15 | 10 | 10 | 15
Average quantity per order, units | 50 | 60 | 60 | 50
Number of processes | 8 | 9 | 7 | 6
Average operating time, min | 8 | 7 | 10 | 12
Non operation time per order, hr | 5 | 5 | 5 | 5
Setup time per order, hr | 3 | 4 | 3 | 4
Average mean time between failure, hr | 235 |  |  | 
Average mean time to repair, hr | 15 |  |  | 
scrap % | 3 | 3 | 3 | 3
Material Cost, SR/part | 110 | 140 | 120 | 150
Machine and operation cost, SR. hr | 50 |  |  | 
Holding cost rate, %/year | 35 |  |  | 
Plant Operation time | 10 hr / day, 6 days / week |  |  | 

## Slide 8: Problem #2 Solution
Solution:
Using Averaging Equations
Average batch size Qa= |  |  |  |  | Σ | ΣQN/ΣN
Q*N | 750 | 600 | 600 | 750 | 2700 | 54
N | 15 | 10 | 10 | 15 | 50 | 
Average Number of processes noa= |  |  |  |  | Σ | ΣnQN/ΣQN
n*Q*N | 6000 | 5400 | 4200 | 4500 | 20100 | 7.44
Q*N | 750 | 600 | 600 | 750 | 2700 | 
Average operating time Toa= |  |  |  |  | Σ | ΣToQNn/ΣQNn
To*Q*N*n | 48000 | 37800 | 42000 | 54000 | 181800 | 9.045
Q*N*n | 6000 | 5400 | 4200 | 4500 | 20100 | 
Average Setup time Tsua= |  |  |  |  | Σ | ΣnNTs/ΣnN
n*N*Ts | 360 | 360 | 210 | 360 | 1290 | 3.49
n*N | 120 | 90 | 70 | 90 | 370 | 
Average non-operation time Tnoa= |  |  |  |  | Σ | ΣnNTno/ΣnN
n*N*Tno | 600 | 450 | 350 | 450 | 1850 | 5
n*N | 120 | 90 | 70 | 90 | 370 | 

## Slide 9: Problem #2 Solution
a) MLT | 
MLT =, hr/batch = | 
N x MLT, hr/month = | 
P1
118.98
1784.74
P2
145.95
1459.48
P3
128.16
1281.65
P4
115.86
1737.84
b) Average MLT |  |  |  |  | 
MLT = hr/batch = |  |  | 125.651404 |  | 
= N x MLT, hr/month = |  |  | 6282.570199 |  | 
Available time, AT = 10x6x4x(220/235) = |  |  |  | 224.681 | 
Production Rate of parts: |  | P1 | P2 | P3 | P4
TP = hr/pc = |  | 0.197 | 0.187 | 0.222 | 0.286
Average Production Rate: |  |  |  |  | 
TP = hr/pc = |  |  |  | 0.220 | 
Rp = 1/TP, pc/hr = |  |  |  | 4.546 | 
c) Plant Capacity |  |  |  |  | 
PC = parts/month = |  |  |  | 2058 | 
d) Utilization: |  |  |  |  | 
Demand (D) = |  |  | 2700 | parts/month | 
U = D/PC = |  |  | 1.31 |  | 
Then the capacity is fully utilized and overtime is required or designing new system to meet the requirements, since Utilization is greater than 1 |  |  |  |  | 

## Slide 10: Problem #2 Solution
h) Average Holding cost | 
Hc = [Cm + (no*(Co x To +Cno))/2] x ((H/100)/12) x MLT/AT , SR/month | 482.656
e) Work in Process for each product: |  | P1 | P2 | P3 | P4 |  |  |  | 
WIP= |  | 1430 | 1754 | 1540 | 1392 |  |  |  | 
f) Average Work in Process in plant: WIP= |  | 1510 Parts/month |  |  |  |  |  |  | 
Part cost/product: |  | P1 | P2 | P3 | P4 |  |  |  | 
Cp = SR/part = |  | 163.33 | 192.5 | 178.33 | 210 |  |  |  | 
 |  |  |  |  |  | Σ | ΣNQCm/ΣNQ |  | 
Average material cost (Cm) = | N*Q*Cm | 82500 | 84000 | 72000 | 112500 | 351000 | 130 |  | 
 | N*Q | 750 | 600 | 600 | 750 | 2700 |  |  | 
g) Average Part cost |  |  |  |  |  |  |  |  | 
Cp = SR/part = |  |  |  |  | 186 |  |  |  | 

## Slide 11: Problem #3
Question 3
A plant having 18 machines produces a part being processed through six machines in batch of 30 parts. 20 batches of parts are launched each week. Average operation time = 30 min., average setup time per machine = 5hr, non-operation time per machine = 12 hr, and scrap rate =3% as mentioned in table 1. Machine and labor cost= 80 SR/hr, raw material cost 300 SR/part, holding cost rate= 35%/year.
Determine:
a) MLT, WIP, holding cost and part cost
b) If the machines are replaced by CNC machines on which operation time = 15 min., setup time per machine =8hr, and non-productive time per machine =8hr, and scrap rate= 1%. Machine and operation cost = 150 SR/hr and material cost is the same. What are the number of CNC machines. Then determine MLT, WIP, holding cost and part cost.

## Slide 12: Problem #3
Product type | M/Cs | CNC*
Number of batch per week,N | 20 | 20
Average quantity per batch, units,Q | 30 | 30
Number of processes,n | 6 | 6
Average operating time, min ,To | 30 | 15
Non operation time per bach, hr,Tno | 12 | 8
Setup time per batch, hr,Tsu | 5 | 8
scrap % | 3 | 1
Material Cost, SR/part | 300 | 300
Machine and operation cost, SR.hr | 80 | 150
Plant Operation time; 8 hr / day, 5 days / week |  | 
* all operations on are carried out a CNC machine with the same setup |  | 

## Slide 13: Problem #3 Solution
Solution: |  |  |  |  |  |  | 
a) For conventional machine: |  |  |  |  |  |  | 
1- Manufacturing Lead Time: |  |  |  |  |  |  |  | 
MLT = hr/batch = |  | 194.7835 |  |  |  |  |  | 
= N x MLT, hr/week = |  |  |  |  |  |  | 3895.6701 | 
2- Production Rate: |  |  |  |  | 
TP = hr/pc = |  |  |  |  | 0.682
Rp = 1/TP, pc/hr = |  |  |  |  | 1.466
3- Capacity: |  |  |  |  |  | 
PC = parts/week = |  |  |  | 175 |  | 
4- Utilization: |  |  |  |  |  |  | Then the capacity is fully utilized and overtime is required or designing new system to meet the requirements, since Utilization is greater than 1 |  |  |  |  | 
required parts/week, D = 600 |  |  |  |  |  |  |  |  |  |  |  | 
plant to be utilized , D/PC = |  |  |  |  |  | 3.43 |  |  |  |  |  | 
5- Work in Process: |  |  |  |  |  |  |  | P/batch | P/week |  | 
WIP= |  |  |  |  |  |  |  | 2922 | 58435 |  | 
6- Part cost: Cp |  |  |  | 
Cp =SR/part = |  |  |  | 540
7- Holding cost |  |  |  |  | 
Hc = SR/part = |  |  | 275.3189 |  | 

## Slide 14: Problem #3 Solution
b) For CNC machine |  | 
Each machine carry the six operation combined |  | 
\To =∑ operation time of all operations & no = 1 |  | 
1- Manufacturing Lead Time: |  | 
MLT= no x [Tsu+(Q/(1-p))*n*To+Tno], hr/batch = |  | 61.45
= N x MLT1, hr/week = |  | 1229.09
2- Production Rate: |  | 
TP =[Tsu+(Q/(1-p)*n*To]/Q, hr/pc = |  | 1.782
Rp = 1/TP, pc/hr = |  | 0.561
Find Number Of CNC M/cs |  |  |  | 
Alternative 1; Determine the number at demand D=(600) a week |  |  |  | 
N = D/(RP*AT) =600/(40*RP) |  | 27 |  | 
Alternative 2; Determine the number at current capacity D=(234) a week |  |  |  | 
N = D/(RP*AT) =175/(40*RP) |  | 8 |  | 
For first alternative; n=27 |  | 
3- Capacity: |  | 
PC = parts/week = |  | 606
4- Utilization: |  |  | 
required parts/week, D = 600 |  |  | 
plant to be utilized , D/PC = |  |  | 0.99
Then the capacity is used 99% |  |  | 
5- Work in Process: | P/batch | P/week
WIP= | 921 | 18436

## Slide 15: Problem #3 Solution
For second alternative; n=8 | 
3- Capacity: | 
PC = parts/week = | 179
4- Utilization: |  |  | 
required parts/week, D = 600 |  |  | 
plant to be utilized , D/PC = |  |  | 3.35
Capacity does not meet required production and over time of 235% is required |  |  | 
5- Work in Process: | P/batch | P/week
WIP= | 921 | 18436
6- Part cost: Cp | 
Cp = SR/part = | 525
7- Holding cost | 
Hc = SR/part = | 85.312