## Slide 1
Lactate dehydrogenase reaction
Notes: https://www.lahc.edu/classes/chemistry/arias/FlowChart101.pdf

## Slide 2
Factors that Affect Enzymatic Analysis:

## Slide 3
Enzyme activity is measured in vitro under conditions that often do not closely resemble those in vivo. The objective of measuring enzyme activity is normally to determine the amount of enzyme present under defined conditions, so that activity can be compared between one sample and another, and between one laboratory and another.
The factors that affect the activity of an enzyme include substrate concentrations(s), pH, inhibitors and temperature.

## Slide 4
Reagent
For liver & kidney LDH
0.1 M Tris, pH 7.4,
1.5 mM sodium pyruvate - dilution range 0.05 to 0.5 mM
5 mM NADH (prepared fresh)
Enzyme extract
For muscle LDH,
0.1 M Tris, pH 7.4
0.1 M lactate stock solution - dilution range5 to 13 mM
5 mM NAD+ (Prepared fresh)
Enzyme extract

## Slide 5
The effect of pH on enzyme activity:
1- Enzymes are active only within a limited range of PH e.g. pH 5 to 10
2- The optimum PH which is the maximum activity is attained.
3- Six different PH buffers ranged from 4 to 9 have been used:
PH 4, and 5 were Acetate buffers
PH 6, and 7 were potassium phosphate buffers
PH 8, and 9 Tris buffer for for preparation see appendix).

## Slide 6
Bell-Shaped curve

## Slide 8
Method
B4
B6
B5
T4
B7
T6
T5
T7
B10
T8
B8
T10
In each 2.7 ml of buffer
0.1 ml substrate
0.1 ml of NADH
Read the absorbance at 340 nm

## Slide 9
The effect of Temperature on enzyme activity:
Temperature affects enzyme activity in much the same way as it affects other chemical reactions. Thus it is important when carrying out an enzyme assay to ensure that the temperature remains constant, and also that you know exactly what it is. Enzyme activity has been studied at different temperature 20, 30, 40, 50, 60 and 70 °C.

## Slide 10
Method
B20
B40
B30
T20
B50
T40
T30
T50
B70
T60
B60
T70
In each 2.7 ml of buffer
0.1 ml substrate
0.1 ml of NADH
Read the absorbance at 340 nm