## Slide 1
2 7 8
Micropipette Tutorial
From the Office of
Science Lab
Technical Assistant
CCC

## Slide 2
2 7 8
This is a Micropipette it is used to accurately transfer small quantities of liquid.
On this model the desired volume can be adjusted within the range of microliters (μL).

## Slide 3
Some Micropipettes have preset volumes and cannot be adjusted.
This pipette will only deliver 200μL.

## Slide 4
How does it work?
It works much like a syringe that would deliver an injection.
Inside there is a spring loaded piston that moves up and down.
2 7 8

## Slide 5
The plunger has two stops:
- at the First Stop the piston moves through the volume that is set on the pipette. (In this case 278μL)
2 7 8
2 7 8
278μL

## Slide 6
- The second stop is extra travel used for certain circumstances like evacuating the tip, or drawing up more than the volume indicated on the pipette
2 7 8
2 7 8
278μL
- Extra volume (? μL)

## Slide 7
- Find all three positions.
2 7 8
2 7 8

## Slide 8
2 7 8
Proper Use 

## Slide 9
2 7 8
Set the correct volume on your micropipette by turning the adjustment knob (typically the plunger button).
This pipette’s range is 200-1000 μL and is set to deliver 278μL
Setting Volume
2 7 8

## Slide 10
2 7 8
Settings can vary between models and manufacturer s.
This pipette’s range is 20-100 μL and is set to deliver 27.8μL
However you might see the following readings for this exact setting on different pipettes:
Setting Volume
2 7 8
2 7 . 8
2 7 8
The first two make the decimal places obvious,
while the last one implies the tenths place if you know the range.

## Slide 11
2 7 8
Settings can vary between models and manufacturer s.
This pipette’s range is 1-10 μL and is set to deliver 2.78μL
However you might see the following readings for this exact setting on different pipettes:
Setting Volume
2 7 8
2 .7 8
2 7 8
Some companies will change the color of the plunger button.

## Slide 12
Attaching tip
Be sure to choose the proper size tip.

## Slide 13
2 7 8
Attaching tip
Press the pipette into the tip firmly to create an airtight seal.

## Slide 14
2 7 8
Attaining a Sample
STEP ONE – press plunger to first stop and hold.
HOLD

## Slide 15
2 7 8
Attaining a Sample
STEP TWO – Insert tip into sample only far enough to ensure it stays submerged but not to the bottom where it will get blocked
HOLD
KEEP the pipette VERTICAL at all times

## Slide 16
2 7 8
Attaining a Sample
STEP THREE – Allow plunger to return to the home position SLOWLY so you don’t draw in air bubbles, or splash sample up into tip or the pipette itself.
KEEP the pipette VERTICAL at all times

## Slide 17
Attaining a Sample
Removed tip from sample before the plunger was all the way home
Likely allowed the plunger to move to home too quickly.
CORRECT

## Slide 18
2 7 8
Delivering the Sample
STEP FOUR – insert tip into the area you wish to deliver your sample. (in this case a gel for DNA fingerprinting)
KEEP the pipette VERTICAL at all times

## Slide 19
2 7 8
Delivering the Sample
STEP FIVE – depress the plunger slowly to the first stop, then continue to the second stop, this will evacuate the entire contents of the tip. And HOLD
HOLD
KEEP the pipette VERTICAL at all times

## Slide 20
2 7 8
Delivering the Sample
STEP SIX – While still holding the plunger at the second stop. Withdraw the tip from the well.
HOLD
KEEP the pipette VERTICAL at all times

## Slide 21
2 7 8
Delivering the Sample
STEP SEVEN – Allow the plunger to return home.
KEEP the pipette VERTICAL at all times

## Slide 22
2 7 8
Discarding the Tip
STEP EIGHT – Place tip into the opening of the waste container, then depress the tip ejector.
WASTE
Tip Ejector
Be sure to use a new tip each time.
KEEP the pipette VERTICAL at all times

## Slide 23
Things to AVOID !!
278
Never use a pipette in anything but a vertical orientation.

## Slide 24
Things to AVOID !!
278
Never use a pipette without a tip.

## Slide 25
HAPPY PIPETTING

## Slide 26
2 7 8

## Slide 27
2 7 8