## Slide 2
A Pharmaceutical powder is a mixture of finely divided drugs or chemicals in a dry form that may be intended for internal (oral powders) or external (topical or dusting powder) use.
Granules are prepared aggregates of powdered materials to form a larger particle (2-4 mm). Granules may be used as such (granules of medicinal value) or in making tablets and capsules (because of better flowability of granules compared to powders).
(Very fine particles do not flow as freely as large particles). The flowability of powders and granules is measured by
the angle of repose.

## Slide 3
1-Time-consuming preparation
2-Inaccuracy of dose( size of measuring spoon, density of powder, humidity, degree of settling , fluffiness.
3-Unsuitability for many unpleasant tasting, hygroscopic and deliquescent drugs
Disadvantage of powders:
Advantages of powders :
1-flexibility of compounding.
2-Good chemical stability as compared with fluids
3-Rapid dispersion of ingredients (because of small particle size causes more rapid dissolution in body fluids, increases drug bioavailability, and decreases gastric irritation compared with tablets)

## Slide 4: Powders as a dosage form may be provided to the patient in bulk or divided
1- Bulk Powders
Bulk powder is limited to non-potent drugs.
- The powder mixture is packed into a suitable bulk container to facilitate dosing, such as;
A wide mouth glass jar
A perforated or sifter can for external (dusting) powder, e.g.
Talc powder.
An aerosol container for topical application.
- dusting powder
- effervescent powder
- antacids, laxatives, dietary
nutrient supplements….
are multidose preparations consisting of solid, loose, dry particles of varying degrees of fineness. They contain one or more active ingredients, with or without excipients and, if necessary, coloring matter and flavoring substances.

## Slide 5
Examples for powders commonly dispensed in a bulk form
1- Powders used in a dry form
2- Powders to be dissolved in water before use
3- Powders for reconstitution
1- Powders used in a dry form
A- Powders for topical application e.g. antibacterial and antifungal powders, or non-
medicated powders e.g. Talc powder (protective action).
Dusting powders are applied to various parts of the body as lubricants, protective, absorbents, antiseptics, antipruritics, anti bromhidrosis agents, astringents and
antiperspirants.
B- Dental cleansing powders (Dentifrices) generally containing a soap or detergent, mild abrasive and an anticariogenic agent.
C- Insufflations: They are medicated finely divided powders to be applied into body cavity, e.g. ear, nose, throat or vagina, by means of a device known as "insufflator" or a powder blower. Specialized equipment has been developed for the administration of micronized powders of relatively potent drugs. The Norisodrine Sulfate Aerohaler Cartridge (Abbott) is an example
General purpose insufflator

## Slide 6
2- Powders to be dissolved in water before use
A- Antacids and laxatives (large dose) are used by mixing the directed amount of
powder (usually one teaspoonful) in a portion of water before swallowing
B- Dietary/Food supplements
C- Douche powders (e.g. vaginal douche) are dissolved in warm water before as antiseptics or cleansing agents for a body cavity application. They may be formulated for nasal, otic or ophthalmic use. Generally, since aromatic oils are included in these powders. Dispensing in wide-mouth glass jars serves to protect against loss of volatile materials and permits easy access by the patient

## Slide 7
Bulk powders in the market
Talc powder
(Perforated can)
Dental powder
Nutritional supplement

## Slide 8
3- Powders for reconstitution (important)
A- Oral antibiotic; for stability problems the antibiotic is prepared in a dry form (powder or granules) and packed in a sealed bottle, a given amount of water is added before use Once it is reconstituted the patient should be warned of the
short shelf life (usually 1-2 weeks).
B- Powders for injection;
They may be classified as bulk or divided powders. Injections of drugs that are unstable in solution must be made immediately prior to use and are presented as sterile powders in ampoules. Sterile water for injection is added from a second
ampoule and the injection is used immediately.

## Slide 9: 2- powders for external use
Examples:
- Douche powders
- Dentifrice powders
- Triturates
- Insufflations
- Dusting powders
Types of Bulk powders
1- Oral powders:
Examples: Antacid powder
Oral antibiotic powder
Laxative powder
These generally are supplied as finely divided powders or effervescent granules. The finely divided powders are intended to be suspended or dissolved in water or mixed with soft foods, e.g, applesauce, prior to administration

## Slide 10: 2- Divided powders
Divided powders are similar formulations to bulk powders but individual doses are separately wrapped.
Traditionally in papers (unsatisfactory for most products, specially if the ingredients are hygroscopic, volatile or deliquescent). Modern packaging materials of foil and plastic laminates have placed paper wrapping (WHY?)
because they offer superior protective qualities and are amenable to use on high speed packaging machines.
- They also may be dispensed in metal foil, small heat-sealed plastic bags or other containers
Examples:
- Packets
- Cachets
- Powders for injection

## Slide 11: Effervescent powders
Formulation
:
- Bulk powders or divided powders
- Packed in separate packages of contrasting colors.
- The contents are mixed in a quantity of water at the time of dosing.
- The liquid is consumed just after the reaction begin to subside

## Slide 14: Effervescent granules
* Contain sodium bicarbonate and either citric acid, tartaric acid or sodium biphosphate in addition to the active ingredients.
* On solution in water, carbon dioxide is released as a result of the acid-base reaction. The effervescence from the release of the carbon dioxide serves to mask the taste of salty or bitter medications.
* The completed product must be dispensed in tightly closed glass containers to protect it against the humidity of the air.

## Slide 16
Preparation of powders
1- Reduction of particle size of all ingredients to the same range to prevent stratification (separation of the large and small particles)
2- Sieving
3- Weighing each ingredient
4- Mixing
5- Packaging

## Slide 17
1- Size Reduction
Effect of particle size in Pharmacy
Smaller particle size and increased surface area, leads to:
Uniform distribution of the drug substance in a powder mixture or solid dosage form to ensure dose to dose content uniformity.
More impalpability and spreading of dusting and cosmetic powders
More stability of suspensions (suspendability of the particles intended to remain undissolved but uniformly dispersed in a liquid vehicle (fine dispersion 0.5-10µm)
Increasing rates of dissolution, reaction, drying, extraction, and bioavailability ..etc
Penetrability of particles intended to be inhaled for deposition deep in the respiratory tract (aerosols)1-5µm
Lack of grittiness of solid particles (ointments and creams)
Is the process of reducing large solid units or substance into smaller unit mass, coarse particles or fine particles. It is also termed comminution, grinding or pulverization.

## Slide 18
Disadvantages of excessive size reduction
Possible change in polymorphic form
Possible degradation by heat
Less flowability
Static charge problems
Air adsorption, hence, less wetting

## Slide 19
A. Mechanisms of size reduction on large scale
Compression: positive pressure, e.g., nut crusher, ball mill
Impact: material is stationary and hit by an object ,e.g., hammer mill
Shear: cutting force, e.g., scissors, colloid mill
Attrition: breaking the edges of the solid either by impact or particle collisions(fluid energy mill and roller mill)
Hammer mill
fluid energy mill
colloid mill

## Slide 20
a. Trituration
This method refers to the process of reducing substance to fine particles by rubbing them in a morter with a pestle. This method used in breaking up aggregates of powders.
B. Mechanisms of size reduction on small scale

## Slide 21
b.

## Slide 22: 2- Mixing(blending) of Powders
Importance:
Ensure an even distribution of the active component(s)
Ensure an even appearance of the dosage form
Ensure that the dosage form releases the drug at the correct site and at the desired rate
- Blending is used when two or more substances are to be combined to form a uniform powder mixture.
- Depending upon the nature of the ingredients and the amount of powder to be prepared, mixing may be by Spatulation, trituration, Levigation, or tumbling

## Slide 23: Small-Scale Mixing Equipment
1- Spatulation
The blending of powders with a spatula (movement through the powder) on a tile or paper sheet used sometimes for small quantities or when the mortar and pestle technique is undesirable.
It is not suitable for large quantities of powders or for powders containing one or more potent substance because homogenous blending may
not occur.

## Slide 24: 2- Trituration
This method is used to comminute ( reduce particle size) & to mix powders.
A porcelin preferred than glass morter.
A glass morter is preferrable for chemicals that stain a porcelin. When granular or crystalline materials are to be incorporated into powdered product ,these materials are comminuted individually and then blended together in the morter.

## Slide 26: 3- Levigation
In this process
A- paste is first formed by the addition of a suitable non-solvent to the solid material.
B-Particle-size reduction then accomplished by rubbing the paste in a mortar with a pestle or on an ointment’ slab using a spatula.
C- This technique is used to incorporate solids into ointment and suspension

## Slide 27
4- Tumbling (Large-Scale Mixing Equipment)
The ideal mixer should
1- produces a complete blend rapidly to avoid product damage.
2- It should be cleaned and discharged easily
3- be dust-tight
4- requires low maintenance and low power consumption.
- The powder enclosed in a large container which rotates generally by a motorized process
- Such blenders are widely employed in industry to blend large amounts of powders

## Slide 28
V-shape blender
Double cone blender

## Slide 29: Factors affecting mixing efficiency by tumbling mixers
1. Too high a rotation speed will cause the material to be held on the mixer walls by centrifugal force, and too low a speed will generate insufficient bed expansion and little shear mixing.
The addition of baffles or rotating bars will also cause convective mixing, for example the V‑mixer with agitator bar.
Presence of significant difference in particle size, as segregation is likely to occur.