## Slide 1
Opto 225 practice guide
Lens Power Measurement
Ms.Menwah AL-Matrafi,MSc
malmatrafi@ksu.edu.sa
Notes: <number>

## Slide 2: Methods of Lens Power Measurement
Trial lens hand neutralization
Lensometer
  Much greater accuracy may be obtained with the lensometer than with trial lens hand neutralization

## Slide 3: Trial Lens Hand Neutralization
Two lenses neutralize each other when placed in contact with each other so that the combined power of the two lenses is equal to zero
An unknown lens is neutralized by a known trial lens of equal power but opposite in sign

## Slide 4: Trial Lens Hand Neutralization

## Slide 5: Trial Lens Hand Neutralization
This is performed in the absence of a lensometer
It is used qualitatively as a means for estimation in many clinical and dispensing situations
It often involves simply identifying if it is a plus, a minus, or a toric lens
It more accurately estimates low power plus and minus lenses than toric lenses

## Slide 6: Trial Lens Hand Neutralization
It is used to measure the front vertex power of the lens

## Slide 7: Trial Lens Hand Neutralization
View a large distant cross target through the lens
Hold lens on visual axis, at arm’s distance
Align lens such that the cross target is continuous
Move lens vertically, observe motion of horizontal line
Move lens horizontally, observe motion of vertical line

## Slide 8: Trial Lens Hand Neutralization
For a plus or a minus lens, linear motion is used to neutralize power
  If observe “against motion,” use plus lens
  If observe “with motion,” use minus lens

## Slide 9: Trial Lens Hand Neutralization
For a plus or a minus lens, linear motion is used to neutralize power

## Slide 10: Trial Lens Hand Neutralization
For a toric lens, rotational motion is used to find the axis
  If observe “against motion,” use plus cylinder axis
  If observe “with motion,” use minus cylinder axis

## Slide 11: Trial Lens Hand Neutralization
For a toric lens, rotational motion is used to find the axis

## Slide 12: Trial Lens Hand Neutralization
Place known trial lens against front surface of unknown lens
No movement indicates neutrality
A minus or plus lens (i.e., a spherical lens) has the same speed and direction of motion in both the vertical and horizontal meridians
In the case of a toric lens (i.e., spherocylindrical lens), neutralize one limb of the cross target at a time

## Slide 13: Trial Lens Hand Neutralization
Example
  An unknown lens is neutralized in the horizontal meridian with +3.00D and the vertical meridian with +2.00D
  Prescription of unknown lens:
    +3.00 -1.00 x 180
  Power cross:

## Slide 14: Trial Lens Hand Neutralization
Large distant cross target

## Slide 15: Trial Lens Hand Neutralization
Plus lens

## Slide 16: Trial Lens Hand Neutralization
Minus lens

## Slide 17: Trial Lens Hand Neutralization
Toric lens

## Slide 18: Lensometry
Definition
  “Lenso” = lens
  “metry” = measurement of

## Slide 19: Lensometer

## Slide 20: Lensometer Purpose
Neutralizing a pair of glasses
  To determine the prescription
Verifying a pair of glasses
  To confirm the accuracy of fabricated glasses
Duplicating a pair of glasses
  To determine the prescription, and the lab duplicates the exact prescription

## Slide 21: Lensometer
It is used to measure the back vertex power or front vertex power of the lens

## Slide 22: Lensometer
To find the back vertex power, place the concave side of lens against lens stop

## Slide 23: Lensometer
To find the front vertex power, place the convex side of lens against lens stop

## Slide 24: Lensometer
In the case that the lens is a sphero-cylindrical prescription, the lensometer is used to determine the cylinder axis
It is used to locate the optical center of the lens
The lensometer is used to measure the amount of prism in the lens

## Slide 25: Lensometer Systems
Observation system (Keplerian telescope with two plus lenses, an inverted target image)
  Objective lens
  Eyepiece (ocular lens)
  Reticle (concentric circles and cross hairs focused by eyepiece)

## Slide 26: Lensometer Systems
Focusing system (Badal lens system)
  Light source
  Target (cross hairs)
  Standard lens (+20.00D)
  Lens stop
  Power wheel

## Slide 27: Lensometer Schematic

## Slide 28: Observation System
The Keplerian telescope consists of an objective lens, an eyepiece, and a reticle
The two plus lenses are positioned so that their two focal points coincide with each other
The unknown lens whose power is to be measured or neutralized is positioned at the lens stop (the location of the secondary focal plane of the standard lens)

## Slide 29: Lensometer Operation
With the instrument set at zero, an illuminated target (light source) is positioned at the focal length of a plus lens (standard lens) usually a +20.00D lens
Diverging rays of light from the illuminated target are bent by the standard lens and parallel light emerges from focusing system into the observation system, which is viewed through the telescope by the observer

## Slide 30: Lensometer Operation
When the lens of unknown power is introduced, the image of the illuminated target is thrown out of focus

## Slide 31: Lensometer Operation
The target is movable
By moving the target closer to or farther from the standard lens, the refractive power of the unknown lens can be neutralized
  Closer to standard lens for plus lens neutralization
  Farther from standard lens for minus lens neutralization

## Slide 32: Lensometer Operation
The physical distance forward or backward that the target moves indicates the power of unknown lens for the meridian being measured

## Slide 33
eyepiece
Lens holder
Lens stop
Axis wheel
Power wheel
Lens stage
Risley prism
Lensometer Anatomy

## Slide 34: Lensometer
reticule
target
1
2
3
Sphere line
Cylinder lines

## Slide 35: Lensometer

## Slide 36: Lensometer Preparation
Focus the eyepiece of the lensometer for the examiner’s eye
  With the power wheel set on zero, turn the eyepiece as far counter-clockwise as possible
  Then slowly turn it clockwise until the reticule first comes into sharp focus

## Slide 37: Lens Measurement Preparation
Insert the spectacles
  If testing a pair of glasses, always check the right lens first
  Place the pair of glasses in the lensometer with the ocular surface away from you
  The lens is held in place by the lens holder and is held level on the lens table
  Center the lens by moving it so that the image of the lensometer target is aligned in the center of the eyepiece reticle

## Slide 38: Single Vision Lens Measurement
To measure single vision lenses, either back vertex powers or front vertex powers must be found

## Slide 39: Single Vision Lens Measurement
Determine which part of the target is used for determining the spherical component and which part of the target is used for determining the cylindrical component
Rotate the power wheel until the lines (or the spots) are in clear focus
If the power is spherical, all the lines (or spots) will be clear
Note the power on the power wheel

## Slide 40: Types of Target

## Slide 41: Single Vision Lens Measurement
If the spherical and cylindrical lines do not come into focus at the same time, the lens has a cylindrical component
Rotate the power wheel until the spherical lines focus with the less minus (or more plus) power
Orient the target rotation dial (axis wheel) so that the spherical lines are perfectly straight

## Slide 42: Single Vision Lens Measurement
Read the power and record as the spherical component of the prescription
Focus the cylindrical lines by rotating the power wheel to more minus (or less plus) power (90 degrees away)
The difference in power between the two principal meridians is the amount of minus cylinder power in the lens
Read the axis of the cylinder from the axis wheel

## Slide 43: Single Vision Lens Measurement
Example
  +1.00 -2.00 x 120
  Power wheel sphere setting

## Slide 44: Single Vision Lens Measurement
Example
  +1.00 -2.00 x 120
  Power wheel cylinder setting

## Slide 45: Single Vision Lens Measurement
Mark the optical center (OC)
  Make sure that the lens is centered and the spectacle is sitting on the lens table evenly
  Use the OC marker on the lensometer to spot the lens
  Three dots will be marked
    The center dot marks the OC
    The other two dots indicate the 0 to 180 horizontal line
Position and read the second lens

## Slide 46: Single Vision Lens Measurement
When both lenses have been measured and marked, measure the distance between optical centers of the lenses (DBOC or geometric center distance)

## Slide 47: Multifocal Lens Measurement
To measure bifocal and trifocal lenses, front vertex powers must be found
  This is especially true for lenses with high distance and near powers
  Again, front vertex power is measured by turning spectacles around with back surface of the lens toward the operator (i.e., the convex side of the lens against the lens stop)

## Slide 48: Multifocal Lens Measurement
Measure the distance portion of multifocal lenses, in the same way as with single vision lenses
Turn the glasses around backward so that the temples face the operator
Find the distance front vertex power
Find the near front vertex power
Record the addition power (Add), which is the difference between the distance and near prescriptions

## Slide 49: Prism
Changes direction of light going through a lens

## Slide 50: Prism Purpose
To treat a binocular vision problem
To shift the visual field
To improve the lens appearance through prism thinning

## Slide 51: Prism
It is often divided equally between the two lenses of spectacles for balance and aesthetic reasons

## Slide 52: Types of Prism
Horizontal prism
  Base in (BI)
  Base out (BO)
Vertical prism
  Base up (BU)
  Base down (BD)
Oblique prism
  A combination of horizontal and vertical prisms

## Slide 53: Types of Prism and Lens

## Slide 54: Methods of Achieving Prism in Lens
Grinding
  Usually applied when a large amount of prism is required
  Lens is custom-made
  Optic center is often not on lens
Decentration
  Usually applied when a small amount of prism is required
  With spherical prescription, it is easier to deal with decentering than with spherocylindrical prescription

## Slide 55: Prism Measurement
The purpose is to verify if the prescription contains the desired prismatic effect
Verification of prism in prescription is done similarly to measurement of lens power using the lensometer
The only difference is in the means by which the target is positioned in the lensometer

## Slide 56: Prism Specification

## Slide 57: Prism Verification
To verify the prescribed prism when the amount of prism is known
  The center of the illuminated target is positioned at the location on the circular mires corresponding to the prism required

## Slide 58: Prism Verification
Example 1:
  If the right lens calls for 2 prism diopter BU, then the illuminated target would be positioned at the “2” ring above the center of the mires

## Slide 59: Prism Verification
Example 1:

## Slide 60: Prism Verification
Example 2:
  If both lenses contain 1.5 prism diopter BO, then the target would be placed at the 1.5 ring to the left of the center of the mires for the OD lens and to the right of the center of the mires for the OS lens
  Mark the major reference point (MRP) with the OC marker and measure the distance between the MRP of the lenses (i.e, the patient’s distance PD)

## Slide 61: Prism Verification
Example 2:

## Slide 62: Prism Measurement
In an unknown lens
  Patient may come in with a prescription that you are not sure if it contains prism in the lenses
  After power of the lenses are neutralized and the optic centers are marked, measure the distance between the optic centers (DBOC)
  If DBOC does not equal to the patient’s distance PD, then there is prism in the lens

## Slide 63: Prentice’s Rule
P = d * F
  P = prism power (in prism diopters)
  d = decentration (in cm)
  F = refracting power of the lens (in diopters)

## Slide 64: Prentice’s Rule
Example:
  Rx = -4.00DS OU
  Patient’s distance PD = 62mm
  DBOC = 72mm
  P = d * F
  = (72 – 62mm)/2 x 1cm/10mm * (-4.00D)
  = 0.5cm * (-4.00D)
  = 2 prism diopters BI in each lens

## Slide 65: Prentice’s Rule
Example:

## Slide 66: Recording
Record the prescription for each lens separately
Record the amount of induced prism in each lens, if applicable

## Slide 67: Recording
Example 1
  OD -3.00DS Add +2.00
  OS -1.50 -0.75 x 180 Add +2.00

## Slide 68: Recording
Example 2
  OD +2.50 -0.75 x 080 2 prism diopter BI
  OS +1.00 -0.25 x 110 2 prism diopter BI