## Slide 1: The Principles of Laboratory Safety
KSU Fellowship in Clinical Pathology
Clinical Biochemistry Unit
2016 – 2017

## Slide 2: Objectives
Understand the Laboratory hygiene.
Identify the laboratory hazards.
Take proper precautions to protect your self and others.
Act effectively in an emergency.

## Slide 3: What you need to know?
Risk assessment.
Laboratory hygiene.
Required PPE.
Safe working practices.
Emergency response.

## Slide 4: Why does it matter?
Safe working protects:
  You
  Other lab workers
  Cleaners
  Visitors
  Your work

## Slide 5: General Safety Rules
Lab safety is everyone’s responsibility.
Lab safety policy and procedures MUST be strictly followed.
You MUST perform RISK ASSESSMENTS.

## Slide 6: How to do a Risk Assessment?
Determine hazards and evaluate risks
Use all relevant available data
Determine controls needed to minimise those risks
Document the assessment
Agree it with your supervisor
Use those control measures
You will receive specific training on how to do this
in your department

## Slide 7: Materials Safety Data Sheets (MSDS)
Are to be provided by Supplier’s with all deliveries
MUST be Accessible to EVERYONE in the workplace
Must be current
Must be made available to attending physician in the event of exposure

## Slide 8: The MSDS tells you:
Identity.
Ingredients.
Hazards identification.
First aid.
Fire fighting.
Accidental Release Measures/Spill Clean-up.
Handling and storage - Exposure controls and Personal Protection.
Physical and chemical properties.
Disposal.

## Slide 9: Laboratory hygiene
Never eat, drink or smoke in a laboratory
Never apply cosmetics
Never touch your face, mouth or eyes
Never suck pens or chew pencils
Always wash your hands before you leave
Roll up loose sleeves.

## Slide 10: Laboratory hygiene
Keep your workplace tidy
Clear up waste, deal with washing up and put things away as you finish with them
Make sure everything is safe before you leave things unattended
A tidy laboratory avoids accidents to everyone
X

## Slide 11: Protecting yourself
Always use appropriate clothes and personal protective tools:
  Lab coat.
  Safety goggles.
  Masks.
  Gloves.
  No open shoes.
  No eye lenses.
Know the location of:
  Fire extinguisher and fire blanket.
  Shawer and eyewash stations.
  First aid kit.

## Slide 12: Protecting yourself
Wear the clothing and protective wear identified in your risk assessment
Laboratory coats must be kept fastened
Don’t wear sandals or open shoes
Long hair must be tied back

## Slide 13: Protecting yourself - gloves
There are many different types of protective glove
Use the correct ones for the job you will be doing
Remember that you need to select chemical protection gloves according to the materials and/or substances with which you will be working
Remove your gloves before using instruments, telephone or leaving the laboratory

## Slide 14: What are the general hazards in a laboratory?
Fire
Breakage of glassware
Sharps
Spillages
Pressure equipment & gas cylinders
Extremes of heat & cold
Chemical hazards
Biological hazards
Radiation
  And many more!

## Slide 15: Avoiding Fires
Flammable substances
  Use minimum quantity
  Store in special storage cabinet
  Use temperature-controlled heating sources
    (eg water-bath rather than hot-plate or Bunsen burner)

## Slide 16: Minimise fire damage
Make sure corridor fire doors and laboratory doors are kept shut at all times

## Slide 17: Fire Safety
Make sure that you know what to do:
  If you have a fire
  If you hear a fire alarm
If you are a member of staff you must attend fire training annually. Post graduates should also seriously consider doing so.

## Slide 18: Fire Safety- R.A.C.E
Procedures to follow in the event of a fire emergency
R – Remove or secure individuals in immediate danger.
A – Activate the alarm by pulling a fire pull station located
in the corridors and calling 953.
C – Confine the fire by closing windows, vents, and doors.
E – Evacuate to a safe area.

## Slide 19: Fire extinguisher

## Slide 20: Glassware
Use correct techniques for the insertion of tubing onto glassware
Never use glassware under pressure or vacuum unless it is designed for the job and suitably shielded
Dispose of chopped or broken glassware – it is a risk to you and others
Always dispose of broken glass in a glass bin or sharps bin and not in a general waste bin

## Slide 21: Spillages
Clear up spillage promptly
You will already have determined how to do this as part of your risk assessment
Dispose of any hazardous material as toxic waste
Messy workers are usually poor workers!!

## Slide 22: Gas cylinders
Never use without formal training
Minimise the number in a laboratory
  Store externally whenever possible
Cylinders are heavy and can do serious damage to you if they fall
  Ensure that they are chained when in use
  Move only with a cylinder trolley
Use regulators & control equipment suitable for the gas concerned
Consider the consequences if your cylinder leaks

## Slide 23: Cryogenics
Liquid gases are extremely cold and can cause burns
Liquid gases evaporate and many can cause asphyxiation
If you need to take cryogens in a lift, there are special procedures to follow – speak to your supervisor or a senior member of technical staff
You must have special training to use them

## Slide 24: Electrical Equipment
Always do a visual check on electrical equipment before use, looking for obvious wear or defects
All portable electrical equipment must have a current “PAT test” sticker
NEVER use defective equipment
Lay electrical cords where no one can trip on them.
Be sure your hands and your lab area are dry before using electrical equipment.
Unplug cords by pulling the plug, not the cord.

## Slide 25: Laboratory Equipment
Never use any laboratory equipment unless you are trained & have been authorised to do so
As well as injuring yourself you may cause very costly damage

## Slide 26: First Aid
All laboratory workers should undergo simple first aid training
  For ALL chemical splashes, wash with plenty of water for 10 minutes
  Control bleeding with direct pressure, avoiding any foreign bodies such as glass
Report all accidents to your supervisor or departmental safety officer

## Slide 27: Protecting your health
If you have an allergy to lab materials or suffer from a medical condition which may affect you in the laboratory (eg diabetes or epilepsy), ensure that your supervisor knows

## Slide 28: Biological Safety
All biological samples are considered potentially infectious.
Should be handled and processed using strict precautions.

## Slide 29: Waste Materials
Part of your risk assessment will be to determine how to dispose of waste lab materials safely
  Solvents and oils must be segregated into the correct waste bottle or drum
  Your department will help you determine what to do with chemical or biological materials
Do not put materials down the drain or in with normal waste unless authorised to do so

## Slide 30: Working outside normal hours and at weekends
You will need to attend training courses and have permission from the head of the department before working outside normal hours
Most experimental work is not permitted
Your supervisor will explain the requirements in more detail

## Slide 31: When in doubt – ASK!!!
Do not carry out a new or unfamiliar procedure until you have been fully trained & understand the precautions necessary for safe working.
DO NOT GUESS!!!!

## Slide 32: Key Points to Remember
Remember these four basic principle of laboratory safety:
Conduct a risk assessment for each protocol you perform.
Select appropriate safety measures.
Maintain a safe laboratory environment.
Prepare for emergencies.