## Slide 1: PROCESS CONTROL
CHAPTER I
INTRODUCTION

## Slide 2: Introduction
In any industrial plant the aim is to produce standard and high quality products and sell them at prices which make profit. These purposes can be achieved in a successfully designed and controlled processes.

## Slide 3: Operational Objectives
Safety
Production Specifications
Environmental Regulations
Operational Constraints
Economics

## Slide 4
Optimization: combination of several variables together with most suitable conditions.
Optimum conditions are important for
Continuity
Quality
Economics
of processes.
“main variable”

## Slide 5
Important Characteristics of Process Control Systems
The focus of the engineer must be on the process. (Pc)
The dynamic behavior of the individual units and the process as a whole is to be understood.
It is always the best to utilize the simplest control system that will achieve the desired objectives.
The design of a process determines how it will respond dynamically and how it can be controlled.

## Slide 6
CONTROL: To maintain desired conditions in a physical system by adjusting selected variables in the system.
Some Examples:
Consider the continuously
mixed heating tank. Where aim is to provide constant temperature for the output fluid.

## Slide 7
Consider a person driving an automobile with an objective of staying in a specific lane.
Determine the location of the automobile
Determine or calculate the change required to maintain the automobile at its desired position on the road
Change the position of the steering wheel by the amount calculated to bring about the necessary correction.

## Slide 8
Consider a house in a cold climate which is to be maintained near a desired temperature by circulating hot water through a heat exchanger
Temperaturere of the room is determined by a thermostat
This temperature is compared with the desired temperature or range of temperature
If the temperature is below than the desired, the furnace and the pump are turned on; if the temperature is above the furnace and pump are turned off.

## Slide 9
Controller
Final Control
Element
Measuring Element
Process
Desired value
inputs
outputs

## Slide 10: input output
Input refers to a variable that causes an output.
Driving example;
input: steering wheel position
output: position of the automobile
Heated room example;
input: fuel to the furnace
output: room temperature

## Slide 11: In any process desired value is defined based on Control Objectives
Control Objectives:
Safety
Environmental Protection
Equipment Protection
Smooth Plant Operation and Production Rate
Product Quality
Profit Optimization
Monitoring and Diagnosis

## Slide 12: Important Characteristics of Process Control Systems
Focus of the engineers must be on the process. (Pc)
The dynamic behavior of the individual units and the process as a whole is to be understood.
It is always best to utilize the simplest control system that will achieve the desired objectives
The design of a process fundamentally determines how it will respond dynamically and how it can be controlled.

## Slide 13: 1.What does a control system do?
Control: To maintain desired conditions in a physical system by adjusting selected variables in the system.
In control Systems:
A specific value or range is used as a desired value for the controlled variable
The conditions of the system are measured
Each system has a control calculation or algorithm
The results of calculation are implemented by final control element

## Slide 14: Control Types
Feedback Control; uses direct measurements of the controlled variables to adjust the values of the manipulated variables. The objective is to keep the control variables at desired levels.
Feedforward Control; uses direct measurement of the disturbances to adjust the values of the manipulated variables. The objective is to keep the controlled output variables at desired levels.
Cascade Control; different combinations of two types

## Slide 15: 2. Why is Control Necessary?
There are two main reasons for control.
The first reason for control is to maintain the measured variable at its desired value when disturbances occur.
The second reason for control is to respond to changes in the “desired value”.
In the analysis of plant operation the desired values are determined by control objectives.

## Slide 16: 3. Why is Control Possible?
The proper design of plant equipment is essential for plant control to be possible and for control to provide good dynamic performance.
Sensors should be
Correct
Fast
With enough capacity.
which are based on adequate equipment design.

## Slide 17: 4. How is Control Done?
A process can be controlled either by human beings manually or by necessary instrumentation automatically.
Automobile driving example; feedback control by human action
Most automatic control is implemented with electronic equipment which uses levels of current or voltage to represent values to be communicated.

## Slide 18: 5. Where is Control Implemented?
Control items as sensors and final control elements are in the process and displays and control calculations might be both in the process and in the centralized control facility.
Generally the plant never operates on “automatic pilot” and a person is always present
to perform tasks not automated
to optimize operations
to interfere with situations when an unusual or dangerous situation occurs.

## Slide 19: 6. What Does Control Engineering “Engineer”?
Process Design
Measurements
Final Control Elements
Control Structure
Control Calculations

## Slide 20: 6.1. Process Design
A key factor in control engineering is the design of the process so that it can be controlled well. For this purpose systems should be responsive and few disturbances should occur.
“A responsive control system” means the controlled variable responds quickly to adjustments in the manipulated variable.
Frequency and magnitude of disturbances should be reduced.

## Slide 21: 6.2. Measurements
The important decisions are
selection
location
of the sensors.
“one can control only what is measured”
The engineer should select sensors that measure important variables rapidly, reliably and with sufficient accuracy.

## Slide 22: 6.3. Final Control Elements
Final control elements provide the necessary changes in manipulated variables which are determined by control calculations. The selection of best final control element and selection of the location are important considerations.

## Slide 23: 6.4. Control Structure
The engineer must decide some very basic issues in designing a control system.
This is similar to adjusting either the hot or cold water valve opening to control the temperature of water in a shower or making this directly on the heating source.

## Slide 24: 6.5. Control Calculations
After the variables and control structure have been selected the model equations are developed which use the measured and desired values in calculating the change in manipulated variable.

## Slide 25: 7. How is Process Control Documented?
The studies on process control system should be documented in order to be
understandable
stable
In order to avoid misunderstanding , standard symbols developed by Instrument Society of America (ISA) are used.

## Slide 26
In standard Drawing:
all process equipment is drown in solid lines
sensors are designated by a circle connected to the point in the process where they are located
process control loops are shown by dashed lines.

## Slide 27
The first letter in the instrumentation symbol indicates the type of variable measured
The subsequent letter(s) give information about the function performed.
A | analyzer
F | Flow rate
L | Level of liquid or solid
P | Pressure
T | temperature

## Slide 28: 8. What are Some Simple Control Strategies?
In the plant there exist a large number of possibilities for placing sensors and final control elements.
Every process control system is to be verified for;
Casual process relationship
Determination of the action the controller would take in response to a disturbance or a change in desired value.

## Slide 29: PROCESS CONTROL LAWS !
First Law: The best control system is the simplest one that will do the job.
Second Law: You must understand the process before you can control it.
Third Law: The control is never possible if the mathematical model can not be developed.

## Slide 30: Behavior of System Variables
1. In process control two types of variables exist
Manipulated variables, which can be adjusted
Controlled variables, which are affected by the adjustments.
2. There exists a specified range for the variables.
3. The effectiveness of control to maintain the process at desired conditions depends on;
Sign and magnitude of response
Speed of response
Shape of response
4. The analysis of the possible variations in the system and sensitivity of the dynamic behavior to those variations are important in the modeling.

## Slide 31: Feedback Control
TT
Controller
steam
Heat exchanger
Final control element
Sensor (Temperature Transmitter)

## Slide 32
If the inlet process temperature decreases, thus creating a disturbance, its effect must propagate through the heat exchanger before the outlet temperature decreases. Once this temperature changes, the signal from transmitter to the controller also changes. It is then that the controller becomes aware that a deviation from set-point has occurred and that it must compensate for the disturbance by manipulating the steam valve. The controller then signals the valve to increase its opening and thus increase the steam flow.

## Slide 33
The advantage of feedback control is that it is a very simple technique that compensates for all disturbances. Any disturbance affects the controlled variable and once this variable deviates from set point , the controller changes its input in such a way as to return the temperature to the set point.
The feedback loop does not know, nor does it care, which disturbance enters the process. It tries only to maintain the controlled variable at set point and in so doing compensates for all disturbances.

## Slide 34
The feedback controller works with minimum knowledge of the process. In fact, the only information it needs is in which direction to move. How much to move is usually adjusted by trial and error.
Feedback control is the most common control strategy in the process industries. Its simplicity accounts for its popularity.

## Slide 35
The disadvantage of feedback control is that it can compensate for a disturbance only after the controlled variable has deviated from set point. That is, the disturbance must propagate through the entire process before the feedback control scheme can initiate action to compensate it.

## Slide 36: Feed forward Control
TT
Controller
steam
Heat exchanger
Final control element
Sensor (Temperature Transmitter)

## Slide 37
The objective of feed forward control is to measure the disturbances and compensate for them before the controlled variable deviates from set point. If applied correctly, the controlled variable deviation would be minimum.
Suppose that in heat exchanger example the major disturbance is the inlet temperature. To implement feed forward control the disturbance first must be measured and then a decision is be made how to manipulate the steam to compensate for this change.

## Slide 38
The complements of process control to engineering implies that for a good control design is important and is a result of a hierarchy of control objectives which depend on the operating objectives for the plant.
We would like processes to run at the designed steady state, however processes would not.

## Slide 39
In designing control systems or strategies the dynamic behavior of the process is very important, therefore we should have knowledge about process dynamics and modeling.

## Slide 40: Major Steps in Control System Development

## Slide 41
FINAL CONTROL SYSTEM
Control Objectives
Develop Process Model
Devise Control Strategy
Select hardware and software
Install Control System
Adjust Controller Settings
Available Information
Physical and
Chemical Principles
Process Control
Theory
Experience
Management
Objectives
Computer
Simulation
Available Data
Computer
Simulation
Vendor
Information
Engineering Activity
Information Base

## Slide 42: Example 1
steam
F, T
Fi, Ti
h
Fst
Consider the tank heating system shown in the figure.
A liquid enters the tank with a flow rate Fi (ft3/min) and a temperature of Ti (0F) where it is heated with steam having a flow rate of Fst (lb/min). Let F and T be the flow rate and temperature of the stream leaving the tank.
The tank is considered to be well stirred, which implies that the temperature of the effluent is equal to the temperature of the liquid in the tank.

## Slide 43
The control objectives of this heater are:
To keep the effluent temperature T at the desired value Ts.
To keep the volume of the liquid in the tank at a desired value Vs.
The operation of the heater is disturbed by external factors such as changes in the feed flow rate Fi and temperature Ti. ( If nothing changed, then after attaining T=Ts and V=Vs we could leave the system alone without any supervision and control.

## Slide 44
F, T
Fi, Ti
Thermocouple
Controller
Set-point
A thermocouple measures the temperature of the fluid in the tank. Then this temperature is compared with the desired value yielding a deviation
ε = Ts – T
The value of deviation is sent to a control mechanism which decides what must be done in order for the temperature to turn back to the desired value.

## Slide 45
F, T
Fi, Ti
Thermocouple
Controller
Set-point
Notice that feed forward control does not wait until the effects of the disturbances has been felt by the system, but acts appropriately before the external disturbance affects the system anticipating what its effect will be.

## Slide 46
F, T
Fi, Ti
Level Measuring
Device
Controller
To keep the volume at its set point or the liquid level hs we measure the level of the liquid in the tank and we open or close the effluent flow rate.
hs

## Slide 47
F, T
Fi, Ti
Level Measuring
Device
Controller
hs

## Slide 48
F, T
Fi, Ti
Controller
FT

## Slide 49
For this example;
input variables are: Fi, Ti and Fst (which denote the effect of surroundings on the process)
output variables are: F, V and T (which denote the effect of process on the surroundings)

## Slide 50
The input variables can be further classified into the following categories:
Manipulated (or adjustable) variables, if their values can be adjusted freely by the human operator or a control mechanism.
Disturbances, if their values are not the result of adjustment by an operator or a control system.

## Slide 51
The output variables are also classified into the following categories;
Measured output variables, if their values are known by directly measuring them.
Unmeasured output variables, if they are not or cannot be measured directly.

## Slide 52
For any system, definition of manipulated and controlled variables can only be made depending on specified control structures.