## Slide 1: Spectrophotometric methods for determination of proteins
BCH 333 [practical]

## Slide 2
Objectives:
Determination of proteins using three spectrophotometric methods:
Bicinchoninic acid (BCA, Smith) Method.
Bradford Method.
Warburg-Christian Method ( A280/ A260 Method).

## Slide 3
Quantitative
Qualitative
refers to descriptions or distinctions based on some quality or characteristic rather than on some quantity or measured value. It can be a form of analysis that yields the identity of a compound.
refers to a type of information based in quantities or else quantifiable data

## Slide 4
-In this experiment three of these methods will be studied. Two are newer methods which are widely used and one is an older method.
-In the newer methods chemical reagents are added to the protein solutions to develop a colour whose intensity is measured in a spectrophotometer.
The third method relies on direct spectrophotometric measurement.

## Slide 5
1.Bicinchoninic acid (BCA, Smith) Method:
-The method has a high sensitivity, as low as 1 μg protein can be detected.
-The reagents are available as kits.
Principle:
The blue colour resulting from this method is due to
complex formation of the nitrogens of the peptide bonds with Cu2+ producing Cu+ under alkaline conditions.
b) Cu+ chelated by BCA to produce a copper-BCA complex with maximum absorption (λmax) of 562 nm.

## Slide 7
2.Bradford Method:
-This method is based on protein binding of a dye to arginine residues.
-Fast, accurate and high sensitivity [1 μg protein can be detected].
-The method is recommended for general use, especially for determining protein content of cell fractions and assessing protein concentrations for gel electrophoresis, about 1- 20 μg protein for micro assay or 20-200μg protein for macro assay.

## Slide 8
Principle:
-Binding of the dye Coomassie Brilliant Blue G-250 to protein in acidic solution causes a shift in wavelength of maximum absorption (λmax) of the dye from 465nm to 595nm.
-Both hydrophobic and ionic interactions stabilize the anionic form of the dye, causing a visible colour change.
-The absorbance at 595nm is directly proportional to the concentration of the protein. [The colour is stable for one hour.]

## Slide 9
3.Warburg-Christian Method ( A280/ A260 Method):
Is easy, sensitive and fast. It has a sensitivity of about 0.05- 2.0 mg protein/ml.
it is not accurate.
Principle:
-This method is based on the relative absorbance of proteins and nucleic acids at 280nm and 260nm.
-Tyrosine and tryptophan residues in a protein absorb in the ultraviolet at 280nm. Since the amounts of these residues vary greatly from protein to protein, the method is best used only for semiquantitative analysis of protein samples.
-Nucleic acids which contaminate samples interfere with this method. This problem is overcome by the fact that nucleic acids absorb more strongly at 260nm than at 280nm, while the reverse is true for proteins.

## Slide 10
-Calculate the protein concentration in the unknown from the following equation:
-[A280 x correction factor =……… mg/ml protein].
-or [groves formula]:
Protein concentration [mg/ml]=[1.55 X A280]-[0.76 X A260]
A280 _________
A260 __________
A280/ A260 _________
Correction factor ______________
Unknown concentration ________________________ mg/ml

## Slide 11
-A protein solution that has a low A280/A260 ratio: Highly contaminated by DNA.
[It shows a higher absorbance at 260nm comparing to absorbance at 280nm.
-A protein solution that has a high A280/A260 ratio: Less contaminated by DNA.
[It shows a lower absorbance at 260nm comparing to absorbance at 280nm.

## Slide 12
Questions:
-Reaction requires alkaline condition?
-methods depends on the absorption properties of proteins molecules in the solution?
-Bicinchoninic acid method and biuret test are both quantitative tests and depend on reducing Cu+2. [ ]