## Slide 1: Quality control of tablets
Lecture 2
Notes: <number>

## Slide 2: Dissolution
 It is a routine quality control procedure. The dissolution rates also helps to correlates the bioequivalence of drug products.
 To ensure that the preparation comply with product specification, as it is a requirement for regulatory approval of marketing for the registered product.
 To indicate the performance of the preparation under the in vivo conditions.
To differentiate between formulations and to evaluate the possible effect of the formulation and other processes variables on drug bioavailability.
Notes: <number>

## Slide 3: Factors affecting dissolution of a tablet
1. Disintegration is the important first step to drug dissolution in a tablet.
2. Particle size of drug substance.
3. Solubility and hydrophobicity of the drug; type and amount of disintegrant, diluent, binder, lubricant, glidant and the coating type and thickness.
4. Solubility and dissolution also influenced by pH of the media, media composition, change in the crystalinity of drug, temperature, paddle speed.
5. Manufacturing method (compactness of the granulation and compression force used in tableting)
Dissolution test is a standard requirement for tablets and capsules.
USP gives standards for tablet dissolution; there are many apparatus for drug release and drug dissolution for immediate release, extended release and enteric-coated tablets.
Notes: <number>

## Slide 4
The rate of dissolution is given by Noyes and Whitney:
Where,
dc/dt= dissolution rate of the drug
K= dissolution rate constant
Cs= concentration of drug in stagnant layer
Cb= concentration of drug in the bulk of the solution at time t
=
k (Cs- Cb)
dc
dt
<number>

## Slide 6: Dissolution test apparatus
Stirrer shaft
Paddle
Thermostated water bath
Glass vessel
USP apparatus II
Notes: <number>

## Slide 7
Glass vessel 1000 ml volume
Cylindrical Stainless
steal Basket formed
from a screen
(USP apparatus I)
Paddle
(USP apparatus II)
Stirrer shaft
Notes: <number>

## Slide 8: Stirred vessel method
Basket type
Paddle type
Notes: <number>

## Slide 9: Media used in dissolution test: - Purified water. - Simulated gastric fluid. - Simulated intestinal fluid. - Solvents mixture may be used if the drug solubility is very low.  Dissolution test is performed in-process and on the final product.
Notes: <number>

## Slide 10: • The amount of drug dissolved within a certain time period is determined by taking samples from the dissolution medium and analyzed after specified time intervals. • Limit (BP): 75% of the drug should be dissolved within 30 minutes, unless otherwise specified by the manufacturer.
Acceptability criteria for immediate release tablets (USP):
Q, is the amount of dissolved active ingredient specified in individual monograph, expressed as percentage of labeled content of dosage unit.
Stage | Units | Acceptance Criteria
S1 | 6 | Each unit is not less than Q + 5%
S2 | 6 | Average of 12 units (S1 + S2) is equal to or greater than Q, and no unit is less than Q-15%.
S3 | 12 | Average of 24 units (S1 + S2 +S3) is equal to or greater than Q, not more than 2 units are less than Q-15%, and no unit is less than Q-25%.
Notes: <number>

## Slide 11: Friability test
Tablets that tend to powder, chip & fragment when handled:
1. lack elegance & consumer acceptance.
2. Create excessive dirt/ dust in areas of manufacturing as coating & packaging.
3. Can also add to a tablet's weight variation or content uniformity problems.
Why measure friability?
Notes: <number>

## Slide 12: Another application of the friability test capping or laminate when stressed by attrition inside the rotating drum of friability tester.
Capping
Lamination
Good tablet
Notes: <number>

## Slide 13:  The laboratory friability tester is known as the Roche friabilator.  To examine this, tablets are subjected to uniform tumbling motion for specified time and weight loss not more than 1% generally is considered acceptable for most products. % friability = (W0 – Wf / W0) x %. W0 = initial weight. Wf = final weight.
Friabilty tester
Notes: <number>

## Slide 14: Tablets damaged during friability testing
Number of tablets selected for friability test:
Tablet unit weight less than ≤ 650 mg: Take a sample of whole tablets as near as possible to 6.5 g.
Tablet unit weight more than or equal > 650 mg: Take a sample of whole 10 tablets.
Notes: <number>

## Slide 15: There are many tests are frequently applied to tablets for which there are non-pharmacopoeial requirements but will form a part of manufacture's owner product specifications. 1- Tablet thickness. 2- Tablet hardness. 1. Hardness (Fracture-resistance test):  In general, tablets should be sufficiently hard to resist breaking during normal handling, packaging and shipping, and yet soft enough to disintegrate properly after swallowing.  Hardness of the tablet is controlled by (or is affected by) the degree of the pressure applied during the compression stage.  Hardness is an important criterion, since it can affect disintegration and dissolution.
II. Unofficial tests
Notes: <number>

## Slide 16: Tablet Hardness: The force required to break a tablet along its diameter by applying compression loading. Determine the crushing strength of the tablets. The crushing strength that just causes the tablet to break is recorded (in kg). Tablet hardness should be between 6 – 10 kg.
The Electronics Tablet Hardness tester
Tablet hardness tester
Notes: <number>

## Slide 17:  If the tablet is too hard, it may not disintegrate in the required period of time to meet the dissolution specifications; if it is too soft, it may not be able to withstand the handling during subsequent processing such as coating or packaging and shipping operations.  Chewable tablets are usually much softer (3 kg) and some sustained release tablets are much harder (10-20 kg).  Hardness Variation depends on - compression force, - concentration and type of binding agent
Notes: <number>

## Slide 18: 2. Tablet thickness Tablet thickness is important for tablet packaging; very thick tablets affect packaging either in blisters or plastic containers. The tablet thickness is determined by the diameter of the die, the amount of fill permitted to enter the die and the force or pressure applied during compression
Micrometer (tablet thickness)
Notes: <number>

## Slide 19: Tablet processing problems
1- Capping and lamination
2- Picking and sticking
3- Tablet mottling
4- Binding
1. Capping and lamination:
 Capping occurs when the upper segment of the tablet separates from
the main portion of the tablet & comes off as a cap.
Is a partial or complete separation of the top or bottom crown of tablet from the main body
 Lamination that the tablet splits at the sides into two or more distinct layers.
If tablets laminate only at certain stations, the tooling is usually the cause.
These problems are readily apparent immediately after compression. Friability is the earlier and quickest way of revealing such problems.
Notes: <number>

## Slide 20
These problems are usually caused by: - Air entrapment during compression process among the particles or granules, the resulting tablet expand when the pressure of the tableting is released, resulting in splits or layers in the
tablet.
- Rapid decompression results in tablets that fracture (stress-relaxation)
If the compression is too rapid, air is not given time to escape but remains trapped within the tablet until released by removal of the pressure. Excessive pressure cause slight expansion of the tablet after the pressure is released and capping might occur.
- Excess amount of lubricant which may decrease the tablet strength due to their interference
with the bonding between the particles during compression.
- The binder may be insufficient in amount or unsuitable . Therefore, the granules will be friable and lacking in cohesion.
- Overdrying of granules (granules require a certain moisture content, to assist the action of the binder in producing a firm tablet). - In new punches and dies that are tight fitting this may occur with new sets of tools, when
the air in the granule cannot escape between the upper punch and the die wall.
- The die wear a ring in the area of compression by constant friction so the tablet is distorted within the die causing capping on ejection.

## Slide 21: - Incorrect setup press. If the punch remains below the face of the die, the sweep-off blade cuts off the tablet, leaving the bottom in the die. - An incorrect adjustment of the sweep-off blade can also result in tablet fracture. Elimination of capping & laminating: 1. Increasing the binder. 2. Adding dry binder such as gum acacia , PVP or powdered sugar. 3. Decreasing the upper punch diameter and using flat punches. 4. Slowing the tabletting rate. 5. Reducing the final compression pressure. 6. For moisture-critical granulations, the addition a hygroscopic substance e.g. methylcellulose or polyethylene glycol PEG4000, can help to maintain proper moisture level.
- A deep Concave punches produce tablets that cap. The curved part of such tablets expands
while the body of the tablet cannot, which establishes a shear stress that produces the fracture.
Notes: <number>

## Slide 22: 2- Picking is the removal of the surface material of the tablet by the punch (a portion of the tablet surface is missed). Sticking is the adhesion of the tablet materials to the die wall (dull, scratched, or rough tablet faces). These problems are caused by excessive moisture or the inclusion of materials with low melting point (PEG & stearic acid) in the formulation. This problem could be managed by addition of suitable anti-adherent. Increase lubrication.
Picking
Sticking
Additional binder may make the granules more cohesive. Colloidal silica added to the formula acts as a polishing agent and makes the punch faces smooth. Dilution of the active ingredient with additional higher melting point materials and consequent increase in the size of the tablet may help.
Notes: <number>

## Slide 23: 3- Tablet mottling is unequal color distribution, with light or dark areas. This problem occurs when a drug has different color than the tablet excipients or when a drug has colored degradation products. This problem also caused by intragranular migration of the soluble dye during the drying stage which may give rise to dry granules with a highly colored outer zone and interior. During compaction granules are fractured and the colorless interior is exposed resulting in mottled tablet.
To overcome this difficulty, change the solvent and binder system, reduce the drying temperature, grind to smaller particle size.
Notes: <number>

## Slide 24
- Migration of colors may be reduced by drying the granulation slowly at low temperatures and stirring the granulation while drying.
- Addition of natural starches, or dye migration inhibitors such as acacia 3%, tragacanth 1%
and talc 7%.
- Using dye lakes (combination by adsorption of a water-soluble dye to a hydrous oxide of a heavy metal resulting in an insoluble form of the dye)