## Slide 1: Radiology of the abdomen
Radiology department
Dr. A. Alhawas

## Slide 2: Outline:
Imaging modalities used to study the abdomen.
Anatomy and normal appearance of the abdomen.
Common pathological cases.

## Slide 3: Imaging modalities:
Conventional X-Ray.
Barium studies ( flouroscopy )
US.
CT.
MRI.
Nuclear medicine.

## Slide 4: Conventional Radiography (X-ray)
Often used as first imaging modality.
Cheap.
Useful for some radio-opaque stones and bowel obstruction and localization of the catheters.

## Slide 5: Radiograph (X-ray)
Image features:
  Projectional image.
  Image contrast determined by tissue density.
  Good evaluation for the bones, bowel distension and constipation.
  Can be portable.
Disadvantages:
  Radiation ( minimal ).
  Poor soft tissue contrast

## Slide 6: Barium studies ( fluoroscopy )
Often used in GIT abnormalities.
Cheap.
Use barium or gastrographin.
Recently replaced by endoscopy and colonscopy.
Useful in assessing esophageal motility and small bowel.

## Slide 7
Image features:
  Projectional image.
  Image contrast determined by tissue density and oral contrast.
  good evaluation of GIT.
Disadvantages:
  Radiation.
  Poor soft tissue contrast

## Slide 8
It has many procedures such as:
Barium swallow.
Barium meal.
Small bowel follow through.
Small bowel enema
Barium enema.

## Slide 10: US
Ultrasound.
Use high frequency sound wave ( no radiation hazard ).
Contrast between tissue is determined by sound reflection, depend on nature of the organ and physical density.

## Slide 11: US
Good resolution.
Used to assess the liver, GB, vascular structures, kidneys, UB, pancreas and spleen.
Real time imaging and fast scan
Can be done portable.
Disadvatages:
  Operator dependant.

## Slide 12
B mode:
C mode :

## Slide 13: Computed Tomography ( CT )
Same basic principle of radiography
More precise
costly.
Can not be done portable.
Useful for trauma, stone, tumor, infection.
Scan time usually takes few minutes ( 1 – 7 minutes ).

## Slide 14: CT:
Image features:
Cross sectional images.
Image contrast determined by tissue density +/- contrast.
Better evaluation of soft tissue.
Can assess vascular structures =) need I.V. contrast.
It is better than x- ray in assessment of ST and bones.

## Slide 15: MRI
Magnetic resonant imaging.
Better evaluation of soft tissue.
Expensive.
Useful for soft tissue pathology:
Tumor, infection,

## Slide 16: MRI
Use strong magnetic field.
Can not be done portable.
No radiation hazard.
The scan usually take long time ( 30 – 60 mins)
Very susibtible to motion and metallic objects.

## Slide 18: Nuclear medicine
Gama camera.
Radioactive isotopes.
Functional test
(physiology).
very expensive.
Useful for:
Assessing the active tumors, bone involvement and renal functions.

## Slide 19: Nuclear medicine
Image features:
Projectional image.
Image contrast by tissue uptake and metabolism.

## Slide 20: Objectives:
Introduction.
Imaging modalities used to study the back.
Anatomy and normal appearance of the abdomen.
Common pathological cases.

## Slide 22: CT

## Slide 28: MRI

## Slide 29: MRI

## Slide 30: Objectives:
Introduction.
Imaging modalities used to study the back.
Anatomy and normal appearance of the abdomen.
Common pathological cases.

## Slide 31
50 y/o male patient presented with gradual abdomen distension.

## Slide 32
24 Y/O patient presented with sudden pain in the epi-gastric area and back.

## Slide 33
30 Y/O female patient presented with right upper quadrant pain.
She had tendrness in the right subcostal margin.
Lab test showing leukocytosis.

## Slide 34
Thickned wall
Stone
Comet tail.

## Slide 35
THANK YOU