## Slide 1: Size Reduction
Importance in Pharmacy
Smaller particle size and increased surface area, leads to:
More uniformity of weight and drug content
More impalpability and spreading of dusting and cosmetic powders
More stability of suspensions.
Increasing rates of dissolution, reaction, drying, extraction, ..etc

## Slide 2: Disadvantages of excessive size reduction
Possible change in polymorphic form
Possible degradation by heat
Less flowability
Static charge problems
Air adsorption, hence, less wetting

## Slide 3: Mechanisms of size reduction
Compression: positive pressure, e.g., nut crusher, ball mill
Impact: material is stationary and hit by an object ,e.g., hammer mill
Shear: cutting force, e.g., scissors, colloid mill
Attrition: breaking the edges of the solid either by impact or particle collisions(fluid energy mill

## Slide 4: Size Reduction Equipment Hammer Mill Intermediate crusher Feed P.S.:0.5-50mm, Product P.S.: 0.1-5 mm Size control:Hammer speed, screen size, feed size Use of deflectors to present the particles into hammer impact Advantages: Ease of cleaning, Minimum scale-up problems Disadvantages: Clogging of screen, heat build up on milling, Mill and screen wear

## Slide 5: Ball Mill
Fine crusher (Feed size: 1-5 mm. Product size: <0.2 mm)
Mechanism of size reduction: impaction and sompression
Critical speed= 76.6/square root of D. At this speed the centrifugal force becomes greater than the gravitational force and the balls held at the mill walls without milling
Advantages: wet or dry milling, continuous, abrasive material can be milled
Disadvantages: long milling time, tedious cleaning, high power consumption

## Slide 6: Fluid Energy Mill
Ultra-fine particle size production
Feed p. size:5OO microns
Product p. size:5-30 micons (Ultra-fine)
Grinding medium: superheated steam or
compressed air
Mechanism of size reduction: attrition and impaction
Built in classifiier
Advantages:
*Suitable for thermo-labile substances
because of the effect of the expanding gasses
*Inert gasses can be used to minimize oxidation
*Effective in producing huge surface area

## Slide 7: Colloid Mill
A colloid mill is used to reduce the particle
size of a solid in suspenn, or to reduce the
droplet size of a liquid suspended in another
liquid. This is done by applying high
levels of hydraulic shear.
It is frequently used to increase the stability
of suspensions and emulsions.

## Slide 8: Colloid Mill
The mill consists of a rotor and stator
Clearance from zero to1 mm
Thin film of material is passed
Between working surfaces is
Subjected to high shear
Product size: < 5 microns

## Slide 9
Particle size reduction
On small scale:
A: Trituration
B: Pulverization
C: Levigation